## Slide 1: ECFA DRD4 Work-Package(s) 4.5
Blake Leverington, as interim volunteer coordinator, on behalf of the participating groups
Physikalisches Institut, Heidelberg Universitaet

## Slide 2: WP 4.5
Task 4.5.1:
“Develop an improved radiation hard scintillating fibre with a fluorescence decay time less than 4 ns.”
The standard fast fibre is over 25 years old (SCSF-78M and -78MJ from Kuraray)
  Peaks at 450nm, 3.5m attenuation length, 2.8ns decay time
  3HF has a decay time of 8ns, but peaks at 550nm.
Goal: A new fibre with larger Stoke’s Shift (to >500nm ) would improve the transmission after irradiation of the fibre
  Should have same or better light yield, attenuation, decay time, and stable in time.
From the thesis of R. Ekelhof, 2016. TU Dortmund
Lots of “promising, but…”
Intrinsic attenuation length 3.5m
Approx. Operational range of 78MJ

## Slide 3: WP 4.5
Task 4.5.1 Milestones:
First, identify new scintillators, fluorescent dyes, or fibre modifications
  Market, literature (organic chemistry journals), simulation. Make contacts.
Obtain samples and characterize the bulk scintillator material  Possibly the hardest part. We can’t produce our own.
  Radiation hardness, timing, wavelength
Production of fibre samples (a few km) with Kuraray
  In contact with positive response. Production facility closed until mid-2024.
Testing and qualification of prototype fibre samples
  Light yield, attenuation length, timing, radiation hardness
Task 4.5.1 Deliverables:
  Report on candidates (between 2 and 3)
  Report on any produced prototype. Not guaranteed to find any.
SP32 and SP33 Sample 2 months after irradiation at CERN (~50kGy).

## Slide 4: Participating Groups
EPFL
  Has produced a few fibre based trackers and telescopes for various experiments and projects
  SiPM development with Hamamatsu and FBK; microlenses; irradiation studies
  Fibre winding for LHCB SciFi Tracker
  Cryo-cooling of SiPMs for LHCb Upgrade 2
  Investigating new scintillators with polymer chemists at EPFL
  Good connection with Kuraray (fibres)
Heidelberg
  Module production for LHCb SciFi Tracker
  Irradiation studies of Fibres
  Development of LHCb Upgrade 2 Fibre and Pixel Tracker
  Ion-beam profile monitor for HIT clinic
  Investigating new scintillators for fibres
WP 4.5 | 4.5.1
CERN SY-BI | x
CERN-EP | x
CERN-LHCb | x
Clermont-Ferrand | x
Heidelberg | x
Lausanne - EPFL | x
No. of groups | 6
CERN-LHCb + -EP + SY-BI
  SPACAL for LHCb ECAL LS3 and Run5/6 Upgrades
  Irradiation of Scintillators
  LHCb SciFi QA
  Scintillator irradiation and characterization
  Beam Instrumentation
Clermont-Ferrand (Pascal Perret et al.)
  LHCb SciFi Tracker Electronics
Other groups expressed interest in the WG, but not willing to commit to the WP

## Slide 5: Resources
Group |  | FTE available |  |  |  | add. FTE needed |  |  |  | funds available [kEUR] |  |  | 
Short name | Country | 2024 | 2025 | 2026 | >2026 | 2024 | 2025 | 2026 | >2026 | 2024 | 2025 | 2026 | >2026
CERN SY-BI | CE | 0.10 | 0.10 | 0.10 | 0.10 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 
CERN-EP | CE | 0.10 | 0.10 | 0.10 | 0.10 | 0.00 | 0.00 | 0.00 | 0.00 | 1.00 | 1.00 | 1.00 | 
CERN-LHCb | CE | 0.10 | 0.10 | 0.10 | 0.10 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 
Clermont-Ferrand | FR | 0.10 | 0.10 | 0.10 | 0.10 | 0.00 | 0.00 | 0.00 | 0.00 | 1.00 | 1.00 | 1.00 | 
Heidelberg | DE | 0.2 | 0.4 | 0.4 | 0.4 | 0.00 | 0.00 | 0.00 | 0.00 | 7.00 | 7.00 | 7.00 | 
Lausanne - EPFL | CH | 0.4 | 0.4 | 0.4 | 0.4 | 2 | 2 | 2 | 2 | 50 | 50 | 50 | 10