## Slide 1: Digital single photon detector with highest sensitivity
Fabrice Retiere (TRIUMF)
Work done within the PHoton for Astro-particle and Applied Research (PHORWARD) group at TRIUMF
Collaboration with U.Sherbrooke (QC, Canada) for the Photon to Digital Converter

## Slide 2: Aim: Digital SPAD arrays
Scalability
  High cumbersome analog solution when area > few m2
High performance
  Timing resolution and re-triggering
  Eliminate after-pulse
  Lowest dark noise
Address specific SPADs
  Position reconstruction
  Wavelength filtering
~0.1nF/mm2
Analog to Digital
Conversion
Comparator (more power)
Waveform digitizer
Amplifier
Need power
to buffer
capacitance
Photon search engine
In software or firmware
Photon time stamp
AQ
Active
Quench
Digital processing
Photon time stamp
Photon
Photon
Bias
Bias

## Slide 3: Aim: back-side illuminated SPAD arrays
Versatility
  Visible to IR via thickness control
  Deep UV through Back-side surface processing
    Unconventional Anti-reflective coating: black silicon, graphene, 3D structures
  Non-photon detection
    Minimum ionizing
    keV scale electron (hybrid photo-detector)
    Dark matter
3
CMOS (in 2D or 3D)
Aka. electronics
Molecular bonding
Ultra-thin contact 1-5nm
Thin passivation ~100nm
e-
Low drift field region
Drift field region
Avalanche region
photon
CMOS
Aka. electronics
Molecular bonding
Ultra-thin contact 1-5nm
Thin passivation ~100nm
Low drift field region
Drift field region
Avalanche region
photon
Front Side illumination (ala Sherbrooke)
e-
Back side illumination
e-
h
e-

## Slide 4: Asset: Vacuum Ultra-Violet Efficiency reflectivity and Absorption setup (VERA)
For example: inferring the number of electrons produced per VUV photon

## Slide 5: Asset: MIEL
FBK Reflected Light and Laser Spot
2D Emission Map
IX-83 Microscope
Vacuum Chamber
SPAD
Cooled X-Y Stage
Vacuum Window
Dichroic Mirror
Emission Filter
Emitted Light
SiPM Surface
Objective
Spectroscopy
Imaging
A)
B)
Diffraction
Grating
Spectrometer and Cryogenically Cooled Camera
300 - 1500nm
Tunable laser

## Slide 6: Assets: simulations
Collaboration with ANSYS – Lumerical
Development of ”Quanta Level Avalanche Diode Simulator” (QLADS)
  Mixing charge carrier and photon transport
  U. Alberta, TRIUMF, U. Victoria
  Current focus on non-photon applications: Minimum Ionizing, keV electrons and dark matter
Example: QLADS used with diffusion region on top for MIP detection (ASGAP concept)

## Slide 7: Act: from concept to design to implementation
Analog BSI
  FBK + BSI processing at Teledyne-e2v
  Other option
2D implementation. Hoping to establish collaboration
  Heidelberg (Peter Fischer) + Fraunhoffer
  Use Lfoundry process in collaboration with DESY?
2.5D with FBK?
3D implementation
  Teledyne-DALSA + Sherbrooke: focus on front-side illuminated will likely continue for several more years
    New Canadian grant to expand access to DALSA. Results in April 2024.
  Establish collaboration with EPFL?

## Slide 8: Act: finding a path to making BSI SPAD
Find one or more facility to make prototypes
Simulate implementation and physical processes as well as possible
  Fairly clear path forward for that
Deal with Intellectual Property
  By now, most ideas have been claimed
  But ownership is not always clear
  Major roadblock overall
My hope is that we can build a functional collaboration within DRD4 to develop high performance digital BSI SPAD array in less than 5 years

## Slide 9: Act: development and funding strategies
Our (Canadian) funding situation
  Ongoing project funding
    nEXO and liquid Argon (DarkSide) supporting SiPM testing infrastructure and Sherbrooke Photon to Digital Converter R&D
  Some R&D funding
    SuperContinuum laser development
    Preparing new “Innovation Driven Integrated Detector” major request
  Some tech transfer funding
    Neutron detector for General Fusion
    Early Forest fire sensing system
Lacking funding and path forward for new detector fabrication
  Canada is now part of Horizon program
    Not exactly sure what it means
    But may be a path forward
  Can we pull resources together?
    Fabrication
    Design
    Characterization
Task 4.1.x → enabling the digital SPAD array revolution in PP/NP

## Slide 10: The end

## Slide 11: Building upon Photon to Digital Converter
PDC developed for Astro-particle physics
“Front-side” illuminated single photon detector
Designed at U.Sherbrooke (QC, Canada)
Built at Teledyne-DALSA (QC, Canada)
Parent, Samuel, et al. "Single photon avalanche diodes and vertical integration process for a 3D digital SiPM using industrial semiconductor technologies." 2018 IEEE Nuclear Science Symposium and Medical Imaging Conference Proceedings (NSS/MIC). IEEE, 2018.
JF Pratte NSS 2022 plenary talk

## Slide 12: Mitigation strategies
Minimize diffusion region thickness → limited by efficiency requirements
Absorb photons at front and back surface
Absorb photons in trenches
  The smaller the pitch the better
Minimize production by running at lowest possible gain
  Gain scales by diode capacitance so the smaller the better
CMOS – ch 1
CMOS – ch 2
CMOS – ch 0
Absorb photons at surface
Absorb photons
in trenches

## Slide 13: Quanta-Level Avalanche Diode Simulator (QLADS) for ASGAD
Charge particle simulation
  Use Bichsel cross-section for 45 GeV/c pions
  Normal incidence randomly over all area
Dark noise
  Assess the probability distribution function for the number of avalanches produced by 1 seed avalanche
  Use 50 Hz/mm2 for scale
Electron transport
  Random walk
    Diffusion constant = 3.9 um2/ns
    Electron life time = 100 ns
  No explicit EField
Photon from avalanches
  Vary average number of photons per avalanche + Poisson statistics
  Use measured spectrum
  Track photons but absorb on all surfaces
    Simplest but not most conservative

## Slide 14: Event display
Single seed avalanche
MIP
Sam de Jong (UVic)
Primary e- in red
e- from photons in purple

## Slide 15: Beyond ASGAD – Back-side illuminated for everything
CMOS
CMOS
p+
p
n+
n
SiO2
Poly
CMOS
p-epi
CMOS
Front side avalanche diode
Back side avalanche diode
Extended
80um
5-20um
5-50um
Ultra-thick
100-500 um
Geiger mode avalanche
VUV – Blue photon
Charged particle
Un-depleted
p-epi
depleted
Electron trajectories
Linear avalanche
Neutron or dark matter
Hole trajectories
Even dark matter search

## Slide 16: From trench isolated LGAD to Single Photon Avalanche Diode
G. Paternoster et al. 10.1109/LED.2020.2991351
Picture of a SPAD from the Photon to Digital Converter system

## Slide 17: Wavelength that are problematic

## Slide 18: The 3D integrated master plan

## Slide 19: Light emission to crosstalks
Light emission assumptions:
  At p-n junction – maximum field
  Isotropic
External cross-talk
  Photon escaping the SiPM surface
Internal cross-talk
  Photons being absorbed in a neibhoring SPAD
We measure photons escaping with objective acceptance
Single Photon Avalanche Diode