## Slide 1: Applications enabled by precise time & frequency services and their integration into existing networks
Dr. Jeroen C. J. Koelemeij
Vrije Universiteit Amsterdam (The Netherlands)
GÉANT Time and Frequency Workshop
CERN
February 8, 2024
Research carried out in collaboration with/with support from:
Marc Weiss Consulting

## Slide 2: White Rabbit research in the Netherlands
Many groups active in WR worldwide
WR research in the Netherlands:
Nikhef Amsterdam (WR hardware, KM3NeT neutrino telescope)
VSL Delft [UTC(VSL)]
SURF (NREN)
JIVE Dwingeloo (VLBI radio astronomy)
ASTRON (LOFAR radio telescope)
VU Amsterdam
   OPNT B.V. (spin-off company, 2014)

## Slide 3: Local fiber-optic testbed (WR + ultrastable laser)

## Slide 4: WR: subnanosecond network timing
Atomic clock
Graph: WR project website
White Rabbit (see also talk Javier Serrano, CERN)
  Other technologies exist (e.g. ELSTAB, Poland) with even better performance
WR residual timing errors can be as small as 0.1 ns
0.1 ns timing happens to be the requirement for two potentially ground-breaking new network technologies…
‘Timing’ = node clocks display same time of day

## Slide 5: 1. Quantum Internet
Quantum networks:
  Now: Quantum Key Distribution (QKD) – secure exchange of quantum information (photons)
  Future: networks of entangled qubits and photons for distributed quantum information processing
qubit A
qubit B
photon A
photon B
optical network
detector 1
detector 2
optical beam
splitter
Quantum information processing requires entangling qubits A and B
Entanglement achieved if two photons arrive at the same detector
- but only if two photons are indistinguishable: same color, same arrival time
In practice: photon emissions must be timed within 0.1 nanosecond*
* Moehring et al., Nature 449, 68 (2007); Stolk et al., PRX Quantum 3, 020359 (2022)

## Slide 6: 2. PNT systems beyond GNSS
GNSS: global navigation satellite systems
PNT: positioning, navigation and timing
Electromagnetic wave at speed of light in vacuum: 1 ns  0.3 m
  c = 299 792 458 m/s
Uncertainty GNSS receiver: 5-50 ns, or 1.5-15 m (or even worse)
Lane-level positioning of cars (decimeter-centimeter level) requires ~ 0.1 ns…
Quantum Internet requires ~ 0.1 ns…

## Slide 7: WR can help achieve this – but how?
Must use existing fiber-optic infrastructure, in parallel with telecom data
WR pro: telecom equipment, facilitates acceptance by network operators
WR con: bidirectional optical path needed, barrier to acceptance
  Can be solved by WDM VSL, SURF, VU, VTT, CSC; Dierikx et al., IEEE TUFFC 63, 945 (2016)
~100 km optical fiber
carrying many Tb/s
+ subnanosecond time
MUX
DEMUX
Service channel
WR channels
Up to 100
other optical channels
(>100 Gb/s each)
WR channels
Optical wavelength division multiplexing (WDM)
See also: outcomes CLONETS project https://www.clonets.eu/clonets.html
WR via WDM : E.F. Dierikx et al. IEEE Trans. Ultrason. Ferroelectr. Freq. Control 63, 945-952 (2016)
Earlier time transfer protocol via WDM: Lopez et al., Appl. Phys. B 110, 3 (2013)
Optical wavelength division multiplexing (WDM)

## Slide 8: Example: SURFnet8
P. Boven, C. van Tour, R. Smets. Demonstration of VLBI synchronization via existing SURFnet/LOFAR network. ASTERICS GA Deliverable D5.14. https://www.asterics2020.eu/sites/default/files/documents/asterics-d5.14.pdf
Westerbork
Dwingeloo
VSL
ESTEC
SMD
WR time distribution over live SURFnet8 production network (2019)
Purpose: synchronize Dwingeloo radio telescope to Westerbork telescope array
  H2020 ASTERICS project – VLBI demonstration using WR synchronization
  Similar: LOFAR radio telescope
2024: Nationwide time & frequency network rolled out by SURF
169 km WR link

## Slide 9: WR and positioning – how?
PNT through hybrid optical-wireless networks: ‘SuperGPS’ project

## Slide 10: ‘SuperGPS’ project (collaboration with Delft University of Technology, VSL Delft, and private partners)
Aviation
Relativistic geodesy
GNSS
1. Reference atomic clock
2. Subnanosecond time through fixed network
3. Wireless network for decimeter-level positioning (TDoA)
No dependence on satellites in space
Secure (fiber-optic) connections
Received signal power 106 times that of GNSS
Gerard
Janssen
Christian
Tiberius

## Slide 11: ‘SuperGPS’ project (collaboration with Delft University of Technology, VSL Delft, and private partners)
Aviation
Relativistic geodesy
GNSS
Back-up system for PNT through GNSS
Could also support quantum networks and distributed quantum computing
Gerard
Janssen
Christian
Tiberius
1. Reference atomic clock
2. Subnanosecond time through fixed network
3. Wireless network for decimeter-level positioning (TDoA)
No dependence on satellites in space
Secure (fiber-optic) connections
Received signal power 106 times that of GNSS

## Slide 12: WR network VSL – TU Delft
Network map (Delft)
Erik Dierikx
Yan Xie
UTC(VSL)

## Slide 13: Hybrid optical-wireless network
WR subnanosecond time distribution through optical fiber

## Slide 14: Hybrid optical-wireless network
WR subnanosecond time distribution through optical fiber + wireless PNT

## Slide 15: Field trial & performance
The Green Village site @TU Delft, Sep 2020
Network map (Delft)
Positioning with 10 cm uncertainty
Wireless network time distribution with subnanosecond uncertainty
Radio spectrum and modulation similar to 4G/5G networks
Koelemeij et al., Nature 611, 473 (2022);
Tiberius et al., NAVIGATION: J. Inst. Nav. Sep. 2023, 70 (3) navi.589

## Slide 16: Redundancy and fail-over
GNSS backup & quantum networks: security and reliability are of the essence, and so must be timing accuracy, availability and integrity
BUT: WR designed for single reference clock: single point of failure
Need for redundant clocks and paths + fail-over mechanisms
Challenge: seamless fail-over
(clocks drift by nanoseconds)

## Slide 17: Network timescale based on a clock ensemble
Clock 1
Clock 2
Clock 3
WR
S1
WR
S2
WR
S3
WR switch measures time differences
between all three clocks:
{ x12(t), x13(t), x23(t) }

## Slide 18: Network timescale based on a clock ensemble
Clock 1
Clock 2
Clock 3
WR
S1
WR
S2
WR
S3
{x12(t), x13(t), x23(t)}
Timescale algorithm
Clock comparison data used by
timescale algorithm to determine
optimum ‘average time’ (=ensemble time)
See for example
Weiss & Weissert, Metrologia 28, 65 (1991)
Greenhall, IEEE TUFFC 59, 491 (2012)
and references therein

## Slide 19: Network timescale based on a clock ensemble
μstepper
Clock 1
Clock 2
Clock 3
WR
S1
WR
S2
WR
S3
{x12(t), x13(t), x23(t)}
WR S1
Correction 1
Timescale algorithm
Timescale algorithm provides time
correction to be applied to each clock
Microstepper allows
correcting the clock
output without
disturbing the clock itself
Timescale
ouput
To users

## Slide 20: Extensions for increased redundancy
μstepper
μstepper
μstepper
Clock 1
Clock 2
Clock 3
WR
S1
WR
S2
WR
S3
{x12(t), x13(t), x23(t)}
WR S1
WR S2
WR S3
Correction 1
Correction 2
Correction 3
Time-scale algorithm
{x’12(t), x’13(t), x’23(t)}
Many options for redundant
measurements and systems
To users
To users
To users

## Slide 21: Time measurement and time production networks
μstepper
μstepper
μstepper
Clock 1
Clock 2
Clock 3
WR
S1
WR
S2
WR
S3
WR S1
WR S2
WR S3
Correction 1
Correction 2
Correction 3
Time-scale algorithm
Time measurement
network
Time production
network
Similar concept proposed by
Cosart, Imlau, Zampetti
IEEE Comms. Mag. April 2023, p.28

## Slide 22: Proof-of-principle clock ensemble
Measurement network monitors four ‘clocks’
Algorithm: simple mean of clock times  improves stability of production network time
Rodrigo González
Escudero
Marc Weiss
Sougandh
Kannoth Mavila

## Slide 23: The power of clock ensemble algorithms
Multiple clocks offers not only redundancy, but also more stable network time!
Simulation (to be tested in a WR network with real atomic clocks soon):
Future UTC(?)
Échelle Atomique Libre and TAI based on WR?
Circular T every second (instead of daily/weekly)?

## Slide 24: Layered network & organic growth
Start with backbone network
Deploy WR only there where necessary
WR gear can also provide time through other protocols (NTP, PTP)
  Energy grids, mobile networks, data centers, financials, …
WDM: add ultrastable laser wave
Reserve 24 channels per fiber pair
  Fiber 1: 2 WR, 2 WR calibration
  Fiber 2: 2 WR, 2 ultrastable laser
  25 GHz spacing?
Bidirectional rings and/or other redundant topologies, over shared or
dedicated dark fiber
High-reliability UTC
to cloud over NTP/PTPv2/PTPv2.1
UTC PoP
UTC PoP
UTC PoP
Redundant UTC time inputs
(e.g. NMI, GPSDO, Galileo receiver, …)
UTC PoP
WR Grandmasters
(GMs)
WR Boundary
Clocks (BCs)
See also: Krehlik et al., IEEE TUFFC 64, 1884 (2017), and:
CLONETS Deliverables, https://www.clonets.eu/clonets.html

## Slide 25: Thank you!
VU Amsterdam
Rodrigo Gonzalez Escudero
Marc A. Weiss (ext. consultant)
Sougandh Kannoth Mavila
Rob Kortekaas
Kjeld Eikema
TU Delft
Han Dun
Cherif Diouf
Christian Tiberius
Gerard Janssen
VSL
Erik Dierikx
Yan Xie
University of Amsterdam
Klaasjan van Druten
Sumit Sarkar
Philippe Bouyer
Florian Schreck
JIVE
Paul Boven
SURF
Rob Smets
Sander Klemann
Paul Klop
CERN
White Rabbit team
Questions: j.c.j.koelemeij@vu.nl