## Slide 1: Status of EBTS and Plans for 2024-2025
12 December 2023 @ BGC Collaboration Meeting
A. Rossi, work by M. Sameed, M. Ady, C. Castro, O. Stringer, H. Zhang, …

## Slide 2: Electron Beam Test Stand (EBTS) Quick Recap
S. Sadovich, A. Kolehmainen

## Slide 3: Outline
Status of Future BGC on EBTS
  Final Design and Integration
Status of HEL Collector
  Fabrication, Assembly and Installation
Summary

## Slide 4: BGC v4.1 Requirements
Gas
  Ability to operate with all three gases (N2, Ne, Ar)
  Provision of appropriate gas bottles and pneumatic equipment
Gas jet
  Gas jet density same as v3 instrument (1016 m-3) or larger
  Curtain length to be able to see the beam with 40 mm OD (so 60 mm curtain at 45 degrees).
  Curtain width same as v3 instrument (0.5 mm) or smaller –
  Curtain variation same as v3 instrument (5%) or less
  IC background pressure same as v3 instrument (10-7 mbar) or less
  Replaceable/adjustable skimmer 3.
Image Acquisition
  Provision of laser + camera for alignment and target/grid for camera focusing
  Provision of optics, image intensifier(s), filter(s), and camera(s), for 3 gases + BTV
  Addition of BTV on the DN63 port (design can be done by CERN)
Performance Evaluation
  Maximum 1 s integration for electron beam of 10 keV, 5 A, 40 mm diameter
  Aiming for 100 µm image resolution at the above parameters

## Slide 5
Imagining system
Gas curtain generation section
Interaction chamber
Beam direction
Alignment laser
Dump chamber
4th skimmer
1 m
Gas curtain direction
Insertable target
M. Ady, O. Sedlacek, C. Castro Sequiero, O. Stringer, H. Zhang
DN40 port now looks at the center of the interaction chamber
DN63 port now looks at the center of the interaction chamber
DN100 port now extends all the way to the pumping group (removed adapter piece)
DN63 port replaced with DN100 port downstream of the interaction chamber
BGC v3
BGC v4.1
BGC Design @EBTS

## Slide 6: BGC Design @EBTS
Imagining system
Gas curtain generation section
Interaction chamber
Beam direction
Alignment laser
Dump chamber
4th skimmer
1 m
Gas curtain direction
Insertable target
BTV (with OTR screen) installed on the DN63 port
BGC v3
BGC v4.1
M. Ady, O. Sedlacek, C. Castro Sequiero, O. Stringer, H. Zhang

## Slide 7: BGC v4.1 Design
Imagining system
Gas curtain generation section
Interaction chamber
Beam direction
Alignment laser
Dump chamber
4th skimmer
1 m
Gas curtain direction
Insertable target
Skimmer 4 is now installed on the interaction chamber
150 mm
4th Skimmer: 85 mm x 1.12 mm
BGC v3
BGC v4.1
M. Ady, O. Sedlacek, C. Castro Sequiero, O. Stringer, H. Zhang

## Slide 8: BGC Design @EBTS
Imagining system
Gas curtain generation section
Interaction chamber
Beam direction
Alignment laser
Dump chamber
4th skimmer
1 m
Gas curtain direction
Insertable target
Dump chamber is now made entirely from standard parts (DN100-DN160 4-Way Reducing Cross)
Camera for alignment laser
Pfeiffer TMP HiPace 700
Standard Pfeiffer pressure gauges
DN 100 Gate Valve
BGC v3
M. Ady, O. Sedlacek, C. Castro Sequiero, O. Stringer, H. Zhang

## Slide 9: BGC v4.1 Requirements (Simulation Results)
Gas
  Ability to operate with all three gases (N2, Ne, Ar)
  Provision of appropriate gas bottles and pneumatic equipment
Gas jet
  Gas jet density same as v3 instrument (1016 m-3) or larger – 1.3 x 1016 m-3
  Curtain length to be able to see the beam with 40 mm OD (so 60 mm curtain at 45 degrees).
  Curtain width same as v3 instrument (0.5 mm) or smaller – 0.2 mm
  Curtain variation same as v3 instrument (5%) or less – 3%
  IC background pressure same as v3 instrument (10-7 mbar) or less – 10-8 mbar
  Replaceable/adjustable skimmer 3.
Image Acquisition
  Provision of laser + camera for alignment and target/grid for camera focusing
  Provision of optics, image intensifier(s), filter(s), and camera(s), for 3 gases + BTV
  Addition of BTV on the DN63 port (design can be done by CERN)
Performance Evaluation
  Maximum 1 s integration for electron beam of 10 keV, 5 A, 40 mm diameter
  Aiming for 100 µm image resolution at the above parameters

## Slide 10: BGC v4.1 Integration
Top View
H. Zhang

## Slide 11: BGC v4.1 Integration
Side View
H. Zhang

## Slide 12: HEL Collector
HEL Collector Details
  Entrance aperture: 80 mm
  Gun-Collector Potential: up to +5 kV
  Beam Current: up to 5 A
Benefits
  Works with both DC and pulsed electron beams
Challenges
  Vacuum/pumping requirements are high
  Reflected / secondary electrons needs to be suppressed  BGC
  Requires high voltage platform
A. Kolehmainen, M. Sameed
Retarder
Repeller
Collector
Back Repeller

## Slide 13: Status of HEL Collector
Design
Complete
Installation
Planned for Q1 2024 (tentatively during week of 11 March)
Simulations
Fabrication
All parts ordered
Fabrication ongoing
Delivery in March 2024
I. Tabian
Complete
T. Coiffet, A. Gerardin, L. Deparis
A. Kolehmainen

## Slide 14: Summary
Design, simulations, and integration model for BGC v4.1 on EBTS almost complete…design should be approved during BGC collaboration meeting and drawings should be finalized and approved to start procurement…delivery June 2024?
HEL collector fabrication and assembly underway, delivery scheduled for Q1 2024

## Slide 15: Thank You !
Questions?

## Slide 16: Backup Slides

## Slide 17
Current 3rd skimmer design, host 35 mm skimmer maximum. Is that enough?

## Slide 18: HEL Design under study
Hollow e-beam
p-beam
BPM
BPM
SC solenoids
Collector
(electron beam dump)
electron gun
compensation dipole
beam gas curtain (BGC) profile monitor
Accelerates a hollow electron beam up to
5 A and 15 keV
Control the e-beam
beam position monitor (BPM)
Compensates the kick
produced by the steering solenoids

## Slide 19: Electron Gun
Cathode Parameters
  OD: 16.10mm, ID: 8.05mm
  Current Density: 3.3 A/cm2
Electron Beam Parameters
  Beam Current: 0-5 A
  Beam Energy: 0-15 keV
Pulse Modulator (Marx Generator)
  Pulse Duration: 1us - 100us
  Rise/Fall Time: 200 ns
  Repetition Frequency: 1Hz - 50 Hz
A. Kolehmainen, D. Perini, S. Sadovich, G. Stancari, T. Coiffet, M. Plantier
Glowing Hollow Cathode
HEL Gun v1 (FNAL)
HEL Gun v3 (CERN)

## Slide 20: Electron Gun
A. Kolehmainen, D. Perini, S. Sadovich, G. Stancari, T. Coiffet, M. Plantier
HEL Gun v1 (FNAL)
HEL Gun v3 (CERN)
2 mA
25 mA
45 mA
88 mA
139 mA
Gun Characterization
  Measurements at both FNAL and CERN
  Comparison of experimental results with simulations (SAM / WARP / CST / TRAK)

## Slide 21: EBTS Solenoids and Correctors
400A
560A
800A
* Current at Gun Solenoid
BTV
BPM
BDB
Gun
A. Rossi
Notes: A schematic of the Electron Beam Test Facility is shown in fig. 1. The magnetic system is designed to ensure the confinement of the electron beam and its transport to the collector. It is composed of ambient temperature (water cooled) solenoid magnets, depicted in blue. Each magnet is provided with horizontal and vertical dipoles to steer the electron beam to either compensate for mechanical misalign- ment or displace it and measure the range of the BPM. The modularity allows to have different magnet configurations installed, depending on need and number of components present at the facility. At the gun side, a pair of magnets provides an extended region of constant field. The vacuum system is divided into two volumes by an all-metal auto- matic gate valve. One volume is reserved for the electron gun and a diagnostic box (detailed later), and the other for any equipment that needs testing. Each volume is equipped with a pumping system capable of keeping a pressure in the range of 10−8 mbar during electron beam operation.

## Slide 22: EBTS Solenoids and Correctors
400A
560A
800A
* Current at Gun Solenoid
BTV
BPM
BDB
Gun
Beam Compression
A. Rossi
Notes: A schematic of the Electron Beam Test Facility is shown in fig. 1. The magnetic system is designed to ensure the confinement of the electron beam and its transport to the collector. It is composed of ambient temperature (water cooled) solenoid magnets, depicted in blue. Each magnet is provided with horizontal and vertical dipoles to steer the electron beam to either compensate for mechanical misalign- ment or displace it and measure the range of the BPM. The modularity allows to have different magnet configurations installed, depending on need and number of components present at the facility. At the gun side, a pair of magnets provides an extended region of constant field. The vacuum system is divided into two volumes by an all-metal auto- matic gate valve. One volume is reserved for the electron gun and a diagnostic box (detailed later), and the other for any equipment that needs testing. Each volume is equipped with a pumping system capable of keeping a pressure in the range of 10−8 mbar during electron beam operation.

## Slide 23: EBTS Solenoids and Correctors
400A
560A
800A
* Current at Gun Solenoid
BTV
BPM
BDB
Gun
H/V Correction
A. Rossi
Notes: A schematic of the Electron Beam Test Facility is shown in fig. 1. The magnetic system is designed to ensure the confinement of the electron beam and its transport to the collector. It is composed of ambient temperature (water cooled) solenoid magnets, depicted in blue. Each magnet is provided with horizontal and vertical dipoles to steer the electron beam to either compensate for mechanical misalign- ment or displace it and measure the range of the BPM. The modularity allows to have different magnet configurations installed, depending on need and number of components present at the facility. At the gun side, a pair of magnets provides an extended region of constant field. The vacuum system is divided into two volumes by an all-metal auto- matic gate valve. One volume is reserved for the electron gun and a diagnostic box (detailed later), and the other for any equipment that needs testing. Each volume is equipped with a pumping system capable of keeping a pressure in the range of 10−8 mbar during electron beam operation.

## Slide 24: Beam Instrumentation at EBTS

## Slide 25: Beam Profile Monitors
1. YAG:Ce Screens
2. Pin-Hole Faraday Cup
3. BTV Screen
(Scintillation or OTR)
4. Beam Gas Curtain (BGC)
Beam Diagnostic Box (BDB)
BTV+BGC

## Slide 26: Beam Diagnostic Box
Pin Hole Faraday Cup
Vacuum Pump
Vacuum Gauge
Gas Injection
Pin Hole Faraday Cup
YAG:Ce Screens
Vacuum Pump
Vacuum Gauge
Gas Injection
F. Guillot-Vignot
Notes: The diagnostic box consists of a 6-arm chamber (pictured on the left hand side in fig. 2), where a movable YAG Ce scintillator screen and a multi-hole Faraday Cup (FC) can be inserted to measure the electron beam profile and intensity. The other arms are used for gas injection (for venting the vac- uum system with nitrogen), pressure measurement, support of the structure, and one spare arm. The light produced at the YAG screen is collected by a camera positioned behind a viewport at the back of the collector

## Slide 27: YAG:Ce Screens
Screen Details
  Two screens (Al-coated and ITO-coated) on a linear translator
  50 mm diameter
Benefits
  High photon yield (2 x 10⁴ photons/MeV)
  Short decay time (~100 ns)
  Very high image resolution
Challenges
  Image saturation and/or screen damage at high beam current or long pulse duration
Al-coated
YAG:Ce Screens
ITO-coated
F. Guillot-Vignot
Notes: The diagnostic box consists of a 6-arm chamber (pictured on the left hand side in fig. 2), where a movable YAG Ce scintillator screen and a multi-hole Faraday Cup (FC) can be inserted to measure the electron beam profile and intensity. The other arms are used for gas injection (for venting the vac- uum system with nitrogen), pressure measurement, support of the structure, and one spare arm. The light produced at the YAG screen is collected by a camera positioned behind a viewport at the back of the collector