## Slide 1: Final cooling RF cavity and solenoid coil integration.
Alexej Grudiev
30.11.2023

## Slide 2: Example of final cooling design
Transverse size of the muon beam in transport solenoid: 3sigma ~ 30mm
To transport the beam a beam pipe of ~ 50 mm radius would be fine.
Solenoids of ~100 mm inner radius could provide such a transport channel
Elena Fol
Preliminary

## Slide 3: Example of RF cavity
LHC TDR v3, p59
RF frequency range: 20 – 200 MHz
CERN PS 40 MHz RF cavity: 1.6m diameter, 1m long
Far from fitting into the schematic on previous slide
Would be very difficult if not impossible to put inside of a 3.5T solenoid

## Slide 4: Possible combination of RF cavities and coils
solenoid
solenoid
solenoid
solenoid
solenoid
solenoid
solenoid
solenoid
Interleaving RF voltage gaps with solenoid coils allow to combine small solenoid radius with large cavity radius
Bz is not constant in such a channel. Implication on the beam transport must be evaluated
It will define the maximum gap size for a given coil radius

## Slide 5: Some conclusions
Obvious disadvantage is that accelerating gaps are separated by the coils. Impact on the real estate gradient must be evaluated.
Main advantage of proposed cavity-coil layout is potential reduction of the magnetic stored energy (~R2), etc
There might be other “side-effect” advantages
  Easier access to the cavity: RF coupler, tuner, RF probes, vacuum pumping, etc
  Using ferrite loaded cavity outside of the solenoid coils becomes not impossible
  Coupling cavities into a larger accelerating structure, “a la” DTL, becomes an interesting option
Similar approach might be applied to other solenoid coil transport channels (Front end, bunch merge, reacceleration, …)