## Slide 1
Particle IDentification (PID) in the HMPID
Erlend Flatland
University of Agder / CERN

## Slide 2
Outline
HMPID Description
HMPID structure
Particle IDentification (PID) in the HMPID
Current PID algorithm in the HMPID

## Slide 3
HMPID Description

## Slide 4
HMPID description
The HMPID gets track information from the ITS, TPC, TRD and TOF
HMPID has 5 % of TPC acceptance
Notes: The PID in HMPID is a joint effort;
  The HMPID gives an estimate of the mass with help of information given by other detectors
The HMPID gets track information from the ITS, TPC, TRD and TOF

## Slide 5
ALICE event display
Notes: ALICE-PHO-GEN-2022-009
https://cds.cern.ch/record/2841865
ALICE event displays and geometry rendering of lead-lead ion collisions during Run 3
Event displays of the first Pb-Pb collision of Run3 taken at ALICE which sees its first event displays of heavy ion - lead-lead (Pb-Pb) - collisions during Run 3. Lead beams travelled for 3 days (17-19 November) in the LHC accelerator. ALICE is one of the main experiments on the LHC who profits mostly from the results of the lead-lead ion beam optimized to study the collisions of nuclei. The aim is to study the physics of strongly interacting matter at the highest energy densities reached so far in the laboratory.
Photograph: Dobrigkeit Chinellato, David
Keywords: ALICE; Run 3
Note: General Photo

## Slide 6
RADIATOR
15 mm liquid C6F14, n ~ 1.2989 @ 175nm, βth = 0.77
ALICE-HMPID (High Momentum Particle Identification Detector) performs charged particle track-by-track identification by means of the measurement of the emission angle of Cherenkov radiation and of the momentum information provided by the tracking devices.
HMPID description
PHOTON CONVERTER
Reflective layer of CsI QE ~ 25% @ 175 nm. The largest scale (11 m2) application of CsI photo-cathodes in HEP
≈ 5 % of TPC acceptance
PHOTOEL. DETECTOR
- MWPC with CH4 at atmospheric pressure (4 mm gap) HV = 2050 V.
- Analogue pad readout
It consists of seven identical proximity focusing RICH counters.
Notes: Cherenkov photons are emitted if the velocity threshold βth = 0.77 is exceeded in the Radiator
Credits to Giacomo Volpe https://indico.cern.ch/event/1246704/?view=nicecompact
The Cherenkov photons are detected using Multi-Wire-Proportional-Chambers (MWPC) flashed with CH4 and equipped with Pad-segmented cathodes
activated with a 300 nm thick layer of CsI [6, 4].
In the HMPID, the production of Cherenkov radiation is done by using a radiator medium in the form of liquid C6 F14 (perfluorohexane) [6].

## Slide 7
HMPID description
CsI photo-cathode is segmented in 0.8x0.84 cm pads
Six photo-cathodes per module
Notes: Credits to Giacomo Volpe https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 8
Cherenkov radiation

## Slide 9
Cherenkov radiation
For the given material, with refractive index n(λ, T),
Cherenkov radiation occurs if the velocity-threshold is exceeded:
A charged particle emits Cherenkov radiation if its velocity exceeds the phase velocity of the medium it travels through.
phase velocity of medium
Velocity threshold
RADIATOR
15 mm liquid C6F14, n ~ 1.2989 @ 175nm, βth = 0.77
Typical phase velocity of the HMPID radiator :
An analog can be made to the creation of sonic booms when the speed of sound is exceeded
Notes: Credits to Giacomo Volpe https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 10
Cherenkov radiation
The Cherenkov photons will form a cone-like shape along the particle trajectory and have an angle
(the Cherenkov angle), increasing with speed.
Cherenkov angle
The relation between the particle’s speed 𝛽 and the Cherenkov angle is given by the Cherenkov equation:
Notes: Figure on right :
Blair Ratcliff and Jochen Schwiening. “Cherenkov Counters.” In: Handbook of Particle Detection and Imaging.
Ed. by Claus Grupen and Irène Buvat. Berlin, Heidelberg: Springer Berlin
Heidelberg, 2012, pp. 453–471. isbn: 978-3-642-13271-1.
doi: 10.1007/978-3-642-13271-1_18.
url: https://doi.org/10.1007/978-3-642-13271-1_18.

## Slide 11
HMPID Structure

## Slide 12
HMPID Structure
Track impact parameters
Track inclinations
• MIP position (xp, yp) in PC-plane
• Impact point on RAD
• Track polar angle θp
RAD
PC
(xp, yp)
• Track azimuthal angle ϕp
ϕp
Cherenkov patterns for different θp
θp
Notes: Figure adapted from HMPID TDR:
Dariusz Czerwinski et al. “Alice Technical Design Report of the High Momentum Particle
Identification Detector.” In: Sept. 1998.
Isbn : ISBN 92-9083-134-0.

## Slide 13
Particle IDentification (PID) in the HMPID

## Slide 14
PID in the HMPID
0 1 2 3 4 5 p (GeV/c)
1 10 100 p (GeV/c)
TRD e /π
PHOS γ /π0
TPC + ITS
(dE/dx)
π/K
π/K
π/K
K/p
K/p
K/p
e /π
e /π
HMPID
(RICH)
TOF
EMCAL
Solid: track-by-track
Dashed: only statistical
“Relativistic rise”
Momentum ranges for PID in ALICE
Notes: The HMPID carries out particle identification by means of measurement of the emission angle of Cherenkov photons, combined with momentum measurements provided by the central tracking systems in ALICE (ITS and TPC) [14].
Credits to Giacomo Volpe https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 15
PID in the HMPID
Particle IDentification (PID) in the HMPID
For PID : the mass and charge of the mass has to be known to establish which specie a particle is
The PID in HMPID is a joint effort;
  The HMPID gives an estimate of the mass with help of track information given by other detectors (ITS, TPC, TRD and TOF)

## Slide 16
PID in the HMPID
Cherenkov angle ( θc ) to be measured by the HMPID
By inverting the equation, m can be calculated
Momentum (p) given from TPC
Refractive index (n) is constant
Particle IDentification (PID) in the HMPID
Notes: Figure adapted from HMPID TDR:
Dariusz Czerwinski et al. “Alice Technical Design Report of the High Momentum Particle
Identification Detector.” In: Sept. 1998.
Isbn : ISBN 92-9083-134-0.

## Slide 17
PID in the HMPID
Event Display
Notes: The biggest challenge in Particle IDentification in the HMPID is in PbPb collisions because of lower Signal-to-Noise Ratio (SNR)
Credits to Giacomo Volpe https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 18
PID in the HMPID
Track-MIP matching
Every track to be reconstructed has to be matched with a Minimum Ionizing Particle (MIP) cluster on the HMPID Photo-Cathode
The MIP has distinct features in detected charge and cluster size
One can do a separation of MIPs from photons by applying cuts for the charge and size
  For instance, 200 ADC channel charge and more than 2 pads fired

## Slide 19
PID in the HMPID
Track-MIP matching
The distance from the extrapolated track to the MIP is a crucial parameter for PID
A cut for the distance is applied; only reconstructing tracks under a certain distance
Notes: Credits to Giacomo Volpe https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 20
PID : Parameters
Track impact parameters
Track parameters
• MIP position (xp, yp) in PC-plane
• Impact point on RAD
→ Extrapolated to PC
Cluster map
All clusters in a given chamber of an event
Clusters have numerous features, most important :
size (number of pads fired)
Charge
Position (x, y)
• Track azimuthal angle ϕp
• Track polar angle θp
• Track momentum p
PID in the HMPID
ϕp
RAD
PC
(xp, yp)
Notes: Figure on top adapted from HMPID TDR:
Dariusz Czerwinski et al. “Alice Technical Design Report of the High Momentum Particle
Identification Detector.” In: Sept. 1998.
Isbn : ISBN 92-9083-134-0.
Credits to Giacomo Volpe for figure on bottom https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 21
Current PID algorithm in the HMPID :
Difficulties with PID in Pb-Pb collisions in the HMPID
PID workflow in the HMPID
Hough Transform Method
Single and ring-average Cherenkov photons distributions
Evaluation of performance

## Slide 22
Difficulties with PID in Pb-Pb collisions in the HMPID
The biggest challenge in PID in the HMPID is in Pb-Pb collisions because of lower Signal-to-Noise Ratio (SNR)
Current PID algorithm in the HMPID
PID workflow in the HMPID
The PID algorithm involves finding emitted Cherenkov photons in the Photo-Cathode emitted by a track matched with a MIP
Background signals are for instance emitted photons that belongs to other tracks, feedback photons and secondary charged particles
The ability to distinguish the actual signal (the Cherenkov photons) from background signals are limited.

## Slide 23
PID workflow in the HMPID
Try to match every track given by the tracking devices that intersects the HMPID acceptance with MIPs in the HMPID Photo-Cathode (PC) [MatchHMP.cxx#L391]
Particle IDentification (PID) is undertaken using the Hough Transform Method (HTM)
The method is used for track-by-track identification of charged particles in the HMPID
Current PID algorithm in the HMPID
PID workflow in the HMPID
For every event, the following is done :
If the track is matched with a MIP : evaluate the distance from the MIP to the extrapolated track’s intersection with the PC-plane [MatchHMP.cxx#L538]

## Slide 24
PID workflow in the HMPID
Only consider tracks that are under a certain distance threshold
Current PID algorithm in the HMPID
PID workflow in the HMPID
  Fit the matched MIP-track pair, to allow increased precision of the track
(the position of the MIP is used to fit the track) [MatchHMP.cxx#L496]
  Evaluate the Cherenkov angle θc of the track by combining the matched track-MIP information with all the clusters in the intersected chamber.
The Cherenkov angle is estimated using the Hough Transform Method [MatchHMP.cxx#L563] [Recon.cxx#L49]

## Slide 25
Current PID algorithm in the HMPID
Current PID algorithm in the HMPID :
Hough Transform Method (HTM)

## Slide 26
Hough Transform Method (HTM)
Current PID algorithm in the HMPID
Hough Transform Method
Background discrimination is performed exploiting the Hough Transform Method (HTM).
HTM is an efficient implementation of a generalized template matching strategy for detecting complex patterns in binary images.
Notes: Credits to Giacomo Volpe for figure on bottom https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 27
Mapping to one-dimensional space
cluster coordinate
impact track parameter
solution in one dimensional mapping space ηc
Cherenkov
angle
⇓
(x,y) → ((xp,yp,θp,ϕp), ηc)
A “Hough counting space” is constructed for each charged particle :
Current PID algorithm in the HMPID
Hough Transform Method
  For every cluster in the chamber, the photon
Cherenkov angle ηc is evaluated [Recon.cxx#L77]
  The photon emission angles are reconstructed
using a backtracing loop method [Recon.cxx#L145]
Notes: Let ηc,i ​ represent an individual value, and let ηc denote the collection of all such values

## Slide 28
Mapping to one-dimensional space
Photon-cluster hit map
Photon Cherenkov angles
“Hough counting space”
ηc, track
“Cherenkov angle space”
Current PID algorithm in the HMPID
Hough Transform Method
cluster coordinate
(x,y) → ((xp,yp,θp,ϕp), ηc)
nclusters entries in cluster map
nclusters entries
Notes: This figure is just meant to mimic the pattern of an orthogonal track and the mapping to the Hough Counting space
It does not come from real data or from simulation

## Slide 29
Hough counting space
The reconstruction of ηc for all clusters within a chamber for a given track is referred to as the 'Cherenkov angle space', or the 'Hough Counting space'.
Current PID algorithm in the HMPID
Hough Transform Method
This distribution is also referred to as a single Cherenkov photon distribution ηc, track
The single-photon distribution (ηc, track) of many tracks ηc with the similar momentum is gaussian, and has standard-deviations (angular resolution) depending on various parameters

## Slide 30
Angular resolution
For a track with inclination angles and momentum, each cluster in the chamber has its distinct angular resolution
The angular resolution varies with the detector status, inclination angles and the position of the MIP and cluster.
The RMS resolution is found by the propagation of each of the variables :
Chromatic error (E) : Spread in photon-energy
Geometric error (RW) : Track inclination
Localization error (R) : Cluster position
Track inclination angles (θp)
Current PID algorithm in the HMPID
Hough Transform Method

## Slide 31
Angular resolution :
Typical values
Current PID algorithm in the HMPID
Hough Transform Method
From HMPID TDR
Notes: Dariusz Czerwinski et al. “Alice Technical Design Report of the High Momentum Particle Identification Detector.” In: Sept. 1998. isbn: ISBN 92-9083-134-0.

## Slide 32
Angular resolution :
Chromatic error (1/2)
Current PID algorithm in the HMPID
Hough Transform Method
The spread of the photon energy in the radiator leads to the spread in the refractive index and subsequently Cherenkov angle per photon.
The distribution can be modelled as a gaussian distribution:
The detector is calibrated; the mean value of the photon energy for a given run is known.
Notes: More is explained later under Angular resolution : Chromatic error (E) : Detector status

## Slide 33
Angular resolution :
Chromatic error (2/2)
For photons in same ring :
𝛽 (track velocity) is constant
radiator temperature T is constant
photon energy (through wavelength λ) differs
  → n is different
Spread in ηc around θc
Current PID algorithm in the HMPID
Hough Transform Method
ηc
Notes: More is explained later under Angular resolution : Chromatic error (E) : Detector status

## Slide 34
Angular resolution :
Geometric Error
Current PID algorithm in the HMPID
Hough Transform Method
Unknown emission point of Cherenkov photons in the radiator, assumed to happen in the middle of the radiator width.
Uniform distribution of emission point

## Slide 35
Angular resolution :
Localization error
Current PID algorithm in the HMPID
Hough Transform Method
=

## Slide 36
Angular resolution :
Track inclination errors
Current PID algorithm in the HMPID
Hough Transform Method
Occurs due to errors in the measurement from the tracking devices.
Assumed to be constant with

## Slide 37
sq, 0.5 T ≈ 10 mrad
sq, 0.2 T ≈ 7 mrad
Track inclination, 0.5 Tesla
Track inclination, 0.2 Tesla
Current PID algorithm in the HMPID
Hough Transform Method
Angular resolution with field strength
Notes: Credits to Giacomo Volpe for figure on bottom https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 38
ηc
Single photon distribution for one track
Single photon distribution for many tracks in same momentum range
Monte Carlo (MC) simulated events by Pion-gun
Tracks per chamber on average around 5
Fixed momentum 2.7..2.8 [GeV/c]
Single Cherenkov-photon distributions
Current PID algorithm in the HMPID
Hough Transform Method
Note that both are single-photon distributions
nclusters entries in map
ηc, track
Collect for many tracks
Notes: Monte Carlo simulated events by Pion-gun
Tracks per chamber on average around 5
Fixed momentum 2.7..2.8 [GeV/c]

## Slide 39
*For the given run. Depends on temperature, photon energy
Current PID algorithm in the HMPID
Hough Transform Method
Single Cherenkov-photon distributions
Mean value
ηc
p = 2.7-2.8 [GeV/c]
mπ= 0.1396 [GeV/c] # mass of pion
n = 1.291 [-]*
Peak (μ) of ηc distribution approximately equivalent to
Notes: Monte Carlo simulated events by Pion-gun
Tracks per chamber on average around 5
Fixed momentum 2.7..2.8 [GeV/c]

## Slide 40
The distribution has a tail, which can be attributed to the background signal
  The configuration from the plot above is a MC simulated Pion-gun with very high track-multiplicity (on average around 5 per chamber)
ηc
Current PID algorithm in the HMPID
Hough Transform Method
Single Cherenkov-photon distributions
Standard deviation
If one establishes a certain range around the calculated Cherenkov angle, one can analyze the symmetry of the distribution to distinguish the signal from the background
Notes: Monte Carlo simulated events by Pion-gun
Tracks per chamber on average around 5
Fixed momentum 2.7..2.8 [GeV/c]
* The particle Gun is configured with 40-70 tracks in the acceptance
o2-sim -n"$nev" -e TGeant3 -g boxgen --configKeyValues "BoxGun.pdg=211; BoxGun.phirange[0]=-5; BoxGun.phirange[1]=60; BoxGun.number=45; BoxGun.eta[0]=-0.5 ; BoxGun.eta[1]=0.5; BoxGun.prange[0]=2.7; BoxGun.prange[1]=2.8;" $simWorker --run ${runNumber}

## Slide 41
HTM : Width of sliding window
The width of the window is chosen to allow the majority of the signal to be included
Currently 45 mRad is used : HMPIDReconstruction/Recon.h#L61
45 mRad corresponds to 3-4 sigma of the single photon angular resolution
Current PID algorithm in the HMPID
Hough Transform Method
ηc, track
Notes: The above is not coming from real data or MC simulations, it is only meant for illustrative purposes
This is just for illustration purposes and does not match 45 mRad

## Slide 42
HTM : Sliding window iteration
The sliding window is iterated with 1 mrad in the Cherenkov angle space
Current PID algorithm in the HMPID
Hough Transform Method
ηc, track
Bins of 1 mRad is applied to the histogram [/Recon.h#L60C28-L60C28]
The iteration is done from 0 rad to 0.75 Rad [Recon.cxx#L531-L537]
The histogram will have k = 750 bins
Notes: The above is not coming from real data or MC simulations, it is only meant for illustrative purposes
This is just for illustration purposes and does not match 45 mRad

## Slide 43
HTM : Weighting procedure
Current PID algorithm in the HMPID
Hough Transform Method
ηc, track
Fit of background
Weights of photons
Single photon distribution
A weighting procedure for the selection of photons is applied
The weighting applied to each bin k is inversely proportional to the corresponding ring area for the bin
The weighted histogram is the number of photons in the given bin multiplied with the weight of the bin
Recon.cxx#L539-L561
Notes: The above is not coming from real data or MC simulations, it is only meant for illustrative purposes

## Slide 44
HTM workflow 1/3
Current PID algorithm in the HMPID
Hough Transform Method
Weighting
Recon.cxx#L563-L581
Notes: The above is not coming from real data or MC simulations, it is only meant for illustrative purposes
This is just for illustration purposes and does not match 45 mRad

## Slide 45
Current PID algorithm in the HMPID
Hough Transform Method
The sum of the weighted photons in the window :
The width of the sliding window is
Sum of weights
In window
Bin K with highest
The photons in the window at this bin is called the “Hough selected photons” ηc, selected
The number of photons in the window is
HTM workflow 2/3
Recon.cxx#L582-L589
Find the bin K in which is the highest weighted sum in the window
Notes: The above is not coming from real data or MC simulations, it is only meant for illustrative purposes
This is just for illustration purposes and does not match 45 mRad

## Slide 46
Current PID algorithm in the HMPID
Hough Transform Method
The Cherenkov angle ⟨θc⟩ of the track is provided by the weighted average of ηc, selected, track
is the weight for the photon i in bin k
HTM workflow 3/3
→ ⟨θc⟩ is the ring average of the Hough selected photons
Notes: The above is not coming from real data or MC simulations, it is only meant for illustrative purposes
This is just for illustration purposes and does not match 45 mRad

## Slide 47
Current PID algorithm in the HMPID
Current PID algorithm in the HMPID :
Single photon and ring-average Cherenkov photon distributions

## Slide 48
Single photon and ring-average distributions
Ring average / Track Cherenkov angle distribution
ηc
Current PID algorithm in the HMPID
Hough Transform Method
θc
Single Cherenkov photon distribution
The improved standard deviation from the single-photon to the ring-average distribution can be attributed to :
The width of the window of the HTM; which will discard outliers
The θc being the weighted average of the ring-selected photons
Notes: Monte Carlo simulated events by Pion-gun
Tracks per chamber on average around 5
Fixed momentum 2.7..2.8 [GeV/c]

## Slide 49
The ring-average distribution stems from selecting a certain set of photon Cherenkov angles values using the sliding window (The Hough selected photons) for each track to be reconstructed.
Ring average / Track distribution
Single photon distribution
Current PID algorithm in the HMPID
Hough Transform Method
ηc
θc
Relation between single Cherenkov photon and track Cherenkov distributions
The mean values of the single-photon and ring-average Cherenkov angle distributions will be more or less the same
Notes: Monte Carlo simulated events by Pion-gun
Tracks per chamber on average around 5
Fixed momentum 2.7..2.8 [GeV/c]

## Slide 50
The ring-average Cherenkov angle distribution will have a resolution 𝝈ring θc depending
on the average number of Hough selected photons per track ( Nres.cluster) :
Relation between photon distributions
Current PID algorithm in the HMPID
Hough Transform Method
Where is the resolution of the single photon distribution ηc
is the resolution of ring-average Cherenkov distribution θc
θc
ηc
Notes: Monte Carlo simulated events by Pion-gun
Tracks per chamber on average around 5
Fixed momentum 2.7..2.8 [GeV/c]

## Slide 51
Current PID algorithm in the HMPID
Hough Transform Method
From HMPID TDR
Relation between photon distributions
Notes: Monte Carlo simulated events by Pion-gun
Tracks per chamber on average around 5
Fixed momentum 2.7..2.8 [GeV/c]

## Slide 52
Average number of selected photons
Current PID algorithm in the HMPID
Hough Transform Method
θc
ηc
Just a crude estimate
One can calculate the average number of Hough selected photons by the equation :
For the data above :
Notes: Monte Carlo simulated events by Pion-gun
Tracks per chamber on average around 5
Fixed momentum 2.7..2.8 [GeV/c]

## Slide 53
Current PID algorithm in the HMPID
Current PID algorithm in the HMPID :
Evaluation of performance

## Slide 54
n constant
p from other detectors measured by the HMPID : θc
Each point in the scatter plot represents a reconstructed track
Reconstructed Cherenkov angles for multitude of tracks
Current PID algorithm in the HMPID
Evaluation of performance
PID using the HTM in the HMPID on Run 2 data : Scatterplot of Cherenkov angle versus momentum
Notes: Credits to Giacomo Volpe https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 55
Distributions at fixed momentums
The distribution per specie is evaluated for a fixed range of momentum
Current PID algorithm in the HMPID
Evaluation of performance
Efficient discrimination of all species is possible in 2.5..2.6 GeV/c range
The ring-average angular resolution
[3-5 mRad in previous examples] inherently limits the ability to distinguish species at higher momentums
Overlap between pions and kaons occurs in the 3.8..4.0 GeV/c range
Run 2 data
Notes: Hadron separation on Run 2 data
Credits to Giacomo Volpe https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 56
Comparing pp vs Pb-Pb for fixed momentums
Current PID algorithm in the HMPID
Evaluation of performance
Notes: Hadron separation on Run 2 data
Good separation is seen in the Proton-Proton events, whereas overlapping is seen in the lead-lead events
Credits to Giacomo Volpe https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 57
PID efficiency
0.2 Tesla
0.5 Tesla
Current PID algorithm in the HMPID
Evaluation of performance
High multiplicity events: B = 0.2 and 0.5 Tesla comparison
Higher momentum
+ more Cherenkov photons emitted
Theoretical values θc,i comes closer to each other
+ Better track inclination (smaller θp )
Less skewed Cherenkov ring patterns
Better angular resolution per photon-cluster
MC data
Notes: Pion IDentificaiton accuracy distributed over momentums using the HTM on MC data
Credits to Giacomo Volpe https://indico.cern.ch/event/1246704/?view=nicecompact

## Slide 58
To measure the production of pions, kaons and protons over a wide pT range, results from five different independent PID techniques/detectors, namely ITS, TPC, TOF, HMPID and kink-topology (for kaons), are combined.
In their overlap pT regions the spectra from the different PID techniques are consistent within uncertainties:
  the results are combined in the overlapping ranges using a weighted mean with the independent systematic uncertainties as weights.
The HMPID constrains the uncertainty of the measurements in the transition region between the TOF and TPC relativistic rise methods (around pT = 3 GeV/c). It both improves the precision of the measurement and validates the other methods in the region where they have the worst PID separation.
HMPID separation power in σ unit as a function of pT
Current PID algorithm in the HMPID
ALICE charged hadrons yields evaluation strategy
Notes: Credits to Giacomo Volpe :
https://indico.cern.ch/event/1246704/?view=nicecompact