## Slide 1
PR and release status:
makefile targets,
BSM processes (EWdim6) etc
Andrea Valassi (CERN)
Madgraph on GPU development meeting, 28th May 2024
https://indico.cern.ch/event/1355153
(previous update was on May 14 – only mentioning changes since then)

## Slide 2: Status update for my PRs – Makefiles
Update on my PRs and issues (since May 14 meeting)
  MERGED: PR #798 (separate Makefile targets) – two reviews by OM (thanks!)
    This completely separates C++ and CUDA or HIP targets (extends/completes Jorgen’s earlier PR)
    NB: we now build EITHER “check.exe” OR “gcheck.exe” – we no longer build them together
      “make BACKEND=cuda” and “make BACKEND=hip” build gcheck.exe
      “make BACKEND=avx2” and other SIMD modes (none,sse4,512y,512z) build check.exe
    NB: we no longer link together C++ and CUDA implementations of the same classes
      Main example: runTest.exe EITHER tests C++ OR tests cuda
      (But still keep separate namespaces, because it is cleaner, and in case one day we move to fat binaries...)
  MERGED: PR #841 (rename Makefile targets and variables) – review by OM
    This (hopefully!) rationalizes the naming conventions of build targets and internal makefile variables
    NB: we no longer build “check.exe” or “gcheck.exe” (or runTest.exe) – the names have changed
      “make BACKEND=cuda” builds check_cuda.exe, runTest_cuda.exe, etc
      “make BACKEND=hip” builds check_hip.exe, runTest_hip.exe, etc
      “make BACKEND=avx2” (none,sse4,512y,512z) builds check_cpp.exe, runTest_cpp.exe, etc
      This is consistent with the naming convention for madevent_cuda, madevent_hip, madevent_cpp
      (Note: I kept a single “_cpp” suffix, but if needed it is easy to switch to “_cppnone”, “_cppavx2” etc...)
    This is also true for intermediate .o objects, not only for the final .exe executables
      CPPProcess.o becomes CPPProcess_(cpp|cuda|hip).o
In my opinion this completes what we needed to change in Makefiles for the moment
  NB: standalone builds are still functional and should remain so (POWHEG, reweighting...)
    Cleanup in earlier PRs – cudacpp makefile can either be invoked standalone or from Fortran makefile

## Slide 3: Updates and recap – BSM & other processes
Brief update on my PRs (since May 14 meeting) – Beyond Standard Model models
  New WIP PR #847 (EWdim6) – adds EWdim6 “u d~ > w+ z“ to the repo (Zenny’s process)
    Verified that my earlier BSM patches for SUSY/EFT fix code generation for this too (#615 is fixed)
    Code also builds ok, but HRDCOD=(0|1) builds give different results at runtime (new issue #846)
Recap of pending process-specific issues (mainly BSM, but not only)
  SUSY: #825 (susy_gg_tt madevent tests – xsec mismatch Fortran vs cudacpp)
  SUSY: #826 (susy_gg_t1t1 madevent tests – no xsec in cudacpp madevent)
  HEFT: #833 (heft_gg_bb madevent tests – LHE mismatch Fortran vs cudacpp, FPTYPE=f)
  EWdim6: #846 (ewdim6_ud_wz cudacpp tests – ME mismatch HRDCOD=0 vs HRDCOD=1)
  SM: #806 (gq_ttq cudacpp tests – segmentation fault on AMD GPUs on LUMI)
  Anyone interested in taking a look? Otherwise we can fix these after the release?

## Slide 4: AOB and some next steps
More tests in the ‘launch’ interface, more tweaks in the runcards
  Olivier’s PR #835 (default FPTYPE=m in runcard) has been merged
  However, I would suggest adding also HELINL and HRDCOD to runcard (issue #700)
  And then make the syntax more consistent (e.g. cudacpp_fptype, cudacpp_helinl, etc)
  And more tests, tests, tests
Next priority for me: git repos and transfer scripts
  See also the discussion in issue #661 and in Olivier’s issue #815
  There was some discussion at the general mg5amcnlo meeting about git subrepos
  Keep the madgraph4gpu repo anyway (generated processes, older branche like Lugano, etc)
When the above is done we can think of a release?
  Wait for Stefan’s PR #830 on warps and channel ID arrays (issue #765) or not?
  Nathan’s Intel GPU support in cudacpp (#805): maybe after the release?
  (Aim for end June or beginning July – I am on holiday for the next 2-3 weeks)