## Slide 1: Beam pipe rope support from YE1
Ali Karaki - CMS Engineering and Integration Office
10/12/2023
In collaboration with:
Josef Sestak and Orlando Santos - TE-VSC-BVO Tristan Loic Loiseau - CMS Technical Coordination

## Slide 2
Install rolling support
Open YE3 1.7 m
Open YE2 1.5 m
Install support on YE1 non IP
Swap supports
Survey
Open YE3 2.1m
Open YE2 2.1 m
Engage the rope support from YE1
Survey
Open YE3 3.8 m
Open YE2 3.6 m
Simplifying the opening\closing sequence of the endcaps by the reduction of the number of strokes to fully open\close the detector from 14 to 11.
No more need for the YE3 rolling support. Less risk for the BP and for personnel (radiological). Less time for the installation.
Motivation
Comparison: Steps to open YE3 and YE2 one full stroke with and without the ‘rope’ support
1
2
3
4
5
6
No more need for the sling from the ES cone.

## Slide 3
Support design overview
YE1 spacer ring
Wire ropes passing through the obsolete alignment holes of YE1 spacer ring.
Control the installation\removal of the support remotely from the tower by pulling the ropes.
Rope 1 is the main rope that takes the load, while rope 2 is used to retract rope 1 and keep it in the shadow of the spacer ring.
To be used when the endcaps are in closed configuration (no gap between YE1 and YE2), or in any position of YE1 at |z|<12.3m.
YE1 Non-Ip side
Beam pipe
Rope 2
Rope 1

## Slide 4
Support design overview
Guide point on RE2
Guide points on GE21
Control points (winches)
Pulley system
BP interface

## Slide 5
Pulley system - Permanently installed
1
2
Machining of the block done Waiting the delivery of the pulleys
Concept design by TE-VSC
Installation of the interfaces done on YE-1
Machining of the brackets done
2
2 pulleys block
4 pulleys block
1

## Slide 6
Beam pipe interface
Concept design by TE-VSC
Modified version
Aluminium plates
Derlin support blocks
Pulleys
Support rope Dyneema D5mm
20
Retraction rope Dyneema D5mm
Beam pipe
Design is complete Needs to be machined

## Slide 7
Support Envelope
When YE1 is fully open (10.4 m), the support must be retracted sufficiently to avoid any conflict with the FIN.
FIN
YE1 Inner ring
R705
R790

## Slide 8
Guide point on GE2/1
One pulley with a support plate.
The pulley is fixed to the GE2/1 support bracket.
The support is designed in a way to keep minimum distance between the rope and the GE2/1 chamber and to have the rope concentric with the alignment hole in YE1.
The connection must withstand the forces of R1=11.5 N radially and R2=3.5 N in Z.
Another pulley next to the first one needs to be added to close the rope loop.
GE2/1
GE2/1 Bracket
Alignment hole D80
Dyneema Rope D 5mm
R2= 3.5 N
R2= 11.5 N
V1
V2

## Slide 9
Gap with YE2 (GE2)
YE+1
YE+2
ME+2/1/9
GE+2/1
YE1 Alignment hole
62 mm
ME+2/1/9
GE+2/1
18 mm
The minimum nominal gap between GE2/1 and ME2/1 is 23 mm.
The rope diameter is 5 mm
Therefore, the minimum clearance between the rope and ME/2 is 18 mm.

## Slide 10
Guide point on RE2/2
One pulley guiding the rope.
The pulley is fixed to a set of two adjustable rods (in Z)
The whole assembly is fixed to the RE2/2 bracket.
The connection must withstand the forces of R1=13.5 N radially and R2=5.1 N in Z.
RE+2/2/18
R2= 5.1 N
90
M10 ( For Z Adjustment)
D20
RE2/2 bracket
RE+2/2/19
V1
V2

## Slide 11
Gap with YE2 (RE2)
YE+1
YE+2
RE+2/2/18
ME+2/2/18
ME+2/1/9
ME+2/1/9
ME+2/2/18
RE+2/2/18
60 mm
The guide point on RE2 is at the level of the gap between ME2/1 and ME2/2
The minimum clearance between the rope and YE2 at this level is 60 mm.
192 mm
110 mm

## Slide 12
Winches on YE1 tower
Manual rope winch-Worm gear mechanism Self-braking. Adjustable handle.
Permanently installed. Accessible from the stairs.
Steel bracket bolted to the YE1 tower
Aluminium bracket bolted to the YE1 tower
Support machined
Winches delivered
Free rotation around the vertical axis. Self adjustment
Machining done

## Slide 13
YE1
YE2
View from the balcony
Winch
Winches on YE1 tower
Gap between the rope and the towers in closed configuration
Destructive work done last week

## Slide 14
Mock up
A scaled-down prototype of the inner ring of YE1 was constructed at a 1:2 scale with bosch profiles.
The objective is to experiment with various rope configurations to identify the most effective one for symmetrically raising/lowering the beam pipe.
The configuration below has been identified. However, there was a significant amount of friction caused by the pulleys. Further testing is needed with the appropriate pulleys to address this issue.
YE1 inner ring
Bosch frame

## Slide 15
Conclusion
The new YE1 rope support will significantly simplify the opening/closing procedure of CMS.
A gap was found between YE1 and YE2 to pass the rope. The guiding points are identified, designed, and partially manufactured.
The fix points on the towers were identified and designed. Destructive work done.
Further tests are required on the mock-up with the proper pulleys to decide on the final rope's configuration.
Start the machining of the beam pipe interface, if agreed on the design.
Providing the test goes well, the aim is to install the support by the end of the YETS.

## Slide 16: Back-up

## Slide 17
Fixed interface inside YE1 inner ring
YE1 inner ring- View from TAS side
BP
M16 screws
Aluminium interface
Eye bolt- Adjustable position
4 mm SS cable
Turnbuckle
Adjustment 1
Adjustment 2
Adjustment 3
Dyneema rope – 3 mm 210 DaN

## Slide 18
Interface with the Beam Pipe
48 deg
48 deg
PEEK bar CNC machined
Silicon foam layer 3mm
Eye bolt and shackle (SS)
60 mm

## Slide 19
Position during the run

## Slide 20
Fixed aluminium interface inside the YE1 inner ring, permanently.
Eye bolt with adjustable position to control the angle of the rope.
M16 screws
Aluminium interface
Eye bolt- Adjustable position
Fixed interface inside YE1 inner ring
48 deg
48 deg

## Slide 21
Gap with YE2 (Tower)
YE+1
YE+2
YE+2
YE+1
Rope

## Slide 22
Interface with the Beam Pipe
BP
Sling
Tensioner
Al bar
The BP is in contact with a 15 mm wide sling with adjustable tension.
The sling is flat; therefore, no transversal forces are transmitted due to the BP during the installation/removal of the support.
It is kept permanently inside YE1 but not touching the BP, except when the support is needed.

## Slide 23
F 184 N
Fc1=184 sin(3.58) = 11.5 N
Fc2=184 cos(3.58) = 183.6 N
Fb1=183.6 sin(4.24) = 13.57 N
Fb2=183.6 cos(4.24) = 183 N
Projection on XY Plan
B
C

## Slide 24
F 184 N
Fc3=184 sin(1.131) = 3.55 N
Fb3=184 sin (1.59) = 5.1 N
Projection on YZ Plan
B
C