## Slide 1: Simulation Study of Muon Beam CT and Integration of MuDirac and Geant4 for Muonic X-ray Generation
Zhihao Zhou1,2,3, Yang Li1,2, Jingyu Tang4
1Institute of High Energy Physics, Chinese Academy of Sciences (CAS) 2Spallation Neutron Source Science Center 3University of Chinese Academy of Sciences 4University of Science and Technology of China
MIP 2024 @ Peking University
April 21, 2024

## Slide 2: Contents
Introduction to Experimental Muon Source(EMuS)
Muon Beam Computed Tomography (CT)
  Cosmic-ray muon imaging
  Accelerator-based muon beam CT
    Details of simulation study
    Result, summary, and outlook
Muonic X-ray Elemental Analysis
  Improve the cascade process of negative muons in Geant4 with the use of MuDirac
https://doi.org/10.1002/pssa.202200426

## Slide 3
Experimental Muon Source (EMuS)
EMuS was a research proposal for a muon facility at the China Spallation Neutron Source (CSNS) under the NSFC Fund for Research on National Major Research Instruments (2016–2021).
Two schemes have been designed:
https://doi.org/10.1002/pssa.202200426
  Phase-I or the simplified scheme
Surface muon for μSR applications
Negative cloud muon for muonic X-ray analysis
Surface and decay muons for μSR
High-momentum decay muon for imaging
Negative decay muon for depth-selective muonic X-ray analysis
  Phase-II or the baseline scheme

## Slide 4
https://doi.org/10.1002/pssa.202200426
CSNS accelerator facility provides a proton beam with a kinetic energy of 1.6 GeV, and a repetition rate of 25 Hz. It currently has a beam power of 140 kW, which can be upgraded to 500 kW at Phase-II. EMuS will take about 5% or 25 kW of the total beam power (500 kW) from the CSNS-II accelerator complex.
The high-momentum muon beams for imaging operate at a repetition rate of 2.5 Hz, with a momentum of up to 450 MeV/c and a beam intensity of 7.9×108.
EMuS Baseline Scheme
EMuS baseline scheme layout
DM1 endstation: high-momentum muon beam imaging
DM3 endstation: muonic X-ray analysis

## Slide 5: Cosmic-ray Muon Imaging Methods
Cosmic-ray muons
  Average energy ~4 GeV
  Up to 100 TeV
  ~1/(cm2·s) at sea level
Cosmic-ray muons have been used to image large objects
  Transmission and absorption imaging
  Muon scattering imaging(Muon tomography)
Cosmic-ray muon imaging methods:
transmission and absorption
scattering
(i)
(ii)

## Slide 6: Muon Beam CT
Accelerator-based muon beam
  Controllable momentum
  High intensity
Penetrating power of 450 MeV/c (360 MeV) muons
  Could be used for imaging macroscopic samples
The baseline scheme of EMuS provides possibility of imaging using high-momentum muon beam
Material | Range [mm]
Aluminum | 718
Iron | 271
Copper | 248
Lead | 238
Tungsten | 137
Corresponding to ranges of 590 MeV proton

## Slide 7: Simulation Study of Muon Beam CT
1. Projection Value Calculation
2. Detector Design
3. Collimator Design
4. Result
Detector
Sample
Collimator
Muon beam
Geant4 simulation

## Slide 8: Projection Value
As a tomographic imaging technique, CT images cannot be directly obtained from the detector data. Instead, the data is used to calculate projection values (PVs).
Then, the calculated PVs are used as inputs for the reconstruction algorithm, which is used to produce the final image.
Common CT reconstruction algorithms
  Algebraic Reconstruction Technique (ART, this work)
  Filtered Back Projection (FBP)
  Maximum Likelihood Expectation Maximization (MLEM)
Data
Projection Values
Image
Reconstruction algorithm

## Slide 9
The absorption of X-rays follows the Lambert-Beer law
where is the linear attenuation coefficient, the incident light intensity, and the transmitted light intensity.
For X-ray CT, the PV is
When mono-energetic X-rays pass through a homogeneous medium, the PV is proportional to the distance traveled by the X-rays:
.
This forms the basis of CT reconstruction algorithm.
Data
Projection Values
Image
Reconstruction algorithm

## Slide 10
In early CT scans, the source and detector move at an angle theta to cover the entire cross-section.
The detector and collimator rotate multiple times to collect data from multiple angles.
Nowadays, X-ray CT employs conical beams and detectors with larger areas to achieve multi-layer imaging at once.
source
detector
source
detector

## Slide 11
Proton CT (pCT) uses the energy loss of protons for imaging.
  pCT can assist in proton therapy.
  Proton beams usually from a cyclotron.
  The projection value of pCT is:
Proton beam
HPGe detector
Sample
https://doi.org/10.1088/0031-9155/26/6/001
https://doi.org/10.1016/j.ejmp.2018.10.020
Sample
···
Silicon strip detectors
Range telescope
Proton beam
`
  Current proton CT uses silicon strip detectors (SSD) and silicon pixel detectors (SPD) to improve imaging efficiency.
    SSD: measure the entry and exit positions and angles of protons
    SPD: measure the energy of exiting protons
    With these measurements, trajectories of protons in the sample can be reconstructed using interpolation algorithms.
  In early proton CT, high-purity germanium detectors were used to measure the energy of outgoing protons.

## Slide 12
Relationship between the projection value and the thickness of the material which the muon passes through Good linearity
The materials of samples for the μCT are not limited to those similar to human tissues.
  Proton: nucleon-nucleon interaction
  Muon: mainly electromagnetic interaction
Bethe-Bloch formula with density effect correction
The projection value of μCT is
Simulation
  Aluminum、Iron、Copper、Lead、Tungsten
  1~100 mm
✔️

## Slide 13: Muon Selection for CT
As charged particles, muons undergo multiple Coulomb scatterings (MCS) when passing through objects. This brings challenges in accurately estimating the voxels through which the muons have passed, especially for the pulsed muon beam.
To mitigate the effects of MCS and improve the quality of CT, only muons with incident and exit positions within a limited, small range are selected and labeled as “good”.
The final projection value is the average of the projection values of all “good” muons:
How many“good”muons are needed to obtain a stable projection value?
  Test samples: 100 mm thick iron, copper, and lead
  Result: with >3000 muons, projection values tend to stabilize
Relationship between the projection values of different materials and the number of “good” muons
✔️
select
reject
Fe
Cu
Pb

## Slide 14: Projection Value Calculation
The calculation of projection value was verified with Geant4 simulation.
Simulation settings:
  Small incident beam spot
  Virtual detector
  Sample: aluminum inside iron
  Iron: red cylinder (diameter 100 mm, height 100 mm)
  Aluminum: yellow cuboid (20*100*20 mm3)
Fit to the Line Spread Function of the aluminum edge Resolution ~1.1 mm (σ)
Reconstructed image

## Slide 15: Detector and Track Reconstruction
Detector: range telescope
  Silicon pixel detectors + Degraders
Track reconstruction: inward search tree
  Initially proposed in ALICE experiment at LHC
  Now widely used in proton CT to reconstruct energy
  Fixed threshold:
  Score:
Range telescope model built with Geant4
Yellow: silicon pixel detector
Red: degrader
Schematic of track reconstruction algorithm

## Slide 16: Design of Degrader
Copper
Tungsten
Number of muons
Number of muons
Efficiency
Efficiency
Factors affecting track reconstruction efficiency:
  number of incident muons
  material and thickness of the energy degrader
Track reconstruction efficiency
  : the number of tracks in which the EventID of the seed signal is identical to the EventID of the signal on the first layer
  : the total number of tracks simulated
Test materials and thickness: Cu and W, 2–6 mm
Simulation results indicate that tungsten of 2 mm thick and ~70 muons incident each time is a good working point.

## Slide 17: Design of Collimator
Main design goals of the collimator
  To collimate a small beam spot for CT: |beamX| < 0.5 mm, |beamY| < 5 mm
  To control the number of muons for CT: around 70 muons per pulse
Two components
  Beam spreader (gray)
  300 mm, 2 mm thickness
  Beam collimator (red)
  300 mm, 2000 mm length
Beam intensity for muon CT can be tuned by varying the collimator design.
Design of the collimator with Geant4 simulation
~70 muons remaining after collimation
Momentum of muons after collimation

## Slide 18: Simulation Result
Full simulation of muon beam CT was conducted, including:
EMuS DM1 beam (~108 muons simulated)
Collimator
Sample
Range telescope
Reconstructed image of muon beam CT
Fit to the Line Spread Function of the sample edge yields a resolution of ~1.6 mm (σ)
Momentum distribution of muons after passing through the collimator
~38,000 muons after collimation

## Slide 19
Geant4 simulation and image reconstruction study in the EMuS baseline scheme demonstrate the potential of muon beam CT.
Simulation results suggest that bulk sample imaging with muon CT could be a promising application for muon facilities with high-momentum muon beams.
Current EMuS baseline design would require approximately one week to image a single cross-section of the sample studied in this work.
Improvements:
  Simultaneous irradiation with more beam spots
  Improve the track reconstruction algorithm
Continuous-wave muon beam
  Capability to measure individual muon
Summary and Outlook

## Slide 20: Contents
Muon Beam Computed Tomography (CT)
  Cosmic-ray muon imaging
  Accelerator-based muon beam CT
    Details of simulation study
    Result, summary, and outlook
Muonic X-ray Elemental Analysis
  Improve the cascade process of negative muons in Geant4 with the use of MuDirac
EMuS baseline scheme layout
DM1 endstation: high-momentum muon beam imaging
DM3 endstation: muonic X-ray analysis

## Slide 21
Background: start-to-end simulation of muonic X-ray analysis on EMuS DM3 is performed with G4beamline (a Geant4-based program)
Problem: muonic X-ray emission lines are incorrectly calculated by Geant4, especially for high-energy transition (e.g., K-shell)
Study of Muonic X-ray with Geant4
G4MuonMinusCapture
G4EmCaptureCascade
Finished: transition energy extraction
Ongoing: implementation of transition probability
Finished
Progress:
Developed Python scripts to run MuDirac in multi-process mode (< 1 hour for all nuclides using a 64-core server)
Preliminary solution:
Use MuDirac* to produce muonic X-ray database (energies and probabilities) for all elements
Modify G4EmCaptureCascade to extract the transition energy and probability from database
Create a new messenger class to manage whether to replace the original G4 process (for G4beamline or other Geant4-based program)
Git repository
*MuDirac is a software developed by the ISIS muon group, which calculates the transition energies and probabilities of muon cascade with a precision of a few keV.
https://doi.org/10.1002/xrs.3212
https://doi.org/10.3390/condmat8040101
Transition | Kα (2p-1s) [keV] |  | 
Element | G4bl before | G4bl now | Exp.
29Cu | 1491 | 1502 | 1507

## Slide 22
Intensities are also important for quantitative elemental analysis.
The intensities of the simulated spectra are not correct (either by MuDirac or Geant4).
  Need to consider the initial muon population on initial energy level, i.e. the angular momentum distribution at capture, L-distribution.
  Try to collaborate with MuDirac team and other groups.
Future Improvement

## Slide 23
Thank You!

## Slide 24
Symbol | Definition | Units or Value
 |  | 0.307075 MeV⋅g-1⋅cm2
NA | Avogadro’s number | 6.022 1415(10) × 1023 mol-1
 | Electron mass | 0.510 998 918(44) MeV
 | Atomic number of absorber | 
 | Atomic mass of absorber | 
 | Mean excitation energy | 
 | Density effffect correction | 
 | The mass of incident particles | 
Symbol | Definition | Units or Value
 |  | 0.307075 MeV⋅g-1⋅cm2
NA | Avogadro’s number | 6.022 1415(10) × 1023 mol-1
 |  | 0.510 998 918(44) MeV
 | Atomic number of absorber | 
 | Atomic mass of absorber | 
 | Mean excitation energy | 
 | Density effffect correction | 
 | The mass of incident particles | 
is the maximum energy transfer possible in a single collision.
Backup
Summary of variables used in Bethe-Bloch formula.

## Slide 25
MyMessenger Class
Interact with users and switch between the default process and the customized process.
G4/My
MuonMinusAtomicCapture Class
A class that handles a series of processes following the capture of a muon by an atom, including the formation of muonic atoms, muon cascade processes, and so on.
G4/My
EmCaptureCascade Class
A class that handles muon cascade processes. This class also handles meson cascade processes, but we only modify the mu- process in the MyMuonMinusAtomicCapture class.