## Slide 2: Copyright statement and speaker’s release for video publishing
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to broadcast them online to all registered students and to post them without any further processing on the CAS website.
The author hereby confirms that the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution.

## Slide 3: Accelerators for Beginners and the CERN Complex
Rende Steerenberg – CERN BE/OP
11 March 2024

## Slide 4: Content
Why Accelerators and Colliders ?
The CERN Accelerator Complex
Cycling the Accelerators & Satisfying Users
The Main Ingredients of an Accelerator

## Slide 5: Content
Why Accelerators and Colliders ?
The CERN Accelerator Complex
Cycling the Accelerators & Satisfying Users
The Main Ingredients of an Accelerator

## Slide 6: Creating Matter from Energy
E = m・c2
In our accelerators we provide energy to the particles we accelerate.
In the detectors we observe the matter created
During the Big Bang Energy was transformed in matter

## Slide 7: Looking to smaller dimensions
λ =
h c
E
Increasing the energy will reduce the wavelength
Visible light
λ = 400  700 nm
X-ray
λ = 0.01  10 nm
Particle accelerators
λ < 0.01 nm

## Slide 8: Fixed Target vs. Colliders
Collider
All energy will be available for particle production
Fixed Target
Much of the energy is lost in the target and only part is used to produce secondary particles

## Slide 9: Content
Why Accelerators and Colliders ?
The CERN Accelerator Complex
Cycling the Accelerators & Satisfying Users
The Main Ingredients of an Accelerator

## Slide 10: The CERN Accelerator Complex

## Slide 11
Linac 4
H- ion source at 45 keV
Accelerates beam up to 160 MeV
The chopping scheme allows removing some of the Linac bunches to make the beam fit into the PS Booster RF buckets
Pulse rate 1.2 s

## Slide 12
PS Booster
1st Synchrotron with 4 superposed rings
Circumference of 157 m
Proton energy from 160 MeV to 2 GeV
Can cycle every 1.2 s
Each ring will inject over multi-turns, using charge exchange injection
x’
x
+
-
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
Before stripping foil
x’
x
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Behind stripping foil

## Slide 13: The CERN Accelerator Complex

## Slide 14: PS
The oldest operating synchrotron at CERN
Circumference of 628m
  4 x PSB circumference
Increases proton energy from 2 GeV to max. 26 GeV
Cycle length ranges from 1.2s to 3.6s
Many RF systems allow for complex RF gymnastics
Various types of extractions:
  Fast extraction
  Multi-turn extraction (MTE)
  Slow extraction

## Slide 15: SPS
The first synchrotron in the chain at ~30m under ground
Circumference of 6.9 km
  11 x PS circumference
Increases proton beam energy up to 450 GeV with up to ~5x1013 protons per cycle
Provides slow extracted beam to the North Area
Provides fast extracted beam to LHC, AWAKE and HiRadMat

## Slide 16: The CERN Accelerator Complex

## Slide 17: LHC
Situated on average ~100 m under ground
Four major experiments
Circumference 26.7 km
Two separate beam pipes going through the same cold mass 19.4 cm apart
150 tons of liquid helium to keep the magnets cold and superconducting

## Slide 18
LHC
1232 main dipoles of 15 m each that deviate the beams around the 27 km circumference
858 main quadrupoles that keep the beam focused
6000 corrector magnets to preserve the beam quality
Main magnets use superconducting cables (Cu-clad Nb-Ti)
12’000 A provides a nominal field of 8.33 Tesla
Operating in superfluid helium at 1.9K

## Slide 19: LHC: Luminosity the Figure of Merit
Intensity per bunch
Beam dimensions
Number of bunches
Geometrical
Correction
factors
Maximise Luminosity:
Bunch intensity
Transverse beam size
Beam size at collision points (optics functions)
Crossing angle
Machine availability

## Slide 20: Content
Why Accelerators and Colliders ?
The CERN Accelerator Complex
Cycling the Accelerators & Satisfying Users
The Main Ingredients of an Accelerator

## Slide 21: The LHC Cycle
6.8 TeV
450 GeV
Time
Injection
Ramp
Squeeze
&
Adjust
Stable beams for physics
Dump
&
Ramp down
= Field in main magnets
= Beam 1 intensity (current)
= Beam 2 intensity (current)

## Slide 23: Filling the LHC & Satisfying Fixed Target users
1.2 seconds
PSB
PS
SPS
Time
= Field in main magnets
= Proton beam intensity (current)
= Beam transfer
To LHC clock-wise or counter clock-wise
450 GeV
26 GeV
1.4 GeV

## Slide 24: Content
Why Accelerators and Colliders ?
The CERN Accelerator Complex
Cycling the Accelerators & Satisfying Users
The Main Ingredients of an Accelerator

## Slide 25: The LEIR Accelerator as Example
Building 150

## Slide 26: Vacuum Chamber
The particle beam:
arrives through a transfer line
is injected
is accelerated over many turns in a “circular” machine
is extracted
leaves through a transfer line
Injection(s)
Acceleration
&
Increase of magnetic field
Extraction

## Slide 27: Injecting & Extracting Particles
Injection
Extraction
Extraction
Injection
Extraction

## Slide 28: Injecting & Extracting Particles
Incoming beam
Magnetic field
Injected beam
Circulating beam
No magnetic field
Septum Magnet
Kicker Magnet

## Slide 29: Injecting & Extracting Particles
Extracted beam
Magnetic field
Beam to be extracted
Circulating beam
No magnetic field
Septum Magnet
Kicker Magnet

## Slide 30: Make Particles Circulate
Main Dipoles
Main Dipoles
Main Dipoles
Main Dipoles

## Slide 31: Deviating Charged Particles
Magnetic Lorentz Force:
Moving charged particles are deviated
in a magnetic field

## Slide 32: Oscillatory Motion in the Horizontal Plane
Horizontal motion
Different particles with different initial conditions in a homogeneous magnetic field will cause oscillatory motion in the horizontal plane  Betatron Oscillations
Particle B
Particle A
2π
0
Horizontal
displacement
Machine circumference
Two charged Particles in a homogeneous magnetic field
Particle A
Particle B

## Slide 33: Oscillatory Motion in the Vertical Plane
The horizontal motion seems to be “stable”…. What about the vertical plane ?
Many particles many initial conditions
Vertical
displacement
Many different angles
 s

## Slide 34: Focusing Particle Beams, a bit like a lens
Force on particles
Focusing Quadrupole
De-focusing Quadrupole
Rotated by 90º
QF
QD
QF

## Slide 35: Focusing Particle Beams in LEIR
Main Dipoles
Main Dipoles
Main Dipoles
Quadrupoles

## Slide 36: Accelerating Particles, Using Electrical Fields
Accelerating
Cavity

## Slide 37: Radio Frequency Cavity
Charged particles are accelerated by a longitudinal electric field
The electric field needs to alternate with a harmonic of the revolution frequency

## Slide 38: The Eyes of Operations
Any many more beam properties…..
Beam intensity or current measurement
Transverse beam profile/size measurement
Longitudinal beam profile measurements
Measure the LHC luminosity, number of events per surface and time unit.

## Slide 39: Possible Limitations
Same phase and frequency for driving force and the system can cause resonances and be destructive
Neighbouring charges with the same polarity experience repelling forces
+
+
Moving particles create currents, These currents result in attracting or repelling magnetic fields
Machines and elements cannot be built with infinite perfection

## Slide 41: ISOLDE / HIE-ISOLDE
The PSB proton beam impinges on a target producing a range of isotopes
Two mass separators (GPS & HRS) allow selection of isotopes
The post acceleration of isotopes is being extended
  REX, normal conducting accelerating structures
  HIE-ISOLDE, super conducting LINAC

## Slide 42: AD-ELENA
Receives fast extracted proton beam from PS at 26 GeV/c on a target
Every million protons yields about one usable antiproton at 3.5 GeV/c.
AD decelerates beam in stages down to 5.3 MeV
ELENA will further decelerate down to 100 keV
Experiments:
  ASACUSA, ALPHA, AEGIS, BASE, GBAR

## Slide 43: PS for LHC
72 bunches
Eject 36 or
h = 7 or 9
h = 21
h = 84
Eject 24 or
48 bunches
Controlled blow-ups
gtr
Split in four at flat top
25 ns
26 GeV/c
BCMS (8 PSB b.)
Standard (6 PSB b.)
8b4e (7 PSB b.)
80 bunches (7 PSB b.)
Standard: 72 bunches @ 25 ns
BCMS: 48 bunches @ 25 ns
The PS defines the longitudinal beam characteristics

## Slide 44: Example: Wall Current Monitor
A circulating bunch creates an image current in vacuum chamber.
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
bunch
vacuum chamber
induced charge
The induced image current is the same size but has the opposite sign to the bunch current.
resistor
Wall Current Monitor (WCM)
Insulator
(ceramic)