## Slide 1
Richard Scrivens, BE Dept, CERN.
CAS@CERN, March 2024

## Slide 2: Layout
Electron Sources
  Thermionic
  Photo-Cathodes
Ion Sources
  Particle motion in plasmas
  Protons
  Negative Ions
  ECR Ion Source
  Radioactive Ions
Electron and Ion Sources
Notes: Essential part of Particle Accelerators
Will talk about e and Ion Source.
Will NOT talk about exotic sources (p-, e+, muon, pion etc)

## Slide 3: Every accelerator chain needs a source!
AWAKE
LINAC4

## Slide 4: Every accelerator chain needs a source!
Principles of the electron guns, with thermionic and photo cathodes
Principles of ion sources, and the types used at CERN.
Protons
Ions

## Slide 5
Electron Sources
  Thermionic
  Photo-Cathodes
Ion Sources
  Particle motion in plasmas
  Protons
  Negative Ions
  ECR Ion Source
  Radioactive Ions

## Slide 6: Electron Sources - Basics
HT
Power Supply
Insulator
Cathode
(Electron source)
Beam
E-field
Chamber
The classic Cathode Ray Experiment
Crookes Tube
Notes: What is shown is a Crookes Tube. Electrons come from the cathode from back ion acceleration, they ionise the residual gas, and fluoress the glass.
Used by the likes of Hittorf, Goldstein and Thompson to explain what cathode rays are, and discover the electron.

## Slide 7
Electron Sources
  Thermionic
  Photo-Cathodes
Ion Sources
  Particle motion in plasmas
  Protons
  Negative Ions
  ECR Ion Source
  Radioactive Ions

## Slide 8: Electrons – Thermionic Emission
Electrons inside a cold cathode are in the lowest energy states, and do not have enough energy to escape the material.
As the material is heated, some electrons move to higher energies.
Cathode emission is dominated by the Richardson Dushmann equation.
Material
Electrons
Energy
Energy difference between highest energy electron and vacuum
Work Function fs

## Slide 9: Electrons – Thermionic Emission
Therefore, at high temperatures there is an ELECTRON CLOUD around the material. The current density can then be found by integrating the available electrons and their energy.
This electron current is available
to be pulled off the surface…
Richardson-Dushmann equation
Rev. Mod. Phys. 2, p382 (1930)
This factor A is not achieved in practice (some electrons are reflected from the inner surface)
J: current density of electrons
Notes: Available electrons are those above the work function.
“A” is a pseudo constant – but NOT temperature dependent.

## Slide 10: Electrons – Thermionic Emission
 | A Acm-2K-2 | Uwork eV
W | 60 | 4.54
W Thoriated | 3 | 2.63
Mixed Oxide | 0.01 | 1
Cesium | 162 | 1.81
Ta | 60 | 4.12
Cs/O/W | 0.003* | 0.72*
LaB6 | 29 | 2.66
*- A and work function depend on the Cs/O layer thickness and purity
Element melting point v work function for selected metals : Nature does not provide an ideal solution
Notes: www.peakpeak.com/~jdavis/boron/LaB.htm for LaB6 melting point - Richardson-Dushmann A for LaB6 from Charged Particle Beams book, chp7
Metal melting point v work function from (http://www.lns.cornell.edu/~hoff/LECTURES/08S_688/08S_688_080225.pdf
)
Very hot cathodes can lead to a thermal limited emittance.

## Slide 11: CLIC Drive Beam Thermionic Gun
Cathode
Test Stand
CLIC – Compact Linear Collider.
Drive Beam – High intensity e-beam used to drive the high energy beam.
The CLIC Drive Beam Electron Gun is a Thermonic Gun.
Cathode System
Dispenser
Cathode

## Slide 12
Electron Sources
  Thermionic
  Photo-Cathodes
Ion Sources
  Particle motion in plasmas
  Protons
  Negative Ions
  ECR Ion Source
  Radioactive Ions

## Slide 13: Electrons – Photo Emission
The energy of an electron in a material can be increased above the vacuum energy by absorbing photons - photoelectric effect.
 | Uwork (eV) | lc (nm)
W | 4.5 | 275
Mg | 3.67 | 340
Cu | 4.65 | 267
Uwork
METAL
VACUUM
E
EFermi
For metals:
Low quantum efficiency (Qeff<4x10-4) requires high power lasers.
Very robust and simple to use cathode material.
Quantum efficiency
Notes: K2CsSb is bialkali, used as the photo cathode in photo multiplier tubes – Sb=Antimony. K=Potassium.
Cs2Te requires UV laser (highest powers are not yet available), Cs:GaAs and K2CsSb can work with green lasers.

## Slide 14: Electrons – Photo Emission
Uwork
SEMI-COND
VACUUM
E
EFermi
EGAP
Ea
 | Eg+Ea (eV) | lc (nm)
GaAs | 5.5 | 225
Cs2Te | ~3.5 | 350
K2CsSb | 2.1 | 590
Semi-conductors can produce higher Quantum Efficiency at longer wavelengths.
Difficult to use in a high radiation area of an electron-gun (x-rays and ions cause decomposition and surface damage).
Cs2Te (Cesium Telluride) – High Quantum Efficiency in UV wavelength.
From: Mengjia Gaowei
Notes: K2CsSb is bialkali, used as the photo cathode in photo multiplier tubes – Sb=Antimony. K=Potassium.
Cs2Te requires UV laser (highest powers are not yet available), Cs:GaAs and K2CsSb can work with green lasers.
PhotoCathode Response plot:
https://indico.cern.ch/event/759878/contributions/3151886/attachments/1733384/2806102/P3_2018_Cs2Te__BNLtemplate.pdfMetals:

## Slide 15: Electrons – Photo Emission
Cs2Te cathodes produced in house at CERN.
Cs and Te evaporators produce a vapour, which condenses on the Cu substrate.
Cathode must be stored and transported under vacuum – or produced in-situ.
During cathode production, control of ratio of the 2 elements in the vapour to produce the correct stoichiometry for the cathode, and the highest Quantum Efficiency.

## Slide 16: CLEAR RF Photo Electron Source
Photo cathode
  The RF gun accelerates to 5MeV in ~15cm, which combats space charge forces.
  The short laser pulses (~6ps) generate short electron bunches from the Cs2Te photo cathode.
  The laser can pulse at a different harmonic of the RF system. 1.5GHz laser-electron bunches are created, using RF 3GHz acceleration.
Nd:YLF – 4x frequency -> UV
Notes: CONSTRUCTION OF THE PROBE BEAM PHOTO-INJECTOR OF CTF3, Proceedings of EPAC 2006, Edinburgh, Scotland, MOPLS114
See also https://indico.cern.ch/getFile.py/access?contribId=28&resId=22&materialId=poster&confId=177701

## Slide 17: CLEAR RF Photo Electron Source
Electron Current | 0.9 A
Electron Energy | 5-6 MeV
Emittance | 20 mm.mrad
Pulse | 150ns @ 5 Hz
Notes: Status and progress of the CTF3 probe beam: http://indico.cern.ch/getFile.py/access?contribId=26&sessionId=1&resId=2&materialId=slides&confId=45580

## Slide 18
  FCC-ee plans to use a photo-cathode based 2.8GHz RF electron gun.
  Collaboration with PSI, ICJ lab (Orsay) and INFN (Frascati).
  Cathode Type: Cs2Te
  Bunch Structure: A train is 2 bunches length=7ps, spacing=25ns, repetition=200Hz.
  FCC-ee top up injection scheme requires 100% variability of intensity on-demand.
  Positrons created by shooting 6 GeV electrons on target.
FCC-ee Electron Gun

## Slide 19
Electron Sources
  Thermionic
  Photo-Cathodes
Ion Sources
  Particle motion in plasmas
  Protons
  Negative Ions
  ECR Ion Source
  Radioactive Ions

## Slide 20: Ion Sources - Basics
An Ion Source requires an “ion production” region and an “ion extraction” system.
In most (but not all) cases, ion production occurs in a plasma.
A plasma or discharge chamber
Material input
Power to create a plasma / discharge
A hole to let the ions out!
An extraction system

## Slide 21: Ion Sources - Basics

## Slide 22: Ion Sources - Basics
Hydrogen plasma (for protons or H-) from an RF source.
Hydrogen plasma emits a pink light from an atomic transition.

## Slide 23
Electron Sources
  Thermionic
  Photo-Cathodes
Ion Sources
  Particle motion in plasmas
  Protons
  Negative Ions
  ECR Ion Source
  Radioactive Ions

## Slide 24: Ion Source Essentials
Many sources work on one of two electron heating techniques:
  Cathode – Anode Discharge: A DC voltage between the cathode and anode is used to accelerate the electrons.
  RF Discharge: An RF electromatic wave is sent into the chamber, and the electric field can accelerate electrons.
The electrons impact on the injected material in the source to produce ions. The gas can be a compound form (e.g. Carbon from CO) or from a vapour (e.g. lead vapour from an oven).

## Slide 25: Ion Source Essentials
Electron impact ionization of atoms/molecules

## Slide 26
R. Rejoub, B. G. Lindsay, and R. F. Stebbings, Phys. Rev. A 65, 042713 (2002)
Except H: Y.-K. Kim and M.E. Rudd, Phys. Rev. A 50, 3954 (1994)
Ionization Cross Section by Electron Impact
We need to create electrons, accelerate them to a few times the ionization potential of the material, and get them to interact with atoms.
Highest probability is at ~3-5x the ionization potential.
Ion Source Essentials

## Slide 27
A simple source can produce electrons from a cathode, accelerate them to ~100eV, and let them strike atoms in a gas.
Ion Source Essentials
Cathode
Grid
Ionization
region
R.L. Gill, A. Piotrowski, NIM A, Vol 234 (2), p213, 1985.
http://dx.doi.org/10.1016/0168-9002(85)90907-6

## Slide 28: Plasma Particle Motion
B
E
B

## Slide 29
In order to control the electrons and ions, we make use magnetic fields to alter the particle trajectories.
Ion Source Essentials

## Slide 30: Plasma Particle Motion
B
cf: opposite to classical energy – velocity equation !

## Slide 31
Electron Sources
  Thermionic
  Photo-Cathodes
Ion Sources
  Particle motion in plasmas
  Protons
  Negative Ions
  ECR Ion Source
  Radioactive Ions

## Slide 32: Ion Source – Duoplasmatron – Linac2
Solenoid
Cathode
Anode
Gas feed
Expansion Cup
Proton Current | 200 mA
Proton Energy | 90 keV
Emittance | ~0.4 mm.mrad
Pulse for LHC | 20us @ 1 Hz
# protons / pulse | 2.5x1013
# LHC bunches | ~24 *
* Creation of LHC bunches is a complicated process, this is an example for 50ns LHC bunches
Notes: Magnetic = 2 ROLES. Stop electrons to walls. Increase path length.

## Slide 33
Electron Sources
  Thermionic
  Photo-Cathodes
Ion Sources
  Particle motion in plasmas
  Protons
  Negative Ions
  ECR Ion Source
  Radioactive Ions

## Slide 34: Ion Sources – Negative Ions
In 2021 – CERN moved from Linac2 produced protons to Linac4 produced H- ions (at higher Linac energy).
H- give the possibility for stripping injection into PSB synchrotron.
 | Electron Affinity (eV)
H | 0.7542
He | <0
Li | 0.6182
Be | <0
B | 0.277
C | 1.2629
N | <0
O | 1.462
F | 3.399
The bonding energy for an electron onto an atom is the Electron Affinity.
Ea < 0 for Noble Gases
Large Ea for Halogens
Two categories of negative ion sources
  Surface – an atom on a surface can be desorbed with an extra electron (whose wave-function overlapped the atom).
  Volume – Through collisions, e-capture and molecular dissociation, negative ions can be formed.
AB + e → A- + B A + B → A- + B+
AB* + e → A- + B A+ + B → A- + B2+
Notes: Dissociative attachment Atomic Double charge transfer
Dissociative attachment to vibrationally excited state Atomic Two electron capture

## Slide 35: H- Surface Ion Production
Cs
H+, H2+
H-
e-
Cs
e-
e-
Surface
Protons from the plasma are accelerated to the cathode, which has a coating of caesium, producing a low work function.
The protons desorbed from the low work function surface, with an additional electron.
The plasma must not be too hot, to avoid ionising the H-.
Penning, Magnetron, RF sources can produce H- this way.

## Slide 36: Ion Sources – Negative Ions – Linac4
Linac4 Ion Source uses a 2MHz RF driven plasma
Plasma is created using 2MHz RF in a solenoid coil.
A surface near the extraction is coated with cesium, evaporated from an oven at the back of the source.
The plasma protons strike the cesium surface and H- are emitted.

## Slide 37: Ion Sources – Negative Ions – Linac4
Solenoid Antenna – plasma heating
Magnets slow stop hot electrons
Electrodes with Cs surface coating

## Slide 38: Ion Sources – Negative Ions – Linac4
Electrons (yellow) are extracted along with negative ions (red).
Electrons can be separated with a dipole B field in extraction.
In the Linac4 RF source electron current is:
  >1 A without caesium
  ~ 35mA with caesium
-45kV
-25kV
-35kV
0kV

## Slide 39
Electron Sources
  Thermionic
  Photo-Cathodes
Ion Sources
  Particle motion in plasmas
  Protons
  Negative Ions
  ECR Ion Source
  Radioactive Ions

## Slide 40: Ion Source – ECR – Linac3
Electron Cyclotron Resonance Ion Source (ECR)
For a given magnetic field, non-relativistic electrons have a fixed revolution frequency.
The plasma electrons will absorb energy at this frequency (just as particles in a cyclotron).
If confined in a magnetic bottle, the electrons can be heated to the keV and even MeV range.
Ions also trapped by the charge of the electrons, but for milli-seconds allowing mutliple ionisation.
The solenoid magnetic field still allows losses on axis – these ions make the beam.
Frf
Frf
Electron orbit
½ RF period later
Notes: After Fecr – go to drawing

## Slide 41: Ion Source – ECR
CERN ECR4 – Built by GANIL

## Slide 42: Ion Source – ECR – High charge states
No filament is needed, greatly increasing the source lifetime.
Singly, multiply and highly charged ions can be produced by these sources (although the source construction will influence this). A  A+  A2+  A3+ Stepwise ionisation.
Gaseous ions are easily made. Metallic ions come from an OVEN or from a compound gas (e.g UF6 for uranium).
In the afterglow mode, the ion intensity increases AFTER switching off the micro-waves.

## Slide 43
Ion Source – ECR – High charge states + industry solutions
Plasma density increases with frequency and associated magnetic field.
Example: VENUS source and Berkeley, Ca, uses superconducting solenoid and sextapole magnets.
Industry can now provide turnkey solutions for ECR ions sources, usually using permanent magnets.

## Slide 44
Lead (Pb) is evapourated from a micro oven in the source

## Slide 45
Electron Sources
  Thermionic
  Photo-Cathodes
Ion Sources
  Particle motion in plasmas
  Protons
  Negative Ions
  ECR Ion Source
  Radioactive Ions

## Slide 46: Ion Source – Radioactive Ions – ISOLDE
A gas/vapour of new isotopes is produced from 1.4GeV protons onto a target.
The ion source is used to ionize the gas.
The ions will be mass selected in an ion spectrometer.
An important goal is to have a high conversion rate of the desired gas to ions.
The sources must be robust to work in the extreme radiation environment. For example minimize use of any organic compounds.
The sources can help to reduce the contamination (i.e. stable/other isotopes of the same mass) through some selective process (e.g. using lasers to selectively ionize the atom of interest).
Notes: Magnetic = 2 ROLES. Stop electrons to walls. Increase path length

## Slide 47
For sources, all we have seen so far is the ion generation.
You still have to add the high voltage systems, pumping, cooling, power convertors, controls…

## Slide 48: Summary
Electron Source Summary
  Thermionic Source. Some thermal electrons are above the Work-Function.
  Use low work-function or high melting point materials to obtain the most electrons
  Photo-cathodes – Use photons above the work-function or Eg+Ea.
  Metals – Stable but have a low quantum efficiency
  Semiconductors – high Qeff, but can be unstable and degrade in use.
Ion Source Summary
  Plasmas are a common production method for ions.
  There are many ways to produce, heat and confine a plasma, leading to many source types.
  CERN already uses quite an array of these types.

## Slide 49: Further Reading
Handbook of Ion Source, B. Wolf, Boca Raton, FL: CRC Press, 1995
Ion Sources, Zhang Hua Shun, Berlin: Springer, 1999.
The Physics and Technology of Ion Source, I. G. Brown, New York, NY: Wiley, 1989
Large Ion Beams: Fundamentals of Generation and Propagation, T. A .Forrester, New York, NY: Wiley, 1988
CAS – 5th General School (CERN 94-01 ) and Cyclotrons, Linacs… (CERN-96-02 )

## Slide 50
Thank you for your attention.

## Slide 51
A: Richardson-Dushman constant
B: Magnetic field
D: Diffusion rate
E: Particle Kinetic Energy
E: Electric field
J: Current density
m: Particle Mass
n: Particle density
T: Temperature
U,V: Voltage
v: Particle velocity
vdrift: Particle drift velocity
b: Relativistic beta
g: Relativistic gamma
fs: Work Function (Voltage)
n: Collision Frequency
rc: Cyclotron Radius
wc: Cyclotron Frequency

## Slide 52: Ion Sources - Basics
Ion Sources at CERN.
Linac2 – Protons - Dupolasmatron
Linac3 – Ions (Pb, O, Ar) – ECR
ISOLDE – Radioactive ions – Surface, laser, Electron Bombardment.
Linac4 – Negative Hydrogen – RF

## Slide 53: Electrons – Thermionic Emission (the maths)
Conducting materials contain free electrons, who follow the Fermi-Dirac energy distribution inside the material.
When a material is heated, the electrons energy distribution shifts from the zero temperature Fermi distribution.
EFermi
Number of Free Electrons
These electrons can escape the material
Notes: 2 non-integer spin particles cannot occupy same energy level (Pauli exclusion)
Hence Fermi-Dirac equation gives the occupation of conduction electrons at different energy levels.
Integrate the equation above the work-function

## Slide 54: ECR Source – Magnetic Mirror
B1
B2
F1
F2
v
A force acts in the opposite direction to the
Increasing B field
Vdrift
Energy is transferred
from Vdrift to Vecr
= magnetic moment
K = total kinetic energy
x
y

## Slide 55
By applying a magnetic field, electrons can have longer path lengths inside the source, and the rate of ionization is increased.