## Slide 1
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to broadcast them online to all registered students and to post them without any further processing on the CAS website.
The author hereby confirms that the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution.
Copyright statement and speaker’s release for video publishing

## Slide 2
High Luminosity LHC – Status and Prospects
CAS March 2024
Markus Zerlauth with acknowledgements to O.Brüning, M.Lamont, L.Rossi, J. Wenninger and many other CERN colleagues

## Slide 3
LHC design performance and HL-LHC upgrade goals
(Main) Technical challenges of the HL-LHC upgrade
Inner Triplet String
Preparing HL-LHC operation and performance ramp-up
Conclusions
Outline
3

## Slide 4
LHC design performance and HL-LHC upgrade goals
(Main) Technical challenges of the HL-LHC upgrade
Inner Triplet String
Preparing HL-LHC operation and performance ramp-up
Conclusions
Outline
4

## Slide 5: Introduction: LHC Performance Goals
p collisions Ebeam > 5 TeV LHC: E = 7 TeV
Collision energy: Higgs discovery requires ECM > 1 TeV
Instantaneous luminosity: rate of events in detector
Integrated luminosity: total number of events L
depends on the beam lifetime, the LHC cycle and
‘turn around’ time and overall accelerator efficiency
rare events L > 1033cm-2sec-1 L = 1034cm-2sec-1
300 fb-1 with 1barn = 10-28m2 and femto = 10-15
[3.5/4TeV; 6.5TeV; 6.8TeV]
[2×1034cm-2sec-1]
[270 fb-1]

## Slide 7: After that it’s been quite a ride

## Slide 8
Run 3
]

## Slide 9: Goal of HL-LHC upgrade project
Many questions remain! (Higgs properties/couplings?, more than just 1 Higgs? Beyond SM physics? Dark Matter/energy?)
The main objective of the HL-LHC is to determine and build a hardware configuration and a set of beam parameters that will allow the LHC to reach the following targets:
Prepare machine for operation beyond 2025 and up to the early 2040s
Devise beam parameters and operational scenarios for:
# enabling at total integrated luminosity of 3000 fb-1
# implying an integrated luminosity of 250 fb-1 per year,
# design oper. for μ ≤ 140 ( peak luminosity 5 x 1034 cm-2 s-1)
Implies overcoming several limitations in the existing LHC!!!
Cryo cooling of triplet magnets & radiation damage in triplet magnets & machine efficiency!
But also for the experiments!!
 Need for an Upgrade!
5 events
400 events

## Slide 10
Increase bunch population
Higher Intensity
Smaller
Reduced emittance
Smaller beam size at IP
Crossing angle reduction factor
Shorter bunches, smaller crossing angle, crab cavities
Increase F

## Slide 11: HL-LHC Design Parameters
LHC Magnet system
LHC injector complex
LHC injector complex
HL-LHC triplet magnets
HL-LHC crab cavities
Machine operation &
availability
Notes: To be updated with last version before the CMSDAS meeting

## Slide 12
Run3 operation
Approval of
HL-LHC Project
EU funded HiLumi
Design Study
HL-LHC Operation
We are here
1.5 years until start of Long Shutdown 3
75% of the project budget of ~1.1 BCHF already committed
The project is ready for installation start in 2026!  endorsed by 2023 C&SR

## Slide 13
LHC design performance and HL-LHC upgrade goals
(Main) Technical challenges of the HL-LHC upgrade
Inner Triplet String
Preparing HL-LHC operation and performance ramp-up
Conclusions
Outline
13

## Slide 14: HL-LHC technology landmarks
No accelerator upgrade project has so many challenging novelties covering such a broad technology spectrum
Technology intensive project!
Major upgrades in P1 and P5, large fraction of LHC will remain unchanged

## Slide 15
Q2
27 MGy
MCBX3 20 MGy
Cold bore insulation
≈ 35 MGy
ATLAS
CMS
Epoxy and most insulation materials
will become brittle at these radiation levels and loose their mechanical integrity!!!
HL-LHC Technical Challenges: Triplet Magnets
Operation beyond 2025:
Requires replacement of LHC Triplet magnets
10 x the luminosity  Requires new, more radiation resistant triplet magnets
15

## Slide 16
CMS
ATLAS
Need for shielding and larger crossing angle results in aperture of 150 mm, requiring novel Nb3Sn superconductors
Longer Triplet assembly implies longer distance over which the 2 LHC beams share the same path!
ca. 40 unwanted [parasitic] collision points
Crossing angle & Crab Cavities
New HL-LHC Triplet Layout

## Slide 17: New interaction region layout
New insertion and final focusing magnets
  Main quadrupole magnets MQXFA (Q1, Q3) from AUP and MQXFB (Q2) from CERN
  Superconducting separation and recombination dipoles, D1 from Japan and D2 from Italy
  Higher Order Corrector package (CP) and orbit correctors (MCBX) from Italy and Spain
LHC
HL-LHC
ATLAS
CMS
ATLAS
CMS

## Slide 18
Requires larger aperture!
70 mm at 210 T/m 150 mm diameter 140 T/m
8 T peak field at coils  12 T field at coils (Nb3Sn)!!!
Need to replace existing triplet magnets with radiation hard system (shielding!) such that the new magnet coils receive a similar radiation dose @ 10 times higher integrated luminosity!!!!!  Shielding!
Tungsten blocks
Capillaries
US-LARP MQXF magnet design
Based on Nb3Sn
technology
 New magnet technology!
HL-LHC technical bottleneck:
Radiation damage to inner triplet magnets

## Slide 19
Nb3Sn quadrupole: Transition from Prototype to Series production
Second short (1.5 m) under preparation for test at CERN
Insertion of coil package inside mechanical structure of the first IT quad prototypes (4.2 m long) in LBNL-USA
19

## Slide 20: Improvement Plan for MQXFB
After steady progress with prototypes and first of series which already reached acceptance criteria at 1.9K, MQXFB03 is the 3rd magnet of 3-stage strategy, integrating full set of improvements for cold mass assembly, magnet loading and coil manufacturing
It was tested in Q3/Q4 2023 and is the first 7.2-m-long MQXFB magnet to achieve target current of 16.53 kA at both 1.9 K and 4.5 K.
It shows good endurance after 2 warm-up/ cooldown cycles with no retraining at 1.9 K; no ramp rate degradation up to 100 A/s; initial training quenches at 1.9 K are all in coil ends

## Slide 21: Magnets
Arrival of AUP magnet @ CERN

## Slide 22: HL-LHC Challenges: Crossing Angle I
Maximize the number of Protons:
non-linear fields from long-range beam-beam interaction:
 Operation requires crossing angle
efficient operation requires large beam separation at unwanted collision points  Separation of 10 -12 s  large crossing angle at Interaction Point!
Insertion Layout:
ca.130m  150m
ca.50m
Operation with ca. 2800 bunches @ 25ns spacing  approximately 30 unwanted collision per
Interaction Region (IR).

## Slide 23: HL-LHC Technical Challenges: Crab Cavities
Geometric Luminosity Reduction Factor:
Challenging space constraints – 194 mm separation between the 2 beams
 requires compact cavity design
Crab Cavities:
effective cross section
Full Crossing angle:
285 mrad LHC TDR
-> 329 mrad in LHC op
-> 500 mrad HL TDR
DQW
RF-Dipole
nom LHC
nom HL-LHC
early LHC
23

## Slide 25: Industrial DQW Series (RI)
1st pre-series jacketed cavity with excellent results, metrology to be finalized before acceptance
2nd cavity in metrology and cold tests soon

## Slide 26
Crab cavity cryo-module for installation in the SPS
26

## Slide 27
UA57
US57
UR55
UL57
UPR57
PC IT
PCs IT Trims
DFX
DSHX
DFHX
CDBs
PIC,BIS
QDS
CLIQ
Warm Diodes
DCM
Q1
Q2A
Q2B
Q3
CP
D1
OC PCs
D1 PC
Cold Diodes
OC EE
DSHM
D2 PC
D2 OC EE
Cold box
CDBs
DFM
DFHM
DQHDS
D2
Q4
Q5
Q6
Valve box
D2 OC PCs
Crab
Cavities
RF Powering
UW57
TAXN
Cooling and Ventilation
Operation with levelled lumi calls for longer physics fills
Low radiation areas for electronics
Accessibility of equipment -> increased maintainability
But up to 100m between PC and magnets!
HL-LHC Technical Challenges: Machine Efficiency

## Slide 28: IR1/5 underground civil engineering completed in 2022
Most of the work was conducted during LS2  vibration impact
Transition to LHC tunnel
Work started at End Run1 during 2018
Construction Finished End 2022
28
Notes: 18

## Slide 29: Completion of Surface buildings in 2023
SF17
SHM17
SD17
SE17
SU17
Example Point 1
20th January 2023
Celebration Ceremony: Point 5
Work Ended Spring 2023

## Slide 30: HL-LHC Technical Challenges: Cold powering systems based on flexible sc link using MgB2 superconductor
D2
DSHM
DFHM
Q1
Q2A
Q2B
Q3
CP
D1
DCM
DFM
DFX
DSHX
DFHX
Diam ca. 90mm
> 100kA @ 25K
30
DSHM
DSHX

## Slide 31: Mg2B Superconductor and Superconducting link
Cable production complete !
More than half of flexible cryostats at CERN
Assembly of the first complete
system incl. flexible cryostats
is ongoing
Demo-3 in SM18
Successfully Demonstrated
Concept between 2020 / 22
with > 120kA @ 30K
31

## Slide 32
SC-Link-DFHX assembly in pictures
Complete System Test ongoing in SM18

## Slide 33: The realization of HL-LHC is a truly international collaboration
Q1
Q2a
Q2b
Q3
D1
DFX
DFM
Connection to LHC (UL)
Service gallery (UR)
TAXS
Crab cavities
UA Gallery
Q4
TAXN
Service cavern
SC Links
D2
Collimators
CP
DFHX
DFHM
DQHDS
Notes: 17

## Slide 34
LHC design performance and HL-LHC upgrade goals
(Main) Technical challenges of the HL-LHC upgrade
Inner Triplet String
Preparing HL-LHC operation and performance ramp-up
Conclusions
Outline
34

## Slide 35
HL-LHC IT STRING: P5L
P5
P5L
P5R
SPS
HL-LHC
P1
P2
P3
P4
P5
P6
P7
P8
HL-LHC Cost & Schedule Review 2022, November 2022

## Slide 36: HL-LHC testing facilities in SM18
SRF Section
Magnet Testbenches
Cold-powering Test Area
IT Test Area

## Slide 37
The IT STRING will deliver the first complete experience of installing and operating the IT zone
The scope of the IT STRING is to represent, as best as reasonably achievable in a surface building, the various operation modes to STUDY and VALIDATE the COLLECTIVE BEHAVIOUR of the different systems of the HL-LHC’s IT zone (magnets, magnet protection, cryogenics of the magnets and of the superconducting link, magnet powering, vacuum, alignment, interconnections between magnets, and the superconducting link itself).
The IT STRING Scope
Ref. HL-LHC IT STRING Scope https://edms.cern.ch/document/1693312/1
Early involvement of OP would be extremely important and beneficial for later commissioning in machine

## Slide 38: IT String Status in pictures
On top of the empty metallic structure
Under the metallic structure
PC and Energy Extraction racks installed on the metallic structure
Cryo Distribution
Q4 2024
Q2-Q4 2025
Q1’26
Q2’26
Q1’25

## Slide 39
All eight converters ramping from -10A to +10A | Imeas [A]
slides.of Y. Thurel are here for more details
The 120 A circuits are with the smallest current ratings among all STRING circuits. They rely on known LHC technology.
FIRST 10 Ampers in the HL-LHC IT STRING

## Slide 40
LHC design performance and HL-LHC upgrade goals
(Main) Technical challenges of the HL-LHC upgrade
Inner Triplet String
Preparing HL-LHC operation and performance ramp-up
Conclusions
Outline
40

## Slide 41: HL Installation in the LHC during LS3 @ P1&P5

## Slide 42: HL-LHC hardware commissioning to start already in mid 2028, machine checkout in Q2 2029!

## Slide 43: Start of HL-LHC exploitation and performance ramp-up

## Slide 44: Then another miracle happens…
Extension of the ALICE run beyond LS4 and the planned LHCb upgrade in LS4, both will have an impact on LHC operation and on the performance reach of HL-LHC.

## Slide 45
LHC design performance and HL-LHC upgrade goals
(Main) Technical challenges of the HL-LHC upgrade
Inner Triplet String
Preparing HL-LHC operation and performance ramp-up
Conclusions
Outline
45

## Slide 47: Conclusions:
MQXFB02
D1
proto
Repaired
MB Dipole
CP
MQXFBP3
Nb3Sn Technology validated
Superconducting Link demonstrated
Crab Cavity Operation and Production demonstrated
Civil Engineering Work Completed
1st Part of Collimation Upgrade completed
The project is on Track for installation
during LS3 starting in 2026
Stay Tuned for completion of the IT-String installation in 2023/24 and operation @ cold as of 2025!
All magnet productions on good track!

## Slide 48: TDR V1.0 - The last version of the TDR including the added scope - 2020
V0.1 Published in electronic version for the October 2016 Cost & Schedule review
EDMS: 1723851
and as CERN Yellow Book in October 2017
Updated Version V 1.0 published as
CERN Yellow Book in December 2020
https://e-publishing.cern.ch/index.php/CYRM/issue/view/127

## Slide 50: Ideal (HL-)LHC operation
1x1034 cm-2s-1
Event pile-up in experiments >200
Levelling with
crab-cavity

## Slide 51: Flexible MgB2 superconducting links
MgB2 cable:
  90 mm
Itot > 100 kA @ 25 K
 90 mm
L= 60 m
MgB2
System demonstrator in SM 18
DEMO2
Demonstration of 2 x 20kA +
2 x 7kA in June
in MgB2 @ 30K
in flexible cryostat
over 60m [54kA total]
51

## Slide 52: MgB2 Cable Assemblies (1/2)
Successfully HV tested both in industry and at CERN
Received from ICAS 2nd (Triplets) and 3rd (Matching Sections) MgB2 series cables
  Wire grading and cable map approval procedures established
  Continuous tests at CERN of extracted strands from each constituent cable before approving further operations – 694 test pieces in 2021
  Production planned to be completed by end 2022
 90 mm
To be produced: 5+5 Units

## Slide 53: SC Link Cryostats
Received first series SC Link cryostat for Triplets – produced in industry
Final length for Triplets: 74.5 m
Leak/pressure tests at the company
Delivery & Reception @ CERN
  Optimization of leak test procedure
  Visual and endoscopic inspections, dimension controls

## Slide 54: First DFHX constructed @ CERN (2/3)
Completed blank assembly of DFHX and
studied of MgB2/HTS routing

## Slide 55: DFX Cryostat
Completed pre-series DFX by SOTON (UK1 ) !
D2
DSHM
DFHM
Q1
Q2A
Q2B
Q3
CP
D1
DCM
DFM
DFX
DSHX
DFHX
CERN-UK1 collaboration under addendum #4 of KE3299/TE/HL-LHC
Design, Manufacturing, QC & CE certification under the responsibility of Southampton University
PRR 3 March 2020. 1.5 intense years from raw material procurement to completion of qualification and CE certification by notified body
Completed in March 2022 at LTI Metaltech & delivered to CERN

## Slide 56
Re-Organisation of the HL-LHC Project Office
Departure of Beniamino di Girolamo
 Appointment of Lars Jensen as new Collaboration Officer
Request after the Cost & Schedule Review 2022 to separate Budget and Schedule Office
 Reinforcement of the Schedule monitoring & control
 Redefinition of Project Office Mandates and names
 Dedicated Schedule Officer to be appointed by the end of the year
Internal Audit of the HL-LHC project by CERN audit team
 Revision and update of ALL HL-LHC related mandates
Migration of the Project Webpages to the New SharePoint platform
https://cern.sharepoint.com/sites/HL-LHC/WP1/SitePages/Collaborations.aspx -> new Collaborations office pages
https://cern.sharepoint.com/sites/HL-LHC/ -> new project Intranet
https://cern.sharepoint.com/sites/HL-LHC/CB/ -> new HLCB site
The HL-LHC Project is in the process of
Strengthening the liaison with the CERN central support team and
Safety Units for the
LS3 Organization

## Slide 57: HL Project Management and Organsiation

## Slide 58
MQXFB03 is the 3rd magnet of 3-stage strategy, integrating all recovery actions
  (1) improved cold mass assembly and fixed point;
  (2) improved magnet loading to avoid overshoot;
  (3) improved coil manufacturing to remove hump & belly.
It was tested in Q3/Q4 2023 and is the first 7.2-m-long MQXFB magnet to achieve target current of 16.53 kA at both 1.9 K and 4.5 K.
It shows good endurance after 2 warm-up/ cooldown cycles with no retraining at 1.9 K; no ramp rate degradation up to 100 A/s; initial training quenches at 1.9 K are all in coil ends (2 training quenches at 4.5 K upon reaching target current plateau under investigation).
Recovery Plan for MQXFB
Quench Performance of 7.2-m-Long MQXFB03 Quadrupole Magnet at CERN
Performance limitation and phenomenology observed on previous, full-length, MQXFB magnet straight sections (near apex of hump & belly) have been overcome and root cause has been eliminated.
Series production has been launched (next magnet, MQXFB04, already loaded).
Ramp rate sensitivity of 7.2-m-Long MQXFB03 Quadrupole Magnet at CERN
- New coldmass
- New loading
- New coils

## Slide 59
Highlights on MQXFA (US Contribution)
AUP has completed the assembly and has successfully tested on an horizontal bench at Fermilab the first Q1/Q3 cryo-magnet (LQXFA01).
LQXFA01 includes 2 4.2-m-long quadrupole magnets: MQXFA03 and MQXFA04, which were previously tested in vertical station; neither of them exhibited any retraining.
LQXFA01 was shipped to CERN and arrived in SMI2 on 28 November 2022.
It will be retested at CERN on upgraded test bench A2 in Spring 2024 prior to installation in the string (but cannot be used as is for tunnel installation).
Warm thanks to all of those in LMF, EN-MME and HSE who contributed to resolve the issue of weld procedure qualification and paved the way for use of this cryomagnet in the string.
Courtesy of D. Duarte Ramos (CERN TE-MSC)
First AUP LQXFA01 cryomagnet mounted on Cryostat Tooling in SMI2 at CERN
Quench summary of LQXFA01 tested horizontally at Fermilab
Courtesy of S. Feher and G. Ambrosio (Fermilab)

## Slide 60: Nb‒Ti Magnets for HL-LHC
Good progress on industrial productions of Nb‒Ti magnets for HL-LHC, thanks to efficient collaborations with partner institutes; production of remaining MCBXF correctors to be internalized by CIEMAT and CERN.
Courtesy of S. Farinon (INFN-Genova) and A. Foussat (CERN TE-MSC)
8-m-long, 105-mm-double aperture D2 dipole magnet prototype (4.5/5.3 T bore/peak field @12.23 kA)
6.7-m-long, 150-single-aperture D1 dipole magnet (5.6/6.58 T bore/peak field @12.11 kA)
Courtesy of T. Natsumoto (KEK) and J.-C. Perez (CERN TE-MSC)
1.2/2.2-m-long, 150-single-aperture nested dipole magnet corrector (2.1/4.13 T bore/peak field @1.58 kA)
Courtesy of F. Toral (CIEMAT) and J.-C. Perez (CERN TE-MSC)
MCBXFB04
2-m-long, 105-mm-double aperture, CCT orbit corrector magnet (2.6/2.94 T bore/peak field @394 A)
Courtesy of Q. Xu (IHEP) and A. Foussat (CERN TE-MSC)
MCBRD04
High-order corrector magnets production completed; all magnets tested and accepted; cryostating of first corrector package underway at SMI2.
Courtesy of M. Statera (INFN-Milano) and E. Gautheron (CERN TE-MSC)
After E. Todesco (CERN TE-MSC)

## Slide 61: Status MQXFA – Q1 & Q3- Assemblies at AUP
8 out of 20 magnets build, tested and validated!
From 15 that were produced – 3 during COVID  all non-conformed being repaired  2 repaired validated
MQXFA08b & MQXFA14b repaired and validating coil replacement procedure and coil production planning
Endurance test on MQXFA05: 50 quenches, 5 TC  magnet remains @ nominal! ✓
Unscheduled mechanical robustness test for MQXFA11  road accident ✓
Magnet passed acceptance criteria at vertical test station ✓
CA-01: First cold mass reaching nominal performance – no retraining after thermal cycle
Nonconformities but accepted in close collaboration with AUP to assure in-time delivery for IT-String
 shipment on its way  Arrival at CERN in December [acceptable for IT-String, not yet for machine]
Cabling completed: https://newscenter.lbl.gov/2023/08/30/cabling-for-lhc-upgrade-wraps-up/
Second Cold-Mass Assembly being prepared for testing at FNAL  second out of 10 CMA
STATUS
CA01 Leaving FNAL October 30th 2023
CA01 Arriving @ CERN November 28th 2023

## Slide 62: Lift Installation in Pt1 and Pt5
    PM17 issue resolved thanks to help of many CERN teams (EN-ACE, SCE, HSE WP17,…)
25/01/2023
concrete spalling
30/01-03/02/2023
Inspection
30/06/2023
Closure of NC
Impact on Schedule minimized by swapping start of Lift Installation from Pt1 to Pt5, but overall ca. 6 month lost for installation of technical infrastructure
 Not critical, completion of Technical Infrastructure installation still before start of LS3

## Slide 63: CERN accelerator complex

## Slide 64: LHC Injector Upgrade Project (LIU)
HL-LHC performance relies on more intense and brighter bunches from injector complex (2.2E11p / 2um at SPS extraction wrt to LHC nominal of 1.15E11p / 3.4um)
25ns beam limited by space charge in PS, PSB, SPS; SPS RF power and SPS longitudinal instabilities
50ns beam limited by PS longitudinal instabilities & SPS space charge and SPS TMCI

## Slide 65: LHC Injector Upgrade Project (LIU)
Linac4 in for Linac2 | H- injection into PSB at 160 MeV Expected double brightness for LHC beams out of the PSB
Booster | Increase energy to 2 GeV New RF system New main power supply
PS | Injection at 2 GeV Beam production schemes Feedback systems: new wide-band longitudinal feedback; transverse feedback against head-tail and e-cloud instabilities
SPS | Power upgrade of the main 200 MHz RF system Electron cloud mitigation through a-C coating (baseline) or beam induced scrubbing
Successfully deployed during LS2 in 2019/2020

## Slide 66: Electron cloud and cryogenic heat load
Electrons are inevitably produced inside the LHC beam chamber. Seed electrons (e.g. from synchrotron radiation) hitting chamber’s walls and ejecting secondary electrons
These electrons can subsequently be accelerated by the proton bunches. When they hit the vacuum chamber wall, they have a probability of ejecting more electrons, the cycle continues, and the electron cloud (e-cloud) is created.
Parameter of interest is the Secondary Emission Yield (SEY), which is the average number of electrons produced per impact
E-cloud both affects beam quality and considerable increases heat load on cryogenic system -> Potential limitation + electricity cost!

## Slide 67: Electron cloud and cryogenic heat load
Mitigation: ‘Scrubbing’ runs where increased bunch intensity and train lengths are injected to condition the beam screens
Evolution of the secondary emission yield (SEY) over the 2022 scrubbing run has shown a
A clear reduction of the average SEY is observed in every sector
Conditioning is initially fast and gets slower as the SEY decreases

## Slide 68: SEY evolution over scrubbing run
Significant conditioning has taken place in every sector
  Sector 78 showed significantly higher SEY than the other sectors from the beginning, and stays higher even after conditioning
  Sectors 34 and 45 continue to show the lowest SEYs, as in Run 2
SEY start of Run3
SEY today

## Slide 69: SEY comparison to 2018
A first analysis has been performed to compare the present cell-by-cell SEY to 2018
In most sectors, the SEYs are currently very close to their 2018 values (at 450 GeV)
  The differences are within the error bars of the analysis
Sectors 67 and 78 still show much higher SEY than in 2018
Sector 56 shows a mildly higher SEY than in 2018
SEY in 2018
SEY in 2022

## Slide 70: Outline
HL-LHC design parameters and upgrade goals
Start of LHC Run 3 and lessons learnt for HL-LHC era
  Completion of LHC Injector Upgrade
  E-cloud and heat load
  UFOs and Radiation to Electronics
  Magnet training
  Machine Availability and physics output
Preparing HL-LHC operation
  IT String
Current Project planning and performance ramp-up

## Slide 71: UFOs and their interactions with the LHC beams
Examples of orbits of charged dust particulates around the LHC beam. Beam screen height is ~37 mm
Dust samples from the ceramic tube of an injection kicker magnet. (b) shows an enlarged view of an Al2O3 particle with a radius of about 5 um
Dust particles are inevitably present in the LHC vacuum chamber
They get charged and can travel along the electric and magnetic fields of the beam and the surrounding magnets
Interactions with the high intensity proton beams generate fast, localised beam losses that affect operation (and can generate magnet quenches)

## Slide 72: UFO conditioning in Run2 compared to 2022

## Slide 73: UFO rate 2015 vs 2022
Conclusion:
Expected re-conditioning of UFOs at the start of Run3.
Much lower quench margins at 7 TeV and with HL-LHC beam parameters
  Could have a considerable impact on machine availability (especially early in the run)!
(Part) of physics behind UFO mechanism still not fully understood

## Slide 74: Quench limits vs UFOs
Conclusion:
Expected re-conditioning of UFOs at the start of Run3.
Much lower quench margins at 7 TeV and with HL-LHC beam parameters
  Could have a considerable impact on machine availability (especially early in the run)!
(Part) of physics behind UFO mechanism still not fully understood
6.5 TeV
7 TeV

## Slide 75: Radiation to Electronics
2015:
Start of the year: nQPS SEEs (introduced in LS1)
Rest of the year: mainly FGC2 in the arc
2016:
SEE rate reduction mainly due to lower arc radiation levels (vacuum conditioning)
2017:
Further improvement thanks to FGClite deployment in ARC; most R2E events in power converters in RR (upgraded in LS2 with radiation tolerant versions)
2018:
Increased radiation levels in DS of IP1 and IP5 due to TCL6 opening → impact on QPS equipment (possibly lifetime related, i.e. no longer linear versus integrated luminosity)

## Slide 76: Outline
HL-LHC design parameters and upgrade goals
Start of LHC Run 3 and lessons learnt for HL-LHC era
  Completion of LHC Injector Upgrade
  E-cloud and heat load
  UFOs and Radiation to Electronics
  Magnet training
  Machine Availability and physics output
Preparing HL-LHC operation
  IT String
Current Project planning and performance ramp-up

## Slide 77: LHC machine sectorisation
Sector
1
5
DC Power feed
3
Octant
DC Power
2
4
6
8
7
For superconducting magnets, no DC powering across IPs
Main DC power feed at even points (MB, MQ), some DC power feed at odd points
8 main dipole + 16 quadrupole circuits in LHC
LHC Sector
arc cryostat
Commissioning possible for each sector independent of other sectors
More complex powering system and tracking between sectors

## Slide 78: Training quenches RB Circuits
Collision energy of (HL-)LHC is strictly linked to achievable current of the 1232 (= 8 x 154) LHC main dipole magnets
5 sectors reached 6.8 TeV equivalent, 3 sectors reached 7 TeV
No sign of permanent degradation.

## Slide 79
Training history RB.A23
54 circuit quench events,
64 magnet training quenches,
301 magnet heater firings
The 64 quenches in S23 after the 2nd additional TC came as a surprise, as usually training goes faster after a TC
Detailed analysis of the dipole training campaigns is ongoing, including results from reception tests in SM18.

## Slide 80: Total nr of quenches in LHC main dipoles
Nr of quenches in the same dipole magnet | Nr of dipole magnets
5 | 3
4 | 11
3 | 56
2 | 154
1 | 446
0 | 562
Conclusion:
Still 562 dipole magnets (45%) never experienced a training quench in the LHC since 2008.
Some circuits (including corrector circuits) showed much longer training than in previous campaigns, and their behavior will be closely monitored in the coming years.
Desired operating currents can still be reached (with only a few exceptions) 14 years after the start of the LHC, with several thermal cycles, numerous current cycles, radiation, and large number of quenches.
a quench is a very violent process (especially in the high-current circuits), and that each quench implies a certain unavoidable risk (short-to-gnd, internal short, quench heater failure, etc).
Decision of collision energy post LS3 will inevitably involve a cost/benefit analysis of required re-training effort (which implies technical risks and considerable time!)

## Slide 81: Progress and (initial) training of HL-LHC triplet magnets
Six magnets of type MQXFA from AUP reached performance
  Operation at nominal current plus 300 A, both at 1.9 K and 4.5 K
  Perfect memory, i.e. no retraining, and some robustness
Powering test of conform MQXFA magnets (J. Muratore, B. Ahia, S. Feher et al.)

## Slide 82: Progress and (initial) training of HL-LHC triplet magnets
MQXFBP3 includes the new procedures used for LHe vessel integration
  Nominal plus 300 A reached during first powering with one training quench
  No degradation, three thermal cycles
MQXFBP3 on SM18 test bench (left) and test results (right)
(S. Izquierdo Bermudez, F. Mangiarotti, et al.)

## Slide 83: Advancements on MQXFBP1 diagnosis
MQXFBP1 performance limitation (6.5 TeV) analysis had a significant breakthrough in January 2022: analysis of limiting coil 108
  Broken filaments in a strand always in the same position of the cross-section, in several sections close to the transition in the poles –in agreement with voltage tap and quench antenna localization
Broken filaments in coil 108, limiting MQXFBP1 (M. Crouvizier, A. Moros, S. Sgobba, et al.)

## Slide 84: Outline
HL-LHC design parameters and upgrade goals
Start of LHC Run 3 and lessons learnt for HL-LHC era
  Completion of LHC Injector Upgrade
  E-cloud and heat load
  UFOs and Radiation to Electronics
  Magnet training
  Machine Availability and physics output
Preparing HL-LHC operation
  IT String
Current Project planning and performance ramp-up

## Slide 85: Machine Availability vs Physics output – an example
TS1
TS2
TS3

## Slide 86: Machine Availability vs Physics output – an example

## Slide 87: What defines the productivity / physics output?
Physics output is a function of…
time producing physics beams
turnaround between successive experiments
time to clear faults
physics performance during experiments
machine understanding
& operator skill
Availability
Maintainability
Scheduling

## Slide 88: Availability vs HL-LHC luminosities

## Slide 89
Beam dumps
RF
1720 Power converters
> 9000 magnetic elements
7568 Quench detection systems
1088 Beam position monitors
4000 Beam loss monitors
150 tonnes Helium, ~90 tonnes at 1.9 K
140 MJ stored beam energy in 2012
370 MJ design and > 700 MJ for HL-LHC!
830 MJ magnetic energy per sector at 6.5 TeV
 ≈ 10 GJ total @ 7 TeV
LHC 27km circumference: Big & Cold
Injection B2
Injection B1

## Slide 90
1983 : First studies for the LHC project
1988 : First magnet model (feasibility)
: Approval by the CERN Council
1996-1999 : Series production industrialisation
: Declaration of Public Utility &
Start of civil engineering
1998-2000 : Placement of main production contracts
2004 : Start of the LHC installation
2005-2007 : Magnets Installation in the tunnel
2006-2008 : Hardware commissioning
2008-2009 : Beam commissioning and repair
2010-2025 : Physics exploitation
14 TeV proton-proton accelerator-collider built in the LEP tunnel
Lead-Lead (Lead-proton) collisions
A 27 km circumference collider…
Ca. 20 years magnet development!!!
 Significant Time scale extending well beyond that of a physicist’s career!!!
Ca. 30 years machine development!!!
LHC (Large Hadron Collider)

## Slide 91
10 GJoule  flying 700 km/h
Energy stored in the LHC magnet system [8.3T]: 10 GJoule
Energy stored in the two beams: 720 MJ [ 6 1014 protons (1 ng of H+) at 7 TeV ]
700 MJ melt one ton of copper
700 MJoule dissipated in 88 us (1 turn)
 8 TW
Installed World Electrical Capacity:
3.8 TW
560 tons
10 GJoule  55 km/h
88’000 tons
Beam Dump robustness [core and windows]
Kicker reliability -> many kicker elements
-> Failure likelihood & reliability
Sectorization!!
-> Tracking
-> [ppm]!!!
1 electron volt = 1,602× 10-19 joule
Energy management Challenges in the LHC
Notes: 91
Aircraft carrier

## Slide 92: (Ideal) LHC cycle and machine efficiency
Minimum of 2h between end of one, and start of the next fill
Average LHC Turnaround time of 4-5h!!!!
Average LHC fill length of 8h  65% of scheduled physics time!!!
ca. 50% in LHC operation including faults at best conditions!
This becomes more challenging with increased Collider size and Requires even more powerful injector complex!!!!
92

## Slide 93: Reality…. 3 typical weeks of LHC Machine operation….

## Slide 94: Ideal HL-LHC operation with luminosity levelling
1x1034 cm-2s-1
Event pile-up in experiments >200
Levelling with
crab-cavity

## Slide 95
V. Shiltsev,
Physics Uspekhi 55
(2012) 965
2020
2030
LHC
HL-LHC
Proton / Proton
Proton / Anti-proton
Polarized Proton / Proton
Electron / Proton
Worldwide Integrated Luminosity prior to LHC: ca. 11 fb-1
LHC Design Goal: 300 fb-1  LHC likely to reach end of Run3: 350 fb-1 to 400 fb-1
HL-LHC goal: 3000 fb-1 to 4000 fb-1 !
x 35
x 10
Peak luminosities of Hadron Colliders

## Slide 96: HL-LHC targets a rich and diverse physics programme
Ions (ALICE 3 proposed for LS4)
b-physics (LHCb upgrade proposed for LS4)
Forward physics (PPS2)
Neutrinos (SND, FASERnu, FPF)
Long Lived Particles (GPDs, FASER, MoEDAL, CODEX-b, milliQan, MATHUSLA, ANIBUS, FPF)
Fixed target (SMOG-2, Crystal-FT)
Headline deliverable is 3 ab-1 p-p but the physics programme promises to be impressively diverse…
https://www.ichep2022.it

## Slide 97
source: L. Rossi
97
Nb3Sn
HL-LHC with 11-12T
16 T for HEP
Almost a commodity!
  15-20 t per year for MRI
  ITER needs 500 t
ca x5 cost LHC Nb-Ti
Brittle material
HTS (needed  20 T)
 on going R&D!
Bi-2212: cost today 2-5x Nb3Sn
YBCO: cost today 10x Nb3Sn
SC Magnet
technology

## Slide 98
courtesy: L. Rossi (CERN)
Transition from NbTi to Nb3Sn:
HL-LH lead the R&D for 11-15T magnets based on Nb3Sn technology:
15-20 years R&D program
Transition to HTS:
Assume R&D period of similar size  2035?
98
Magnet development requires substantial R&D effort!!!
Transition from NbTi to Nb3Sn: requires similar length of R&D!
HL-LHC led the R&D for 11-15 T magnets based on Nb3Sn technology:
Started in early 2000
15-20 years R&D program
 Ready by 2025
High Field superconducting Magnets