## Slide 1: Few words on Accelerators The CERN Accelerator Complex
Ilias Efthymiopoulos Ph.D. – Accelerators Physics Group (ABP)
ATSOA – 03.06.2024, CERN
Acceleration using RF
Rolf Wideroe – Thesis (1926)
First resonant accelerator

## Slide 2: The CERN
CERN is the world’s biggest laboratory for particle physics.
CERN’s mission: explore the origins of matter using high-energy particles, understand the fundamental particles and laws
Pillars in CERN’s mission
  Research
  Technology & Innovation
  Education & Training
  Collabration (world – wide)

## Slide 3: What are the accelerators?
The accelerators or strictly speaking
the charged particle accelerators
Are electromechanical systems “machines” capable of producing high-energy particle beams

## Slide 4: Why do we need high-energy?
To create new particles
To probe and study the structure of matter
Planck’s constant
Structure | size [m] | energy [GeV]
atom | Å ⇒ 10-10 | ~10-5
nucleus | 10 ferm ⇒ 10-14 | ~0.1
nucleons | 1 fm ⇒ 10-15 | ~1
quark | 10-3 fm ⇒ 10-18 | ~103
< quark | 10-4 fm ⇒ 10-19 | ~104
Structure | size [m] | energy [GeV]
atom |  | ~10-5
nucleus | 10 ferm ⇒ 10-14 | ~0.1
nucleons | 1 fm ⇒ 10-15 | ~1
quark | 10-3 fm ⇒ 10-18 | ~103
< quark | 10-4 fm ⇒ 10-19 | ~104
Energy of LHC!

## Slide 5: The CERN Accelerator Complex

## Slide 6: The LINAC 4 Proton source and linear acceleration
H- ion source at 45 keV
Accelerates beam up to 160 MeV
The chopping scheme allows removing some of the Linac bunches to make the beam fit into the PS Booster RF buckets
Pulse rate 1.2 s

## Slide 7: The LINAC 4 Proton acceleration
x’
x
+
-
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
Before stripping foil
x’
x
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Behind stripping foil
1st Synchrotron with 4 superposed rings
Circumference of 157 m
Proton energy from 160 MeV to 2 GeV
Can cycle every 1.2 s
Each ring will inject over multi-turns, using charge exchange injection

## Slide 8: The ISOLDE Facility Radioactive Ion Beam production and Acceleration

## Slide 9: The PS Proton & ion acceleration
The oldest operating synchrotron at CERN
Circumference of 628m
  4 x PSB circumference
Increases proton energy from 2 GeV to max. 26 GeV
Cycle length ranges from 1.2s to 3.6s
Many RF systems allow for complex RF gymnastics
Various types of extractions:
  Fast extraction
  Multi-turn extraction (MTE)
  Slow extraction

## Slide 10: The PS East Area Proton extraction – secondary beams, experiments
Particle Beams
Initial beam
(e-, p)
target
secondary particles
(e-, e+, γ, π+, π-, Κ+, Κ-,..
ions)
(W, Be, Pb,..)
target
or
decay
tertiary particles
(μ+, μ-, neutrinos, …)
Reduction ~104 in beam flux each time

## Slide 11: The nTOF Proton extraction – neutron beam
Study neutron-nucleus interactions (cross-sections)

## Slide 12: The Antimatter Factory (AD – ELENA) Anti-proton beams - deceleration
Receives fast extracted proton beam from PS at 26 GeV/c on a target
Every million protons yields about one usable antiproton at 3.5 GeV/c.
AD decelerates beam in stages down to 5.3 MeV
ELENA will further decelerate down to 100 keV
Experiments:
  ASACUSA, ALPHA, AEGIS, BASE, GBAR, PUMA

## Slide 13: The SPS Proton & Ion acceleration
The first synchrotron in the chain at ~30m under ground
Circumference of 6.9 km
  11 x PS circumference
Increases proton beam energy up to 450 GeV with up to ~5x1013 protons per cycle
Provides slow extracted beam to the North Area and fast extracted beam to LHC, AWAKE and HiRadMat

## Slide 14: The SPS North Area Particle beams – Fixed target experiments
Fixed target physics:

## Slide 15: The AWAKE Facility Plasma wake field acceleration R&D

## Slide 16: The LHC Proton & ion beam collider
Situated on average ~100 m under ground
Four major experiments
Circumference 26.7 km
Two separate beam pipes going through the same cold mass 19.4 cm apart
150 tons of liquid helium to keep the magnets cold and superconducting

## Slide 17: The LHC Proton & ion beam collider
1232 main dipoles of 15 m each that deviate the beams around the 27 km circumference
858 main quadrupoles that keep the beam focused
6000 corrector magnets to preserve the beam quality
Main magnets use superconducting cables (Cu-clad Nb-Ti)
12’000 A provides a nominal field of 8.33 Tesla
Operating in superfluid helium at 1.9K
LHC vacuum :
LHC : ~ 10-7 – 10-10 Pa ⇒ 4×106 – 4×109 atoms/cm3
air density: ~3×1019 atoms/cm3

## Slide 18: The LHC Proton & ion beam collider
LHC vacuum :
~ 10-7 – 10-10 Pa or
4×106 – 4×109 atoms/cm3
air density: ~3×1019 atoms/cm3
Beam collisions

## Slide 19: The LHC LHC Beam Collisions and Luminosity
In a collider the figure of merit for the performance is the Luminosity
Events in experiment
cross-section for the process under stydy
the physics!
beam luminosity
accelerator
Kinematic of the collision
transverse beam size
geometry of the collision
bunches
Protons/bunch
geometry of collision
(impact parameter)

## Slide 20: The LHC Operation beam cycle
6.8 TeV
450 GeV
Time
Injection
Ramp
Squeeze
&
Adjust
Stable beams for physics
Dump
&
Ramp down
= Field in main magnets
= Beam 1 intensity (current)
= Beam 2 intensity (current)
Luminosity half-time

## Slide 21: The LHC Operation – beam filling in injectors
PSB
PS
SPS
Time
= Field in main magnets
= Proton beam intensity (current)
= Beam transfer
To LHC clock-wise or counter clock-wise
450 GeV
26 GeV
1.4 GeV

## Slide 22: The evolution of accelerators …the past
The accelerators played a pivotal role in the foundation of the Standard Model
SPEAR
c-quark
τ-lepton
PETRA
gluon
SppS
W,Z bosons
Tevatron
t-quark
LHC
Higgs

## Slide 23: The evolution of accelerators … the present
Brookhaven National Lab (BNL) - USA
First use of super-conducting cables in the design of magnets, access to high-magnetic fields
Ion collider (Au, Cu, … ions) energies up to 100 GeV/u
Length ~4 km, 1740 magnets
4 experiments (BRAHMS, PHENIX, PHOBOS, STAR)
Basic research for quark-gluon plasma as part of the creation of the Universe
Plans for the construction and operation of EIC – Electron-Ion collider

## Slide 24: The evolution of accelerators … the present
Spallation Neutron Source (SNS), Oak Ridge - USA
  Η- source (p+2e)
  300m linear accelerator with superconducting RF
  accumulator ring (1 MW)
  Liquid mercury (Hg) target
Scattering experiments with neutron beams, material studies, nano-materials, …

## Slide 25: The evolution of accelerators … the present
ALBA Synchrotron Light Facilities – Barcelona Spain
3rd generation synchrotron light, the newest center in the Mediterranean
3 GeV electron beams, 270m long ring
Experiments with soft και hard Χ-rays
Studies for bio-technology, material science, nano-technology
6’000 beam hours/year for the experiments, 2’000 users/year from Universities, Research Centers, and Industry.
  65% users from Spain, 35% from other countries

## Slide 26: The evolution of accelerators The Livingston diagram
The Livingston graph shows the evolution of accelerators in the past century
Until the end of 20th century, the achieved energy increased by an order of magnitude every 6-10 years
New technologies emerge to replace or complement older ones
But:
The beam energy is not the only performance figure for the accelerator evolution
The beam intensity, beam size or brightness are also importan parameters, depending on the application
Energy
/year

## Slide 27: The evolution of accelerators CERN – the HL-LHC upgrade
The HL-LHC will use new technologies to provide 10 times more collisions than the LHC.
Two fronts:
  higher bunch intensity up to 2.1e11 ppb
  crab crossing scheme
Higher luminosity would give access to rare phenomena, greater precision and discovery potential.
HL-LHC will start operating in 2028 and run until 2041.

## Slide 28: The evolution of accelerators CERN – the high-energy frontier
stage 1: FCC-ee (Z, W, H, ) as Higgs factory, electroweak & top factory at highest luminosities
stage 2: FCC-hh (~100 TeV) as natural continuation at energy frontier, pp & AA collisions; e-h option
highly synergetic and complementary physics programme, common civil engineering and technical infrastructures
FCC integrated project allows the start of a new, major facility at CERN within a few years of the end of HL-LHC
- 2040
2045 - 2060
2070 - 2095

## Slide 29: The evolution of accelerators … the future
Linear electron accelerator with plasma wake-field technology as Higgs factory: (CM ~216 GeV)
Advantages: acceleration with small energy spread in energy, small emittances
Challenges: acceleration of positron, multiple plasma cells, integrated luminosity
W.P. Leemans & E. Esarey, Physics Today, March 2009

## Slide 30: The evolution of accelerators … the future
Muon Collider
Variable center of mass from Z, H (~200 GeV) up to 10 TeV – clear path for higher energies !
Advantages : no synchrotron radiation losses for muons, optimized energy consumption
Challenges : required development of several new technologies for the production of the muon beams, the emittance reduction and fast acceleration

## Slide 31: Οι επιταχυντές σήμερα … πέρα από την φυσική των σωματιδίων
>35’000 επιταχυντές σε λειτουργία σε όλο τον κόσμο:
  44% για ραδιο-θεραπεία
  41% για εμφύτευση ιόντων
  9% για βιομηχανικές εφαρμογές
  4% ερευνα στις χαμηλές ενέργειες
  1% παραγωγή ισοτόπων για θεραπεία
  <1% έρευνα
Επιταχυντής tandem για έρευνα υλικών και εργα τέχνης
Εμπορικό σύστημα για εμφύτευση ιόντων
To Rhodotron της ΙΒΑ για την παραγωγήή ισχυρών δεσμών ηλεκτρονίων
Γραμμικός επιταχυντής ηλεκτρονίων για ράδιο-θεραπεία
Cyclotron προτονίων για παραγωγή ραδιο-ισοτόπων
Θεραπεία καρκίνου
Ανάπτυξη ημι-αγωγών
Υλικά: αποστείρωση, χρονολόγηση με C, επεξεργασία αερίων διύλησης
Υλικά: μικρο-ανάλυση, φασματογράφοι μάζας, PIXE (particle-induced X-ray emission)
PET και SPECT απεικόνισης

## Slide 32
For the slides I used images and text from past presentations from collegues, past CAS or JUAS schools, publications and information from web and Wikipedia. Many thanks to all.
In case of questions contact met in my e-mial: Ilias.Efthymiopoulos@cern.ch