## Slide 1
MICROMEGAS TECHNOLOGY
6th DITANET Topical Workshop on Detection Techniques
Centro Nacional de Aceleradores - CNA
Seville , Spain
Thomas Papaevangelou
IRFU, Centre d’Etudes de Saclay, Gif sur Yvette CEDEX, France

## Slide 2
Description
  Technology, meshes
  Bulk Micromegas
  Microbulk
  Micromegas on a chip
  Resistive
Performance
  Gain, stability and uniformity
  Resolution
  Sparks
Applications and examples
  Particle Physics
  Nuclear Physics
  Applied science
Outline

## Slide 3: The detector

## Slide 4: Micro Pattern Gaseous Detectors (MPGD)
Best technology for gaseous detector readout:
Micro Pattern Gaseous Detectors
more robust than wires
no E×B effect
fast signal & high gain
low ion backdrift
better ageing properties
easier to manufacture
lower cost
big surfaces
Talk by Serge Duarte Pinto
Notes: Giomataris et.al., NIM A376 (1996) 29
F. Saul, NIM A386 (1997) 531

## Slide 5
Micromegas Concept
Two-region gaseous detector:
Conversion region
  Primary ionization
  Charge drift
Amplification region
  Charge multiplication
  Readout layout
    Strips (1/2 D)
    Pixels
Separated by a Micromesh
Very strong and uniform electric field
Drift field
typical 102-3 V/cm
Amplification field
typical 104-5 V/cm
Amplification
gap: 50-100 mm
γ
Mesh signal
Pixels / strips
signals
MICROMEsh GAseous Structure
Giomataris, Charpak (1996)
Y. Giomataris et al., NIM A 376 (1996) 29
In 1st Micromegas
Fishing line spacers have been used
metallic micromesh (typical pitch 50μm)
sustained by 50-100 μm pillars
simplicity
single stage of amplification
fast and natural ion collection
discharges non destructive

## Slide 6
The multiplication takes place in high E field (> 20 kV/cm)
between the anode (strips, pads) and the mesh in one stage
small size (50-100 μm)
fast signals (< 1 ns)
short recovery time (~150 ns)
high rate capabilities (> MHz)
high gain (up to 105 or more)
micromesh signal
strip 1
A GARFIELD simulation
of a Micromegas avalanche
(Lanzhou university)
strip 2
strip 3
Micromegas Concept

## Slide 7
Stable gain – non sensitive to flatness defects or temperature and pressure variation  good energy resolution
Ref: Y. Giomataris, NIM A419, p239 (1998)
E1
E2
E1> E2
V
The gain variation exhibits
a minimum for :
d = V/Bp
Parallel plate detector gain:
Townsend coefficient α:
Gain variation:
Virtue of the small gap

## Slide 8
200 mm
Electroformed
Chemically etched
Wowen
Pillars
Deposited by vaporization
Laser etching, Plasma etching…
Many different technologies have been developped for making meshes (Back-buymers, CERN, 3M-Purdue, Gantois, Twente…)
Exist in many metals: nickel, copper, stainless steel, Al,… also gold, titanium, nanocristalline copper are possible.
Can be on the mesh (chemical etching) or on the anode (PCB technique with a photoimageable coverlay).
Diameter 40 to 400 μm
Meshes
Micromegas technology

## Slide 9: Bulk Micromegas technology
Well established technique
Woven Inox mesh 30 µm
vacrel 128 µm
Readout pads
Readout plane + mesh all in one
  Result of a CERN-Saclay collaboration (2004)
  Bulking: Process to encapsulate the mesh on a PCB (mesh = stretched wires)
  Motivations for using bulk Micromegas
  the mesh is held everywhere:
  the mesh is held everywhere
  robustness , closed to dust
  can be segmented
  repairable
  large area detectors feasible and robust!
Lamination of Vacrel
Positioning of Mesh
Encapsulation
Development
FR4
Photo-imageable
polyamide film
Stainless steel
woven mesh
Border frame
Spacer
Contact to Mesh
Base Material
I. Giomataris et.al., NIM A560 (2006) 405
pillar
pad

## Slide 10: Bulk Micromegas technology
Bulk Micromegas: The pillars are attached to a woven mesh and to the readout plane
  Typical mesh thickness 30 μm, gap 128 μm
  Uniformity, robustness, lower capacity, easy fabrication, no support frame, small surrounding dead region 
  Large area detectors feasible and robust!
  Curved surfaces
  Mass production!
  Mesh thickness & bigger gap: some disadvantages in special applications:
  Good but limited energy resolution (~18% @ 6keV)
  Restrictions on support material
  More sensitive to pressure variations
pillar
pad

## Slide 11: Microbulk Micromegas technology
Microbulk Technology
  The pillars are constructed by chemical processing of a kapton foil, on which the mesh and the readout plane are attached. Mesh is a mask for the pillars!
  Typical mesh thickness 5 μm, gap 50/25 μm
  The advantages of a bulk micromegas but with enhanced performance.
  In addition: uniformity, clean materials, stability
  Energy resolution (down to 10% FWHM @ 6 keV)
  Low intrinsic background & better particle recognition
  Low mass detector
  Very flexible structure
  Higher capacity
  Fabrication process complicated
  Fragility / mesh can not be replaced
Readout plane + mesh all in one
Micromesh
5µm copper
Kapton 50 µm
Readout pads
An I. Giomataris and R. De Oliveira idea
Lower capacitance
Under development

## Slide 12: Microbulk Micromegas technology
Microbulk Technology
  The pillars are constructed by chemical processing of a kapton foil, on which the mesh and the readout plane are attached. Mesh is a mask for the pillars!
  Typical mesh thickness 5 μm, gap 50/25 μm
  A microbulk has all the advantages of a bulk micromegas but with enhanced performance.
  In addition: uniformity, clean materials, stability
  Energy resolution (down to 10% FWHM @ 6 keV)
  Low intrinsic background & better particle recognition
  Low mass detector
  Very flexible structure
  Higher capacity
  Fabrication process complicated
  Fragility / mesh can not be replaced
Readout plane + mesh all in one
Micromesh
5µm copper
Kapton 50 µm
Readout pads
An I. Giomataris and R. De Oliveira idea
Lower capacitance
Under development
Microbulk radiopurity:
 mostly Cu & Kapton
Measured with HPGe at Canfranc:
raw material (double clad kapton foil)
samples from old CAST detectors
Results in μBq/cm2 | 232Th | 235 U | 238U | 40K | 60Co
Microbulk | <9.3 | <13.9 | 26.3±13.9 | 57.3±24.8 | <3.1*
Kapton-Cu foil | <4.6* | <3.1* | <10.8 | <7.7* | <1.6*
Cu-Kapton-Cu foil | <4.6* | <3.1* | <10.8 | <7.7* | <1.6*
*Level obtained from the Minimum Detectable Activity of the detector
S. Cebrian et al., Astropart. Phys 34 (2011) 354-359

## Slide 13: Building a 2D Microbulk
Kapton foil (50 μm), both side Cu-coated (5 μm)
Construction of readout strips/pads (photolithography)
Attachment of a single-side Cu-coated kapton foil (25/5 μm)
Construction of readout lines
Capton Etching & Vias construction
2nd Layer of Cu-coated kapton
Photochemical production of mesh holes
Kapton etching & Cleaning
Square pads connected through 2 extra layers
Combination of “strips” and pads connected through one extra layer:
2 types of 2D readout schemes:

## Slide 14: Microbulk mesh types
A “standard” for 50 μm gap: 30 μm holes placed in 100 μm pitch
Alternative: hexagonal arrangement for better optical transparency
Pillars: Areas without holes & full etching underneath normal holes
  Less material / capacity

## Slide 15: Segmented mesh microbulk
Motivation:
Production simplification
Mass minimization
Large surfaces possible
“Real” XY
Ideal for:
Low mass neutron beam profilers/detectors
Large area low background detector
Challenges:
Etching of a segment foil
No mesh trigger  AGET electronics
First prototypes !

## Slide 16
I. Giomataris
Medipix2
surface: 1.4 x 1.6 cm2
Matrix of 256 x 256
pixel size: 55 x 55 µm2
P. Colas et al., NIMA535(2004)506
M. Cambell et al, NIMA540(2005)295
M. Chefdeville et al., NIMA556(2006)490
H. Van der Graaf, J. Timermans et al.
Great resolution
Single electron counting!!
Gas On Slimmed SIlicon Pixels (GOSSIP)
Under study for ATLAS SLHC tracker
Micromegas + micro-pixels
InGrid technology
Notes: 16

## Slide 17: Micromegas with resistive strips
Different technologies of resistive films developped @ CERN (R. de Oliveira)
Electrode de dérive
Micro-grille
5 mm
128 µm
Film résistif (kapton) ou pâte
(1k-500MΩ/☐)
Protection against sparks
and/or
spread of the charge
M. Dixit et al., NIM A518 (2004), 721
Isolant (prepreg – 75 µm)
Anodes
Resistive kapton (2 MΩ/☐)
Resistive paste (250 MΩ/ ☐)
Resistive strips (400 kΩ/ ☐)
Resistive Pads
(a few tens of kΩ/☐)
Characteristics:
Resistive strips connected to the ground
Thin insulating layer between of the resistive and readout strips
AC coupling of signals
Sparks are neutralized through the resistive strips to the ground

## Slide 18: General performance

## Slide 19: Gain curves for argon mixtures
iC4H10
CO2, CH4
C2H6
Micromegas Mesh : 50 mm gap of 10x10 cm² size

## Slide 20: Gain stability
Conventional Micromegas (2006)
2% Isobutane
Change Vmesh
From 320->324V
Microbulk (2011)
Bulk (2008)
Micromegas in CAST (2003-2011):
Excellent long term stability!

## Slide 21: Energy resolution
Microbulk: 55Fe Calibration with Ar – 5% isobutane
@ 1 bar FWHM @ 6 keV = 11.5 %
Microbulk: energy resolution
optimum for gain ~5x103 (Argon)
Bulk: 55Fe Calibration with Ar – 5% isobutane
@ 1 bar FWHM @ 6 keV = 17.6 %
Microbulk: electron transmission
for Argon mixtures

## Slide 22: Spatial resolution
Conventional Micromegas calibration @ Panter with X-Ray telescope
Microbulk: Image taken using a collimator with the words “axion cast”
σμΜ = (24±7) µm .25 mm pitch
σμΜ = (36±5) µm, .5 mm pitch
Bulk: Spatial resolution measurements for the MAMA project (sLHC)
Ar Iso (95:5)
B = 5T
Resolution in the pressence of a magnetic field
  ~ 50 µm independent of the drift distance

## Slide 23: Radiation hardness
106/mm2/s
G. Puill, et al., IEEE Trans. Nucl. Sci. NS-46 (6) (1999)1894.
No space charge effect in radiation > 30 mC/mm² > 25 LHC years
High rate capability with 8 keV x-rays

## Slide 24: Sparking probability
Spark probability ~ 5.10-9 (He+10% isobutane @ gain ~ 10000)
Limitations due to sparks:
Dead time (up to 1 ms for mesh recharging )
Electronics destruction protection by diodes and decoupling capacitances
Detector damages Sparks not destructive!
Delbart et al., NIM A478 (2002), 205-209
SPARK in a Standard Bulk
SPARK in a resistive detector
Sparks are reduced by the use of resistive anodes
Topology of the sparks is very different: smaller in amplitude and shorter in time
The effect in dead time in resistive detectors is probably much smaller
Possibilities:
Resistive anode
Segmented mesh
Double stage amplification

## Slide 25: Applications - Examples

## Slide 26: Conventional Micromegas applications
Micromégas Concept for Laser MégaJoule
Piccolo in Casaccia reactor
COMPASS
40x40 cm2 Micromegas
N-TOF
NA48
High rate, high resolution

## Slide 27: Applications of Bulk Micromegas
T2K
CLAS 12
F. Mayet et al. J. Phys. Conf. Ser. 179:012011, 2009
C. Grigon et al. JINST 4:P11003,2009.
Prototype directional dark mater TPC: MIMAC (Micro-TPC Matrix of Chambers)
First prototype: 3 cm × 3 cm with a
2 D readout with 200 µm pitch pixels (128 in each direction)
Next step 10 cm × 10 cm with 200 µm pitch to be tested in February
(512 in each direction)
Recoils from 144 keV
neutrons in 100 mbar Isobutane

## Slide 28: Application of Bulk Micromegas
96 Y strips
96 X strips
Y
X
N_TOF beam profiler:
 6x6 cm2 (2x106 strips, 0.5 mm pitch)
drift gap = 4 mm
converter: 10B4C enriched in 10B, 2 m and 24 nm
Ar + (10%)CF4 + (2%) iC4H10

## Slide 29: Applications of Bulk Micromegas
1 of the 3 TPCs of near detector of T2K experiment in Japan
S. Anvar et al. NIM A602:415-420, 2009
J. Bouchez et al. NIM A574:425-432,2007
CLAS12 (Jefferson Lab) : Micromegas central and forward tracker
P. Konczykowski et al. NIM A612:274-277,2009
T2K: large area
CLAS 12: flexible structure

## Slide 30: Towards large detectors: ATLAS @ sLHC
I. Giomataris
Scope
Phase I: 1034 cm‐2 s‐1 Complement present CSC 32 x 1 m2
Phase II: L = 1035 cm‐2 s‐1 400 chambers of 1–2 m2

## Slide 31: The bulk lab @ SEDI, CEA Saclay
laminator
Oven
Vacuum press
Mesh stretching

## Slide 32: Microbulk application
Ar 2% iso
@ 4,75 bar
Test with 241Am alpha source: 0.7% FWHM @ 5.4 MeV
0,7%
Test with Xe @ 2 bar
<4.5% @ 4.75 bar
NEXT : a gas Xenon neutrino TPC
Excellent energy resolution essential
Microbulk studies with Ar & Xe gas at high pressures
2nbb
0nbb
Q value
12 cm × 12 cm
Pads ~ 8 mm2

## Slide 33: Microbulk application
n_TOF
Low mass online neutron flux monitor:
Minimize beam perturbation and induced background
Cover a wide energy range
Drift Cathode (1):
25 m coppered (1 m) Kapton + 1.5 m of B-10
Drift Cathode (2) :
1.5 m aluminised (~ nm) mylar + 1 mg U-235 (99.94%)
Micromesh + Anode strip:
Micro-Bulk (5 m Cu)
+ 50 m Kapton (with 70500 holes )
+ 5 m Cu )
Fission chamber for σf
Fission tagging for σγ
Fission fragment angular distribution

## Slide 34: Microbulk application
Micromegas detectors in CAST: low background
Continuous improvement of Micromegas detectors inside CAST experiment.
2008: 3 Micromegas (Microbulk technology) installed in 3 of the 4 CAST magnet apertures, replacing traditional Micromegas and TPC
Sunrise side detector
Sunset side detectors
 | Typical rates
TPC | 85 counts/h (2-12 keV)
MM | 25 counts/h (2-10 keV)
CCD | 0.18 counts/h (1-7 keV)
New Microbulk MM | 1-2 counts/h (1-7) keV

## Slide 35
1 week with 109Cd source
0.005 Hz trigger rate
First approach to final background limited only by intrinsic radioactivity (from microbulk, chamber materials, inner shielding):
< 2·10-7 counts keV-1 cm-2 s-1 [2-7 keV] (~1 count/day)
This result shows that background levels >20 times lower that current CAST MM nominal background are possible via shielding improvement.
0.2 Hz trigger rate
Microbulk application: Ultra Low Background

## Slide 36
Helioscope prospects
I. Irastorza et al., JCAP 1106 (2011) 013
New magnet
X-ray optics
Low background Micromegas
Microbulk application: Ultra Low Background

## Slide 37: The ILC TPC project
I. Giomataris
Large International collaboration
~ 40 m average!!
Pad size 2x6 mm
ILC TPC prototype
with Micromegas
ILC TPC with Micromegas,
L = 4.6 m, D = 3.4 m
Event in DESY test beam
1st TPC prototype
Ion feed back supression
No ExB effect

## Slide 38: Micromegas in radiography
Tumor
SUBATECH beta imager
g-ray scanner
Neutron imaging: Beam tests at the Orphee
Nuclear plant 3x108 thermal neutrons/cm2/s
6Li converter : 50 µm
Conversion gap : 400 µm
Amplification gap : 50 µm
Self-supported 50 mm micromesh
Hole diameter (µm) | s +/- D s (µm)
400 | 58 +/- 5
300 | 57 +/- 19
200 | 63 +/- 8
160 | 43 +/- 4
Spatial resolution
F. Jeanneau, Proc. SPIE 4785, 214 (2002)

## Slide 39: Micromegas for forest fire detection
Q.E & Sensitivity
Photodiode Q.E.(200nm)70%
FORFIRE Q.E.(200nm)1%
However
Photodiode minimum signal  5 pA 
Photodiode minimum sensitivity 
  5107 photons
FORFIRE minimum sensitivity 
  5102 photons
FORFIRE: Developement of a solar blind detector sensitive to UV (200 – 250 nm)
The project received a European subsidy of 1.1 million € within the framework of the FP7 program-Small and Medium Enterprises.
Micromegas detector + solid photocathode (CsI)
Single electrons seen
By FORFIRE Micromegas

## Slide 40: Summary
Micromegas is a state-of-the-art MPGD
The different manufacturing techniques offer characteristics that make the detector attractive for a vast field of applications. Noting:
Excellent energy – spatial - time resolution
Low mass detectors
Radiation hardness
Low background
Uniformity
Flexible structures
Time Stability
Large areas
Ongoing research on
Resistive layers
Capacitance reduction
Mesh optimization
Further material decrease
  Spark protection
Optimization of the manufacturing techniques (will) allow standardized production.
Large area detectors
Mesh segmentation
  New “real” X-Y structure
Mass production

## Slide 41: END

## Slide 42: Backup slides

## Slide 43: Nuclear Physics/Particle Physics needs
Tracking of charged particles in high energy (NP/PP) and high intensity beam (NP) (ex: 3×107 particles/s from 200 GeV muon beam)
High spatial resolution better than 100 μm in (NP: small/PP: large) volume
Ageing of the detector limited (NP/PP)
Low noise and full efficiency (NP/PP)
High rate (NP)
Limited incident track scattering (NP/PP)
High mean atomic number <Z> to use the gas as a target (NP)
Fast readout signal and fast electronics (NP/PP)
Low material and low cost (NP/PP)

## Slide 44: CAST: a helioscope “a la Sikivie”
CAST sensitivity per detector
0.3 counts/hour for
gaγγ= 10-10 GeV-1 and A = 14.5 cm2
Axions would be produced in the Sun’s core and re-converted to x-rays inside an intense magnetic field. P. Sikivie, Phys. Rev. Lett. 51, 1415–1417 (1983)
CAST is using a prototype superconducting LHC dipole magnet able to track the Sun for about 1.5 hours during Sunrise and Sunset.
Operation at T=1.8 K, I=13,000A, B=9T, L=9.26m
Expected signal
X-Ray excess during tracking
at 1-10 keV region
Low X-ray background detectors required to observe a signal.
Axion properties
neutral pseudoscalar
practically stable, very low mass,
very low interaction cross-sections
  excellent candidates for dark matter
L = g (E•B) a
Axions couple to photons

## Slide 45: CAST microbulk energy resolution
CAST expected signal: 1-10 keV X-rays
Detector characteristics:
6x6 cm2 active area
106x106 strips, 550 μm pitch
3 cm drift
5 μm mylar window with strongback
1.43 bar Ar – 2.3% isobutane (non flammable)
55Fe Calibration with Ar – 2.3% isobutane @ 1.43 bar
Illumination of whole area from ~ 0.7 m distance
FWHM @ 6 keV = 15.5 %
55Fe Calibration with Ar – 5% isobutane @ 1 bar
Collimated source to avoid border effects
FWHM @ 6 keV = 11.5 %

## Slide 46: Low background
CAST is in phase II since 2005.
Changing buffer gas density changes axion mass sensitivity  new discovery potential for each setting.
Alignment with the sun for ~1 hour per setting demands detector background ~0 counts/hour
How the low background is achieved:
Offline analysis
  Particle identification
  Readout scheme
  Energy resolution & short signal risetime
Low radioactivity materials
Shielding for external radiation (archeological Pb + Cu + Cd + Polyethylene + Nitrogen flushing). Compact size!

## Slide 47
Saclay
  Micro-TPC
  standard Micromegas
  amorphous-Silicon protection
  against discharges
  6 cm height field cage
TimePix/Micromegas chambers
Field cage
Cover
Micromegas
mesh
Medipix2/TimePix chip
Windows for X-ray sources
Windows for
β sources

## Slide 48: InGrid: Integrated GEM/Micromegas Grid
Si wafer + Micromegas
Grid
Si wafer + GEM
Walls
Grid
Pillars
Integrate a GEM or Micromegas detector directly on a chip …
NIKHEF (MESA+, Univ. Twente)

## Slide 49: InGrid: Integrated GEM/Micromegas Grid
NIKHEF (MESA+, Univ. Twente)
substrate
photo-resist
20 μm pitch
50 μm pitch
Deposit photo-resist & UV exposure
  define the amplification gap (tens of μm)
  define the grid support (pillars/walls)
Deposit metal & pattern
  define the grid geometry
Develop unexposed photo-resist
  cleaning
… using wafer post-processing :
The substrate could be:
  naked or patterned wafer of Si
  readout chip
Integrate a GEM or Micromegas detector directly on a chip …

## Slide 50
n-TOF: Trasparent Micromegas Micro-bulk for neutron beam monitoring
Drift Cathode (1) = 25 m coppered (1 m) Kapton +
1.5 m of B-10
Drift Cathode (2) = 1.5 m aluminised (~ nm) mylar +
1 mg U-235 (99.94%)
Micromesh + Anode strip = Micro-Bulk (5 m) +
50 m Kapton (with 70500 holes ) + 5 m Cu )
Count rate for 1 mg of U-235
New

## Slide 51
Neutron beam profiler for n-TOF S. Andriamonje et al.,Nucl.Instrum.Meth.A481:120-129,2002 J. Pancin et al., Nucl.Instrum.Meth.A524:102-114,2004
Neutron reaction rate
Low gamma sensitivity
n-TOF beam profile
n + 6Li  3H + 

## Slide 52
Micromégas application to neutron tomography
Hole diameter (µm) | s +/- D s (µm)
400 | 58 +/- 5
300 | 57 +/- 19
200 | 63 +/- 8
160 | 43 +/- 4
Spatial resolution
Next step : 2D neutron imaging
F. Jeanneau, Proc. SPIE 4785, 214 (2002)
Beam tests at the Orphee Nuclear plant
3 108 thermal neutrons/cm2/s
Image of the Gd mask
Hole diameters
6Li converter : 50 µm
Conversion gap : 400 µm
Amplification gap : 50 µm
Self-supported 50 mm micromesh

## Slide 53
Micromégas Concept for Laser MégaJoule and ICF Facilities
M. Houry et al., NIM,557(2006)648
The g insensitivity of Micromégas applied to neutron spectroscopy
on Inertial Confinement Fusion experiments
Time response < 500 ps
< 15 cm >
HV1
HV2
Gas In
Gas Out
Microstrips
Microstrips
Ref: CEA/DIF/DCRE/SDE M. Houry
2mm CH2 converter
65 strips (1.6 mm pitch)
DEMIN group (CEA/DIF/DCRE and DAPNIA)

## Slide 54
Drift electrode
Challenges
Very small Micromegas
Seal detector
High radiation resistance
High temperature
Large dynamic range
Piccolo Micromegas
Nuclear reactor in-core neutron measurement
J. Pancin et al., NIMA, 592(2008)104
Succesfully tested at the CELINA 14 MeV neutron source facility at CEA-Cadarache

## Slide 55
Energy resolution
Fe = 0.13-0.17
Fg = 0.7-0.9 for wire chamber
But Fg for Micromegas is certainly lower ~0.3-0.5
Primary
fluctuations
(Fano factor)
Fluctuations
in the gain