## Slide 1
D. Novelli1,2, L. Alfonso 2, A. Bersani2, B. Caiffi2, S. Farinon2,
S. Mariotto3 , T. Salmi4 , L. Bottura5, ...
1Sapienza University of Rome , 2INFN – Genoa , 3INFN and University of Milan, 4Tampere University , 5CERN
Performance limits of accelerator dipole and quadrupole for a Muon Collider

## Slide 2: Collider Magnets Requirements
Field: 16 T peak (IR 20 T)
Length: 10…15 m (x 700)
Space between magnets: 300 mm
Radiation heat load: 5 W/m
Cumulative dose: 20…40 MGy
Aperture
Courtesy of Patricia Borges de Sousa
https://indico.cern.ch/event/1250075/contributions/5357594/
! Need for high fields in large apertures
Assuming 10 TeV machine and coil at 4.5 K

## Slide 3: General Assumptions
A Python code is used to implement the analytic formulas for the cos-theta magnets in sector coil approximation.
( is 60° for the dipole and 30° for the quadrupole)
Dipole
Quadrupole
In our analysis, we included three superconducting materials, NbTi, Nb3Sn and HTS (ReBCO), at three different cold mass operating temperatures:
  1.9 K NbTi
  4.5 K and HTS (ReBCO)
  20 K HTS (ReBCO)
(
The contribution of the iron yoke is assumed to be +1.5 Tesla on the magnetic field.
Limitations are introduced by
  Cost
  Stress
Plots of the Magnet Aperture (A) – Bore Field (B) phase space can be useful to show the allowed region.
  Margin
  Protection

## Slide 4: General Assumptions
Aperture
150 mm
Aperture
150 mm
Plots of the Magnet Aperture (A) – Bore Field (B) phase space can be useful to show the allowed region.
Coil width:
Structures:
SS cost: 10 EUR/kg (HL-LHC)
Iron yoke:
Fe cost: 8 EUR/kg (HL-LHC)
Aperture
150 mm
Total cost of the magnet = 400 kEUR/m ( twice FCC-hh)
Cost of the labour = 20 kEUR/m (LHC)
Materials | Peak Stress [MPA] | Operating T [K] | T margin [K] | SC cost [EUR/kg] | Aspirational SC cost [EUR/kg]
NbTi | 100 | 1.9 | 1.5 (LHC) | 330 | 330 (today value)
Nb3Sn | 150 | 4.5 | 2.5 (HL-LHC) | 2000 | 700 (FCC target)
ReBCO | 400 | 20 | 2.5 (HL-LHC) | 8000 | 2500 (realistic projection)
Bore
Coil
Structures
Iron
The assumptions made for the cost model
are very important !
Higher cost Thinner coil
  Higher current density
    Problem with quench protection
    Work close to the critical surface (margin limit)
  Higher pressure on midplane Stress limitations
Example diagram with bore aperture set at 150 mm.

## Slide 5: A-B Plots Explanation
Prohibited area
Allowed area
Cost reduction
Increasing maximum stress
Decreasing operating temperature
Maximum coil width reached
change behaviour
Maximum coil width reached
change behaviour
The limit changes: in this case, before the intersection, the stricter limit is the stress while after it is the margin
The stress limit considers the maximum mechanical stress we can have on the coils, starting from the analytical formula for the midplane pressure of cos-theta magnet in sector coil approx.
The margin limit is the limit due to the SC material itself, starting from the Bottura’s fit for the critical current density.

## Slide 6: Dipole – A-B Plots
Two possible configurations can be 16 T, 100 mm ( ) and 12 T, 150 mm ( )
Nb3Sn is limited by peak stress and operating margin
HTS is limited by cost production and peak stress
NbTi is intrinsically limited by the which doesn’t allow to reach high field
The initial design target ( – 16 T, 158 mm) is in the not allowed area.

## Slide 7: Dipole – A-B Plots
Two possible configurations can be 16 T, 100 mm ( ) and 12 T, 150 mm ( )
The initial design target ( – 16 T, 158 mm) is in the not allowed area.
Can we consider a smaller aperture?
Currently, we are considering a thickness of 40 mm for the tungsten screen;
If we could halve it, it would mean reducing the aperture diameter by 40 mm.
With HTS we can have an operating temperature of 20 K

## Slide 8: Quadrupole – A-B Plots
We are performing the same graph for the quadrupole to define the final design targets
This is still a work in progress
For each material, the main limitation is the margin.

## Slide 9: Protection Limit ( Courtesy by Tiina Salmi – https://indico.cern.ch/event/1240045/ )
NbTi, hotspot temperature limit 350 K:
  Low conductor cost allows large coil and low current density  protection does not limit design
Nb3Sn, hotspot temperature limit 350 K:
  Higher cost starts to limit the coil size and force higher current density  protection may become a limitation
ReBCO, hotspot temperature limit 200 K:
  High cost requires small coil and very high current density  Protection will be a limiting factor
In all cases we assume 40 ms protection delay between original quench and quench protection system efficiency.
Summary of steps:
Current density vs. dipole field
Maximum energy density vs. current density
Aperture vs. stored energy density
Aperture vs. bore field, assuming constant coil cross-section (as limited by conductor cost)

## Slide 10: Combined Function Magnet
Combined Function Magnet with Asymmetric Coil
https://indico.cern.ch/event/1043242/contributions/4448798/attachments/2279860/3873498/MCM20210712SCFM.pdf
Dipole inside a Quadrupole and viceversa:
https://indico.cern.ch/event/1147940/contributions/4818189/attachments/2429583/4160091/2022-04-21_US-MAP%20SR%20and%20IR%20magnets_AZv3.pdf

## Slide 11: Conclusions
We are working on the performance targets for the collider ring dipoles and quadrupoles, showing the limits introduced by cost, mechanics and protection. The allowed magnet aperture (A) - magnetic field (B) phase spaces are provided and discussed, representing the starting point to define possible beam optics which are also acceptable from a technological point of view.
Next steps:
  Iterate with beam physics as the nominal optics and adjust design targets in accordance.
    How much can we reduce the aperture by working with HTS at 20K?
  Analysis of non-insulated and metal-insulated coils for quench protection.
  Solve the problem of the neutrino flux in the straight sections Combined function magnets
  Move toward more realistic configurations FEM
  Develop preliminary designs for possible 10 TeV muon collider ring magnets.

## Slide 12
Thank you for your attention
D. Novelli1,2, L. Alfonso 2, A. Bersani2, B. Caiffi2, S. Farinon2,
S. Mariotto3 , T. Salmi4 , L. Bottura5, ...
1Sapienza University of Rome , 2INFN – Genoa , 3INFN and University of Milan, 4Tampere University , 5CERN

## Slide 13
Backup Slides

## Slide 14: Cost Model
(using FCC-hh as benchmark)
The total cost of the magnet is the same for all materials !
(using LHC as benchmark)
where
(using D2 HL-LHC as benchmark)
(using D2 HL-LHC as benchmark)
Material | 
Sn | 
aspirational value | 
aspirational value | 
Material | 
aspirational value | 
aspirational value | 
Escalated price in 2016
The right value in 2016
Corresponds to the FCC target
The value of today (2023)
A realistic projection for the next years
Bore
Coil
Structures
Iron

## Slide 15: Cost Model
where
Using the main LHC dipoles as a reference
We can express the cost of the magnets as a function of the internal radius and the coil width.
The cost of the magnets is function of:

## Slide 16: Cost Model
where
Using the main LHC dipoles as a reference
We can express the cost of the magnets as a function of the internal radius and the coil width.
The cost of the magnets is function of:
Coil width:
Structures:
Iron yoke:
Bore
Coil
Structures
Iron
Poles

## Slide 17: Stress Limit
Then, through the load line formulas, the gradient in the bore is:
Then, through the load line formulas, the magnetic field in the bore is:
The addition of an iron contributes:
Constants
Coil width
from the cost model, in function of the material, of the sector coil
Dipole
Quadrupole
Variables
Geometrical considerations:
Dipole
Starting point
At the first order of approximation, the midplane pressure is:
For fixed , the current density can be computed:
The addition of an iron contributes:
At the first order of approximation, the midplane pressure is:
For fixed , the current density can be computed:
Quadrupole
Reference: https://doi.org/10.15161/oar.it/143359
NbTi = 100 MPa
Nb3Sn = 150 MPa
ReBCO = 400 MPa
155 kEUR/m
Dip = 60°
Quad = 30°

## Slide 18: Iron Discussion
Iron cannot be analyzed analytically because it saturates at 1.5-2 T, and beyond that value, it becomes complicated as it is no longer linear and, therefore, cannot be treated with analytical formulas.
Since we are interested in fields greater than 10 T, the analytical approach is useless in the first few tesla range.
In order to consider the iron contribution and to not underestimate the allowed region, we added 1.5T "hard code" to the magnetic field and to the gradient.
Analytical approach https://doi.org/10.15161/oar.it/143359
Bore field [T]
Iron yoke width [mm]

## Slide 19: Peaking Factor
Dipole
Quadrupole
The magnetic field in the aperture for a sector dipole is:
The magnetic field in the aperture for a sector quadrupole is:
We used the approximation at the first order.
It is good for because the second term (n=3) is zero.
We used the approximation at the first order.
It is good for because the second term (n=6) is zero.
The peak field is into the conductor: different formula for B https://doi.org/10.15161/oar.it/143359

## Slide 20: Peaking Factor
We need a peaking factor to switch between peak field and bore field for the sector dipole dipole.
The ratio between peak field and bore field follows the hyperbolic fit:
where r is the aperture radius ad w is the coil width of the sector coil

## Slide 21: Margin Limit
Intersection:
depends on the material
Dipole
Quadrupole
Intersection:
depends on the material
Constants
Coil width
from the cost model, in function of the material, of the sector coil
Dipole
Quadrupole
Variables
Geometrical considerations:
Dipole
Starting point
Quadrupole
Reference: https://doi.org/10.15161/oar.it/143359
NbTi = 100 MPa
Nb3Sn = 150 MPa
ReBCO = 300 MPa
155 kEUR/m
Dip = 60°
Quad = 30°
( The magnetic field is calculated at the reference radius )

## Slide 22: Margin Limit
Critical Current Density ( Jc )
NbTi
, dipole
, dipole
, dipole
, quadrupole
, quadrupole
, quadrupole
Constants
Coil width
from the cost model, in function of the material, of the sector coil
Dipole
Quadrupole
Variables
Geometrical considerations:
Starting point
NbTi = 100 MPa
Nb3Sn = 150 MPa
ReBCO = 400 MPa
155 kEUR/m
Dip = 60°
Quad = 30°

## Slide 23: Margin Limit
Critical Current Density ( Jc )
Nb3Sn
, dipole
, dipole
, dipole
, quadrupole
, quadrupole
, quadrupole
Constants
Coil width
from the cost model, in function of the material, of the sector coil
Dipole
Quadrupole
Variables
Geometrical considerations:
Starting point
NbTi = 100 MPa
Nb3Sn = 150 MPa
ReBCO = 400 MPa
155 kEUR/m
Dip = 60°
Quad = 30°

## Slide 24: Margin Limit
Critical Current Density ( Jc )
ReBCO
, dipole
, dipole
, dipole
, quadrupole
, quadrupole
, quadrupole
Constants
Coil width
from the cost model, in function of the material, of the sector coil
Dipole
Quadrupole
Variables
Geometrical considerations:
Starting point
NbTi = 100 MPa
Nb3Sn = 150 MPa
ReBCO = 400 MPa
155 kEUR/m
Dip = 60°
Quad = 30°