## Slide 1
Neutron Science with Gaseuos Detectors
Review and DRD1-WP9 Hints
Gabriele Croci
University of Milano-Bicocca
Department of Physics «G. Occhialini»
Milano, Italy
1st DRD1 Collaboration Meeting
CERN

## Slide 2
Outline
Neutron detection principles
  Thermal neutrons
  Fast neutrons
3He
  3He based detectors for thermal and fast neutrons
  3He shortage
Novel trends
  Wire-based solutions
  MPGD
  RPC
I apologize if I did not cite some research in this talk for sake of time ….

## Slide 3
Neutron Interaction and detection
Neutron interaction and detection critically depends on the neutron energy
  This implies that also your detector must be «customized» for a specific neutron energy range
  It is quite difficult to realize a detector for all neutrons
Several classifications of neutrons based on their energies
  Cold neutrons En<25 meV
  Thermal neutrons 25 meV <En< 0.1 eV
  Epithermal neutrons 0.1 eV <En< 100 keV
  Fast neutrons 100 keV <En< 100 MeV
  High energy neutrons En> 100 MeV
Neutron interaction probability and detection efficiency depends on the macroscopic cross section as
where is called macroscopic cross section and is defined as the product of σ(E) i.e the cross section and and n i.e. the target density of scattering centres

## Slide 4
Basic principle to realize a neutron detector
Storage
Converter material depends on the neutron energy you want to detect
Detector is optimized following the requirements of the neutron science you want to explore

## Slide 5
Thermal neutrons

## Slide 6
3He based detectors: principle
n + 3He  p + 3H + 0.76 MeV σ(λ) = 5333 barn * λ/1.8 Å
Single Wire Proporional Chamber
Increase n (density of scattering centres) by increasing pressure (up to several bars)
Very rubust and simple geometry
Relatively low operation voltages
Most diffused geometry: 3He-tubes

## Slide 7
3He tubes applications
Very high efficiency to thermal neutrons
Wide application in all present «neutron science» facilities (i.e. spallation sources and reactors)
  ISIS (UK)
  SNS (USA)
  ILL (FR)
  J-PARC (JP)
  …

## Slide 8
but…
Shortage of 3He gas
3He tubes (as SWPC) are limited in rate capability
 Maybe an issue for future high intensity neutron sources like ESS
Thanks to R. Hall-Wilton

## Slide 9
Most common alternative materials to 3He: 10B and 6Li
Solid converters (1/2)

## Slide 10
Most common alternative materials to 3He: 10B and 6Li
Solid converters (2/2)
Converting Layer
Substrate

## Slide 11
Novel wire-based solutions (mainly for ESS..)
MultiGrid detector – 10B based
MG
He-tubes
Multi-SWPC- Large area
High efficiency
Millimetric Spatial resolution
Developed by ILL and ESS
ESS

## Slide 12
Novel wire-based solutions (mainly for ESS..)
MultiBlade detector – 10B based
MWPC-based
High efficiency
Millimetric space resolution
High rate
Application: FREIA / ESTIA
Reflectometry instruments at ESS
Developed by ILL and ESS

## Slide 13
RPC for neutron detection

## Slide 14
MPGD detectors born for tracking and triggering applications (detection of charged particles)
In order to detect neutral particles you need a converter
  Thermal Neutrons: 10Boron converter
    Neutrons are detected using the productus (alpha,Li) from nuclear reaction eg: 10B(n,alpha)7Li
  Fast Neutrons: Polyethylene converter + Aluminium
    Neutrons are converted in protons through elastic scattering on hydrogen
MPGD offer the following advantages
  Very high rate capability (MHz/mm2) suitable for high flux neutron beams like at ESS
  Submillimetric space resolution (suited to experiment requirements)
  Time resolution from 5 ns (gas mixture dependent)
  Possibility to be realized in large areas and in different shapes
  Radiation hardness
  Low sensitivity to gamma rays (with appropriate gain)
Two dedicated workshops in the last years
  https://indico.cern.ch/event/265187/ (2013)
  https://indico.cern.ch/event/365840/ (2015)
MPGD for neutron detection

## Slide 15: For sake of time I skip all Micro Strip Gas Chamber application to neutron detection I will concentrate on GEM, Micromegas and THGEM

## Slide 16: GEM thermal neutron detector
n
α
Low efficiency detector (few %)
Triple GEM detector equipped with an aluminum cathode coated with 1μm of B4C: first bGEM prototype
Exploit the 10B(n,α)7Li reaction in order to detect thermal neutrons
B4C coated aluminium cathode mounted on its support
B4C coated aluminium cathode assembled inside the bGEM chamber layout
Detector Schematics
Several groups around the world (UNIMIB-INFN-CNR, CERN, J-PARC, CSNS …) developed similar solutions

## Slide 17: Performances
G. Croci et Al, 2013
40 MHz/cm2

## Slide 18: The CASCADE GEM detector
Each GEM has two 10B layers
Last GEM operated as amplifier
10 GEM foils for ~ 50% efficiency
Christian J. Schmidt et al (GSI, Darmstadt)
2D-200 CASCADE Detector (200x200 mm2)
INFM - Perugia Forschungszentrum Jülich Hahn Meitner Institut - Berlin
Ruprecht Karls Universität - Heidelberg AGH University of Sci. and Tech. - Krakow
GEM-foils coated with 10B and 2D readout structure
Power supply and thermal management
FPGA based readout board
ASIC frontend- electronic
18
Detector entrance window (100 µm Al)

## Slide 19: CASCADE GEM detector performances
~ 1-3 mm spatial resolution with 1.56 mm pixel size
10 MHz/cm2 counting rate capability
Old PC Mouse
A radiography with the CASCADE GEM detector TOF Dynamics Achieved with CASCADE
Tesa-Tape Dispenser
Water Flow-Indicator
CEA DSM Irfu
Christian J. Schmidt et al (GSI, Darmstadt)

## Slide 20
Multi Boron GEM detector
GEM foils of 10x10 cm2 covered on both sides with 1μm of 10B4C.
Stacking of 6 Boron-coated (BGEM) foils coupled with three standard GEM foils.
Gas Mixture Ar-CO2 (70%-30%).
Padded anode made of 256 pads of 6x6 mm2
6MBGEM detector coupled with GEMINI electronic readout

## Slide 21
At 1,8 Å (25 meV) efficiency is 16%
Multi Boron GEM detector performances

## Slide 22: Gd-GEM for NMX @ ESS
Position resolution σ <300 μm reached with Triple GEM, APV-25
Detection efficiency < 12 % at normal incidence of neutron
D. Pfeiffer et al, 2016 JINST 11 P05011

## Slide 23: Micromegas for neutron radiography
 6Li converter : 50 µm
 Conversion gap : 400 µm
 Amplification gap : 50 µm
 Self-supported 50 m micromesh
 Gassiplex cards readout
Gadolinium object
Holes
Imaging Mask: Gadolinium foil (5x5 cm², 25 µm thin) holes from 75 to 500 µm
HV1
HV2
e-
Charged particle
amplification (50 m)
Micromesh
E1 ~ 1kV/cm
E2 ~ 40kV/cm
100 µm
conversion (400-700 m)
neutron
CEA/DSM-IRFU + CEA/DRT-LIST-DETECS collab.
« classical » micromegas prototype
Li6 converter
Thanks to A. Delbart

## Slide 24: Imaging capabilities of the prototypes
3 108 thermal neutrons/cm2/s
Image of the Gd mask
Beam tests at the Orphee Nuclear plant
350 m
Tomographic image of a multi-wires cable (∅ 6 mm, 12 wires, ∅ 0.5 mm each)
F. Jeanneau, IEEE TRANSACTIONS ON NUCLEAR SCIENCE, VOL. 53, NO. 2, APRIL 2006
Distorted tomograhy reconstruction with ~160 m resolution because of the pillars supporting the “classical” micromegas mesh
Should be greatly improved today by use of the 2D micro-­‐‑bulk
Thanks to A. Delbart

## Slide 25
Fast neutrons

## Slide 26
3He tubes applications – fast neutrons
3He detectors can be also used to detect fast neutrons if an appropriate moderator is placed around the detector
BONNER SPHERES

## Slide 27: Typical fast neutron converter
Detection of recoiling protons produced by neutrons in plastic
Proton energy after the proton recoil:
With this cathode only a proton recoiled by a neutron incident with an energy and an incidence angle above than a certain threshold can be detected by the charge particle detector, like GEM, MM, …
This introduces also a directionality selection effect to the detector,
Not in scale.....

## Slide 28
200 mm
352 mm
nGEM fast neutron detector

## Slide 29
 | a0=MAX [count] | a1 = σX [mm] | a2 = σy [mm] | a3 = μx [mm] | a4 = μy [mm]
Beam 0 | 299.248 | 17.4720 | 14.5132 | 56.4488 | 48.9141
Beam 1 | 284.144 | 17.4720 | 14.5132 | 102.848 | 49.1036
Beam 2 | 284.677 | 17.4720 | 14.5132 | 53.2270 | 101.164
Beam 3 | 304.999 | 17.4720 | 14.5132 | 100.733 | 101.799
Beam 4 | 269.801 | 17.4720 | 14.5132 | 56.7838 | 73.0534
Beam 5 | 237.176 | 17.4720 | 14.5132 | 96.3992 | 73.5918
The detector is suitable for reconstructing different beams
nGEM Imaging performance

## Slide 30: GEM Neutron Spectrometer (for fusion neutrons)
Det.
converter
(thin)
TPR concept
vacuum
3.4 to 4.2 %
about 8%.
M. Scholtz, 2023 ITPA Diagnostic meeting
Developed by AGH and IFJ, Poland

## Slide 31: DEMIN : Micromegas Detector for Neutron spectroscopy for MégaJoules Laser and Inetial Confinement Fusion experiments
Prototype speciﬁcations
 80x80 mm2 « classical » micromegas with 40 x 1 mm width strips
 500 m thick drift volume, ﬁlled with He+10%C4H10+10%CF4
 CH2 converter
Front-end electronics
 Fast current preamp + MATACQ readout (SEDI)
 40 electronic channels
Ref: M. Houry et.al., NIM A 557 p648 (2006)
Up to 30 MeV neutron spectrum diagnostics for inertial conﬁnment DD and DT fusion
Thanks to A. Delbart

## Slide 32: DEMIN : performances
DT SHOT, 31769; 4.1013 n14MeV
Primary neutrons
Scattered Neutrons in the target bay
 induced by neutrons
Tertiary neutrons time window
Time (ns)
Signal (mV)
T0
30 eV/mm stopping power of 1 MeV e- in gas
 the thinner drift gap, the better the  rejection
Ref: M. Houry et.al., NIM A 557 p648 (2006)
Thanks to A. Delbart

## Slide 33: Micromegas Neutron beam loss monitor for ESS
Cadmium envelop
→ to absorb the incident thermal neutrons
Polyethylene moderator
→ to thermalize the incident fast-neutrons
B4C layer (1.5 - 2 µm)
→ Increase neutron detection efficiency
Double Micromegas: back to back
→ ~5mm drift → optimize for dynamic range
Gas: He2 (≈ 1.1 bar) or N2, Ne…
→ He is better for photon discrimination Addition of a quencher: CO2, methane, ...
Zoom
Two objectives: monitoring and safety
Challenges
RF cavities emit 's → background for ionization chambers used as BLMs
Imposible of beam tunning, loss origin of gammas
Continuous monitoring of small losses is needed
Signature of beam loss: fast neutrons
Thanks to A. Delbart
Developed by CEA

## Slide 34
n’
n
p
2D Readout Board
Antistatic HDPE layer
(no charging up)
THGEM1
THGEM2
ΔV
E
Detector Concept:
n scatter on H in HDPE-radiator
foils, p escape the foil.
p induce e- in gaseous conversion gap.
e- are multiplied and localized
in THGEM-detector.
Combine several 1D radiographs
 2D cross sectional tomography.
Detector design:
-) Foils thickness (2.5 MeV neutron)
-) Gas gap thickness (Deposited Energy)
-) Converter height (Axial resolution)
-) Number of converter foils (Detector Length)
Detector Performances:
-) Spatial Resolution
-) Efficiency of transport e- in small gap
-) Detector Efficiency
Cortesi et al. 20012 JINST 7 C02056
Multi-layer converter + THGEM detector

## Slide 35: Conclusions
The concept of a neutron detector is quite difference from the concept of charged particle detector
  You have to face mainly with the «efficiency» challenge
3He crisis and the need of high rate capability detectors fostered several novel applications
Novel wire, RPC and MPGD solutions have been successfully developed in the last 10-15 years and are considered enough mature to be used in future spallation sources like ESS
In WP9 we have to start from this point and further advance

## Slide 36
General remarks to realize a neutron detector
A possible WP9 Guideline
Detectors must be chosen/DESIGNED for the speciﬁc application. Typical application is “counting above threshold”
Requirements to be considered when designing neutron detectors:
Gamma-ray sensitivity
Count rate
Time/space resolution
Environment (B ﬁeld, temperature etc)
Low budget material
Low intrinsic radioactivity
Digitize! (if possible)

## Slide 37: Spare Slides

## Slide 38
Neutron Interaction and detection (2/2)
  In order to realize a neutron detector we thus need a material with a sufficiently high cross section. Nature offers some (but not many materials with such features)
  These materials are used to “convert” neutrons into charged particles
  Neutrons interact with nuclei through the strong force and thus through nuclear intections

## Slide 39
3He tubes applications – fast neutrons
3He detectors can be also used to detect fast neutrons if an appropriate moderator is placed around the detector
BONNER SPHERES

## Slide 40
Novel wire-based solutions
Jailousie detector
Developed by Heidelberg
CDT©

## Slide 41: Measurement of ISIS-vesuvio 2D thermal neutron beam profile
The measured FWHM is around 3 cm compatible with ISIS-Vesuvio data
3 cm
G. Croci et Al, NIMA (2013)

## Slide 42
Thermal neutron measurements as a function of detector gain
Comparable with X-ray GEM rate capability (1MHz/mm2 = 100 MHz/cm2)
40 MHz/cm2
Expected rate with  = 7.88 x 108 n/cm2s and GEM = 5% is 39.4 MHz/cm2

## Slide 43: NitroGEM neutron beam monitor
The NitroGEM monitor has been designed for use on high intensity neutron beamlines
Nitrogen:
Low efficiency: N2 absorption cross section 1.9 barn at 1.8 Å
Reaction: n+14N->p+14C, 620 keV proton energy
Good to measure gamma/neutron separation, efficiency
Standard GEM from CERN:
Standard electronics used to readout 3He tubes at ISIS
Developed by ISIS

## Slide 44
We developed a new prototype increasing the number of borated strip to 16, in order to obtain an higher efficiency.
Now we used an anode with PADs having a different geometry. There are 32x4 PADs and each PAD is 3x24 mm².
Detector window is placed on the side of the anode with 32 PADs. In this way detector is able to measure also position of small spot beams impinging on the side-on window.
Now we used ceramic strips (Al2O3) 500 µm thick.
10 cm
10 cm
Side-on neutron GEM detector

## Slide 45
We estimated detector efficiency, making a comparison with an 3He tube which has a 100% absolute efficiency at the used peak energy of 5,11 meV.
 | S-GEM | 3He Tube
Overall mean counts [s-1] | 1863 | 6011
Background mean counts [s-1] | 21 | 1586
Signal/Background | 87.7 | 2.8
Efficiency [%] | 31 | 99
Detector efficiency was evaluated on both detector sides:
16 strips efficiency = 31 ± 1 %
1 strip efficiency = 2,8 ± 0,5 %
Low gamma sensitivity.
Side-on neutron GEM detector performance

## Slide 46: Low massNeutron GEM Beam Monitor
3 mm
pads on kapton
DRIFT
GAIN
Triple GEM
Mylar 12 um
p
Low Material Budget !
Kapton
Pads
Electronics out of the beam

## Slide 47: Beam Monitor : fast neutron efficiency (nTOF)
1 MeV
5 MeV
Efficiency 10-4
mm
mm
40 mm
40 mm
F. Murtas measurements

## Slide 48: ITER Neutral Beam Test Facility at Consorzio RFX
MITICA
Beam of Hˉ/Dˉ at 0.87(H)/ 1MeV(D)
Current:49 A (H)/ 40 A (D)
Surface: >1 m²
Deviation from the uniformity : <±10%
Beam divergence < 7 mrad
Pulse length: 3600 s
Neutralized beam
SPIDER
Beam of Hˉ/Dˉ at 100 KeV
Current density:355 A/m²(H) 285A/m²(D)
Surface : >1 m²
Deviation from the uniformity : <±10%
Pulse length : 3600 s
The ITER project requires additional heating by two neutral beam injectors, each accelerating up to 1 MV at 40 A beam of negative deuterium ions for one hour.

## Slide 49: ChipIR

## Slide 50: Fast neutron beam monitor at CHIPIR-ISIS
CHIPIR is a new beam-line dedicated to the irradiation of microelectronics with atmospheric-like neutrons; it has been built on the second target station of the ISIS spallation source
Specifically dedicated to the study of single event effects and its design is therefore optimized to extract a neutron spectrum as similar as possible to the atmospheric one with intensity increased by a factor up to 109 depending on configuration.
nGEM installed in Chipir
Working point determinaton

## Slide 51: nGEM characterization for CHIPIR-ISIS
nGEM used to measure different beam sizes.
Beam 12 mm x 12 mm
Beam 30 mm x 30 mm
Beam 80 mm x 80 mm
Counting rate stability

## Slide 52: First test of GEM detector for neutron diffraction measurements
Interface with ISIS-DAE: Time of Flight measurement perfomed using standard ISIS TOF DAE  First Time a GEM is inside standard ISIS DAQ System
128 8x8 mm2 pads
GEM – borated cathode
Incident neutron beam
Transmitted neutron beam
INES sample position
GEM position
λ = [ 0.17 , 3.2 ] Å
3He tubes

## Slide 53
TOF- diffractogram recorded from a bronze sample by the GEM detector (to our knowledge the first ever neutron diffractogram recorded by a GEM....)
Time measurements: 18 hours
First test of GEM detector for neutron diffraction measurements
G. Croci et Al, 2014 EPL 107 12001

## Slide 54: BAND-GEM detection principle
Aluminum grids coated on both sides with 10B4C
Using low θ values (few degs) the path of the neutron inside the B4C is increased  Higher efficiency when detector is inclined
96 mm
4 mm
Triple GEM
Padded Anode
Cathode
3D
Grid
System+ middle GEM
n
α
e-
α
10B4C
10B4C
10B4C
10B4C
n
Al=200µm
Al
θ
EGrid
EGG
8 mm
Typical tilt angle Ѳ=5°
3mm
1mm
VCathode
VTopGrid

## Slide 55: BAND-GEM full-module: design and construction
The 3D-C assembled
The GEM foil
The padded anode

## Slide 56: Efficiency vs neutron wavelength
Tilting angle Ѳ = 8°

## Slide 57: Test of the full-module @ TREFF
Neutron beam
BAND-GEM
Monochromatic neutrons with wavelenght λ=4.78 Å
BAND-GEM with GEMINI electronics

## Slide 58: Test of the full-module @ LARMOR beam line (SANS instrument). Preliminary results.
SANS measurement performd with a concentrated ludox silica dispersion sample.
With this sample, the expected 2d map on the detector position is a circular ring moving to larger radius at longer wavelengths.
Neutron beam
Sample
BAND-GEM
1,5 m
BAND-GEM full module with Cd mask

## Slide 59
Test of the full-module @ LARMOR beam line (SANS instrument). Preliminary results.
Circular ring

## Slide 60
General remarks to realize a neutron detector
Detectors must be chosen/DESIGNED for the speciﬁc application. Typical application is “counting above threshold”
Requirements to be considered when designing neutron detectors:
Gamma-ray sensitivity
Count rate
Time/space resolution
Environment (B ﬁeld, temperature etc)
Digitize! (if possible)

## Slide 61
Deposited Energy Spectrum
Distribution of the deposited charge
Signal
Scattering
Cost effective solution: 300 HDPE layer
Conversion Efficiency  ~8%
HDPE foils
Neutrons (2.45 MeV)
Detector Vessel
SSR = Signal-to-Scattering ratio
Layers
Layers
Layers
Layers
Layers
Layers
Parameters
-) HDPE Thickness = 0.4 mm
-) Gas Gap = 0.6 mm
SSR
Multi-layer converter + THGEM detector Performance

## Slide 62: CERN/n-TOF 2D X-Y neutron beam profiler
128 m Bulk-micromegas technology with 2D X-Y readout (CAST-like) Use of 10B(n,a)7Li for up to 1 MeV neutron conversion
Speciﬁcations
Ar+2%iC4H10+10%CF4
 6x6 cm2 active area
  60 mm, 24 nm 10B4C layer on a 1
m copper coated 12,5 m Kapton foil
 212 channels : readout with 2 x 96 ch. Gassiplex cards
Ref: S. Andriamonge et.al., proceedings of ND2010, International Conference on Nuclear Data for Science and Technology
Mesh
HV for the Mesh
Drift electrode (with B-10)
HV for the Drift
20 m kapton window
HV protection
X & Y strips
+ Y vias
Woven mesh (30 um)
Pyralux pillar (128 m)
X readout Y readout
50 m kapton
Thanks to A. Delbart

## Slide 63: n-TOF beam profile and flux monitor
n-­‐‑TOF beam ﬂux monitoring (2008)
n-­‐‑TOF beam proﬁle (2009)
Ref: S. Andriamonge et.al., proceedings of ND2010, International Conference on Nuclear Data for Science and Technology
Thanks to A. Delbart

## Slide 64: Micromegas in Mimac Fastn
Detection of recoiling neutron energy after scattering with a fast neutron
Drift in a ionization chamber
Amplification using a Micromegas
Read-out on a pixelated anode sampled at 20 ns.
Example of a recoil track in He/Co2 80/20
Developed by Grenoble

## Slide 65: The Piccolo micromegas
In-­‐‑core Nuclear plant integrated neutron ﬂux measurement
Piccolo collaboration (TRADE WG) : IRFU / CEA-DEN
Speciﬁcations
Small sealed 10 cm3 micromegas (160 m)
 Standard design, with woven bulk type mesh
 Non-flammable Ar+2%iC4H10
 Wide neutron energy sensitivity with :
235U et 10B, thermal to several MeV
232Th , En > 1 MeV
H recoils , thermal to several MeV
 Designed for use in the extreme conditions of a reactor core (heated water 300°C, radiation)
 Use of stainless steel & ceramic materials
 4 individually polarized anode channels
 2 readout modes :
counting mode with fast current preamp.
+ 1GHz flash ADC + MATACQ (SEDI)
current mode by mesh current reading for high reactor powe
Tested at TRIGA reactor in Italy
65
Ref: J. Pancin et al., Nuclear Instruments and Methods in Physics Research A 592 (2008) 104–113
Thanks to A. Delbart