## Slide 1: Mu2e Tracker
Aseet Mukherjee (FNAL)
30 January 2024

## Slide 2: Tracker Environment
Generate muons
Stop them, and let them decay… or convert
Detect outgoing electrons
Production Solenoid
Transport Solenoid
Production Target
Stopping Target
Tracker
Calorimeter
(aka the Mu2e Experiment)
Detector Solenoid

## Slide 3: Beam Structure
1700 nsec set by Delivery Ring
700 ns wait to allow fast decays to finish
  But tracker still gets hits
Live
Window
Muons
Protons at Production target
Thin Al disks
Stop >50% of muons
Electrons

## Slide 4: Detector Solenoid
Graded field pushes decay products forward
Uniform field around tracker

## Slide 5: Cosmic Ray Veto (CRV)
By design, covers as much as possible
To access tracker:
  Pull back piece of CRV
  Open DS
  Pull detector “train” out
Slow process

## Slide 6: Particles at Tracker
Before live time
  Electrons “flash” scattering off target
  Fast decay products
Lot of hits to recover from!
Extending into live time
  Protons from Nuclear breakup
  Decay in Orbit (DIO) i.e. usual μ→eν
DIO
  Mostly <½ mμ
  Nuclear recoil smears up to near 105MeV
Notes: Show decay again… and give at-rest spectrum with sharp cutoff

## Slide 7: Tracker Requirements
Near zero material down the center ↔ ambient vacuum
  Lot of unstopped muons, electron flash, DIO
  Even if tracker could handle it, scattering would create background
Low mass in active region
  105MeV electrons scatter a lot
Momentum resolution
  Primary tool to reject background

## Slide 8: Straw Tracker
Small cylindrical volumes tolerate large pressure differential with minimum material
Fine segmentation gives low occupancy
Successfully used in previous experiments
  Most recently, g-2 used essentially identical straws in vacuum

## Slide 9: Transverse Tracker
Straws parallel to
  Difficult to keep mechanical support and readout out of active volume
Straws Transverse to
  Mass easily moved out of active volume
  Difficult pattern recognition
  “Time division” helps

## Slide 10: Time Division
Commercial ADC
DAQ
Measure hit time at both ends of straw
∆t gives estimate of position along straw
Benefits from TDC precision better than needed for drift time
Dual TDC per straw
Implemented in FPGA
Read Out Controller
Implemented in FPGA

## Slide 11: DC-DC Convertor
48V → 5V & 2.5V
Charge pump (no magnetic material)

## Slide 12: HV Disconnect
Thermal fuse triggered by heating a resistor
Allows individual straw to be disconnected
Commercial fuses had issues with size, outgassing, radiation
Pictures are from a worst-case test with excessive parylene

## Slide 13: Straws
5 mm diameter, as thin wall as possible
~1 bar internal pressure for easier testing
Ambient vacuum → ∆P ≈ 100kPa
Use tension to keep straws straight
Double helical wrap
  2×6 μm Mylar + 3 μm adhesive
Metalized inside and outside to reduce leaks

## Slide 14: Straw Leak Testing
Thinnest straws made!
Every straw individually tested
  Purge with CO2, pressurize to 100 kPa
  Place in N2 purged tube, close tube
  Monitor CO2 content
    Fast and cheap: big market for CO2 sensors!
Cross-checked with vacuum tests
Straws slide through ball valve

## Slide 15: Straw Prep
Laser cutter to generate 48 different lengths
Temperature and humidity compensation
0.2mm accuracy

## Slide 16: Straw Installation
Straws pulled to tension into 3D-printed piece
Has fine features to allow epoxy to drip onto straw ends
Straw goes here
Epoxy drips onto straw end

## Slide 17: Sense Wire Installation
25µm gold plated tungsten
Tension with load cell and stepper motor
  Work harden wire as part of installation: Over-tension, then back off
Stepper motor shaft
Pulley
Magnetic clamp
holds wire
Magnetic clamp holds wire
Load cell
Pictures show feeder line (thread). Wire too thin to see)

## Slide 18: “Panel”
120° sector with 96 straws
Small enough to ship
Straw and Panel work done at U. of Minnesota
Ship to Duke U. for metrology

## Slide 19: Straw and Wire Metrology
X-ray (almost) all panels to locate wires and straws relative to survey markers
  15° stereo (tilt X-ray) for measuring Z
σy≈25μm, σz≈ 75μm
Prototype Panel
Panel Stand
X-ray detector
X-ray
Slit
Straws
Red arrow: Wire Blue arrow: Straw edge

## Slide 20: “Plane” and “Station”
Plane: 6 overlapping panels form a complete ring
Station: 2 planes “clocked” to have 12 orientations for straws
Assembled referencing granite table for precision in Z
Assembly precision ~150 μm
Final alignment based on survey points used at Duke

## Slide 21: Vertical Slice Test
Plane with full electronics chain
  Shown horizontal – also run vertical

## Slide 22: Resolution, Efficiency
ε=0.96
σ=2.5ns=170μm
σ=36mm
Drift Direction
Along Straw (time division)
Efficiency

## Slide 23: Leak Testing
Done at every step!
  Panels leak tested
    At U.Mn before shipping
    At FNAL after shipping
  After assembly, planes leak tested
    Precision setup, gets leak rate overnight
    Long term leak test while planes are in storage
Capillary to limit flow
100kPa supply
Read out pressure
sensor in panel

## Slide 24: Leak Rate
Drops ↔ Panel(s) removed
(later repaired)
Looks good so far! But…
  Periodic repairs, not realistic in reality
  Die out over time. Still worrisome
On the other hand
  6 sccm ↔ 10-4 Torr
  10-3 Torr ↔ 60 sccm is acceptable
6 sccm total budget
3 sccm Plane
allotment

## Slide 25: Per-panel Gas Feed
Gas to any panel can be stopped without opening the DS
Do need to access IFB (back of DS)
  Remote control being looked at
Check valves on exhaust side avoid the need for manual valves
216 gas lines
Standard
Flange
Closed valve
(others open)

## Slide 26: Reverse Pressure Protection
Straws crush if ∆P<0
  Disconnected panel would be destroyed when DS was back filled
Custom, very low opening pressure check valve
  Very little space!
  No suitable commercial valve found
Glass ball
O-ring seat
3D-printed
removable insert
Bottom
Open to DS

## Slide 27: Tracker Frame
Kinematic mount for each station
No stress → stable metrology
Sphere in Cup (left)
xyz constraint
Sphere in Groove (right)
yz constraint
Pin in slot (bottom)
z constraint
Check Valves

## Slide 28: Summary & Future R&D
Straws are an appealing option for low mass, high-rate detectors
Looking into even lighter straws for Mu2e-II (and possibly other applications)