## Slide 1
Wednesday, 20 March, Lisbon
Multistage LWFA based on curved plasma channels
Boyuan Li
Shanghai Jiao Tong University, China
ALEGRO Workshop 2024

## Slide 2: Background
Colliders
FEL
Traditional Accelerator
Kilometer-scale accelerator
1MV/cm
Great Change to Accelerators
Laser wakefield acceleration
1GV/cm
CPA Laser
Meter-scale accelerator

## Slide 3: LWFA potential applications
TeV e+ e- Collider
Ultrafast Electron Diffraction
Physics Today, March, 44, 2009
PRST-AB 19, 021302 (2016)
Nature Photonics 11, 293-296 (2017)
Betatron Radiation Source
LWFA based FEL
Nature 595, 516-520 (2021)

## Slide 4: LWFA studies at SJTU
SJTU-Group (2007~)
Leader: Prof. J. Zhang
Topics:
Lasers:
200TW, 10Hz, 25fs (2012~2022)
200+300TW, 1Hz, 25fs (2023~)
20mJ, kHz, 35fs laser
100TW, 2.2μm, 100fs MIR laser
1. Electron injection in Wakefield:
  Phys. Rev. Lett. 114, 084801 (2015); NJP 20, 063031 (2018); Phys. Rev. Lett. 121, 104801 (2018); …
2. Radiation in Wakefield:
  LSA 5, e16015 (2016); Sci. Rep. 6, 29101 (2016); Nat. Photon. 11, 514 (2017); …
3. Multistage LWFA:
  Phys. Rev. Lett. 120, 154801 (2018);
  Materials 16, 3278 (2023); HPLSE 11, e58 (2023); Phys. Rev. Lett. 130, 215001 (2023).

## Slide 5: Motivation for multistage LWFA
?
Dephasing：
Depletion：
Diffraction：
The “3D” limitation:
First proof of staged LWFA, Nature 530, 190 (2016)

## Slide 6: Multistage LWFA by curved plasma channels
Channel term
Curved term
1. Electrons always move in straight plasma channel avoiding transverse dispersion.
2. Driver laser is guided by a curved plasma channel to the following straight channel.
J. Luo, et al. PRL, 120, 154801 (2018)
The staging efficiency approaches to
100% for electron energy higher than 2 GeV in Stage I.
Prof. M. Chen

## Slide 7: Implementation steps
Step I
Stage I: 2GeV electrons in a straight channel
Step II
Stage II: stable guidance of relativistic
laser in curved channel
Step III
Coupling: injecting electrons from Stage I to Stage II and accelerating them in relay
done
done

## Slide 8: GeV electrons in straight channel
High-voltage discharge in gas-filled capillary for plasma channel formation
parabolic plasma profile
Laser guidance and 2GeV electron beam
Straight plasma channel
Stark broadening
3cm-Capillary
X.Z. Zhu, et al. Acta Phys. Sin. 71, 095202 (2022)

## Slide 9: Processing curved capillary
H.Y. Deng, et al. Materials 16, 3278 (2023)
A half circle of curved capillary is etched by MHz laser on the surface of sapphire substrate. Curved capillary is formed by assembling two etched substrates.

## Slide 10: Gas filling design
Fluid dynamics simulations
One-side filling
Two-sides filling
Axially uniform density profile can be obtained with two-sides gas filling.
Y.Q. Zhao, et al. Acta Phys. Sin. 72, 184701 (2023)

## Slide 11: Curved plasma channels
J.L. Li, et al. HPLSE 11, e58 (2023)
Curved plasma channels are created with axially uniform and transversely parabolic density profile by high-voltage discharge in gas-filled curved capillary.
Stable plasma channel can be detected around the peak of discharge current.

## Slide 12: Stable laser guidance in curved plasma channel
Curved capillary with gradually increased curvature
X.Z. Zhu, et al. Phys. Rev. Lett. 130, 215001 (2023)

## Slide 13: Stable laser guidance in curved plasma channel
Laser spot at (a) capillary entrance, (b) capillary exit for ros=20μm, (c) capillary exit for ros=90μm.
ros
E~10 mJ; λ=800 nm; τ=30 fs；w0=33μm (FWHM)
Laser beam can be well guided from curved to straight plasma channels with suitable off-axis distance.

## Slide 14: Stable laser guidance in curved plasma channel
E ~ 3J; λ=800 nm; τ=30 fs；w0=33μm (FWHM)
For relativistic laser, we can get the most stable electron acceleration with optimal off-axis incidence. (monoenergetic and minimal energy spread)
Simulation results show that transverse oscillations of laser beam centroid can be avoided under appropriate off-axis incidence and electron injection in the curved part can be avoided using pure helium gas.
Gas: 99.5% He+0.5 N2
Stage II: the second drive laser is stably guided by a curved plasma channel to the following straight channel.

## Slide 15: Next works
update
200TW, 10Hz, 25fs (2012~2022)
Single laser beam
200TW+300TW, 1Hz, 25fs (2023~)
Two laser beams
300TW
200TW
Control Center
Angle:0~90°
Angle:90~180°
Supercomputer
Laser Room
Target Processing

## Slide 16: Summary
To realize multistage LWFA based on curved plasma channels, we have done the following works:
Getting 2GeV electron beams in the straight plasma channel with centimeter-scale capillary.
Demonstrating stable laser guidance and electron acceleration from the curved to straight plasma channels using appropriate off-axis incidence.
Updating our 200TW single-laser system to 200TW+300TW two-lasers system for the next coupling experiment of multistage LWFA.
Hopefully, we can complete the coupling experiment in 2024.

## Slide 17
Thank you！