## Slide 1: LightPix: Scalable Readout for SiPM-based Detectors
Dan Dwyer (Berkeley Lab)
DRD2 Collaboration Meeting
5-7 Feb 2024

## Slide 2: LightPix: Scalable Cryogenic SiPM Readout Electronics
Rough concept:
Replace LArPix charge-collection pixels with SiPMs
e.g. Prototype 6.4k-channel LArPix-v2 tile
e.g. Darkside-20k prototype light sensor
e.g. Cosmic rays imaged in ton-scale
105-channel LArPix LArTPC prototype
e.g. APEX concept for DUNE
Potential detector formats
R&D Goals:
- Highly-granular cryo-compatible scalable SiPM readout electronics at very low cost
LightPix:
- Adapt existing LArPix ASIC to provide scalable readout for many (e.g. >106) Silicon Photomultipliers
- Reuse demonstrated LArPix system architecture:
Very-low-power (~100 μW/channel), cryo-compatible (87 K), highly-scalable at O($0.10)/channel system cost
- Unique channel for every SiPM (no analog ganging) → Highly granular detector
Full SiPM Coverage
Coupled to light collectors

## Slide 3: LightPix: Comments on Front-End Optimization
Front-end requirements depend strongly on channel occupancy
High-Occupancy Regime: Nphotoelectrons/channel ≫ 1
- Important to capture signal waveform
- Accurate calorimetry
- Pulse shape discrimination
- Demanding requirements on readout electronics performance:
- High-bandwidth (i.e. high-power) front-end / ADC / readout.
→ Gang SiPMs to reduce channel count / power budget
- Or pursue novel techniques (e.g. digital SiPMs)
Low-Occupancy Regime: Nphotoelectrons/channel ≲ 1
- Important to capture hit time (not charge/waveform)
- Calorimetry and PSD come from aggregate (many-channel) data
- Example: Performance of KamLAND hit/no-hit reconstruction
- Front-end can be primitive (e.g. single-photon discriminator & TDC)
- Low power per channel
Many many SiPMs in low-occupancy regime
→ Target of LightPix-v1 R&D
KamLAND Detector:
~1 kton of liquid scintillator surrounded
by ~2000 photomultipliers, MeV-scale physics
Maximizing light collector coverage
for DUNE Far Detector #3:
SiPMs likely in low-occupancy regime

## Slide 4: LightPix ASIC
LightPix-v1:
- Develop and test dedicated time-to-digital converter (TDC)
to provide O(1) ns time resolution
- Add multi-channel coincidence triggering mode to suppress
excess data from dark noise at room temp
Shares LArPix scalable system design:
- 64 channels per chip
- 6,400 channels per cable
- 51,200 channels per controller
Progress:
- Received Aug. 2021
- Power-up, configuration successful
- TDC meets design targets
- Dark count suppression logic validated
- Tested performance of existing front-end performance
with Hamamatsu and FBK VUV SiPMs
Next Steps:
- Optimize front-end for larger SiPMs
LightPix-v1b ASIC
Very-low-power TDC achieves ~ns-scale
precision in response to external pulse
Offset between
external pulse
and TDC stop
signal
TDC
Triggers (normalized)
Tunable TDC (here ~0.5ns/tick)
Photoelectron signal spectrum vs. SiPM bias
with unoptimized LArPix CSA

## Slide 5: LightPix System Testing
LAr Testing:
- LightPix-v1 system coupled to VUV-sensitive SiPMs
Hamamatsu S13370-3075CN (3 mm x 3 mm)
FBK VUV-HD (3 mm x 3 mm)
- Verified detection of VUV (~127 nm) scintillation photons
produced by cosmic rays in liquid argon in existing LArPix TPC
Prototype 50-SiPM board
High-Pressure Helium Testing:
- LightPix-v1 system coupled to 300 VUV-sensitive SiPMs
6 boards of 50 Hamamatsu S13370-3075CN (3 mm x 3 mm)
- Operated up to P = 12 bar, doped with ~1% argon for wavelength shifting
- Verified room-temp dark count suppression, and photon detection in
response to 241Am alpha source
VUV SiPMs readout in joint LightPix/LArPix Network
Helium test chamber
Complete
LightPix
Readout
System

## Slide 6: Future R&D
Enhanced Performance:
- Development for high-occupancy detectors
- Architecture for detector-wide dark count suppression
Enhanced Scalability:
- Operation in high-field environment
- System fabrication/integration techniques
- Alternate photoamplification techniques
Exploring technologies to enable future
very large high-granularity detectors
LIghtPix-v1 ASIC
Prototype 50-SiPM system
APEX Concept
e.g. Darkside-20k
prototype light sensor
LArPix + LightPix TPC Readout

## Slide 7: Backup

## Slide 8: Photon Detector Systems: ArCLight (U-Bern) and LCMs (JINR)
Lessons from Near Detector Light Trap Technologies for a DUNE Far Detector?
  ND achieves ~40% light trap coverage by covering field cage with dielectric light traps
  TBP coating converts LAr scintillation UV to blue, WLS plate/fibers shift blue to green, dichroic film traps, funnels photons to SiPMs
Example: Existing DUNE-ND design
- SiPMs at anode (low field)
- Trap extends into drift field along field cage
- Two styles: WLS plastic core vs. WLS fiber bundle
- Occludes ~3% of volume, charge readout anode
One pixel tile with one WLS plastic light trap attached
Bern ArCLight
Two complete anodes (16 tiles)
with light traps attached, inside
field cage (bottom open for viewing)
Fiber-bundle style light trap:
JINR LCMs
Cathode
Anode
Anode
Instruments 2018, 2(1), 3

## Slide 9: Light Readout Prototyping
View of alternating LCM/ArCLight traps in 2x2 TPC Module 3
LCM (fiber-based) Light Trap from JINR
Scintillation Light traps mounted to Pixel Tiles for 2x2
ArCLight Light Trap from Univ. of Bern

## Slide 10: R&D on Scalability: LArPix-v2 Concept
Design Principles:
Minimize cryo-side components:
- LArPix ASIC is the only active element
- Multiple identical pixel tiles
Reliability:
- Tile robust to single ASIC failures
- Redundant I/O paths (x4 per tile)
Fully-integrated Controller:
- Drives 8 tiles
- Programmable logic
- Clean power
- Built-in DAQ and full OS
All components fabricated commercially

## Slide 11: Near Detector Prototyping: ArgonCube 2x2 LArTPCs
Verified design meets technical requirements:
- Collected >107 cosmic ray events
- Stable HV at ~30kV (~1 kV/cm drift, 2x target)
- Stable Purity at >2ms (>4x target)
- MIP Charge Signal-to-Noise >20:1 (at target)
Typical raw data from cosmic ray interactions
imaged in 3D prototype detectors
Arguably the most performant
ton-scale LArTPC to date.
Continuous streaming readout:
~100% live, independent of scintillation system
Achieved ~200 keV thresholds
Low data rate due to self-triggered design
Example:
LArPix-v2b system, 102,400 pixels, 3.8mm spacing

## Slide 12: 2x2 Demonstrator @ NuMI
2x2 Operation in NuMI Neutrino Beam 2023-2025
- Install four TPC modules in former location of MINOS Near Detector
- Includes upstream/downstream trackers, repurposed from the MINERvA Experiment
Goal:
- Characterize GeV-energy neutrino interactions on argon nuclei
Status:
- TPC Modules installed in cryostat, Oct 2023
- Installation nearing completion, Dec 2023
- Start of operations in early 2024
Operation of a 300k-pixel LArTPC
in a GeV-energy neutrino beam!