## Slide 1: Q-Pix: a scalable pixel readout for liquid noble detectors
James Battat, Wellesley College on behalf of the Q-Pix consortium
DRD2 Collaboration Meeting, Feb. 5-7, 2024, CERN

## Slide 2: Q-Pix: record the time per unit charge
David Nygren, Yuan Mei
arXiv:1809.10213
Integrator with reset
Comparator
Reconstruct current (average)

## Slide 3: Q-Pix: record the time per unit charge
…
Integrator with reset
Comparator
Reconstruct current (average)
David Nygren, Yuan Mei
arXiv:1809.10213

## Slide 4: Q-Pix: record the time per unit charge
Reset threshold: 0.3 fC = 1,900 e-
David Nygren, Yuan Mei
arXiv:1809.10213
Integrator with reset
Comparator

## Slide 5: Q-Pix at scale
Pixel
ASIC
Tile
Tile array

## Slide 6: Prior work
Prototypes (COTS)
  Single-pixel (low noise)
  Multi-pixel (event topology)
ASICs v0

## Slide 7: Q-Pix front-end with sub-fC reset threshold
Demonstrated 0.46 fC per reset (~2,900 e-)
Demonstrated “replenishment” rather than “reset” (prevents lost signal charge)
Demonstrated reconstruction of signal current equivalent to MIP in LAr
Led by Yuan Mei (LBL) and Peng Miao (LBL) arXiv:2311.09568

## Slide 8: Q-Pix front-end with sub-fC reset threshold
arXiv:2311.09568
Simulation
Data

## Slide 9: Multi-channel Q-Pix front-end, event topology
16 channels
COTS integrator and comparator TI IVC102 & AD8561
Measure transverse diffusion of e- in gas TPC at room temp.
Led by UTA (Asaadi) & Wellesley (JB) Upcoming submission, JINST
GEM
Xenon Flash Lamp (fiber)
Readout Electronics
Gold

## Slide 10: Multi-channel Q-Pix front-end, event topology
Upcoming submission, JINST
Transverse diffusion from reset times alone
Measurements consistent with PyBoltz and prior measurements Diffusion constant with E-field, decreases with pressure
Fixed pressure, various drift field
preliminary
Fixed drift field, various pressures

## Slide 11: Q-Pix ASICs (v0 in-hand)
Analog front-end
Digital back-end
+ TSMC 180 nm
+ 16 channels
+ 8 standard (45 uW/chan)
+ 8 low-power (25 uW/chan)
+ Testing underway: measured our
first current-induced triggers
+ TSMC 180 nm
+ 16 channels, differential inputs
+ Ring oscillator, timestamping
+ Wirebonding to test boards underway

## Slide 12: Looking ahead
Multimodal charge & light
LArTPC demonstrators
Further ASIC development

## Slide 13: Multimodal Q-Pix: charge & light
Integrator with reset
Comparator

## Slide 14: Multimodal Q-Pix: charge & light
Ionization charge
Integrator with reset
Comparator

## Slide 15: Multimodal Q-Pix: charge & light
GND
Avalanche electrode → to readout system
Charge
button
Interdigitated
Electrode (IDE)
aSe
Ionization charge
Photogenerated charge
+ Amorphous selenium (aSe) + Direct sensitivity to VUV light
+ Avalanche gain possible
+ Large area coverage
+ Demonstrated at LAr temperatures
+ See e.g.
JINST 18 (2023) 01, P01029 Langmuir 2022, 38, 28, 8485–8494 Review of Scientific Instruments 93, 053103
Elena Gramellini in WP2 this afternoon
Michael Rooks at CPAD 2023
Integrator with reset
Comparator

## Slide 16: ASIC testing and development
LArTPC ASIC demonstrators
Future ASIC versions
New facility under development at Wellesley College
Cryogenic labs at UTA, Manchester, Syracuse.
Higher channel count (64)
Combine analog and digital ASICs

## Slide 17: Wish list / DRD2 synergy
Access (and contribute to) Network of Small Experimental Efforts (NoSEE)
  LAr purification
  LArTPC demonstrators
fC charge sensing / low power T1.1.G1 scale-up T1.1.G2 multimodal Q+L T1.1.G3
Notes: Task 1.1, Goals 1, 2, 3

## Slide 18: Thank you
Q-Pix: low power, low threshold pixel readout for kTon liquid noble detectors
Prototypes demonstrated
  0.46 fC reset threshold
  event geometry from resets
ASICs v0 testing underway
  Room temperature
  LArTPC
Charge & Light R&D ongoing

## Slide 19: Extras

## Slide 20: Example waveform (MIP in LAr)
Threshold: 1.0 fC 6,200 e-
Threshold: 0.3 fC 1,900 e-

## Slide 21: Multimodal Q-Pix: charge & light

## Slide 22: Multi-channel Q-Pix front-end, event topology