## Slide 1: 4 Rod Crab cavity Status
G. Burt on behalf of 4RCC collaboration

## Slide 2: Cavity Shape
Emax @3MV | 32.0 MV/m
Bmax @3MV | 60.5 mT
Transverse R/Q | 915 Ohms
Cavity fitted LHC scenario (84 mm aperture compact transverse size) and has tolerable fields at the design gradient.
Removal of voltage variation.
RT/Q=(V(a)2/wU)*(c/wa)2

## Slide 3
Multipactor
Multipactor on the beam pipe was found on the beam pipe at ~2 MV.
Same type of multipacting was seen on KEKB crab cavity.
Studies with processed surface SEY shows it can be processed through

## Slide 7: 1. Conventional fabrication, ideal RF design
Fabricate from multiple pressed sections (multiple dies)
Multiple multi-axis e-beam welds (esp. rod to end plate joint)
May be possible but weld development needed.
E-beam weld line of sight
Almost parallel weld

## Slide 8: 2. Machine end plates and rods from solid
Consider to make major parts from solid
  Wire EDM pre-forms from ingot
  Machine all surfaces
  Add beam pipes and can
This allows any material thickness or even a variable thickness. Also stiffeners can easily be added.
This will also allow fine detail to be added to avoid multipactor (like the ridges suggested by SLAC for the 800 MHz elliptical cavity)
However a substantial lump of Nb ingot is required (£50k worth)

## Slide 9
Rod profile can be reduced to allow both base plates to be wire etched from a single block of niobium.
This saves the amount of Nb required by 20%.
Clearance of 2mm between both rods to allow wire EDM.
Alternative fab, slightly modified RF design

## Slide 10: Modified Rod Shape
Reduced tip size leads to a 10% increase in peak surface electric field.
 | Original design | Reduced profile
Emax @3MV | 32.0 MV/m | 35.9 MV/m
Bmax @3MV | 60.5 mT | 60.1 mT
Transverse R/Q | 915 Ohms | 963 Ohms
Original
Reduced profile
E Abs
B Abs

## Slide 11: Mechanical Design

## Slide 12: Additional heating on the ports
The lengths of each port has to be carefully chosen to avoid excessive additional losses at the flanges which will make it impossible to measure the Qo of the cavity when testing
50 mm is sufficient for our cavity

## Slide 13: Pressure sensitivity
The outer can needs a thickness of at least 3 mm in order to minimise the pressure sensitivity to below 100 Hz/Torr.
This is a relatively small dependance and is due to the fact that the frequency is dependant on the cavity length and the cavity is quite stiff to longitudinal pressure.

## Slide 14: Stiffening Ribs
The stress on the outer can exceeds the 70 Mpa yield strength of Nb at room temp with 2 bar pressure.
Stiffening ribs were added to the cavity to reduce the stress to tolerable levels.

## Slide 15: Parts after trimming and final polishing

## Slide 16: Cavity Welding
All components inspected for surface imperfections prior to etch.
20 micron etch on all weld joints.
Weld Chamber pumped down to 3.7x10-5 torr before welding.
Surface temperature of all welded components below 160ºF when chamber opened.
All weld seems visually inspected before removing components from chamber.
Post weld cavity leak check performed using copper gaskets, and conflat blanks.
No detectable leaks found (minimum detectable leak of 1.0x10-10 torr ℓ/s)

## Slide 17: 4 Rod prototype built
NIOWAVE

## Slide 18: Tests at CERN SM18
The cavity was prepared for vertical testing mid-November at CERN in SM18.

## Slide 19: 1st test results (preliminary)
Helium processing due to leak?
Low Q probably due to incomplete cleaning.

## Slide 20: We now have lots of LHC crab prototypes