## Slide 1
Jason Hogan
April 3, 2024
2nd Terrestrial Very-Long-Baseline Atom Interferometry Workshop
Multi-photon clock atom interferometry

## Slide 2: Broadband LMT Clock Atom Interferometry
88Sr, 1S0 → 3P1 transition (689 nm)
Broadband: laser cooled atoms (red MOT)
Fast: 601 ħk splitting in ~20 μs
Conventional pulses
Floquet pulses
1S0
1P1
3PJ
461 nm
30.5 MHz
689 nm
7.4 kHz
698 nm
1 mHz (87Sr)
Sr
Ω = 2π × 12 MHz
Floquet modulation technique to symmetrically drive both arms

## Slide 3: Narrowband LMT Clock AI Limits
Laser: 5W, 1 Hz linewidth
87Sr DFG, matter wave lens
Constrained optimization includes:
Spontaneous emission decay
Off-resonant scattering
Detuning errors (Doppler, laser noise)
Intensity inhomogeneities
Timing jitter
Interferometer enhancement factors >104 theoretically possible, but transitions are too slow (at this power)
For gravitational wave detection in MAGIS, need the 1S0 → 3P0 transition (698 nm)
Full scale MAGIS detector (on Earth) requires extreme LMT, beyond state-of-the-art
Simulation effort to understand future limits

## Slide 4: Multiphoton Clock Atom Interferometry Motivation
87Sr only
87Sr
Boyd et al., Science (2006).
1S0  3P0 clock transition in Sr at 698 nm is only naturally allowed in fermionic 87Sr
Bosons have interesting properties:
Scalar polarizability of clock states
Zero linear Zeeman shift in ground state
High natural abundance
Reduced interaction strength (e.g., 88Sr)
Easier state preparation (I=0)
Possible to make BEC (e.g., 84Sr)
Proposal: Use multi-photon excitation to populate 3P0 state for atom interferometry
Potential to engineer the effective coupling strength for faster pulses, better LMT

## Slide 5: Gradiometer configuration requires collinear light
Long baseline gradiometry for gravitational wave, dark mater detection
Light pulses from alternating directions (LMT enhancement)
For single photon single direction transitions, laser noise is common
For three photon gradiometer, all light must be collinear.
For example: x – x – z

## Slide 6: Polarization requirements
For x-x-z polarization, there is destructive interference between two paths:
Solution: Small magnetic field breaks the symmetry and results in a non-zero coupling
Coupling
Zeeman shift

## Slide 7: Three photon Rabi oscillations
Here: 29 kHz Rabi frequency with 10 Gauss field, 5 W/cm2 (360 micron beam)
2.5 GHz detuning of 688 nm, 9.9 MHz detuning of 689 nm
Peak transfer limited by intensity inhomogeneity in this proof of principle
689 nm, 688 nm, 678 nm lasers locked to frequency comb; scan three photon resonance
Detection using state-selective repump followed by 461 nm push pulse
Verified that transition requires all four fields
We observe minimal decay to unwanted states, consistent with density matrix simulation

## Slide 8: Magnetic tuning of three photon Rabi coupling
Some examples:
12 kHz Rabi frequency at 4 Gauss field
49 kHz Rabi frequency at 19 Gauss field
Three photon coupling depends on:
(ratio of Zeeman shift to 689 nm detuning)
Two regimes:
The magnetic field tunes the effective dipole moment by angle , changing the projection onto the light polarization:
High Rabi frequency with modest magnetic fields, intensities

## Slide 9: Atom interferometry demonstration
Atom interferometry between 1S0 → 3P0 levels of 88Sr using the three photon transition
Mach-Zehnder sequence
Shows phase coherence over longer times
Proof of concept for future long-baseline atom interferometer applications

## Slide 10: Summary
Three photon transition opens up the use of bosons for atom interferometry and clocks
Small magnetic field allows for collinear light, otherwise forbidden by selection rules
   Semi-classically, the magnetic field adds a torque that “rotates” the atomic state on a timescale faster than the natural lifetime
Demonstrated proof of concept atom interferometer
Next steps
Higher power laser, bigger beams to reduce inhomogeneous loss
Optimize parameters (magnetic field, 689 detuning) to minimize spontaneous emission – ultimate limits?
Possible alternative to 87Sr 698 nm transition for MAGIS-100 (?)
   May offer an advantage for LMT atom optics by engineering an effective transition with strong coupling but long excited state lifetime