## Slide 1: Introduction to Particle Accelerators for the CERN-Solvay Student Camp
Rende Steerenberg – BE/OP
28 May 2024

## Slide 2: Content
Why Accelerators & Colliders?
The CERN Accelerator Complex
An Accelerator’s Main Ingredients
A Brief Word on the Future

## Slide 3: Content
Why Accelerators & Colliders?
The CERN Accelerator Complex
An Accelerator’s Main Ingredients
A Brief Word on the Future

## Slide 4: What is the first physics formula that jumps in your mind?

## Slide 5: E = M c2
This is the most famous equation of twentieth-century physics.
It is a statement that mass and energy are two forms of the same thing, and that one can be converted into the other.
In our accelerator we add Energy to the particle through our RF systems and observe the Mass created in the experiments.

## Slide 6: Creating Matter from Energy
E = m・c2
In our accelerators we provide energy to the particles we accelerate.
In the detectors we observe the matter created
During the Big Bang Energy was transformed in matter

## Slide 7: Looking to smaller dimensions
λ =
h c
E
Increasing the energy will reduce the wavelength
Visible light
λ = 400  700 nm
X-ray
λ = 0.01  10 nm
Particle accelerators
λ < 0.01 nm

## Slide 8: Fixed Target vs. Colliders
Collider
All energy will be available for particle production
Fixed Target
Much of the energy is lost in the target and only part is used to produce secondary particles

## Slide 9: The Aim:
Verify the Standard Model
Search for physics beyond the Standard Model
Specific assemblies of quarks
form hadrons.
Protons, Neutrons, pions,..
Gravitational force
Electromagnetic force
Strong interacting force
Weak interacting force
For every particle there is a corresponding anti-particle

## Slide 10: Content
Why Accelerators & Colliders?
The CERN Accelerator Complex
An Accelerator’s Main Ingredients
A Brief Word on the Future

## Slide 11: The CERN Accelerator Complex

## Slide 12: The LHC Cycle
6.8 TeV
450 GeV
Time
Injection
Ramp
Squeeze
&
Adjust
Stable beams for physics
Dump
&
Ramp down
= Field in main magnets
= Beam 1 intensity (current)
= Beam 2 intensity (current)

## Slide 13: Filling the LHC & Satisfying Fixed Target users
1.2 seconds
PSB
PS
SPS
Time
= Field in main magnets
= Proton beam intensity (current)
= Beam transfer
To LHC clock-wise or counter clock-wise
450 GeV
26 GeV
1.4 GeV

## Slide 14: Content
Why Accelerators & Colliders?
The CERN Accelerator Complex
An Accelerator’s Main Ingredients
A Brief Word on the Future

## Slide 15: What does “Relativity” in an accelerator mean for you?

## Slide 16: Towards Relativity…
PSB
Newton:
PS
SPS / LHC
velocity
energy
c
Einstein:
Energy and mass increase not much velocity

## Slide 17: What units for energy do you know?

## Slide 18: The Units we use for Energy in Accelerators
The energy acquired by an electron in a potential of 1 Volts is defined as being 1 eV
Thus 1 eV = 1.6 x 10-19 Joules
The unit eV is too small to be used today, we use:
  1 KeV = 103, MeV = 106, GeV = 109, TeV = 1012

## Slide 19: The Energy in the LHC beam
The energy in one LHC beam at high energy is about 320 Million Joules
This corresponds to the energy of a TGV train going at 150 km/h
...... but then concentrated in the size of a needle

## Slide 20: The LEIR Accelerator as Example
Building 150

## Slide 21: Travelling through nothingness
In the LHC vacuum is also used as thermal insulator
Vacuum in a mostly stainless steel vacuum chamber is required to avoid the particles to interact with the gas molecules
Especially important for low energy particles and anti-matter particles, but also for colliders ….

## Slide 22: Injecting & Extracting Particles
Extraction
Injection
Injection

## Slide 23: Injecting & Extracting Particles
Incoming beam
Magnetic field
Injected beam
Circulating beam
No magnetic field
Septum Magnet
Kicker Magnet

## Slide 24: Septum Magnet

## Slide 25: Injecting & Extracting Particles
Extracted beam
Magnetic field
Circulating beam
Circulating beam
No magnetic field
Septum Magnet
Kicker Magnet

## Slide 26: Make Particles Circulate
Main Dipoles
Main Dipoles
Main Dipoles
Main Dipoles

## Slide 27: Deviating Charged Particles
Magnetic Lorentz Force:
Moving charged particles are deviated
in a magnetic field

## Slide 28: Any ideas about how strong magnet fields in dipole magnets can be?

## Slide 29: Motion in the Horizontal Plane
Horizontal motion
Different particles with different initial conditions in a homogeneous magnetic field will cause oscillatory motion in the horizontal plane  Betatron Oscillations
Particle B
Particle A
2π
0
Horizontal
displacement
Machine circumference
Two charged Particles in a homogeneous magnetic field
Particle A
Particle B

## Slide 30: Motion in the Vertical Plane
The horizontal motion seems to be “stable”…. What about the vertical plane ?
Many particles many initial conditions
Vertical
displacement
Many different angles
 s
Any ideas on how to solve this issue?

## Slide 31: Focusing Particle Beams, a bit like a lens
Force on particles
Focusing Quadrupole
De-focusing Quadrupole
Rotated by 90º
QF
QD
QF

## Slide 32: Focusing Particle Beams in LEIR
Main Dipoles
Main Dipoles
Main Dipoles
Quadrupoles

## Slide 33: Accelerating Particles, Using Electrical Fields
Accelerating
Cavity

## Slide 34: Radio Frequency Cavity
Charged particles are accelerated by a longitudinal electric field
The electric field needs to alternate with a harmonic of the revolution frequency

## Slide 35: RF Cavities
Variable frequency cavity (PS)
Super conducting fixed frequency cavities (LHC)
Fixed frequency cavities (SPS)

## Slide 36: The Eyes of Operations
Beam intensity or current measurement
Transverse beam profile measurement
Longitudinal beam profile measurements
Any many more beam properties…..
Measure the LHC luminosity, number of events per surface and time unit.

## Slide 37: Possible Limitations
Same phase and frequency for driving force and the system can cause resonances and be destructive
Neighbouring charges with the same polarity experience repelling forces
+
+
Moving particles create currents, These currents result in attracting or repelling magnetic fields
Machines and elements cannot be built with infinite perfection

## Slide 38: Content
Why Accelerators & Colliders?
The CERN Accelerator Complex
An Accelerator’s Main Ingredients
A Brief Word on the Future

## Slide 39: Luminosity, the Figure of Merit
Intensity per bunch
Beam dimensions
Number of bunches
Geometrical
Correction
factors
High-Luminosity LHC
X 2
Maximise Luminosity:
Bunch intensity
Transverse beam size
Beam size at collision points
Crossing angle
Machine availability

## Slide 40: H- injection, a Key LIU Ingredient
Charge exchange injection with H-
x’
x
+
-
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
Before stripping foil
x’
x
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Behind stripping foil
Phase Space Painting is possible (various particle distributions)

## Slide 41: The LHC Injector Upgrade Project is Completed
PS:
  Injection energy increase from 1.4 GeV to 2 GeV
  New Finemet® RF Longitudinal feedback system
  New RF beam manipulation scheme to increase beam brightness
LINAC4 – PS Booster:
  New LINAC 4 with H- injection
  Higher injection energy
  New Finemet® RF cavity system
  Increase of extraction energy
SPS
  Machine Impedance reduction (instabilities)
  New 200 MHz RF system
  Vacuum chamber coating against e-cloud
These are only the main modifications and this list is not exhaustive

## Slide 42: The High Luminosity LHC Project
New IR-quads (inner triplets)
  New 11T short dipoles
  Collimation upgrade
  Cryogenics upgrade
  Crab Cavities
  Cold powering
  Machine protection
  …

## Slide 43: Possible Future Accelerators
Compact Linear Collider (CLIC)
Linear e+e- collider up to 3 TeV
Future Circular Collider (FCC)
100 TeV pp collisions in 100km ring
Requires new magnet technology
e+e- collider (FCC-ee) as 1st step
High Energy LHC in the present LHC tunnel
~ 30 TeV with FCC magnet technology
European Strategy for Particle Physics

## Slide 44: Follow us…
https://op-webtools.web.cern.ch/Vistar/vistars.php