## Slide 1: Rome Tor Vergata Group Task 6 - manufacturing
A. Rocchi on behalf of Rome Tor Vergata group

## Slide 2: Singlet stratigraphy
The BIS and BIL singlets prototypes have the same stratigraphy:
the gas volume is contained between two readout panels with strips oriented along the long side of the chamber.
small circular dots are glued at the pillars to ensure that the pressure applied by the panels does not compress the gas gap
the sandwich composed of read-out panels and gas volume is closed in a Faraday cage made up of layers of coppered FR4 and copper tape on the edges
Total singlet thickness 13.02 [± 0.90] mm.
Gas gap
Honeycomb
Copper tape
Kapton
Honeycomb
Gas gap
Paper Sticker
Copper tape thickness : 65 µm
Kapton tape thickness: 70 ± 3 µm
Paper stickers thickness: 150 [± 70] µm
Gas-gap thickness: 4.48 mm
Read-out panel thickness: 3.94 ± 0.2mm
FR4

## Slide 3: Gas volume layout
The gas volume consists of two HPL plates 1.5 mm nominal thick with resistivity of about 5 x 10 ^ 9 Ω cm, separated by 1 mm thick pillars. The pillars have the same geometry as those used for the BIS78 and are arranged on a grid with a pitch of 7 cm. The HV is distributed on the HPL panel through a graphite layer with resistivity of approx 350 kΩ/□. The power cables, certified up to 15 kV DC, are connected to the graphite layer by means of a thin copper sheet anchored to low resistivity cords, and housed in a recess created on the frame of the chamber filled with hot melt. The gas is distributed along the short side of the gas gap.
The overall tolerances on the gas volume dimensions are +-1mm for length and width and +-0.2 mm for the thickness.
70 mm
Gas Flow
Gas In

## Slide 4: Read-out panels
The read-out panels consist of three layers:
a 3 mm thick Nomex layer
two 0.4 mm thick coppered FR4 layers glued on the two opposite surfaces
The thickness and material of the panels are selected to optimize the impedance of the strips and the weight of the detector.
The read-out strips are made by photo-etching process on the surface of the panel facing the gas volume
A termination resistor is welded to the ends of each strip and each decoupling wire. The welding process of the resistances on the panel will be optimized using an automatic hot air jet machine
A. Bruni, M. Schioppa

## Slide 5: RO panels and FE Electronics
2,5 cm
15 cm
Chip
2 cm
LV/Clock
The FE Boards will host two connectors: one for the signals, one for the LV power and the TDC clock
two circular holes are positioned on two corners of the FEE for the alignment of the boards with the RO panel
The RO panels have two alignment holes for each FEE board
The RO panels have three holes placed on the corners (one circular and two elliptical) to obtain a submillimeter alignment during the production steps
The read-out panels will be shifted by 31 mm to access the FE board pad for welding
The Back End side will be widened by 1mm as respect to the firsts prototypes to ease the taping.
the read-out strip termination circuit will be designed once the FE Layout has been defined and will be optimized for the dissipationof the heat produced during the boards welding.

## Slide 6
Bachelite
Bachelite
5 mm
2 mm
7 mm
3 mm
Gas
Ground
7.9 mm
first strip
8.6 mm
9.4 mm
10.1 mm
3.9 mm
RO panel strips relative position
Open question on the Ground frame layout
The relative position between the first strip and the gas gap frame is the same for all the singlet types. The first strip starts 10.1 mm from the gas-volume/RO-panel side. The first and last strip width is defined in such a way to have the minimum number of pitch category
BIL A-B: 20 mm
BIS1: 22 mm (first and last strip 1mm tighter )
BIS 2-6: 21.8 mm
Cord 20kΩ/□
Cord 20kΩ/□

## Slide 7: Singlet tolerances
38 mm
38 mm
1736 mm
1660 mm
1662 mm
1734 mm
5 mm space to access the FE weld
A gas gap with a length greater than the nominal values ​​can be used by reducing the access space for welding the FE.
This solution can only be adopted in extreme cases, as it has an impact on the soldering times of the boards, but it is an additional safety factor.
The length of the singlet would be shorter than the nominal value by an amount equal to the excess length of the gas gap

## Slide 8: Mass production optimization for phase2 ATLAS detectors
𝑁𝑜𝑚𝑖𝑛𝑎𝑙 𝑣𝑎𝑙𝑢𝑒 4.66 𝑚𝑚
4 chamber types
  BIL A
  BIL B
  BIS 1
  BIS 2-6
Atlas Attività 2023

## Slide 9: Optimization of the mechanical frame
SC1 & SC2 (2 cm x 30 cm x 1 cm)
30 cm
~ 8 cm
Measurement of the propagation speed
Second coordinate performance
𝒗~ 𝟐𝟎. 𝟐𝟒 𝒄𝒎/𝒏𝒔
y = -0.0988x R² = 0.9995
Atlas Attività 2023
-14
-16
-12
-6
-8
-10
-4
-2
0
0
50
100
150
Delay (ns)
Distance (cm)

## Slide 10: Half glued gas gap test
Overpressure test Eta coordinate
Overpressure test Phi Coordinate
Half glued gas gap has to with with internal pressure of 2 mbar
Atlas Attività 2023
0 mbar
+2 mbar

## Slide 11: CR stand at CERN
Tile 3
Tile 4
Triplet sector
Atlas Attività 2023

## Slide 12: MINICRATES
1212
M
a n y f o l d
HV system
Gas system
Mass production test tools
Atlas Attività 2023