## Slide 1: Funded by the European Union (EU). Views and opinions expressed are however those of the author only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.
Antti Kolehmainen
CERN EN-MME
With input from many colleagues
Muon Collider – Target and Capture status review

## Slide 2: INTRODUCTION
Follow-up of initial presentations in mmWG: https://indico.cern.ch/event/1239921/ and IMCC 2023
Based on the coil lay-out by A. Portone et al. introduced in annual meeting 2024
Radial build
Support systems
He cooling lay-out
Integration
Assembly sequence
NOTE: As a conceptual pre-study, the modelling is done up to a level sufficient for presentation. Some mismatches in geometry etc. exists.

## Slide 3: COILS & COLD MASS
A. Portone et al.: Conductor & Jacket: 33.3 T & 80.7 T
Coils: 100 T
Steel work: 12 T
Coils: 26 T
Steel work: 6 T
Coils: 14 T
Steel work: 4 T
Coil bore: 1400 mm on the jacket
Ø1400
Coil gaps: 480 mm on the jacket

## Slide 4: RADIAL BUILD
Ø1400
Ø1380
VACUUM GAPS: 20 mm
INNER Ø1238 / R619
THICKNESS 12 mm
Outer R586 in current 3D from STI

## Slide 5: COLD MASS SUPPORTING
Individual coil supports – alignment of coils
Common support beam – interface for individual coil and cold supports
Tensioning system to keep the coils together
Calculations required, for them:
Coil alignment requirement for coil supports
Maximum load cases for support dimensioning(transport?)
Coil forces in all cases for the tensioning system

## Slide 6: SUPPORT SYSTEM 20 K – 300K
COLD MASS
300 K Supports
COLD SUPPORTS 20 K – 300 K
FIX POINT – ALL OTHER SLIDING POINTS
INTERCONNECTION BARS - FOR COOLDOWN MOVEMENT AND MAGNETIC FORCE
Calculations required, for them:
  Boundary conditions for cold supports, 300 K supports and interconnection bars(transport accelerations, thermal contraction, magnetic forces etc.)
Interconnection bars cannot support bending – an active cooling of internal cold mass supports may be needed!(maybe for cooldown time too)

## Slide 7: SUPPORT SYSTEM – W-SHIELD
Tungsten segments built inside a cylinder with support interface for suspension
For deformation, cross-section MUST be uniform!(study by C. Accetura)
W-shield suspended from vacuum vessel
30 T
(one end)
2x 30 T
(two ends)
Keep section assemblies together with longitudinal rods
Longitudinal supports to add

## Slide 8: CRYOSTAT SUPPORTS
ATLAS inspired support system – air pads and positioning jacks
Steel surfaces for air pads to minimize friction, air pads maybe removed after installation(not radiation hard)
Thanks to M. Raymond of ATLAS for sharing experience!
Vacuum vessel to have support interface and reinforcements to support both cold mass and W-shield
  Define boundary conditions for analysis
  Vacuum induced stresses must be added

## Slide 9: COILS
Magnets build from pancake windings
First and last pancake of a magnet have a current connection and isolated He connection, others only isolated He connections
Electrical break
He cooled current lead
HTS
Cu former with Ø8 cooling hole
St. steel jacket
Splice
He line

## Slide 10: COIL COOLING LAY-OUT
He supply
58 connections in section 1
He return
58 connections in section 1
Current Leads
2x seven leads for section 1
Sections:
  1st: 6 long and 1 short magnets
  2nd: 6 long and 2 short magnets
  3rd : 7 long and 1 short magnets
Long magnet = 10 pancakes
Short magnet = 5 pancakes
Pancake = 2 connections
Isolating supports
NEXT:
Supports with fix points
Bellows
Calculations

## Slide 11: TUNNEL INTEGRATION
10.2 m
R7.5 m
27 m
6.5 m

## Slide 12: VACUUM
Ø964
8000
Ø4500
Ø4060
Vacuum vessel analysis
  Pressure difference and supporting of sub-assemblies
Bellows to address:
  Vacuum force on bellows = 1.3 MN
  Bellow supporting TO BE ADDED
PUMPING(NOT STUDIED!):
Assumed to be done from distance due to stray field – see next slide
Shown satellite connections crowded with He lines and leads – add pumping connections
NOTE: Beam vacuum is still a simple pipe!

## Slide 13: MAGNETIC FIELD SHIELDING
Courtesy of P. Testoni
Point raised in previous preview – high stray field
  Introduction of the satellites
Analysis assumes 30 % of steel in 2 m thick tunnel wall
2000 mm
30% STEEL

## Slide 14: COLDMASS ASSEMBLY
1. Assemble coils on the common support beam with their respective supports. Place shims between coils
2. Clamp coils together with the axial clamping system
3. Insert the internal thermal shield.
Temporary supports required.
4. Install coil cooling lines and current leads, shown on the next slide

## Slide 15: SHIELDS ASSEMBLY
2. Install lower section of the thermal screen. Connect it to the cold supports
3. Install remaining parts of the thermal screen. Internal thermal shield to be connected to the end plates
4. Insert tungsten shield. Tooling and temporary supports required
1. Lay coldmass on the cold supports and warm support platform

## Slide 16: CRYOSTATING
1. Install magnet assembly into the vacuum vessel with the linear guides. Fix the magnet assembly on the vacuum vessel
Tooling required
2. Connect tungsten shield to the vacuum vessel with links. Remove temporary supports.
3. Complete vacuum vessel front end, realize target connections etc.
Full assembly ~ 170 T
Other sections can follow shown assembly sequence
Prepare sections as far as possible on surface?
  Tunnel work in parallel
  Large assemblies to transport

## Slide 17: CONCLUSION
Coils updated, resulting radial build update done as well – limit for tungsten shield
A detailed coil winding available
Support system updated, boundary conditions in work, analysis work to be done
First lay-out for magnet cooling
Integration updated with satellite connections
Stray field studied
Assembly sequence proposal created
NEXT STEPS?

## Slide 18
Thank you for your attention!
!/?
Your questions/remarks please

## Slide 19: SPARE SLIDES

## Slide 20: Radial build - VERSION 2

## Slide 21: Radial build – VERSION 2
R619
VACUUM GAPS 20 mm
GAP 33 mm

## Slide 22: ACCELERATIONS DURING TRANSPORT
https://edms.cern.ch/document/350433/1.0