## Slide 1: Dry Cooling Strategies for Accelerator Components (Cryocooler based cooling stations)
T. Koettig, M. Chioteli, P. Borges de Sousa, A. Onufrena, B. Naydenov, J. Bremer (CERN TE/CRG)
16th April 2024, IFAST Paris

## Slide 2: Contents
Introduction, from liquid bath cooling towards conduction cooled devices
Cryocooler based systems – additional cooling loops
Counter-flow HEXs
Application examples
Summary

## Slide 3: NbTi superconducting magnets in the LHC at CERN
Bath cooled magnets, heat extraction by He II @ 1.9 K pressurised
130 ton minimum He inventory for the LHC incl. detectors, e.g. LHC dipole magnet VHe=28 l/m
Safety in underground installations, complex inventory management, He cost and availability …
In fully immersed magnets the heat generated in the coil-pack must find its way out to the cold-source via helium path-ways kept clear in the cold-mass construct
In the example left, of the LHC main dipole, heat flows from the coil pack into the annular space between beam-pipe and coil-pack and out via space between the collar laminations
Cold-source

## Slide 4: Nb3Sn fully impregnated magnet coils for HL-LHC at CERN
New electrical and thermal insulation scheme for fully epoxy impregnated coil packages
He II cooling via the annular gap between beam tube and coil package, HL-LHC MQXF magnet VHe=30 l/m
Numerical simulation of heat transfer, He II cooling performance, temperature distribution and Temp. margin
Q2B IR1-HC – power dep. @ peak loc.
He II region (connected passages via poles)
Solid region (17 parts)
MQXF v7 + cold mass
(ST0703448)
Numerical assessment

## Slide 5: Dry cooled prototype of a gantry magnet, design
Adapted from G. Ceruti, Weekly Meeting 13 (26 January 2024) · Indico (cern.ch)
Ø 2.8 mm
Ach = 6.2 mm2
Ø 2.4 mm
Ach = 4.5 mm2
Ø 1.2 mm
Ach = 1.1 mm2
28 channels in parallel for two layers of coil (2x14)
Heat load on inner layer ≈ 3 W
Required to extract 3 W between 4.5 K and 4.7 K using He at 3 bara ≈ 3.2 g/s
How does this flow distribute over the 14 parallel branches? (assuming equal length)
What’s the overall pressure drop?
Δp = 1.5 mbar assuming 1.5 m length of circuit
(same at 300 K, 3 bara is ≈ 600 mbar)
Heat transfer coefficients He flow to former
Branch Ø [mm] | 1.2 | 2.4 | 2.8
[g/s] | 0.036 | 0.235 | 0.353
% of total | 1.1% | 7.3% | 11%
Branch Ø [mm] | 1.2 | 2.4 | 2.8
 | 0.036 | 0.235 | 0.353
 | 1.1% | 7.3% | 11%
Stainless steel former, 3D printed incl. cooling channels => Cooling channel size and distribution – inner layer,

## Slide 6: Cryocooler as cooling source
Keeping in mind large scale applications with their distribution system

## Slide 7
Several applications require a cooling capacity of several Watts at 4.5 K → cooling capacity between cryocoolers and cryoplants
Background: remote cooling
Increased cooling capacity + dry, vibration-free, distributed, remote cooling for a number of applications
Remote cooling principle = Cooling source + convection loop
2-stage
cryocooler
40 K
4.5 K
Fluid circulation loop (e.g. with JT restriction)
Cooling technology gap
2.5 W – 350 W at 4.5 K
Map adapted from: L. Decker, “Overview on cryogenic refrigeration cycles for large scale HTS applications”, 2016.

## Slide 8
Cryogenic cooling of IR cameras / spectrometers in space (e.g. NICMOS on Hubble Space Telescope)
Pre-cooling of dilution refrigerators for quantum sensing/computing
→ from 2 integrated PTR to remote PTR box to cryoplant connection
High-tech applications for remote cooling circuits

## Slide 9
Cryogenic cooling of IR cameras / spectrometers in space (e.g. NICMOS on Hubble Space Telescope)
Pre-cooling of dilution refrigerators for quantum sensing/computing
→ from 2 integrated PTR to remote PTR box to cryoplant connection
Next generation of gravitational wave detectors => mirror cooling @ 4 K – 20 K
Cryogenic mirrors of gravitational wave detectors (e.g. KAGRA)
High-tech applications for remote cooling circuits

## Slide 10
Cryogenic cooling of IR cameras / spectrometers in space (e.g. NICMOS on Hubble Space Telescope)
Pre-cooling of dilution refrigerators for quantum sensing/computing
→ from 2 integrated PTR to remote PTR box to cryoplant connection
Next generation of gravitational wave detectors => mirror cooling @ 4 K – 20 K
SC gantries for proton/heavy-ion therapy
Courtesy: L. Gentini
High-tech applications for remote cooling circuits

## Slide 11
Cryogenic cooling of IR cameras / spectrometers in space (e.g. NICMOS on Hubble Space Telescope)
Pre-cooling of dilution refrigerators for quantum sensing/computing
→ from 2 integrated PTR to remote PTR box to cryoplant connection
Next generation of gravitational wave detectors => mirror cooling @ 4 K – 20 K
SC gantries for proton/heavy-ion therapy
SC RF cavities in particle accelerators
High-tech applications for remote cooling circuits

## Slide 12
Cryogenic cooling of IR cameras / spectrometers in space (e.g. NICMOS on Hubble Space Telescope)
Pre-cooling of dilution refrigerators for quantum sensing/computing
→ from 2 integrated PTR to remote PTR box to cryoplant connection
Next generation of gravitational wave detectors => mirror cooling @ 4 K – 20 K
SC gantries for proton/heavy-ion therapy
SC RF cavities in particle accelerators
Cryostats in confined/radioactive environments etc. that require separation of cooling source from CIF
SQUID sensors in anti-proton decelerator at CERN
Equipment in high-radiation CHARM facility at CERN
High-tech applications for remote cooling circuits

## Slide 13: Remote cooling loops
High effectiveness counter-flow heat exchangers (CFHEX)

## Slide 14: Remote cooling arrangements
Pump
Compressor
Cooling interface
1 bar
(LP)
4-5 bar
(HP)
~4-5 bar
Compressor
Pump
Cooling interface
1 bar
(LP)
4-5 bar
(HP)
~1 bar
Compressor
Pump
Cooling interface
1 bar
(LP)
4-5 bar
(HP)
~1 bar
Very effective heat exchangers !!!
Option for SQUID sensor cooling in CERN Antiproton Decelerator
Wound capillary cooling interface
Alternative cooling of superconducting RF cavities for particle accelerators
Cryogenic mirrors of gravitational wave detectors (e.g. KAGRA)

## Slide 15: Transparent-wall concept
Top view
Epoxy wall
Transparent-wall CFHEX during assembly
Compressor
Pump
Cooling interface
1 bar
(LP)
4-5 bar
(HP)
~1 bar
2-stage
GM cryocooler
Stage 1
Stage 2
CFHEX 2
CFHEX 1
CFHEX 3
Joule-Thomson expansion
Careful sizing for operation in the 10 K - 50 K and 4.5 K – 10 K ranges using the numerical model [1]

## Slide 16: Performance: CFHEX effectiveness
NTU=18.6 ( %)
NTU = 55 ( %)
Transparent-wall designs were implemented for the two coldest CFHEXs
Very high experimental performance achieved with the novel transparent-wall design
NTU >124 ( %)

## Slide 17: Application examples

## Slide 18
Applications: dry SRF cavity cooling
Test setup to study dry colling (system performance, flow in the capillary)
Dry cooling principle

## Slide 19: Cavity wall temperature distribution
He two-phase flow (TPF)
x-position [m]
Capillary: 21 loops, spacing 0.75 cm, length 10.57 m, power 2 W
Numerical simulation!
to be validated by the experiments

## Slide 20: Two-phase flow – flow pattern map calculations
Heat loads and mass flow

## Slide 21: Cavity wall temperature distribution
Flow options – a comparison
Capillary: 21 loops, spacing 0.75 cm, length 10.57 m, power 3 W
He two-phase flow (TPF)
x-position [m]
Capillary: 21 loops, spacing 0.75 cm, length 10.57 m, power 2 W
Courtesy: A. Onufrena et al. CEC 2021, IOP Conf. Series: Materials Science and Engineering
Numerical simulation!
to be validated by the experiments

## Slide 22: Optimum cooling tube diameter/length/fluid pressure
Similar heat transfer of TPF and Sup. crit. 3 bar
Quite higher pressure drop of TPF
Pressure drop comparison
Temperature difference tube wall to fluid core
Numerical simulation of friction and heat transfer, a comparison of flow conditions

## Slide 23
Remote cooling loops with boosted performance
Subcooled 4 bar cooling loop
Remarks:
Single phase flow above crit. pressure
Good heat transfer
CryoFan works better at higher pressure (density)
JT cryocooler systems exit in industry e.g. 9 W @ 4.2 K
Subcooled 4 bar cooling loop – high Q
3-4 x
PTC
PTC

## Slide 24
Envisaged dry cooling test stations at the Cryolab at CERN
GM
GM
GM
GM
PTC

## Slide 25: Summary
Dry cooling
    Enables effective cooling of novel magnet, cavity and detector concepts
    Enables stand alone systems with a physical separation between the cooling source and the object
    Small test stations with an emphasis on large scale conditions
    Future developments towards higher Tc materials Nb3Sn on Cu for cavities or HTS magnets => 20 K
Numerical assessment of fluid flow heat transfer and conduction pathway is required:
    Benefits from reliable, experimentally obtained material properties and interface data
    Enables the parametric study of heat transfer mechanisms in large-scale complex structures
    Can be used early on to aid in magnet design w.r.t. heat extraction and safe operating temperatures

## Slide 26: Thank you for your attention!