## Slide 1
Mar Capeans
HOW TO LIMIT THE ENVIRONMENTAL IMPACT
EDMS 2735914

## Slide 2
OUTLINE
CERN Environmental Reports
B. Delille and S. Kleiner, CERN Health, Safety and Environmental Unit, E. Cennini, CERN Industry, Procurement and Knowledge Transfer, N. Bellegarde and S. Claudet, CERN Accelerator & Technology Sector, FCC team, CLIC team, CERN Site and Civil Engineering Department team
ACKNOWLEDGEMENTS
Environmental protection at CERN
Site development
Future
Outlook
Reporting
Targets
Actions
CERN Masterplan 2040

## Slide 3
590 ha (220 fenced)
2 main sites and 15 satellite sites
670 buildings from 10 m2 to 20.000 m2
65% built before the 70’s
70 km tunnels and 80 caverns
30 km roads
1000 km technical galleries and trenches
9000 persons/daily
490 hostel rooms
8500 working places
4300 parking places in Meyrin, 1400 in Prévessin
25000 daily movements to- and inter-sites
Public transport links in CH, not in FR
KEY FIGURES

## Slide 4
Involving the entire organization
  Environment included in CERN’s main objectives for 21-25
  Strong strategic direction from the DG, endorsed by Council and supported by enthusiastic efforts throughout the organization
  Increasing accountability and governance
Generating transparent and reliable reporting
  Materiality assessment and stakeholder review
  Reporting on GHG emissions since 2019, Global Reporting Guidelines (GRI)
Acting
  Setting targets
  Global strategy with objectives and measures that take up the framework objectives and translate them into operational prioritized measures
STRATEGY

## Slide 5
2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Masterplan2040
2019-2020 Environment Report
2017-2018
Environment Report
2021-2022 Environment Report
2023-2024 Environment Report
Environmental Responsible Procurement Policy Project
Materiality analysis
Environmental Noise policy
Environmentally Responsible Procurement Policy
Baseline year
Energy Performance plan
ISO50001 certification
Green Village
Innovation Programme on Environmental Applications
Environmental Protection Steering Board
STRATEGIC ACTIONS
Energy Management Panel

## Slide 6
MATERIALITY

## Slide 7
Purchased electricity
Vehicles
Particle Detectors
Accelerators
Assets
Waste treatment
Water purification
Business Travel
Employee Commuting
Catering
Procurement
SCOPE 1
Direct
SCOPE 2
Indirect
SCOPE 3
Indirect

## Slide 9
GHG Emissions
Reduction by 28%
TARGETS 2025
ENGAGEMENTS
Energy Consumption
Limit raise by 5%
Water Consumption
Limit raise by 5%
Waste
Increase recycling rate
Noise
Restrict
Commuting
Constant
Biodiversity
Protect

## Slide 10
GHG EMISSIONS
Particle detection (gases)
Reduction target ~13’000 tCO2e/year
Detector cooling
Systems using F-gases will be stopped by end of Run3 and replaced by CO2 cooling for Run4
With forecasted reduction ~40’000 tCO2e/year

## Slide 11
SCOPE 2: INDIRECT EMISSIONS

## Slide 12
Technology: PS East area power converters designed to supply the magnets on a cyclical basis, with an energy-recovery stage between each cycle resulting into 90% electricity consumption reduction: (11 to 0.6 GWh/y)
Campus: Building Global renovations for reduction of losses (energy, water, gas, cooling), densifying occupation
Annual Virtual Energy Bills
Energy performance plan & ISO50001
Hot water from LHC cooling system (P8, 2 x 5 MW heat exchangers) to heat up a residential area (20 GWh/y at peak).
Savings up to ~100 GWh/y since 2010
LHC high availability at ~constant energy consumption
SCOPE 2: ACTIONS ON ENERGY CONSUMPTION
INCREASE EFFICIENCY
USE LESS
RECOVER
PCC to heat Prevessin CERN site (3-4 MW)
LHC Cooling towers at P1 to heat Meyrin CERN site (5-10 MW)

## Slide 13
21/03/2022
SCOPE 3: INDIRECT EMISSIONS

## Slide 14
SCOPE 3: ACTIONS
CERN Environmental Responsible Procurement Policy Project (2021)
Courtesy E. Cennini
WHY BUYING
WHAT DO WE BUY
WHO WE BUY FROM
HOW DO WE BUY
Reasoned negotiation
Suppliers’ performance
Respect of commitments
Fair competition
Payment deadline
As user/owner?
Functional approach
KPIs e.g. % recycled
Buy/Partner/Make
Challenge the need!
Eco-design/Life Cycle Analysis
Resource optimization (water/energy)
Total Cost of Ownership (TCO)
Polluting materials?
Carbon footprint?
Social impact?
(Very) Poorly balanced Countries
Labels/Certification
Local purchase/Diversity
Countries/people exposed
Duty of vigilance/Compliance

## Slide 15
Integration of the latest projects
Integration of SPS land and LHC points
Integration of the Development Guide (CH)
Integration of sustainable development
CERN MASTERPLAN2040

## Slide 16
Framework objectives and measures
MASTERPLAN2040

## Slide 17
WATER
NOISE
MASTERPLAN 2040: Environment

## Slide 18
Initial capacity of 4 MW available for IT equipment with stepwise future increases to 12 MW.
To meet CERN's environmental goals the project incorporates the following considerations :
Designed to be energy efficient with a target PUE (Power Usage Efficiency) of 1.10 (1.15 contractual)
Optimised water consumption via a recirculation system lowering consumption in hot periods
All cleared vegetation will be reconsolidated
The acoustic study used for design of the building follows CERN commitments
A heat recovery system is foreseen for up to 25% of power produced to be recovered
Green terrace on the roof
PREVESSIN COMPUTING CENTER

## Slide 19
Eliminate abandoned vehicles (2021)
10 km Cycle paths (2020)
+40% Bike parkings (2022)
2 E-charging stations (2022)
80 E-bikes (2021)
Increased car-sharing (2022)
Optimization of the car fleet (2023)
Modal points at < 5min walk
Mobility Report (2022 and yearly)
STRATEGIC PRINCIPLES
ROADMAP
ACTIONS
Data driven
Targets
KPIs
MOBILITY
Focus on people needs
Integrate transport modes
Adaptable to the future needs of the organization
Sustainable and eco-responsible
Communicate, cooperate with local actors, and involve the community

## Slide 20
TECHNOLOGY & ENVIRONMENT
FROM CERN TO SOCIETY
CIPEA: Developing advanced technologies linked to environment and sustainability
E.g. solar thermal panels derived from vacuum technology; CO2 cooling technology; superconductive power transmission lines and current leads
FROM SOCIETY TO CERN TO SOCIETY
Enabling rapid access to CERN campus as a test site for technologies linked to environment and sustainability
Accelerating the commercialization of ideas, technologies and prototypes
Involving Young Innovators (new ideas for unforeseen applications)
Challenges: waste management, mobility, energy efficiency for tertiary activities on campus, space management, IoT, Zero-waste, urban analytics, …
INNOVATION PROGRAMME ON ENVIROMENTAL APPLICATIONS
GREEN
VILLAGE

## Slide 21
Integration of an “Eco-design” from the first conceptual design phase onwards, balancing Scientific excellence, Territorial compatibility, Implementation and operation
The environmental evaluation process follows “Avoid-Reduce-Compensate”; includes geology, urbanism, society health and safety, technical development and risks…
Iterative co-development with the Host State partners on high-priority topics such as:
  Consumption of resources: land, soil, water
  Limitation of impacts, e.g. re-use of excavated materials, reduction of surface footprints, energy efficient designs, reduction of traffic and nuisances during construction
  Creation of added value, e.g. supply of waste heat, sharing of technical infrastructures (e.g. electricity, telecommunications, water supply and treatment)
FUTURE STUDIES & ENVIRONMENT
FCC
CLIC
Approaches to increase sustainability:
Overall system design
  Compact (short) accelerator -> high gradient
  Energy efficient -> low losses
  Effective -> small beam sizes
Subsystem and component design, e.g.
  High-efficiency klystrons, permanent magnets
  Heat-recovery in tunnel linings
Sustainable operation concepts
  Recycle energy (heat recovery)
  Adapt to regenerative power availability, Exploit energy buffering potential

## Slide 22
SUMMARIZED AMBITIONS
Reduce direct emissions by 28%
ENERGY: limiting rises in electricity consumption to 5%
WATER: increase in water consumption below 5%
Reduce car fleet
Potential reduction ~ 500 tCO2e/y
Reduce professional travel
Sustainable heating plants
Heat recovery from data centre in Prévessin and cooling towers at LHC PA1
Potential reduction ~1’900 tCO2e/y and ~6’000tCO2e/y
CO2-based detector cooling
Potential reduction ~40’000 tCO2e
Control water effluents (FR)
Control water effluents (CH)
Closed/loop and recycling of cooling water from Cooling towers
100% Inventory of CERN areas of biological interests
40’000 m2 new Green Space
40’000 m2 Renovated buildings
Particle detection (gases)
Reduction target ~13’000 tCO2e
2024
2026
2028
2030
2022
2023
2025
2027
2029
2021

## Slide 23
CERN’s strategy with respect to environment and sustainability is based on three lines of action:
  Reduce the laboratory’s impact on the environment with comprehensive CO2 footprint evaluation and commitment to decrease it,
  Reduce energy consumption and increase energy recovery,
  Develop technologies that can help society to preserve the planet.
Actions to reduce environmental impact require long planning, often long-lead execution and RoI; ambition and long-term planning with short-term actions are crucial. A selection of programs for improving existing infrastructures is a way to put into practice the good intentions, and to acquire expertise.
Scientific/research organizations are often ‘special’ but their environment and sustainability challenges are similar; knowledge exchange on carbon accountings and sharing experiences on reduction actions is important.
Future large-scale science projects will need to carefully address energy management and sustainability, e.g. energy efficiency, energy recovery and carbon accounting; at all levels, from design decisions through construction to operation and decommissioning plans.
OUTLOOK
23