## Slide 1: AWAKE RUN 2 Electron injectors
Steffen Doebert, SY-RF

## Slide 2: AWAKE Run 2
Demonstrate possibility to use AWAKE scheme for high energy physics applications in mid-term future!
Accelerate an electron beam to high energy (gradient of 0.5-1GV/m)
Preserve electron beam quality as well as possible (emittance preservation)
Demonstrate scalable plasma source technology (discharge, helicon)
Goals:
  Need to work in blow-out regime and do beam-loading
  New electron beam based on x-band: 150 MeV, 200 fs, 100 pC, σ = 5.75 µm

## Slide 3: Parameters for both injectors
 | Beam Energy | Energy Spread | Energy stability | RMS Bunch Length | Bunch Charge | Emittance | Beam size plasma focus
Injector 1 |  |  | 1 x 10-2 |  |  | 2 - 5 | 
Injector 2 |  |  | 1 x 10-3 |  |  | 2 | 
 | Beam Energy | Energy Spread | Energy stability | RMS Bunch Length | Bunch Charge | Emittance | Beam size plasma focus
Injector 1 |  |  | 1 x 10-2 |  |  |  | 
Injector 2 |  |  | 1 x 10-3 |  |  |  | 
Working documents held by Rebecca (Injector 2, EDMS 2378918) and John (Injector 1, EDMS 2417022,2588263)
Flexibility in the beam parameters which can be delivered keeping good energy spread and emittance Energy: +- 10%, Charge: up to 400 pC, Bunch length: 0.2-1 ps, beam size : see transport
Constraint space for hardware
Excellent timing stability and synchronisation with laser and self-modulation device; ~ 30 fs stability

## Slide 4: Reference design
Very compact electron injector
 | 0.14 |  | 0.44 | 9 | 
 | 0.14 |  | 0.44 |  | 
Parameter | RF Gun | Buncher | Acc. I | Acc. II
Frequency |  |  |  | 
Gradient |  |  |  | 
N. Cell |  |  |  | 
Parameter | RF Gun | Buncher | Acc. I | Acc. II
Frequency |  |  |  | 
Gradient |  |  |  | 
N. Cell |  |  |  | 
262 |  | 1.0 |  | 0.1-1.0
262 |  | 1.0 |  | 0.1-1.0
Laser parameters
RF parameters
Mohsen Dayyani Kelisani

## Slide 5
Awake schematic RF layout
Total Energy 100- 160 MeV, 10 Hz rep. rate, single bunch
Will use CLIC developed x-band components as much as possible
Multiple RF-power configurations studied
Solenoid
X
X
X
X
X
X
X
X
X
X
X
X
X
X
7-10 MW, S-band
5-10 MW, x-band
Possibly long waveguides 30 m
Round or double height WG needed
PC, 160 -200 MW
25 / 50 MW, x-band
3 structures at 55 MV/m
PC, 15 -20 MW
Solenoid
A, j
Klystron layout on the tunnel

## Slide 6
Injector prototype in CTF2 for CLEAR and AWAKE
ARTI (AWAKE Run2 Test Injector)
Reduced scale prototype, 60 MeV, INFN gun, CLIC-structure as buncher and PSI-linearizing structure for acceleration.
Goal: demonstrate the velocity bunching and emittance preservation with x-band Prototyping of key accelerator hardware and diagnostics
Gaining experience before installation in the AWAKE tunnel

## Slide 7
ARTI status
RF-gun (INFN contribution) and diagnostics operational and under commissioning
Magnets for second phase installed
First ‘CLEAR user’ experiment planned in spring: Vlad’s CBS experiment

## Slide 8
Conclusions
Robust baseline design exists, ‘innovative and conventional’ design with very good stability and flexibility in the final parameters, further optimisation for performance, cost and integration are ongoing Strong support from collaborations: INFN, Uppsala, STFC (UK) and of course CLIC / CLEAR
Prototype injector tests: Very good start of the beam commissioning with the rf-gun. Next step: x-band bunching and acceleration, demonstration of emittance and stability
Compact x-band accelerator can be a model for other external injection experiments for plasma accelerators
and compact x-band applications: medical (DEFT), x-ray sources (CBS), neutron sources
Synergy with future electron/positron colliders at CERN including FCC-ee

## Slide 9
Additional material

## Slide 10
Shunt Impedance [MΩ/m] | 100
Group Velocity vg/c [%] | 2.4
Q-Factor | 7061
Attenuation [1/m] | 0.7
Length [m] | 0.9
X-band structure developments
Travelling wave Constant Impedance
Designed by INFN Frascati, D. Alesini, M. Diomede,
for CompactLight and EuPraxia
Mechanical design made at CERN
CLIC style tolerances
Vacuum brazing design
Structure to be inserted in a solenoid of 150 mm diameter bore radius

## Slide 11
First short prototype under construction
Verify mechanical design, brazing assembly and tolerances needed
Maybe low power RF measurements but no high-power test planned
C. Capelli, N. Chritin

## Slide 12
RF-Design made by D. Alesini, M. Diomede, INFN Frascati
Structure to be inserted in a solenoid of 150 mm diameter bore radius
X-band accelerating structure
Mechanical design

## Slide 13: u-TCA LLRF development with Uppsala
System shipped to CERN from Uppsala, installed in the form CLIC test facility.
RF signal acquisition, generation and feedback/forward loops tested.
Use of DESY BSP and python GUI.
External trigger injection through RJ45 connector on SIS8300KU AMC, distributed to mLVDS lines.
  Currently under test/development (still some bugs to iron out)
Work progressing well on a DESYRDL to CERN/Cheby convertor script.
Modulator and S-band 40MW klystron (above)
MicroTCA crate and LO, CLK generators (right)

## Slide 14
Studied alternative scenarios
Beam dynamics:
3 identical structures, one 50 MW klystron  Save small klystron, waveguide run and buncher structure
RF power variants:
One 25 MW klystron for acceleration, small 8 MW klystron for bunching  less expensive klystron and modulator
Only one 25 MW klystron for everything  less expensive klystron, save second waveguide run and small klystron
Integration scenarios:
Keep Run 1 modulator (PPT) for LINAC 1, instead of two K100 modulators  no new hardware needed
Use K400 modulator instead of PPT  better performance and stability
Replace K400 x-band with 2x K200 x-band  essentially staged scenario to upgrade energy later

## Slide 15: Reference design
Mohsen Dayyani Kelisani

## Slide 16
Tentative RUN 2 injector parameter for 150 MeV
Energy: 151.8 MeV
Energy Spread: 144.5 keV rms =9.5 10-4
Emittance: x/y: 0.7 mm mrad
Bunch length: 60 um rms
Bunch Charge: 100 pC
Only scaled down accelerating gradient, identical initial distributions,
no new optimization

## Slide 17
Tentative RUN 2 injector parameter for 150 MeV

## Slide 18
Tentative RUN 2 injector parameter for 150 MeV

## Slide 19
Laser Pulse Duration
Laser Spot Size
3.1 100pC-1000pC
3. High Current Operation
Flexibility to produce higher charge (for lower plasma density or experimental reasons)
Mohsen Dayyani Kelisani
Changing only laser pulse length and adapting magnetic field slightly

## Slide 20
Max_
Bunch Length
Bunch Emittance
Energy Spread
3.1 100pC-1000pC
3. High Current Operation
Mohsen Dayyani Kelisani
Flexibility to produce higher charge 0.1 to 1 nC per bunch

## Slide 21
ARTI in CTF2
Screen BTV1
Spectrometer
F-Cup
RF-GUN
1 us
200 ns
600 ns
800 ns
400 ns
RF-gun conditioned to 120 MV/m on the cathode
Notes: .

## Slide 23
0.9m
0.9m
0.9m
0.8m
1m
Detailed integration studies have been performed