## Slide 1: External electron injection: from electron source to plasma
S. Doebert and V. Bencini for the AWAKE collaboration

## Slide 2: External electron injection: electron sources
S. Doebert

## Slide 3: AWAKE Run 2
Demonstrate possibility to use AWAKE scheme for high energy physics applications in mid-term future!
Accelerate an electron beam to high energy (gradient of 0.5-1GV/m)
Preserve electron beam quality as well as possible (emittance preservation)
Demonstrate scalable plasma source technology (discharge, helicon)
Goals:
  Need to work in blow-out regime and do beam-loading
  New electron beam based on x-band: 150 MeV, 200 fs, 100 pC, σ = 5.75 µm

## Slide 4: Parameters for both injectors
Flexibility in the beam parameters which can be delivered keeping good energy spread and emittance Energy: +- 10%, Charge: up to 400 pC, Bunch length: 0.2-1 ps, beam size : see transport
Constraint space for hardware
Excellent timing stability and synchronisation with laser and self-modulation device; ~ 30 fs stability
 | 18 MeV injector | 150 MeV injector
Beam Energy (MeV) | 18.5 | 150
Energy Spread (ΔE/E0) (%) | 0.50% | 0.20%
Energy stability (ΔE0/E0) | 1 x 10-2 | 1 x 10-3
RMS Bunch Length (ps) | ≈2-3 | ≈0.2-0.3
Bunch Charge (pC) | 100 -600 pC | 100 pC
Emittance (mm mrad) | 2 - 5 | 2
Beam size (µm) | ~ 190 | 5.75

## Slide 5: 150 MeV injector – beam dynamics design
Very compact electron injector
Simulated parameters within specifications
 | 0.14 |  | 0.44 | 9 | 
 | 0.14 |  | 0.44 |  | 
Parameter | RF Gun | Buncher | Acc. I | Acc. II
Frequency |  |  |  | 
Gradient |  |  |  | 
N. Cell |  |  |  | 
Parameter | RF Gun | Buncher | Acc. I | Acc. II
Frequency |  |  |  | 
Gradient |  |  |  | 
N. Cell |  |  |  | 
262 |  | 1.0 |  | 0.1-1.0
262 |  | 1.0 |  | 0.1-1.0
Laser parameters
RF parameters

## Slide 6
Total Energy 100- 160 MeV, 10 Hz rep. rate, single bunch
Will use CLIC developed x-band components as much as possible
Multiple RF-power configurations studied
Solenoid
X
X
X
X
X
X
X
X
X
X
X
X
X
X
7-10 MW, S-band
5-10 MW, x-band
Possibly long waveguides 30 m
Round or double height WG needed
PC, 160 -200 MW
25 / 50 MW, x-band
3 structures at 55 MV/m
PC, 15 -20 MW
Solenoid
A, j
Klystron layout on the tunnel
150 MeV injector – RF layout

## Slide 7
150 MeV injector – Prototype
ARTI (AWAKE Run2 Test Injector)
Reduced scale prototype, 60 MeV, INFN gun, CLIC-structure as buncher and PSI-linearizing structure for acceleration.
Goal: demonstrate the velocity bunching and emittance preservation with x-band Prototyping of key accelerator hardware and diagnostics
Gaining experience before installation in the AWAKE tunnel

## Slide 8
150 MeV injector – Prototype
ARTI (AWAKE Run2 Test Injector) under commissioning at CERN
RF-gun (INFN contribution) and diagnostics operational and under commissioning
Magnets for second phase installed
First ‘CLEAR user’ experiment planned in spring: (Compton Back-Scattering)

## Slide 9
Conclusions /challenges
Robust baseline design exists, ‘conventional’ design with very good stability and flexibility in the final parameters, further optimisation for performance, cost and integration are ongoing Strong support from collaborations: INFN, Uppsala, STFC (UK) and of course CLIC / CLEAR
Prototype injector tests: Very good start of the beam commissioning with the rf-gun. Next step: x-band bunching and acceleration, demonstration of emittance and stability
Compact x-band accelerator can be a model for other external injection experiments for plasma accelerators and compact x-band applications: medical (DEFT), x-ray sources (CBS), neutron sources. Synergy with future electron/positron colliders at CERN

## Slide 10: External electron injection: beam transfer lines
V. Bencini
Notes: Steffen has presented you the results about the electron sources for Run2c, I am going to speak about the tranfser lines needed to transport electron and protons to the plasma.

## Slide 11: Run2c beamlines layout
Run2c foresees several changes in experiment layout and beamlines configuration
Reconfiguration of proton beam transfer line from SPS to AWAKE.
New 150 MeV witness electron beam line for external injection.
Design optimisation needed to match beam target experimental requirements
Reconfiguration of 18 MeV electron seeding beam line.
Notes: - As mentioned by Edda and Patric, the AWAKE experimental layout will be radically modified for Run2c.
- The existing proton and electron beam lines will moved and a brand new 150 MeV line will be added.
-

## Slide 12: 18 MeV seeding line layout
RF gun + acceleration
Run 1,2a/b configuration
Witness electron beamline would be used as seeding line for Run2c.
New layout constrained by AWAKE tunnel geometry.
Beamline design based on existing hardware, setting stability tolerances and beam input parameters.
848.4 m from TT41 entrance
Run 2c configuration
Parameter | Value
Momentum (MeV/c) | 18
Rep. rate (Hz) | 10
Bunch length (ps (mm)) | 4 (1.2)
Relative mom. Spread | 0.5
Emittance r.m.s. norm. (mm mrad) | 2
Notes: The 18 MeV electron line that today serves as witness beam injector will become a seeding line.

## Slide 13: 18 MeV seeding line optics design
 | Specifications | x-plane | y-plane
 | 200 | 193 | 197
 | 2 | 2 | 2
 | 0.0 | 0.0 | 0.0
 | 0.705 | 0.676 | 0.704
 | 0.0 | 0.0 | 0.0
 | Specifications | x-plane | y-plane
 | 200 | 193 | 197
 | 2 | 2 | 2
 | 0.0 | 0.0 | 0.0
 | 0.705 | 0.676 | 0.704
 | 0.0 | 0.0 | 0.0
[1] Bencini, V., et al “Design of the new 18 MeV electron injection line for AWAKE Run2c” (https://cds.cern.ch/record/2886194/files/document.pdf)
Witness electron beamline would be used as seeding line for Run2c.
New layout constrained by AWAKE tunnel geometry.
Beamline design based on existing hardware, setting stability tolerances and beam input parameters.
New design matches beam experimental target requirements [1].
Error study confirms target stability [1].

## Slide 14: 150 MeV line for external injection
 | Specifications | x-plane | y-plane
 | 5.75 | 5.62 | 6.15
 | 60 | 58.96 | 
 | 2 | 2.2 | 2.3
 | 0.0 | 0.0 | 0.0
 | 0.0 | 0.0 | 0.0
 | Specifications | x-plane | y-plane
 | 5.75 | 5.62 | 6.15
 | 60 | 58.96 | 
 | 2 | 2.2 | 2.3
 | 0.0 | 0.0 | 0.0
 | 0.0 | 0.0 | 0.0
New witness electron beamline will be used to perform external injection in second plasma.
  Beam requirements at the forefront of technological state-of-the-art.
  Design involved a combination of advanced numerical optimization techniques. [2]
  Sextupoles and octupoles essential to compensate for high order effects and achieve design parameters.
  Space charge and synchrotron radiation effects considered in simulation. [3]
[2] Ramjiawan, R., et al. "Design and operation of transfer lines for plasma wakefield accelerators using numerical optimizers."
Physical Review Accelerators and Beams 25.10 (2022): 101602. (https://journals.aps.org/prab/abstract/10.1103/PhysRevAccelBeams.25.101602)
[3] Ramjiawan, R., et al. "Design of the proton and electron transfer lines for AWAKE Run 2c." Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 1049 (2023): 168094. (https://www.sciencedirect.com/science/article/pii/S0168900223000840)
Quadrupole
Dipole
Octopule
BPM
Corrector
BTV
Sextupole

## Slide 15: 150 MeV line for external injection
 | Specifications | x-plane | y-plane
 | 5.75 | 5.62 | 6.15
 | 60 | 58.96 | 
 | 2 | 2.2 | 2.3
 | 0.0 | 0.0 | 0.0
 | 0.0 | 0.0 | 0.0
 | Specifications | x-plane | y-plane
 | 5.75 | 5.62 | 6.15
 | 60 | 58.96 | 
 | 2 | 2.2 | 2.3
 | 0.0 | 0.0 | 0.0
 | 0.0 | 0.0 | 0.0
New witness electron beamline will be used to perform external injection in second plasma.
  Beam requirements at the forefront of technological state-of-the-art.
  Design involved a combination of advanced numerical optimization techniques. [2]
  Sextupoles and octupoles essential to compensate for high order effects and achieve design parameters.
  Space charge and synchrotron radiation effects considered in simulation. [3]
[2] Ramjiawan, R., et al. "Design and operation of transfer lines for plasma wakefield accelerators using numerical optimizers."
Physical Review Accelerators and Beams 25.10 (2022): 101602. (https://journals.aps.org/prab/abstract/10.1103/PhysRevAccelBeams.25.101602)
[3] Ramjiawan, R., et al. "Design of the proton and electron transfer lines for AWAKE Run 2c." Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 1049 (2023): 168094. (https://www.sciencedirect.com/science/article/pii/S0168900223000840)
New design matches beam experimental target requirements [2].
Quadrupole
Dipole
Octopule
BPM
Corrector
BTV
Sextupole

## Slide 16: 150 MeV line – Scattering foils
Studied effects of scattering foils potentially needed for integration. [3]
  Plasma simulations (see John’s talk) show that emittance control can be achieved.
  Optimisation to be performed to further improve beam quality for propagation.
 | x-plane | y-plane
 | 17.23 | 17.63
 | 59.96 | 
 | 16.96 | 16.85
 | 0.0 | 0.0
 | 0.0 | 0.0
 | x-plane | y-plane
 | 17.23 | 17.63
 | 59.96 | 
 | 16.96 | 16.85
 | 0.0 | 0.0
 | 0.0 | 0.0
[3] Ramjiawan, R., et al. "Design of the proton and electron transfer lines for AWAKE Run 2c." Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 1049 (2023): 168094. (https://www.sciencedirect.com/science/article/pii/S0168900223000840)

## Slide 17: 150 MeV line – Error studies
Error studies allowed to define tolerances for alignment, field stability and beam diagnostic resolution. [3]
  Hardware (power converters, magnets, vacuum, diagnostics) technical specification were defined and approved by experts.
  Design and procurement phase is ongoing.
Beam Based Alignment (BBA) procedure was developed and tested in simulations.
  BBA allows to compensate for alignment and field errors.
  Beam size at the experiment strongly depends on the alignment of the active elements down to 1 um level.
   possible and done at ATF2 [4] but still rather challenging.
New beamline has high potential for development and testing of Machine Learning methods developed at CERN. [2]
[2] Ramjiawan, R., et al. "Design and operation of transfer lines for plasma wakefield accelerators using numerical optimizers."
Physical Review Accelerators and Beams 25.10 (2022): 101602. (https://journals.aps.org/prab/abstract/10.1103/PhysRevAccelBeams.25.101602)
[3] Ramjiawan, R., et al. "Design of the proton and electron transfer lines for AWAKE Run 2c." Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 1049 (2023): 168094. (https://www.sciencedirect.com/science/article/pii/S0168900223000840)
[4] Seryi, A., et al. "ATF2 commissioning." 23rd Particle Accelerator Conference" PAC09". Triumf Vancouver, 2009.

## Slide 18: Proton injection
New experimental layout requires reconfiguration of proton transfer line
  Plasma cell position will be shifted of 40 m
  Design relies on existing magnets, to be re-organized to fit the new layout
 | Specifications | x-plane | y-plane
 | 200 | 200.6 | 200.1
 | 4.9 | 4.9 | 4.9
 | 0.0 | 0.0 | 0.0
 | 0.0 | 0.0 | 0.0
 | Specifications | x-plane | y-plane
 | 200 | 200.6 | 200.1
 | 4.9 | 4.9 | 4.9
 | 0.0 | 0.0 | 0.0
 | 0.0 | 0.0 | 0.0
[3] Ramjiawan, R., et al. "Design of the proton and electron transfer lines for AWAKE Run 2c." Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 1049 (2023): 168094. (https://www.sciencedirect.com/science/article/pii/S0168900223000840)

## Slide 19: Proton injection
New experimental layout requires reconfiguration of proton transfer line
  Plasma cell position will be shifted of 40 m
  Design relies on existing magnets, to be re-organized to fit the new layout
 | Specifications | x-plane | y-plane
 | 200 | 200.6 | 200.1
 | 4.9 | 4.9 | 4.9
 | 0.0 | 0.0 | 0.0
 | 0.0 | 0.0 | 0.0
 | Specifications | x-plane | y-plane
 | 200 | 200.6 | 200.1
 | 4.9 | 4.9 | 4.9
 | 0.0 | 0.0 | 0.0
 | 0.0 | 0.0 | 0.0
[3] Ramjiawan, R., et al. "Design of the proton and electron transfer lines for AWAKE Run 2c." Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 1049 (2023): 168094. (https://www.sciencedirect.com/science/article/pii/S0168900223000840)
New design matches beam parameters experimental target requirements [3].
Beam jitter is presently the only parameter above threshold.

## Slide 20: Proton beam jitter
Beam jitter is mainly caused by ripple in proton beam line power converters.
  A relative distance between the p+ and e- beams at injection lower than ≈10 um is needed for emittance control.
  Beam jitter for Run2c can only be estimated from measurements taken in the current configuration and simulations  Relies on several assumptions

## Slide 21: Proton beam jitter
Beam jitter is mainly caused by ripple in proton beam line power converters.
  A relative distance between the p+ and e- beams at injection lower than ≈10 um is needed for emittance control.
  Beam jitter for Run2c can only be estimated from measurements taken in the current configuration and simulations  Relies on several assumptions
  Assuming the same power converters presently in operation, beam jitter would result in ≈10% shots within experimental requirements.
Run2a/b

## Slide 22: Proton beam jitter
Beam jitter is mainly caused by ripple in proton beam line power converters.
  A relative distance between the p+ and e- beams at injection lower than ≈10 um is needed for emittance control.
  Beam jitter for Run2c can only be estimated from measurements taken in the current configuration and simulations  Relies on several assumptions
  Assuming the same power converters presently in operation, beam jitter would result in ≈10% shots within experimental requirements.
  During LS3 most power converters on the proton transfer line will be upgraded (class 3 [5]). Upgrade anyway planned for SPS extraction.
  The upgrade should result in an increase of shots within requirements to ≈30% (Assuming all power converters fall in Class 3 specs).
  Additional improvements in hardware could lead to a further decrease in beam jitter.
Run2a/b
Run2c/d
[5] Gamba, Davide, et al. Beam dynamics requirements for HL–LHC electrical circuits. No. CERN-ACC-2017-0101. 2017.

## Slide 23: Summary and conclusions
A comprehensive simulation study demonstrated the feasibility of delivering electron and proton beams conforming to Run2c specifications (except for proton beam jitter).
Hardware components for all beamlines are already procured (18 MeV and proton line) or in design phase (150 MeV line).
Leveraging CERN's know-how and expertise have been and are crucial at every stage to ensure adherence to specifications and timely delivery.
The knowledge and expertise acquired in the design and operation of electron beamlines are aligned with several CERN projects and initiatives (FCC, CLEAR) and is propaedeutic to other developments (Machine Learning).
The technological advancement arising from the effort to meet the tight experimental parameters (high stability, small beam size) impact the whole plasma accelerator community.

## Slide 24: Backup slides

## Slide 25
RF-Design made by D. Alesini, M. Diomede, INFN Frascati
Structure to be inserted in a solenoid of 150 mm diameter bore radius
X-band accelerating structure
Mechanical design

## Slide 26: u-TCA LLRF development with Uppsala
System shipped to CERN from Uppsala, installed in the form CLIC test facility.
RF signal acquisition, generation and feedback/forward loops tested.
Use of DESY BSP and python GUI.
External trigger injection through RJ45 connector on SIS8300KU AMC, distributed to mLVDS lines.
  Currently under test/development (still some bugs to iron out)
Work progressing well on a DESYRDL to CERN/Cheby convertor script.
Modulator and S-band 40MW klystron (above)
MicroTCA crate and LO, CLK generators (right)

## Slide 27
Studied alternative scenarios
Beam dynamics:
3 identical structures, one 50 MW klystron  Save small klystron, waveguide run and buncher structure
RF power variants:
One 25 MW klystron for acceleration, small 8 MW klystron for bunching  less expensive klystron and modulator
Only one 25 MW klystron for everything  less expensive klystron, save second waveguide run and small klystron
Integration scenarios:
Keep Run 1 modulator (PPT) for LINAC 1, instead of two K100 modulators  no new hardware needed
Use K400 modulator instead of PPT  better performance and stability
Replace K400 x-band with 2x K200 x-band  essentially staged scenario to upgrade energy later

## Slide 28: Reference design
Mohsen Dayyani Kelisani

## Slide 29
Tentative RUN 2 injector parameter for 150 MeV
Energy: 151.8 MeV
Energy Spread: 144.5 keV rms =9.5 10-4
Emittance: x/y: 0.7 mm mrad
Bunch length: 60 um rms
Bunch Charge: 100 pC
Only scaled down accelerating gradient, identical initial distributions,
no new optimization

## Slide 30
Tentative RUN 2 injector parameter for 150 MeV

## Slide 31
Tentative RUN 2 injector parameter for 150 MeV

## Slide 32
Laser Pulse Duration
Laser Spot Size
3.1 100pC-1000pC
3. High Current Operation
Flexibility to produce higher charge (for lower plasma density or experimental reasons)
Mohsen Dayyani Kelisani
Changing only laser pulse length and adapting magnetic field slightly

## Slide 33
Max_
Bunch Length
Bunch Emittance
Energy Spread
3.1 100pC-1000pC
3. High Current Operation
Mohsen Dayyani Kelisani
Flexibility to produce higher charge 0.1 to 1 nC per bunch

## Slide 34
ARTI in CTF2
Screen BTV1
Spectrometer
F-Cup
RF-GUN
1 us
200 ns
600 ns
800 ns
400 ns
RF-gun conditioned to 120 MV/m on the cathode
Notes: .

## Slide 36
0.9m
0.9m
0.9m
0.8m
1m
Detailed integration studies have been performed

## Slide 37: 18 MeV seeding line – error studies
[1] Bencini, V., et al “Design of the new 18 MeV electron injection line for AWAKE Run2c” (https://cds.cern.ch/record/2886194/files/document.pdf)
Output of the study was used to set preliminary tolerances on the injection jitter:
Position jitter:
Angular jitter:
Momentum jitter:
RMS beam jitter at plasma merge resulting from running 1000 errors seeds sampled form normal distribution with tolerances as std. dev.

## Slide 38: 18 MeV seeding line – error studies
[1] Bencini, V., et al “Design of the new 18 MeV electron injection line for AWAKE Run2c” (https://cds.cern.ch/record/2886194/files/document.pdf)
Scan of input beam Twiss parameters to assess effect on beam parameters at plasma merge.
Two figures of merit defined to assess the mismatch at plasma merge:
  : relative percentage error w.r.t. nominal beam size.
  : waste position w.r.t to nominal case (plasma merge).
Results of the scan of the input Twiss and . (a) and (b) show the relative output beam size changein x and y respectively. In (c) and (d) the change in focal point position w.r.t the nominal case is shown.
a)
b)
c)
d)

## Slide 39: 150 MeV line
The first version of the design was finalized by R. Ramjiawan, and the main results are summarized in a paper presently under review*.
Frist step:
  Use genetic algorithms to optimize quadrupoles positions and strengths
  The beam sizes specification were not achieved due to chromatic effects
*Preprint on Arxiv: “Design of the AWAKE Run 2c transfer lines using numerical optimizers” (https://arxiv.org/abs/2203.01605)

## Slide 40: 150 MeV line
In order to compensate for chromatic contributions to beam sizes sextupoles were added
Octupoles were finally added to mitigate detuning with amplitude effects
At each stage a combination of different optimization algorithms was used (Powell, Nelder Mead)
Reached specifications and set baseline design
 | Specifications | x-plane | y-plane
 | 5.75 | 5.97 | 6.11
 | 60 | 59.87 | 
 | 4.8 | 4.82 | 5.41
 | 0.0 | 0.0 | 0.0
 | 0.0 | 0.0 | 0.0
 | Specifications | x-plane | y-plane
 | 5.75 | 5.97 | 6.11
 | 60 | 59.87 | 
 | 4.8 | 4.82 | 5.41
 | 0.0 | 0.0 | 0.0
 | 0.0 | 0.0 | 0.0

## Slide 41: Tolerance studies
Effect of single error type on beam size was used to define tolerances (R. Ramjiawan paper)
Then alignment procedure was optimized to correct for all errors together
Goals
Beam size within
Relative beam offset between e- and p+ beam <
R.M.S of errors used in simulation
BPM resolution:
BTV resolution:
Magnet mover error:
Corrector error:
Initial magnet offsets: r.m.s
e-line power converter ripples = 7 ppm
Momentum jitter = 1e-3
e-line input position jitter = 10 µm

## Slide 42: Alignment procedure
Quadrupole, sextupoles and octupoles need to be installed on movers to reach beam pointing specifications
Three techniques used for alignment
Minimize parasitic dispersion and orbit
Change beam energy
Record the change in position at the BPM
Use corrector to steer the beam trough the quadrupole
Numerical optimization
Use optimization algorithms to align sextupoles and octupoles
Minimize beam size at injection point
Use algorithm that requires low number of function evaluations (BOBYQA)
Centre quadrupoles w.r.t beam orbit.
Change quad strength and record change in BPM reading
Calculate quad-beam position shift
Move quadrupole of -
Quadrupole shunting
Dispersion free steering
Numerical optimization
Alignment procedure consists of a combination of iterations of ①+②+③ (less than 1 hour time)
①
②
③

## Slide 43: 150 MeV line
Error studies defined tolerances for alignment, field stability and diagnostic elements resolution.
Alignment procedure developed and tested in simulations show capability of the system of getting:
  Beam within specs in 95% of cases (1 alignment run)
  Beam within specs in 100% of cases (2 alignment runs)
Technical specifications defined and approved by experts.
Design and procurement is ongoing.

## Slide 44: Proton line
Chicane has t be modified to account for presence of laser mirror.

## Slide 45: Proton beam jitter
The analysis was carried out in three stages:
  Measure power converters ripple and beam jitter in present configuration.
BTV images
BPMs trajectory fit

## Slide 46: Proton beam jitter
The analysis was carried out in three stages:
  Measure power converters ripple and beam jitter in present configuration.
  Find sources of jitter at plasma.
  Perform optics simulations to estimate jitter in Run2c configuration
BTV images
BPMs trajectory fit

## Slide 47: Proton beam jitter
The methodology was tested in simulations
The beam position at every BPM along the line can be expressed as
Unknowns
We want to find

## Slide 48: Proton beam jitter
BPMs resolution is too low to resolve the beam jitter we expect at injection
To overcome this limit trajectory fit technique is applied
Simulation

## Slide 49: Proton beam jitter
Extending the prediction to BTVs and comparing to measurements we find good agreement
The measured jitter can be relied.

## Slide 50: Model Independent Analysis
MIA consists in applying SVD to BPM measurements.
This allows to identifies the main sources of jitter
It produces eigenvectors that allows to identify the sources of jitter by comparison with simulations
 We can apply it to the trajectory fits, which naturally filter out the bpm resolution error
1
2
3
1
2
3

## Slide 51: Model Independent Analysis
x’ = 10 urad
mbg = 100 ppm
mbsg = 100 ppm
We can simulate the effect of different jitter sources and look at the corresponding modes shape.
Optimize sources to find best agreement with measurements
y’ = 10 urad

## Slide 52: Model Independent Analysis
We can simulate the effect of different jitter sources and look at the corresponding modes shape.
Optimize sources to find best agreement with measurements

## Slide 53: Model Independent Analysis
We can simulate the effect of different jitter sources and look at the corresponding modes shape.
Optimize sources to find best agreement with measurements
In y, we hit resolution limit of trajectory fit. We tune simulations to fit BTV measurments

## Slide 54: Propagation in Run2c layout
With the obtained settings for simulations, we can now propagate the simulations to Run2c configuration
Run2a/b
Run2c/d