## Slide 1: CIBDS FMECA
BISv2 Reliability Study Progress Meetings

## Slide 2: Project statistics
Total of 794 components
  Capacitors and resistors in total make up almost 80%
    Average failure rate of 1.8 FITS
  23 transistors
    Failure rate doubled if dual
  Critical component: FPGA
    Failure rate of 11 FITS assumed universally to each critical failure mode

## Slide 3: Failure rates across various design pages Total: 2,788 FITS

## Slide 4: Breakdown of end-effect options
Blind failure
  Blind
  Blind synchronous (only synchronous request sent)
  Blind asynchronous – never used
Link mode
  Blind sent external
  Blind generate external
False dumps
  Asynchronous false dump in local
  Asynchronous false dump
  False dump synchronous
  False dump
Maintenance
merged
1 in 1,000 years
1 in a year
1 in 10 years
1 in a year

## Slide 5
Chart: 
| No Effect | Maintenance | False dump ASYNC LOCAL | Blind SYNC | Blind GENERATE (Link Mode) | Blind SENT (Link Mode) | False dump ASYNC | False dump SYNC | Blind
FITS | 981 | 980 | 22.5 | 39.5 | 13.6 | 22.5 | 45.4 | 668 | 15.5

## Slide 6: Blind failures Total: 15.5 FITS
Contributing components:
OSC1, Oscillator; Parameter change 7.8 FITS (α 100%) x2
Previously in this category:
IC32, Artix-7 FPGA; Short 11 FITS (α 100%)
  ONLY with additional factors (see comment) – 1st order failure: blind sync
if short between SFP RX/TX pins (pins next to each other) -> blind sync + short between pulse to TDU and GND -> blind async
FPGA wouldn't meet timing requirements, could potentially lead to a blind failure
“
“
Notes: FIDES: 2.4 – 3.5 FITS (depends on description options – quality-wise meets the highest categories)
OSC1 7.76 FITS – IQD document (private communications)

## Slide 7: Blind Sync – missing asynchronous request Total: 39.5 FITS
Contributing components:
IC19, MOSFET Drivers; open, short 2 x 1.4 = 2.8 FITS
IC17, Optocoupler; diode/transistor stuck close/short, short from diode 2.3 FITS
IC29, Buffer; Open, short, stuck low 0.7 FITS
IC32, Artix-7 FPGA; Short 11 FITS (α 100%)
And: two resistors, a capacitor and an AND gate (all below 1 FITS).
if considered in local mode, probably not true because feedback to TSU is checked I suppose
“

## Slide 8: Blind Link mode Total: 36.1 FITS
Contributing components:
IC32 Artix-7 FPGA; Stuck low: 11 FITS (α 100%)
IC38 Spartan-7 FPGA; Stuck low: 11 FITS (α 100%)
IC56 Single Buffer Gate; Short, open, stuck low: 0.7 FITS (α 50%)
IC20 RS-485 Transceiver; Open, stuck low: 0.4 FITS (α 27%)
IC21 RS-485 Transceiver; Open: 0.24 FITS (α 17%)
R142 Resistor; Open: 0.22 FITS (α 30%)

## Slide 9: False dump – asynchronous Total: 45.4 FITS
Contributors:
IC32 Artix-7 FPGA; open, stuck high: 22 FITS (α 100%)
ZD1 TVS Diode; short: 3.4 FITS (α 80%)
IC17 Optocoupler; diode or transistor stuck open: 2.9 FITS (α 50%)
LM1 Elbow socket; open, poor contact, short: 2 FITS (α 100%)
D9 High-speed switching diodes; short: 1.8 FITS (α 80%)
Remaining: gates, diodes, buffer, resistors, capacitor and ferrite bead contribute less than 1 FITS each.
All (aside from the FPGA) are in CP Front Panel IO page.

## Slide 10: False dump – synchronous Total: 668 FITS
Top contributors: OSC5 (Monitor FPGA), T15 Dual N-Channel Transistor (Power Management), IC28 FPGA (Monitor FPGA), OSC1 (ARTIX_7_FPGA_IO), IC42 IC43 IC44 (Power Management), ICTX1 and ICRX1Translators

## Slide 11: Behaviour under short of decoupling capacitors?
Saw in uQDS project, that decoupling capacitor shorts (even partial & intermittent) can cause uncontrolled outputs on FPGA level
  Is it clear how CIBDS FPGA will behave under such circumstances (cannot really find answer in documentation - https://docs.amd.com/v/u/en-US/ug483_7Series_PCB ) ?
  For uQDS it is an IGLOO FPGA, where brown-out detection is required - https://onlinedocs.microchip.com/pr/GUID-2952C8AA-A592-489E-8058-3FD06065EDDB-en-US-2/index.html?GUID-F5331690-5A67-4B65-8B6F-4EBF72A08AD6
“In many failure modes (shorts between VCC and GND for example), we would only have a false dump sync, without the asynchronous dump request. This would happen in both A and B paths simultaneously, because they are shared on the same board. The BIS post mortem analysis checks that each synchronous dump is followed by an asynchronous dump request (arriving with a longer latency). So I think it could potentially happen once, but we wouldn’t be able to refill the machine (or even access the CIBDS) afterwards.”

## Slide 12: Maintenance Total: 980 FITS

## Slide 13: Conclusions
Takeaways for the global model
  Blind failures: 15.5 FITS
    Attributed to a single failure mode of an oscillator
  False beam dumps:
    Asynchronous: 45.4 FITS
    Synchronous: 668 FITS
  Link mode malfunction: 36.1 FITS