## Slide 1: Taskforce for common SoC framework in ATS: report
08/02/2024 – BI Technical Board

## Slide 2: SoC Definition
System-on-Chip
in the scope of this initiative, we define SoC an integrated circuit containing a CPU or a multi-processor system, memory interfaces, input/output devices interfaces and FPGA-like programmable logic

## Slide 3: Example: Xilinx Zynq US+ MPSoC
Processing System
Programmable Logic
Application Processing Unit
Multi Arm Cortex-A53
Real-Time Processing Unit
Multi Arm Cortex-R5
Connectivity
Memory Controller
DDR4/3 Support
High-speed
USB3.0, SATA 3.0, PCIe Gen2…
General
GigE, UART, SPI, SD/eMMC…
General-Purpose I/O
FPGA fabric
Logic elements
DSP
BlockRAM
Connectivity
100G Ethernet MAC
PCIe Gen4…
ADCs
DACs
Example: Xilinx Zynq US+ RFSoC
Notes: First of all, the chip has a Processing System block,
that includes 4 Application Processing Units
And 2 Real Time Processing Units.
the RFSoC has also a Programmable Logic block,
connected to the Processing System
And which has FPGA fabric for the implementation of custom logic.
Part of the Programmable Logic block are also the RF components, that are up to 16 high sampling rate ADC
And up to 16 DAC. Speed and number of components depend on the chip generation and type.
Finally, both the Processing System and the Programmable Logic are largely equipped with peripherals and connectivity options.

## Slide 4: Taskforce for SoC Framework (from 31st CTTB)
Goal
  Starting from the current SoC applications in ATS and future needs identify a generic architecture, common services and a proper integration in the accelerator control system to converge towards a common SoC framework
Scope
  All the ATS SoC applications and users in radiation free environment
  Rad-Tol DI/OT SoC and QDS FPGA + uC out of scope
Timeline
  Intermediate reporting at 34th CTTB (24/11/2023)
  Final reporting at 36th CTTB January 2024

## Slide 5: Taskforce for SoC Framework (from 31st CTTB)
Deliverables
  Inventory of the existing SoC applications and future (LS3) needs within ATS
  Identification of commonalities and their potential to converge to a common solution:
    SoC family/families standardisation
    SoC architecture and reference design (i.e. PS/PL generic gateware interfaces)
    Common services (i.e. Diagnostics / monitoring / configuration services, safe booting, RT environment for user defined tasks)
    Embedded Linux support
    Proper integration in the accelerator control system:
      FEC like support vs FEC-PS additional communication layer
      Availability of special services (i.e. Post-mortem, timing)
    High bandwidth data link
    Standardised workflows
    Generic framework to easy the programming and exploitation of the SoC architecture
  Strategy and roadmap towards a common and unified solution with identification of domains for collaboration
  Estimation of resources, timeline, risk and return on investment for the proposed strategy

## Slide 6: Inventory of SoC applications
Summary from ATS SoC Taskforce mid-report to the CTTB

## Slide 7: Inventory
ATS
BE
SY
TE
EN
ABT
AR
BI
EPC
RF
STI
HDO
ABP
ASR
CEM
CSS
EA
GM
ICS
OP
CRG
MPE
PE
MI
EP
MSC
LMF
VSC
VSM
ICM
AA
ACE
CV
EL
HDO
HE
IM
MME
PAS
Omitted (not relevant)
No SoC projects
SoC projects identified
+ HSE

## Slide 8: Inventory
# | Group | Project | Survey
1 | SY-ABT | DKFC | Yes
2 | SY-ABT | FIDS | Yes
3 | SY-BI | HL-LHC BPM / AWAKE | Yes
4 | SY-BI | LHC BPM Cons | Yes
5 | SY-BI | BIPXL Readout | Yes
6 | SY-BI | MIM | Pending
7 | SY-BI | MCOI | Yes
8 | SY-EPC | FGC4 | Yes
9 | SY-RF | - (FBM section) | Comments [1]
10 | SY-RF | SPS RF Beam Control | Yes
11 | BE-CEM | FSI | Yes
12 | BE-CEM | Sambuca | Yes
13 | BE-CEM | Sambuca Motor Driver | Yes
14 | BE-CEM | White Rabbit WREN | Yes
15 | BE-CEM | White Rabbit WRS | Yes
16 | TE-MSC | New MSC platform | Yes
17 | HSE | CROME | Yes
Notes:
[1] Will use AMD Zynq UltraScale+ RFSoC and uTCA architecture.
Chart: 17 SoC projects 15 surveys were received
| SY-BI | BE-CEM | SY-ABT | SY-EPC | SY-RF | TE-MSC | HSE
13 surveys were received | 5 | 5 | 2 | 1 | 2 | 1 | 1

## Slide 9: Estimated number of SoC
Chart: Project sizes (over their lifetime)
| Small (<50) | Middle (<400) | Large (>400)
Sizes | 6 | 3 | 4
1000
1000
600
3
14
25
28
35
40
100
100
100
In total
3500+ SoC
500

## Slide 10: Status and deadlines
Most projects target LS3 for deployment
LS3 confirmed as time horizon for the ATS SoC Common framework
Chart: Deployment deadlines
| Already deployed | Early 2024 | LS3 | LS4 | None yet
Series 1 | 4 | 1 | 9 | 1 | 1

## Slide 11: SoC vendor and family
All projects on AMD Xilinx SoCs
Chart: SoC vendor
| AMD Xilinx
AMD Xilinx | 13
Chart: SoC family
| Zynq Ultrascale+ MPSoC | Zynq 7000 | Zynq Ultrascale+ RFSoC
Series 1 | 10 | 2 | 1
Column1
Most of projects using US+ MPSoC (or planning to)
1-2 RFSoC projects, SoC with same Processing System cores as US+ MPSoC (identical from the software stack point of view)
Xilinx Zynq US+ family candidate for common framework support

## Slide 12: Software and Operating System
Some real-time software:
All bare-metal code (no RT OS)
Support for integration between bare-metal/real-time code with OS is an asset for a common framework
Chart: Do you run real-time software?
| TBD | No | Yes
TBD | 1 | 0 | 0
Bare-metal APU | 0 | 0 | 3
Bare-metal RPU | 0 | 0 | 1
Bare-metal RPU/soft-core | 0 | 0 | 1
No | 0 | 7 | 0
Operating System for Application Processing Unit:
All projects using an OS in their APU interested in adopting FEC-OS
  FEC-OS on SoC: supported by DI/OT framework, same distribution as for new FEC model
  All projects share or might upgrade to same Processing System (ARM Cortex-A53 core based)
  Potential alignment between SoC Common framework and new FEC model

## Slide 13: Integration with accelerator control system
Chart: 
| SoC as HW module of FEC | SoC in the TN
SoC as FEC | 0 | 8
SoC in HSE SCADA | 0 | 1
SoC as node in FEC network | 0 | 1
HW | 3 | 0
FEC-OS  FEC-like services libraries potentially available to SoCs if required
  Configuration, databases, layout
  FESA, or other FEC SW frameworks
  Drivers (EDGE)
  System monitoring and diagnostics
  Network booting with fall-back strategy
  CMW/RDA
  Post-mortem
  Remote console and tools
  General Machine Timing
SoC as HW modules (no OS):
Integration through FEC
SPEXI7U model, RF uTCA systems

## Slide 14: Programmable Logic – Sharing resources
Bus: AXI and Wishbone
IP integration: combination of TCL scripting and graphical block design for most
DMA: mainly application specific use
  Common use case: PS DDR memory – Linux driver
  PL controlled DMA
Others:
  Common gw-sw co-simulation framework
  CI support
  Cheby with EDGE compatibility
  Partial reconfiguration
  Fast data link
VHDL
(8)
SystemVerilog
(5)
HLS
(1)
SystemVerilog
Testbench (1)
(1)
HDL

## Slide 15: Hardware platforms – out of scope
General interest for common hardware solutions
  Few projects designing custom SoC PCBs (WR, FIDS, Sambuca)
  Several projects in the eco-system of DI/OT
  Large interest into generic-purpose System-on-Module (SoM) with application specific carriers
Hardware standardization facilitates framework standardization
Opportunities for shared procurement and step-pricing (sought for/already in place)

## Slide 16: List of libraries, services and contacts identified
OS, sysadmin (BE-CSS-ISA, BE-CEM-EDL)
  Thomas Oulevey, Federico Vaga, N. Tsipinakis
Technical Network (IT-CS-NE)
  Carles Kishimoto, David Gutierrez Rueda
Diagnostics and monitoring (BE-CSS-ISA)
  Frank Locci
Configuration database (BE-CSS-CSA)
  Lukasz Burdzanowski, Bartek Urbaniec
EDGE (BE-CEM-EDL)
  Michel Arruat
Timing (BE-CSS, BE-CEM)
  Greg Kruk and others
FESA (BE-CSS-FST)
  Frederic Hoguin
CMW/RDA (BE-CSS-CPA)
  Wojciech Sliwinski
Post-mortem (TE-MPE-CB)
  M. A. Galilee, J.C. Garnier, G. E. Sanchez
Infrastructure (BE-CEM-IN)
  Ioan Koszar

## Slide 17: Recommendation (WIP)
Extract from the wiki

## Slide 18: Hardware
Vendor | AMD Xilinx | 
SoC model | Zynq Ultrascale+ XCZU17EG-1FFVC1760E (WR & DI/OT) | Zynq Ultrascale+
Reference PCB design | DI/OT System Board v3 (schematic sheets of main building blocks and hardware solutions) | 
For this family of SoCs we intend to ask for the support of the full software stack, FEC like

## Slide 19: Booting
Bootloader | U-Boot + GRUB (FEC-OS) | 
Booting source | Network | Flash memory
Booting fallback source | Flash memory (Golden image) | 
Fail-over mechanism | DI/OT example (part of PCB reference design) | 

## Slide 20: Low level software
Operating system | Linux, Debian (FEC-OS) | 
Drivers' development | EDGE | UIO
RPU - APU hypervisor | OpenAMP (Xilinx tool, no CERN support) | 
A53 baremetal - OS hypervisor | Bmboot (CERN tool) | 
Hard-real-time code | On bare-metal or logic (no RT-patches) | 
Kernel support to be discussed. Availability of flexible recipe to cover also exotic SoCs (32 bit included), with kernel maintenance under responsibility of the project. We are discussing maintenance of a single kernel supported for UltraScale+ by sysadmin, with overlays for each specific applications under the project responsibility. Warning: it comes with development environment version constraints.

## Slide 21: Low level software
For EDGE we intend to ask for memory map driver implementation (high priority), interrupts to be covered in the future, DMA not foreseen at the moment.
Operating system | Linux, Debian (FEC-OS) | 
Drivers' development | EDGE | UIO
RPU - APU hypervisor | OpenAMP (Xilinx tool, no CERN support) | 
A53 baremetal - OS hypervisor | Bmboot (CERN tool) | 
Hard-real-time code | On bare-metal or logic (no RT-patches) | 

## Slide 22: High level software
External monitoring | Same solution as future FECs | 
Internal monitoring | DIOT library (generalized) | 
Time synchronization | NTP | White Rabbit, PTP
Application framework | FESA (including Post-mortem) | 

## Slide 23: Common software blocks and strategies
DI/OT utils: command line interface to the DI/OT monitoring library. It allows for reading local monitoring values as well as reading the configuration of the crate or executing power-cycle command.
Debian packages: For the distribution and version management of the software tools, firmware and FPGA bitstreams we recommend using Debian packages (in-line with the phase 2 of the FEC-OS project). Will require establishing a central repository for Debian packages. Once this is in place, the installation and updates of different software packages or firmware will be done through a standard Debian "apt" command.
Anyway > SoCs connected to the TN, will have NFS mounted and the users can continue to distribute their software update via NFS (as it is done today for FECs). For the time being, FESA will support only this mode.
DMA driver: First option u-dma-buf (standard driver, no CERN support), EDGE to be defined

## Slide 24: Common gateware blocks and strategies
Push toward sharing and reusability of gateware modules:
  Strong recommendation towards CERN accessible repositories
  Collection of pointers to repositories in SoC applications inventory (Wiki at the moment)
  Shared IP repository: starting from CEM-EPC shared repo for DI/OT, following Electronics Forum initiative
  AXI and wishbone buses
  Reference project + Board Support Packages for DI/OT based reference schematics
Possible common interest modules under investigation:
  High bandwidth data transfer module to DDR Memory controller, controlled by PL (meeting tomorrow)
  Fast data link over 10Gb Ethernet: CMS TCP/IP candidate
Development tools:
  Cheby for memory map generation and EDGE tools integration
  Guidelines on sw-gw co-simulation based on QEMU and Questa
  Continuous Integration guidelines and infrastructure (following Electronics Forum initiative)

## Slide 25: CERN Control System Integration
Communication | RDA/CMW (within FESA) | 
Timing | RDA/CMW (XTIM or equivalent for CT events, Dedicated LTIM class for derived events) | WR timing card (PCI) (no SoC driver support foreseen atm)
Configuration storage | CCDB | 
Monitoring | COSMOS | 
Start-up services | LUMENS | 

## Slide 26: Impact on resources (WIP)
Feedback from control groups and experienced equipment groups

## Slide 27: CMW/FESA support
Cost of preparing these services to be production ready:
  Testbed crate with system board and SoC (DI/OT): 4K CHF
  Update and consolidation of CMW integration tests, moving them from Jenkins to the GitLab CI, with a possibility to run them on a normal FEC and on SoC: 3PM
  Adaptation of FESA framework to the new timing library (White Rabbit Timing compatible) – needs to be done anyway for WRT: 2PM
  Timing library implementation based on XTIM (including XTIM modifications): 3PM
  Timing library implementation based on SoC LTIM (if need be): 3PM
  Updating FESA integration tests to work with the new event sources for SoC (XTIM/LTIM): 1PM
  [optional] Use this as an occasion to migrate FESA fwk tests from Jenkins to GitLab: 6PM
Overall additional cost: 4K CHF + 10PM + 6PM [optional for FESA tests migration from Jenkins to GitLab]

## Slide 28: CMW/FESA support
Feasibility of preparing these services to be production ready in 2024:
  Without additional resources not much could be done this year. The plate is full for CMW, FESA and Timing teams
  Adapting FESA to the new Timing library will be done as it is already planned anyway
  With a skilled resource (not a TS), the work could be significantly advanced (but not finished) in 2024 – depending on when the new resource would join
Long-term support cost for SoC:
  2-3PM / year of additional support from 2025 till the end of LS3
  Today it’s around 2PM / year
  Half or more are expected to not be FESA/CMW/Timing issues but our teams will be contacted for help/diagnostics/debugging
  After LS3 we expect the support to stabilize and go down to 2PM / year overall

## Slide 29: COSMOS and LUMENS (CSS/ISA)
75% is already working on Debian FEC
Standard Debian FEC:
  Left-over review and validation: CSS/ISA (< 5d FTE)
SoC adaptation:
  Setup and integration checks: CSS/ISA (< 3d FTE)
  Setup Prometheus service: SoC team + CSS/ISA (<3d FTE)
  SoC checks implementation + Grafana dashboard: SoC team (~1w FTE/check )
Long-term maintenance: covered by existing maintenance plan

## Slide 30: CCS (DB + API + UI Editor)
No substantial changes expected
Small changes expected: ~ 5d FTE

## Slide 31: WIP
Missing estimations from
sysadmin (meeting tomorrow)
EDGE (interrupts and DMA unknowns)
CEM and DI/OT team

## Slide 32: Potentially saved resources
Estimation based on experience of teams who developed and are maintaining SoC systems with the existing level of support
ABT effort:
  gain understanding of petalinux tools and buildchain
  porting between petalinux tools with several modifications, often breaking, to build-scripts, kernel and rootfs
    not to forget full validation and tests after such updates
  contribution to SILECS to make SILECS server compatible to ARMv7, find and help fixing bugs
  design board supervision scripts and integrate in COSMOS with Graphana dashboard
  implement BOOTP network booting in collaboration with IT (CERN AIMS2 server)
    (we have no fallback boot solution)
Between half a year and a full year FTE

## Slide 33: Potentially saved resources
Estimation based on experience of teams who developed and are maintaining SoC systems with the existing level of support
BI-BGI effort:
  Petalinux configuration
  Device tree and code for the DMA access to the data in the FPGA
  Applications running on the SoC to process the data
  REST server for external access
  Vistar for data display
  We don’t have a FESA class or EDGE drivers.
~ 11 months FTE would have been saved if a FEC-OS distribution was available with FESA support.

## Slide 34: Potentially saved resources
Conservative estimation assuming that there could be knowledge transfer: ~ 7 months FTE per project
Considering only SoC projects planning TN integration and currently in the development phase: 6 projects
 Total of at least 42 months FTE
Other saved costs:
Multiplication of protocols (which require support)
Network security vulnerability
Multiplication of hardware solutions

## Slide 35: Timeline and open points

## Slide 36: Feasible timeline – critical components
FEC-OS:
  it is the fundamental basis, discussion tomorrow.
  Image available, it is possible to run test
FESA on SoC:
  Most probably not before 2025
  First tests are ongoing
Your timeline requirements:
  Decision?
  Delivery?

## Slide 37: Open points
FESA on SoC (discussion on FE forum)
  Timing
  Real-time patches
Kernel support and development environment version
  Kernel supported by sysadmin with obligation to update gateware development environment when forced to adopt certain security patches
  Alternative (and only solution for not UltraScale+): kernel maintained by the SoC team (including security patches)
Trouble-shooting and debugging
  Team effort cross department
  Observability and diagnostic tools are fundamental
    Xvc server and Virtual cable + ILA adoption for critical interfaces

## Slide 38: Conclusions

## Slide 39: Summary
CTTB Final report: 23/02/2024 – Check the recommendation on our Wiki!
Two ways of using SoCs in the sector:
  As FEC hardware accelerator: part of a crate, OS discouraged
  As integrated system with FEC-like capability: FEC-like software stack is recommended (and desired!)
FEC-like support for SoCs seems a feasible target for LS3 systems
It maximises the use of the skills and tools we have and their current distribution in the organization, adapting them to a new and complex architecture
Fundamental for sustainability on the long term:
  Push for hardware standardization
  Push for code sharing
  Push for system diagnostics improvement

## Slide 40
Contact us: ats-soc-taskforce@cern.ch
Read about: ATS SoC Wiki