## Slide 1: Follow-up alignment
cf meeting SY-RF, SY-BI, BE-ABP, BE-GM
23.01.2024
https://indico.cern.ch/event/1373059/

## Slide 2: Summary (BE-GM)
Pick-ups mean : 4 button pick-ups + 1 short strip line wrapped in a back-out equipment that will remain in place, per beam, e.g. x2 on each side of CC modules.
For the pick-ups, 3 alignment steps have to be considered:
  Step 1: The fiducialisation of each pick-up: determination of the electrical axis w.r.t. 4 mechanical references (performed by SY/BI); the mechanical fiducialisation (mechanical axis w.r.t. mechanical references) is performed by the metrology lab (EN-MME). Concerning the accuracy: the determination of the electrical axis is performed at better than 10 um, while is reference w.r.t. mechanical interfaces is less straightforward (within 100 um?).
  Step 2: The initial alignment of each pick-up on the top plate of the UAP platform: performed in the CMM environment, no adjustment systems or shims added, just re-machining of the parts if needed, and determination of the pick-ups in the UAP platform referential frame.
  Step 3: The alignment of the platform in the tunnel.
  As a non-FRAS equipped component, the adjustment of the UAP will take maximum once per year, during the YETS.
  The beam offset between CC and pick-ups could be cross-checked using the beam during the commissioning phase.
The alignment roll presented in Wolfgang’s slides p19 looks very challenging:
  A bad Roll has a strong impact on the quality of measurement and leads in a loss of sensitivity, but we should rediscuss what is reasonable and achievable as a value
  The use of a permanent inclinometer (during steps 2 and 3) could help following the roll, with a relative accuracy of 40 urad.
  We should also consider the impact of ground motion (and other constraints) for pitch and yaw (some 1 mrad values shown by Riccardo on other BPMs)
Actions:
Roll tolerances: define what is needed and achievable: Riccardo, Wolfgang, Michal
Organize a visit at SY/BI lab to understand the fiducialisation and initial alignment process: Michal
What is the accuracy of the determination of the electro-magnetic axis of the CC? Rama

## Slide 3: Crab cavities (summary by BE-GM)
For the CC:
  no longitudinal adjustment foreseen after the initial alignment during LS3 (no longitudinal position monitoring is foreseen on the CC, only on the main quadrupoles).
  The alignment tolerances of the CC (on Wolfgang’s slides p11) are all at 3 sigma. A new value has been agreed for the roll alignment: < 1.2 mrad (3 sigma), according to what is achievable. The new value will be updated in Riccardo’s document on tolerances and in the FRAS engineering specification under finalization.
  These tolerances refer to the mechanical axis, not the electro-magnetic axis (what is the accuracy of such a determination)?