## Slide 1
179th FCC-ee optics meeting & 50th FCCIS WP2.2 meeting, 23 February 2024
Frank Zimmermann, CERN
FCC – towards more luminosity
photo: J. Wenninger
Work supported by the European Commission under the HORIZON 2020 project, FCCIS, grant agreement 951754
Alert: this talk was not endorsed by FCC or CERN management !
many thanks to Patrick Janot and Christophe Grojean for inviting this presentation
at the 7th FCC Physics Workshop in Annecy

## Slide 2
FCC-ee – 2nd highest luminosity collider
Marica Biagini
~ same accelerator design
as twin machine CEPC
a few differences
 | FCC-ee | CEPC
#IPs | 4 or 2 | 2
collider SRF up to ZH | 400 MHz, 1- & 2-cell, Nb/Cu, 4.5 K | 650 MHz, 2-cell, Nb, 2 K
collider SRF ttbar | 800 MHz 5-cell, Nb, 2 K | 650 MHz, 5-cell, Nb, 2 K
booster SRF | 800 MHz 5-cell, Nb, 2 K | 1.3 GHz, 9-cell, Nb, 2 K
top-up | in collider | in booster
CEPC for 100 MW SR power & 2 IPs
FCC-ee with 4 IPs
/ IP

## Slide 3
trends from mid-term review
reduce linac rep rate from 400 to 200 Hz
stainless steel chamber for booster
replace 1-cell Z cavities by 2-cell cavities (the same cavities as for W and ZH)
..
risks of lower luminosity
all this is bad news for luminosity …

## Slide 4
most demanding : operation at the Z
Mid-term parameters
11200 bunches / beam
injection at 2x200 Hz = 400 Hz
time to fill the booster = 11200/400 s = 28 s
up + top + down ramp ~ 1s
total cycle time 30 s
we can inject the same beam every 60 s or 1 minute
beam lifetime: 15 minutes
intensity change at 200 Hz injection (400 Hz rep rate)
if we injected at 100 Hz, we would have
at 100 Hz with rad. Bhabha lifetime (22 min) only:
D. Shatilov required, for the “bootstrapping” injection,
to keep the intensity within +/-5%
and this without any errors
→ how can we lower the linac rep rate below 400 Hz,
while keeping the baseline rate of injection ?
A. Vanel
K. Oide

## Slide 5
reduce linac rep rate from 400 to 200 Hz
  new layout without common linac
  operation with 4 bunches / pulse
stainless steel chamber for booster
  larger aperture
  Cu lamination
  more cycles with fewer bunches / cycle
replace 1-cell Z cavities by 2-cell cavities (the same cavities as for W and ZH)
  efficient HOM damping for 2-cell cavities
  one fundamental power coupler per cell ?
  new optics (Raimondi) with larger momentum acceptance?
risk mitigations to be studied

## Slide 6
injector layout baseline
common linac
1.54 GeV → 6 GeV;
400 Hz rep rate,
total S-band linac length 1150 m
DR energy 1.54 GeV
e+ production at 6 GeV
P. Craievich et al.

## Slide 7
alternative injector layout
no common linac for e+ production,
200 Hz linac rep rates,
total S-band linac length 1095 m,
DR energy 2.86 GeV,
e+ production at 2.86 GeV
P. Craievich et al.

## Slide 8
luminosity constraints
injector rate limitation for Z running – factor <2 margin
SR power limit – luminosity could be increased in proportion to SR power
---
beamstrahlung limit
beam-beam tune shift limit
constraint from coherent beam-beam instability
change emittances?
reduce beta *?
note:
if we keep constant,
and are unchanged
need to check limit on
from overlap area
K. Oide

## Slide 9
Mid-term Review Parameters | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45.6 | 80 | 120 | 182.5
beam current [mA] | 1270 | 137 | 26.7 | 4.9
number bunches/beam | 11200 | 1780 | 440 | 60
bunch spacing [ns] | 25 |  |  | 
bunch intensity [1011] | 2.14 | 1.45 | 1.15 | 1.55
SR energy loss / turn [GeV] | 0.0394 | 0.374 | 1.89 | 10.4
SR power [MW] | 100 | 100 | 100 | 100
total RF voltage 400/800 MHz [GV] | 0.080/0 | 1.0/0 | 2.1/0 | 2.1/9.4
long. damping time [turns] | 1158 | 215 | 64 | 18
horizontal beta* [m] | 0.11 | 0.2 | 0.24 | 1.0
vertical beta* [mm] | 0.7 | 1.0 | 1.0 | 1.6
horizontal geometric emittance [nm] | 0.71 | 2.17 | 0.71 | 1.59
vertical geom. emittance [pm] | 1.9 | 2.2 | 1.4 | 1.6
horizontal rms IP spot size [mm] | 9 | 21 | 13 | 40
vertical rms IP spot size [nm] | 36 | 47 | 40 | 51
beam-beam parameter xx / xy | 0.002/0.0973 | 0.013/0.128 | 0.010/0.088 | 0.073/0.134
rms bunch length with SR / BS [mm] | 5.6 / 15.5 | 3.5 / 5.4 | 3.4 / 4.7 | 1.8 / 2.2
luminosity per IP [1034 cm-2s-1] | 141 | 20 | 5.0 | 1.25
total integrated luminosity / IP / year [ab-1/yr] | 17 | 2.4 | 0.6 | 0.15
beam lifetime rad Bhabha [min] | 22 | 16 | 14 | 12
beam lifetime (q+BS+lattice) [min] | 50 | 42 | 100 | 100

## Slide 10
Parameters for 150 MW SR power | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45.6 | 80 | 120 | 182.5
beam current [mA] | 1905 | 206 | 40 | 7.4
number bunches/beam | 16800 | 2670 | 660 | 90
bunch spacing [ns] | <18 |  |  | 
bunch intensity [1011] | 2.14 | 1.45 | 1.15 | 1.55
SR energy loss / turn [GeV] | 0.0394 | 0.374 | 1.89 | 10.4
SR power [MW] | 150 | 150 | 150 | 150
total RF voltage 400/800 MHz [GV] | 0.080/0 | 1.0/0 | 2.1/0 | 2.1/9.4
long. damping time [turns] | 1158 | 215 | 64 | 18
horizontal beta* [m] | 0.11 | 0.2 | 0.24 | 1.0
vertical beta* [mm] | 0.7 | 1.0 | 1.0 | 1.6
horizontal geometric emittance [nm] | 0.71 | 2.17 | 0.71 | 1.59
vertical geom. emittance [pm] | 1.9 | 2.2 | 1.4 | 1.6
horizontal rms IP spot size [mm] | 9 | 21 | 13 | 40
vertical rms IP spot size [nm] | 36 | 47 | 40 | 51
beam-beam parameter xx / xy | 0.002/0.0973 | 0.013/0.128 | 0.010/0.088 | 0.073/0.134
rms bunch length with SR / BS [mm] | 5.6 / 15.5 | 3.5 / 5.4 | 3.4 / 4.7 | 1.8 / 2.2
luminosity per IP [1034 cm-2s-1] | 212 | 30 | 7.5 | 1.88
total integrated luminosity / IP / year [ab-1/yr] | 25 | 3.6 | 0.9 | 0.23
beam lifetime rad Bhabha [min] | 22 | 16 | 14 | 12
beam lifetime (q+BS+lattice) [min] | 50 | 42 | 100 | 100

## Slide 11
Parameters for smaller by* & ey | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45.6 | 80 | 120 | 182.5
beam current [mA] | 1270 | 137 | 26.7 | 4.9
number bunches/beam | 11200 | 1780 | 440 | 60
bunch spacing [ns] | 25 |  |  | 
bunch intensity [1011] | 2.14 | 1.45 | 1.15 | 1.55
SR energy loss / turn [GeV] | 0.0394 | 0.374 | 1.89 | 10.4
SR power [MW] | 100 | 100 | 100 | 100
total RF voltage 400/800 MHz [GV] | 0.080/0 | 1.0/0 | 2.1/0 | 2.1/9.4
long. damping time [turns] | 1158 | 215 | 64 | 18
horizontal beta* [m] | 0.11 | 0.2 | 0.24 | 1.0
vertical beta* [mm] | 0.35 | 0.5 | 0.5 | 0.8
horizontal geometric emittance [nm] | 0.71 | 2.17 | 0.71 | 1.59
vertical geom. emittance [pm] | 1.0 | 1.1 | 0.7 | 0.8
horizontal rms IP spot size [mm] | 9 | 21 | 13 | 40
vertical rms IP spot size [nm] | 18 | 24 | 20 | 26
beam-beam parameter xx / xy | 0.002/0.0973 | 0.013/0.128 | 0.010/0.088 | 0.073/0.134
rms bunch length with SR / BS [mm] | 5.6 / 15.5 | 3.5 / 5.4 | 3.4 / 4.7 | 1.8 / 2.2
luminosity per IP [1034 cm-2s-1] | 282 | 40 | 10.0 | 2.5
total integrated luminosity / IP / year [ab-1/yr] | 34 | 4.8 | 1.2 | 0.3
beam lifetime rad Bhabha [min] | 11 | 8 | 7 | 6
beam lifetime (q+BS+lattice) [min] | 50 | 42 | 100 | 100

## Slide 12
Parameters for 150 MW SRP and smaller by* & ey | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45.6 | 80 | 120 | 182.5
beam current [mA] | 1905 | 206 | 40 | 7.4
number bunches/beam | 16800 | 2670 | 660 | 90
bunch spacing [ns] | <18 |  |  | 
bunch intensity [1011] | 2.14 | 1.45 | 1.15 | 1.55
SR energy loss / turn [GeV] | 0.0394 | 0.374 | 1.89 | 10.4
SR power [MW] | 150 | 150 | 150 | 150
total RF voltage 400/800 MHz [GV] | 0.080/0 | 1.0/0 | 2.1/0 | 2.1/9.4
long. damping time [turns] | 1158 | 215 | 64 | 18
horizontal beta* [m] | 0.11 | 0.2 | 0.24 | 1.0
vertical beta* [mm] | 0.35 | 0.5 | 0.5 | 0.8
horizontal geometric emittance [nm] | 0.71 | 2.17 | 0.71 | 1.59
vertical geom. emittance [pm] | 1.0 | 1.1 | 0.7 | 0.8
horizontal rms IP spot size [mm] | 9 | 21 | 13 | 40
vertical rms IP spot size [nm] | 18 | 24 | 20 | 26
beam-beam parameter xx / xy | 0.002/0.0973 | 0.013/0.128 | 0.010/0.088 | 0.073/0.134
rms bunch length with SR / BS [mm] | 5.6 / 15.5 | 3.5 / 5.4 | 3.4 / 4.7 | 1.8 / 2.2
luminosity per IP [1034 cm-2s-1] | 423 | 60 | 15.0 | 3.8
total integrated luminosity / IP / year [ab-1/yr] | 51 | 7.2 | 1.8 | 0.45
beam lifetime rad Bhabha [min] | 11 | 8 | 7 | 6
beam lifetime (q+BS+lattice) [min] | 50 | 42 | 100 | 100

## Slide 13
“HL-FCC-ee” – highest luminosity collider !
Marica Biagini
CEPC for 100 MW SR power & 2 IPs
FCC-ee with 4 IPs
/ IP
FCC-ee Z
FCC-ee H
FCC-ee W
FCC-ee tt
CEPC tt
CEPC W
CEPC H
CEPC Z
SuperKEKB
KEKB
PEPII
CESR
BINP c/Tau
BINP c/Tau
HIEPA c/Tau
LEP
LEP
PEP
PETRA
DORIS2
VEPP4M
CESR-c
BEPC
SPEAR2
BEPCII
ADONE
DCI
DAFNE
VEPP2000
VEPP2M
ADONE
luminosity [cm-2s-1]
c.m. energy [GeV]
1037
1036
1035
1034
1033
1032
1031
1030
1029
1028
1027
0.5 5.0 50.0 500.0
HL-FCC-ee tt
HL-FCC-ee H
HL-FCC-ee W
HL-FCC-ee Z

## Slide 14
Conclusions
the alternative injector layout looks attractive and could support higher luminosity at reduced linac repetition rate
possible path to increasing the FCC-ee luminosity by a factor 2-3 at all energies, by decreasing by* along with ey, and/or by raising SR power, respecting all other relevant constraints
a good optics and excellent optics control will be essential
increasing luminosity at Z is most challenging; vertical design emittance from IR solenoids should be minimised (presently ~0.5 pm for 4 IPs at Z, Mike Koratzinos, arXiv 2101.05704); at Z also e-cloud could limit #bunches
there might be other ways to boost the FCC-ee luminosity (hor. emittance, crossing angle, hor. beta*, bunch length, bunch charge etc.)