## Slide 2: CAS Advanced Accelerator Physics Collective effects
Part 2: Longitudinal wake fields – impact on machine elements and beam dynamics
Kevin Li and Giovanni Rumolo

## Slide 3: Outline
Part 2: Multiparticle dynamics with wake fields – impact on machine elements and longitudinal beam dynamics
  General introduction to wake fields
  Longitudinal wake fields and the longitudinal wake function
  Energy loss – beam induced heating and stable phase shift
  Potential well distortion, bunch lengthning and microwave instability
Last lecture: Introduction to multi-particle effects, concept of particle distributions, peculiarities of multiparticle dynamics in accelerators, decoherence, filamentation.
This lecture:
  Basic concept of wake fields and how these can be characterized as a collective effect in that they depend on the particle distribution.
  Multiparticle systems and wakefields and impact of these in the longitudinal and transverse planes.
Notes: Perhaps other way round

## Slide 4: Outline
Part 2: Multiparticle dynamics with wake fields – impact on machine elements and longitudinal beam dynamics
  General introduction to wake fields
  Longitudinal wake fields and the longitudinal wake function
  Energy loss – beam induced heating and stable phase shift
  Potential well distortion, bunch lengthning and microwave instability
Last lecture: Introduction to multi-particle effects, concept of particle distributions, peculiarities of multiparticle dynamics in accelerators, decoherence, filamentation.
This lecture:
  Basic concept of wake fields and how these can be characterized as a collective effect in that they depend on the particle distribution.
  Multiparticle systems and wakefields and impact of these in the longitudinal and transverse planes.
Notes: Perhaps other way round

## Slide 5: Wake functions in general
Definition as the integrated force felt by a witness charge following a source charge (‘energy kick’):
In general, for two point-like particles, we have w is typically expanded in the transverse offsets of source and witness particles. This yields the different types of wake fields (dipole, quadrupole, coupling wakes)
2b
L
z
Dx1 (or Dy1)
Dx2 (or Dy2)
Source, q1
Witness, q2

## Slide 6: Wakefields as sources of collective effects
The wake function is a type of electromagnetic response of a device to a charge pulse. It is an intrinsic property of this device and depends on
  The device’s geometry (transitions, cavities, etc.)
  The electromagnetic properties of the materials exposed to the beam (e.g. PEC, finite conductivity, lossy materials, metamaterials, etc.)
The wake function describes the electromagnetic coupling between two point charges as a function of the distance between them

## Slide 7: Longitudinal wake function
Longitudinal wake fields
2b
z
L
Dx1 (or Dy1)
Dx2 (or Dy2)
Source, q1
Witness, q2
Zeroth order with source and test centred
usually dominant
Higher order terms
Usually negligible for small offsets

## Slide 8: Longitudinal wake function
Longitudinal wake fields
2b
z
L
Dx1 (or Dy1)
Dx2 (or Dy2)
Source, q1
Witness, q2
Energy kick of the witness particle from longitudinal wakes

## Slide 9: Longitudinal wake function
  The value of the wake function in z=0 is related to the energy lost by the source particle in the creation of the wake
  W||(0)>0 since ΔE1<0
  W||(z) is discontinuous in z=0 and it vanishes for all z>0 because of the ultra-relativistic approximation
W||(z)
z
Beam loading theorem

## Slide 10: Longitudinal impedance
  The wake function of an accelerator component is basically its Green function in time domain (i.e., its response to a pulse excitation)
    Very useful for macroparticle models and simulations, because it can be used to describe the driving terms in the single particle equations of motion!
  We can also describe it as a transfer function in frequency domain
    This is the definition of longitudinal beam coupling impedance of the element under study

## Slide 11: The energy balance
  In the global energy balance, the energy lost by the source splits into:
    Electromagnetic energy of the modes that remain trapped in the object
      Partly dissipated on lossy walls or into purposely designed inserts or HOM absorbers
      Partly transferred to following particles (or the same particle over successive turns), possibly feeding into an instability!
    Electromagnetic energy of modes that propagate down the beam chamber (above cut-off), eventually lost on surrounding lossy materials
What happens to the energy lost by the source?

## Slide 12: The energy balance
  In the global energy balance, the energy lost by the source splits into
    Electromagnetic energy of the modes that remain trapped in the object
      Partly dissipated on lossy walls or into purposely designed inserts or HOM absorbers
      Partly transferred to following particles (or the same particle over successive turns), possibly feeding into an instability!
    Electromagnetic energy of modes that propagate down the beam chamber (above cut-off), eventually lost on surrounding lossy materials
  The energy loss of a particle bunch
    causes beam induced heating of the machine elements (damage, outgassing) or sparking due to high field
    feeds into both longitudinal and transverse instabilities through the associated EM fields
    is compensated by the RF system determining a stable phase shift
What happens to the energy lost by the source?

## Slide 13: How are wakes and impedances computed?
Analytical or semi-analytical approach, when geometry is simple (or simplified)
  Solve Maxwell’s equations with the correct source terms, geometries and boundary conditions up to an advanced stage
  Find closed expressions or execute the last steps numerically to derive wakes and impedances
b
+ Boundary conditions
  An example: axisymmetric beam chamber with several layers with different EM properties

## Slide 14: How are wakes and impedances computed?
Analytical or semi-analytical approach, when geometry is simple (or simplified)
  Solve Maxwell’s equations with the correct source terms, geometries and boundary conditions up to an advanced stage
  Find closed expressions or execute the last steps numerically to derive wakes and impedances
We are interested in the longitudinal force on a test charge q2 following the source q1 at a distance z (wake per unit length of chamber)
L = 1 m
s
q1
q2
FS

## Slide 15: How are wakes and impedances computed?
Analytical or semi-analytical approach, when geometry is simple (or simplified)
  Solve Maxwell’s equations with the correct source terms, geometries and boundary conditions up to an advanced stage
  Find closed expressions or execute the last steps numerically to derive wakes and impedances
b
t
  An example: a 1 m long Cu pipe with radius b=2 cm and thickness t = 4 mm in vacuum
Highlighted region shows the typical ω1/2 scaling
Scaling is with respect to b:
  Longitudinal impedance ∼b-1

## Slide 16: How are wakes and impedances computed?
Analytical or semi-analytical approach, when geometry is simple (or simplified)
  Solve Maxwell’s equations with the correct source terms, geometries and boundary conditions up to an advanced stage
  Find closed expressions or execute the last steps numerically to derive wakes and impedances
  An example: a 1 m long Cu pipe with radius b=2 cm and thickness t = 4 mm in vacuum
𝔉-1

## Slide 17: How are wakes and impedances computed?
Analytical or semi-analytical approach, when geometry is simple (or simplified)
  Solve Maxwell’s equations with the correct source terms, geometries and boundary conditions up to an advanced stage
  Find closed expressions or execute the last steps numerically to derive wakes and impedances
  An example: a 1 m long Cu pipe with radius b=2 cm and thickness t = 4 mm in vacuum
𝔉-1

## Slide 18: How are wakes and impedances computed?
Numerical approach
  Different codes have been developed over the years to solve numerically Maxwell’s equations in arbitrarily complicated structures
  Examples are CST Studio Suite (Particle Studio, Microwave Studio), ABCI, GdFidL, HFSS, ECHO2(3)D. Exhaustive list can be found from the program of the ICFA mini-Workshop on “Electromagnetic wake fields and impedances in particle accelerators”, Erice, Sicily, 23-28 April, 2014
  Computations can become very challenging if high frequency resolution (long wake) or knowledge of impedance spectrum at high frequency (short excitation) are required, especially for large/complicated geometries
Example of a cavity definition in CST
Longitudinal wake
Re[Z||]
Im[Z||]
Longitudinal impedance
𝔉

## Slide 19: How are wakes and impedances computed?
Numerical approach
  To limit numerical noise, in cases with many resonances, the resonances are first characterized through their frequencies (wri), shunt impedances (Rsi) and quality factors (Qi)
  Then analytical formulae for resonators are used in computations
Longitudinal impedance
wr1 – Rs1 – Q1
wr2 – Rs2 – Q2
wr3 – Rs3 – Q3
wr4 – Rs4 – Q4
wr5 – Rs5 – Q5
wr6 – Rs6 – Q6
wr7 – Rs7 – Q7

## Slide 20: How are wakes and impedances computed?
Bench measurements based on transmission/reflection measurements with stretched wires
  Seldom used independently to assess impedances due to the perturbation introduced by the measurement set up (flanging, presence of wire)
  Usefulness mainly lies in that they can be used for validating 3D EM models for simulations
  New wireless methods being developed for direct impedance measurements minimizing perturbation
A wire is stretched in the middle of the device to simulate the beam
Reflection and transmission coefficients are measured via a VNA
The impedance can be calculated by plugging the measured scattering parameters into the LOG formula

## Slide 21: Signpost
We have learnt what is a wake function and how it is defined in the longitudinal plane. We have introduced the longitudinal impedance.
We have seen how longitudinal wake functions are related to the energy loss of the source particles.
We have discussed the energy balance which contains all the fundamental underlying mechanisms for collective effects related to wake fields and impedances.
We have shown how wake functions and impedances can be computed.
Part 2: Multiparticle dynamics with wake fields – impact on machine elements and longitudinal beam dynamics
  General introduction to wake fields
  Longitudinal wake fields and the longitudinal wake function
  Energy loss – beam induced heating and stable phase shift
  Potential well distortion, bunch lengthning and microwave instability
Notes: Perhaps other way round

## Slide 22: Bunch energy loss per turn
Single traversal of a bunch through an impedance source
  We assume a single bunch of particles that goes only once through a known (characterized) wake/impedance source, representing both
    Single passage (e.g. in a line)
    Energy loss per turn if the bunch passes every turn but the wake fully decays between subsequent turns
  Our goal is to calculate how much energy the bunch loses in this passage due to the electromagnetic interaction

## Slide 23: Bunch energy loss per turn
Single traversal of a bunch through an impedance source
Particle j
excites
Particle i
receives kick
Slice i
receives kick
Slice j
excites

## Slide 24: Bunch energy loss per turn
Single traversal of a bunch through an impedance source

## Slide 25: Bunch energy loss per turn
Single traversal of a bunch through an impedance source
Slice i
receives kick
Slice j
excites

## Slide 26: Bunch energy loss per turn
Single traversal of a bunch through an impedance source
Slice i
receives kick
Slice j
excites

## Slide 27: Bunch energy loss per turn
Multiple traversal of a bunch through an impedance source
  We assume a single bunch of particles that goes multiple times through a known (characterized) wake/impedance source, representing
    Energy loss per turn if the bunch passes every turn and the wake fully keeps ringing between subsequent turns
  Our goal is to calculate how much energy the bunch loses at each passage due to the electromagnetic interaction over several turns

## Slide 28: Beam energy loss per turn
Not one bunch but a train of bunches …

## Slide 29: Bunch energy loss per turn
l(z’ + kC) = l(z’), i.e. assuming that the distribution doesn’t change from turn to turn

## Slide 30: Beam energy loss per turn
Bunch profile and spectrum
Beam profile and spectrum
Replacing the bunch spectrum with the beam spectrum, we can calculate the energy loss from a beam

## Slide 31: Beam energy loss per turn
Replacing the bunch spectrum with the beam spectrum, we can calculate the energy loss from a beam
Ex. parabolic, as shown in the previous slide
Bunch profile and spectrum
Beam profile and spectrum

## Slide 32: Beam energy loss per turn
Replacing the bunch spectrum with the beam spectrum, we can calculate the energy loss from a beam
Bunch profile and spectrum
Beam profile and spectrum
Or for a train of Gaussian bunches

## Slide 33: Impact of beam power loss
Beam power loss
Heating, degradation, damage, outgassing
High local Ē  Sparking
Affect device globally
Affect device locally
Effect on single device
Global effect on the beam
Synchronous phase shift, RF compensation
Coherent instabilities
Transverse
Longitudinal
Notes: The power lost by the beam on a single device may cause localized issues
  Intolerable heating of the device leading to global degradation, damage or inacceptable outgassing
  Intolerable power deposition at specific locations causing localised damage or malfunctioning  Not only total beam power lost on a device but also power distribution over the device
  High localised electric fields causing sparking
The global power loss

## Slide 34: Impact of beam power loss
Beam power loss
Heating, degradation, damage, outgassing
High local Ē  Sparking
Affect device globally
Affect device locally
Effect on single device
Global effect on the beam
Synchronous phase shift, RF compensation
Coherent instabilities
Transverse
Longitudinal

## Slide 35: Case of the SPS extraction kickers
Problem with SPS extraction kickers (MKE)
  Extraction elements through which the beam passes every turn
    Based on a fast pulsed magnet capable of deflecting the whole beam over one turn
    Active only on turn in which beam has to be extracted, otherwise passive but with all its elements (ferrite, conductors) exposed to the beam

## Slide 36: Case of the SPS extraction kickers
Problem with SPS extraction kickers (MKE)
  Extraction elements through which the beam passes every turn
    Based on a fast pulsed magnet capable of deflecting the whole beam over one turn
    Active only on turn in which beam has to be extracted, otherwise passive but with all its elements (ferrite, conductors) exposed to the beam
  Use of beam for LHC filling (4x 200-ns spaced trains of 72x 25-ns spaced bunches) led to inacceptable heating of these elements
    Heating above Curie temperature leads to ferrite degradation  Beam cannot be extracted anymore from the SPS
    Heating causes outgassing and strong pressure rise in the kicker sector, with consequent beam interlocking due to poor vacuum

## Slide 37: Case of the SPS extraction kickers
We need to calculate the power loss in the kicker
  Kicker impedance can be evaluated semi-analytically or via simulations
  Then we apply the energy loss formula

## Slide 38: Case of the SPS extraction kickers
We need to calculate the power loss in the kicker
  Kicker impedance can be evaluated semi-analytically or via simulations
  Then we apply the energy loss formula
Kicker impedance already becomes significant at frequencies for which the beam spectrum has not fully decayed, causing the undesired heating
We need to lower the kicker impedance  Impedance dominated by losses in ferrite  Ferrite shielding

## Slide 39: Case of the SPS extraction kickers
Print striped pattern of good conductor on ferrite (serigraphy)

## Slide 40: Case of the SPS extraction kickers
This almost suppresses the impedance over the bunch spectrum
It however introduces a low frequency peak, which needs to be kept far from beam spectral lines
  Define serigraphy geometry such as to separate impedance peak from beam spectrum as much as possible

## Slide 41: Case of the SPS extraction kickers
This almost suppresses the impedance over the bunch spectrum
It however introduces a low frequency peak, which needs to be kept far from beam spectral lines
Factor 4 less heating measured for 25-ns LHC-type beam at 26 GeV!!
~ 17h run with 25 ns beams at 26 GeV after technical stop

## Slide 42: Signpost
We have further looked into the mechanism of energy loss and have seen the impact of longitudinal impedances on machine elements as these lead to beam induced heating.
We have found that beam induced heating depends on the overlap of the beam power spectrum and the impedance of a given object.
We have seen a real world example of the impact of an objects impedance on the beam induced heating.
Part 2: Multiparticle dynamics with wake fields –
impact on machine elements and longitudinal beam dynamics
  General introduction to wake fields
  Longitudinal wake fields and the longitudinal wake function
  Energy loss – beam induced heating and stable phase shift
  Potential well distortion, bunch lengthening and microwave instability
Notes: Perhaps other way round

## Slide 43: Impact of beam power loss
Beam power loss
Heating, degradation, damage, outgassing
High local Ē  Sparking
Affect device globally
Affect device locally
Effect on single device
Global effect on the beam
Synchronous phase shift, RF compensation
Coherent instabilities
Transverse
Longitudinal

## Slide 44: Longitudinal wakes in beam dynamics
The effect of each localised wake/impedance on each particle in a beam can be described as an energy kick
The accelerator is made of many components, each giving a small kick to the beam particles, which drift freely in between

## Slide 45: Longitudinal wakes in beam dynamics
The effect of each localised wake/impedance on each particle in a beam can be described as an energy kick
The accelerator is made of many components, each giving a small kick to the beam particles, which drift freely in between
For simulations, the impedance is lumped in one place and kicks to beam particles are applied once per turn, with free drift over one turn

## Slide 46: Longitudinal wakes in beam dynamics
The effect of each localised wake/impedance on each particle in a beam can be described as an energy kick
The accelerator is made of many components, each giving a small kick to the beam particles, which drift freely in between
For simulations, the impedance is lumped in one place and kicks to beam particles are applied once per turn, with free drift over one turn
For analytical calculations, both global impedance and RF are smeared over the ring

## Slide 47: Longitudinal wakes in beam dynamics
  For a bunch under the effect of longitudinal wake fields, two different regimes can be found:
    Regime of potential well distortion, i.e. due to the impedance a new equilibrium distribution can be found for the bunch
    Stable phase shift
    Synchrotron frequency shift
    Different matching ( bunch lengthening for lepton machines)
    Regime of longitudinal instability, i.e. no equilibrium distribution can be found under the effect of the impedance, a perturbation grows exponentially
    Dipole mode instabilities
    Coupled bunch instabilities
    Microwave instability (longitudinal mode coupling)

## Slide 48: Potential well distortion and Haissinki equation
The equilibrium distribution in the presence of a longitudinal wake field can be found analytically. The (linearized) longitudinal Hamiltonian with longitudinal wake fields is given as:
We assume a Gaussian matched beam distribution, hence:
Now, choosing for H0 and consider for λ that:
The equilibrium (matched) line charge density is then given by the self-consistency equation (Haissinski equation):

## Slide 49: Potential well distortion and Haissinki equation
The equilibrium distribution in the presence of a longitudinal wake field can be found analytically. The (linearized) longitudinal Hamiltonian with longitudinal wake fields is given as:
We assume a Gaussian matched beam distribution, hence:
Now, choosing for H0 and consider for λ that:
The equilibrium (matched) line charge density is then given by the self-consistency equation (Haissinski equation):
A simple Taylor expansion in z already qualitatively reveals some of the effects of the longitudinal wake fields onto the beam:
First order: shift in the mean position (stable phase shift)
Second order: change in bunch length accompanied by an (incoherent) synchrotron tune shift

## Slide 50: Bunch energy loss per turn and stable phase
  The RF system compensates for the energy loss by imparting a net acceleration to the bunch
  Therefore, the bunch readjusts to a new equilibrium distribution in the bucket and moves to an average synchronous angle DFs
Above transition
Below transition

## Slide 51: Bunch lengthening and mW instability
SPS ring
C = 6900 m
Ekin=25 GeV
z
y
x
Single Gaussian bunch
sz = 0.2 m (0.67 ns)
Ring impedance modeled as broad band resonator with
wr = 700 MHz
Q=1
Rs=
Single RF system
wrf = 200 MHz
Vrfmax = 3 MV

## Slide 52: Bunch lengthening and mW instability
Below MWI threshold
Above MWI threshold
Running the numerical simulation for this case:
Bunch is matched at low intensity (i.e. without impedance)
Two regimes are found:
Bunch lengthening/emittance blow up regime with roughly linear increase of the synchronous phase and bunch length with intensity
Unstable regime (turbulent bunch lengthening)

## Slide 53: Bunch lengthening and mW instability
Below MWI threshold
Above MWI threshold

## Slide 54: Bunch lengthening and mW instability
Below MWI threshold
Above MWI threshold
Below MWI threshold

## Slide 55: Bunch lengthening and mW instability
Below MWI threshold
Above MWI threshold

## Slide 56: Signpost
We have discussed longitudinal wake fields and impedances and examples of their impact on both the machine as well as the beam.
We have learned about beam induced heating and how it is related to the beam power spectrum and the machine impedance.
We have discussed the effects of potential well distortion (stable phase and synchrotron tune shifts, bunch lengthening and shortening).
We have seen one example of longitudinal instability (microwave).
Tomorrow Part 3
 Transverse wake fields and impedances and their effects on the beam
Notes: Perhaps other way round

## Slide 57: End part 2

## Slide 58: The Robinson instability
  To illustrate the Robinson instability we will use some simplifications:
    The bunch is point-like and feels an external linear force (i.e. it would execute linear synchrotron oscillations in absence of the wake forces)
    The bunch additionally feels the effect of a multi-turn wake
z
dp/p0
Unperturbed: the bunch executes synchrotron oscillations at ws

## Slide 59: The Robinson instability
  To illustrate the Robinson instability we will use some simplifications:
    The bunch is point-like and feels an external linear force (i.e. it would execute linear synchrotron oscillations in absence of the wake forces)
    The bunch additionally feels the effect of a multi-turn wake
z
dp/p0
Unperturbed: the bunch executes synchrotron oscillations at ws
The perturbation also changes the oscillation amplitude – unstable motion

## Slide 60: The Robinson instability
  To illustrate the Robinson instability we will use some simplifications:
    The bunch is point-like and feels an external linear force (i.e. it would execute linear synchrotron oscillations in absence of the wake forces)
    The bunch additionally feels the effect of a multi-turn wake
z
dp/p0
Unperturbed: the bunch executes synchrotron oscillations at ws
The perturbation also changes the oscillation amplitude – damped motion

## Slide 61: The Robinson instability
  To illustrate the Robinson instability we will use some simplifications:
    The bunch is point-like and feels an external linear force (i.e. it would execute linear synchrotron oscillations in absence of the wake forces)
    The bunch additionally feels the effect of a multi-turn wake
  Longitudinal Hamiltonian
  Expansion of wake field (we assume that the wake can be linearized on the scale of a synchrotron oscillation)

## Slide 62: The Robinson instability
  The first term only contributes as a constant term in the solution of the equation of motion, i.e. the synchrotron oscillation will be executed around a certain z0 and not around 0. This term represents the stable phase shift that compensates for the energy loss
  The second term is a dynamic term introduced as a “friction” term in the equation of the oscillator, which can lead to instability!
  Equations of motion

## Slide 63: The Robinson instability
  The first term only contributes as a constant term in the solution of the equation of motion, i.e. the synchrotron oscillation will be executed around a certain z0 and not around 0. This term represents the stable phase shift that compensates for the energy loss
  The second term is a dynamic term introduced as a “friction” term in the equation of the oscillator, which can lead to instability!
  Equations of motion
  Ansatz
  Solution
Expressed in terms of impedance

## Slide 64: The Robinson instability
  We assume a small deviation from the synchrotron tune:
    Re(Ω - ωs)  Synchrotron tune shift
    Im(Ω - ωs)  Growth/damping rate, only depends on the dynamic term, if it is positive there is an instability!
  Solution:
  Tune shift:
  Growth rate:

## Slide 65: The Robinson instability
  Solution:
  Stability criterion:
Re[Z||]
Im[Z||]
wr ≈ hw0

## Slide 66: The Robinson instability
  Stability criterion:
 | ωr < hω0 | ωr > hω0
Above transition (η > 0) | stable | unstable
Below transition (η < 0) | unstable | stable

## Slide 67: Robinson damping and instability
Below MWI threshold
Above MWI threshold
Examples of numerical simulations – SPS bunch with single narrow-band resonator wake:
Initializing an otherwise matched bunch with a slight momentum error, two regimes are found:
Regime of Robinson damping when the resonator is detuned to hω0 – ωs. Initial dipole oscillations are damped.
Regime of Robinson instability when the resonator is detuned to hω0 + ωs. Initial dipole oscillations start to are grow exponentially.

## Slide 68: Robinson damping and instability
Below MWI threshold
Above MWI threshold

## Slide 69: Robinson damping and instability
Below MWI threshold
Above MWI threshold

## Slide 70: Robinson damping and instability
Below MWI threshold
Above MWI threshold