## Slide 1: Update on SoC activities in the CERN AT Sector
Greg Daniluk, Irene Degl’Innocenti, Greg Kruk, Dariusz Jakub Zielinski
08/03/2023

## Slide 2: Outline
Introduction
Inventory of SoC Applications in ATS
Summary of the SoC taskforce recommendation
Outlook

## Slide 3: AT Sector and CTTB
ATS: Accelerators and Technology sector at CERN
  Beam (BE)
  Engineering (EN)
  Accelerator Systems (SY)
  Technology (TE)
CTTB: Common Hardware & Software Technologies Technical Board (2021, indico)
  Analyses common hardware & software activities to avoid duplication of work or services
  Stimulates a common approach & strengthens standardisation effort of hardware & software solutions
Big variety of electronics and software systems integrated in the same accelerator control infrastructure
Controls groups (CEM & CSS): central services and support
SoC technology identified as target for fruitful standardization

## Slide 4: Taskforce for SoC Framework (from 31st CTTB)
Goal
  Starting from the current SoC applications in ATS and future needs identify a generic architecture, common services and a proper integration in the accelerator control system to converge towards a common SoC framework
Scope
  All the ATS SoC applications and users in radiation free environment
Timeline
  Intermediate reporting at 34th CTTB (24/11/2023)
  Final reporting at CTTB January/February 2024 (23/02/2024)

## Slide 5: Taskforce for SoC Framework (from 31st CTTB)
Deliverables
  Inventory of the existing SoC applications and future (LS3) needs within ATS
  Identification of commonalities and their potential to converge to a common solution:
    SoC family/families standardisation
    SoC architecture and reference design (i.e. PS/PL generic gateware interfaces)
    Common services (i.e. Diagnostics / monitoring / configuration services, safe booting, RT environment for user defined tasks)
    Embedded Linux support
    Proper integration in the accelerator control system:
      FEC like support vs FEC-PS additional communication layer
      Availability of special services (i.e. Post-mortem, timing)
    High bandwidth data link
    Standardised workflows
    Generic framework to easy the programming and exploitation of the SoC architecture
  Strategy and roadmap towards a common and unified solution with identification of domains for collaboration
  Estimation of resources, timeline, risk and return on investment for the proposed strategy

## Slide 6: Inventory of SoC Applications in ATS
Commented summary of the survey results

## Slide 7: Inventory
ATS
BE
SY
TE
EN
ABT
AR
BI
EPC
RF
STI
HDO
ABP
ASR
CEM
CSS
EA
GM
ICS
OP
CRG
MPE
PE
MI
EP
MSC
LMF
VSC
VSM
ICM
AA
ACE
CV
EL
HDO
HE
IM
MME
PAS
Omitted (not relevant)
No SoC projects
SoC projects identified
+ HSE

## Slide 8: Inventory
# | Group | Project | Survey
1 | SY-ABT | DKFC | Yes
2 | SY-ABT | FIDS | Yes
3 | SY-BI | HL-LHC BPM / AWAKE | Yes
4 | SY-BI | LHC BPM Cons | Yes
5 | SY-BI | BIPXL Readout | Yes
6 | SY-BI | MIM | Comments[1]
7 | SY-BI | MCOI | Yes
8 | SY-EPC | FGC4 | Yes
9 | SY-RF | - (FBM section) | Comments [2]
10 | SY-RF | SPS RF Beam Control | Yes
11 | BE-CEM | FSI | Yes
12 | BE-CEM | Sambuca | Yes
13 | BE-CEM | Sambuca Motor Driver | Yes
14 | BE-CEM | White Rabbit WREN | Yes
15 | BE-CEM | White Rabbit WRS | Yes
16 | TE-MSC | New MSC platform | Yes
17 | HSE | CROME | Yes
Notes:
[1] Legacy system with two units.
[2] Will use AMD Zynq UltraScale+ RFSoC and uTCA architecture.
Chart: 17 SoC projects 15 surveys were received
| SY-BI | BE-CEM | SY-ABT | SY-EPC | SY-RF | TE-MSC | HSE
13 surveys were received | 5 | 5 | 2 | 1 | 2 | 1 | 1

## Slide 9: Estimated number of SoC
Chart: Project sizes (over their lifetime)
| Small (<50) | Middle (<400) | Large (>400)
Sizes | 7 | 4 | 4
1000
1000
600
3
14
25
28
35
40
100
100
100
In total
3500+ SoC
500
250
30

## Slide 10: Status and deadlines
Already 4 operational systems are using SoCs
Majority of SoC activities regard new projects and upgrades
High adoption potential of a common SoC framework for projects in R&D and prototyping stage
Some tools potentially useful for advanced projects as well
Chart: Projects statuses (non exclusive)
| New projects/upgrades | Operational systems
Operational | 0 | 4
Production | 1 | 0
Development | 4 | 0
Prototyping | 7 | 0
R&D | 6 | 0

## Slide 11: Status and deadlines
Most projects target LS3 for deployment
LS3 confirmed as time horizon for the ATS SoC Common framework
Chart: Deployment deadlines
| Already deployed | Early 2024 | LS3 | LS4 | None yet
Series 1 | 4 | 1 | 9 | 2 | 2

## Slide 12: SoC vendor and family
All projects on AMD Xilinx SoCs
Chart: SoC vendor
| AMD Xilinx
AMD Xilinx | 15
Chart: SoC family
| Zynq Ultrascale+ MPSoC | Zynq 7000 | Zynq Ultrascale+ RFSoC
Series 1 | 11 | 2 | 1
Column1
Most of projects using US+ MPSoC (or planning to)
1-2 RFSoC projects, SoC with same Processing System cores as US+ MPSoC (identical from the software stack point of view)
Xilinx Zynq US+ family candidate for common framework support

## Slide 13: Software and Operating System
Some real-time software:
All bare-metal code (no RT OS)
Chart: Do you run real-time software?
| TBD | No | Yes
TBD | 1 | 0 | 0
Bare-metal APU | 0 | 0 | 3
Bare-metal RPU | 0 | 0 | 1
Bare-metal RPU/soft-core | 0 | 0 | 1
No | 0 | 9 | 0
Operating System for Application Processing Unit:
All projects using an OS in their APU interested in adopting FEC-OS
  FEC-OS on SoC: same distribution as for new FEC model
  All new projects have the same Processing System (ARM Cortex-A53 core based)
  Potential alignment between SoC Common framework and new FEC model

## Slide 14: Integration with accelerator control system
Chart: 
| SoC as HW module of FEC | SoC in the TN
SoC as FEC | 0 | 8
SoC in HSE SCADA | 0 | 1
SoC as node in FEC network | 0 | 1
HW | 3 | 0
FEC-OS  FEC-like services libraries potentially available to SoCs if required
  Configuration, databases, layout
  FESA, or other FEC SW frameworks
  Drivers (EDGE)
  System monitoring and diagnostics
  Network booting with fall-back strategy
  CMW/RDA
  Post-mortem
  Remote console and tools
  General Machine Timing
SoC as HW modules (no OS):
Integration through FEC
SPEXI7U model, RF uTCA systems

## Slide 15: Programmable Logic
Bus: Large use of AXI and Wishbone
IP integration: combination of TCL scripting and graphical block design for most
DMA: mainly application specific use
  PS DDR memory – Linux driver
  PL-controlled DMA to inject data in PS DDR
Others:
  Common gw-sw co-simulation framework
  CI support
  Cheby with EDGE compatibility
  Partial reconfiguration
VHDL
(9)
SystemVerilog
(5)
HLS
(1)
SystemVerilog
Testbench (1)
(1)
HDL

## Slide 16: Interfaces
High-bandwidth data read-out 10G ETH:
  2 use cases, but interesting for common framework
Data acquisition protocol: GBTx/LpGBT
SoC to SoC/FPGA: few cases, Aurora protocol
Slow control FEC  SoC over 1G Ethernet:
  Fewer use cases if SoC as FEC
  SILECS
  ROMULUSlib
  REST
  IPbus
  Custom protocol over Ethernet
Chart: Embedded interfaces
| Ethernet 1G | USB 3.0 | I2C/SPI | QSPI | SD/eMMC | UART | PCIe | SATA | CAN
Series 1 | 10 | 2 | 14 | 10 | 9 | 12 | 4 | 2 | 1

## Slide 17: Hardware platforms
General interest for common hardware solutions
  Few projects designing custom SoC PCBs (WR, FIDS, Sambuca)
  Several projects in the eco-system of DI/OT
  Large interest into generic-purpose System-on-Module (SoM) with application specific carriers
Hardware standardization facilitates framework standardization
Opportunities for shared procurement and step-pricing

## Slide 18: Summary of the recommendation
Extract from the taskforce report to 37th CTTB

## Slide 19: Hardware
Vendor: AMD Xilinx
  supported development tools and environment, community
SoC Family: Zynq UltraScale+
  support for the full software stack, under fulfilling of HW requirements (WIP: e.g. Ethernet PHY, DDR memories, remote console tools)
SoC model: Zynq UltraScale+ XCZU17EG-1FFVC1760E (WR and DI/OT)
  access to advantageous step-pricing, compatibility with reference design
Reference PCB design: DI/OT System board v3
  schematic sheets of main blocks, Board Support Package and reference framework project

## Slide 20: Low-level Software
Operating System (OS): Linux-Xilinx kernel, Debian (FEC-OS)
  OS support, basis for tools and services as FECs
  Kernel and device-tree support model under discussion
Booting:
  Bootloader: U-Boot + GRUB (FEC-OS)
  Source: Network booting with fall-back source in FLASH, fail-over mechanism WIP
Hypervisors: OpenAMP (Xilinx support), Bmboot (CERN-EPC tool)
Real-time code: baremetal (R5 if possible) and programmable logic
  No support for OS RT-patches

## Slide 21: High-level Software
External monitoring: FEC-like tools (WIP)
  access to system metrics from central service/server identical to FECs
Internal monitoring: DI/OT library
  access to platform metrics from the SoC applications in Linux
  Configurable and extendible version under discussion
Time synchronization: NTP (ms, default)
  If more precision required: PTP (us), WR (ns)
Software framework: FESA
  supported software framework and integration in control system, BUT SoC solution for timing and no RT

## Slide 22: Common software blocks and strategies
Monitoring library interface: DI/OT utils
  Command line interface to the DI/OT monitoring library (reading local monitoring values, reading configuration, executing power-cycle command)
  Generalization to other SoC platform depends on hardware and additional resources
Software, firmware and bitstream distribution: Debian packages
  Distribution and version management of the software tools, firmware and FPGA bitstreams
  In-line with the phase 2 of the FEC-OS project
  Will require establishing a central repository for Debian packages
  Alternative and only solution for FESA: NFS

## Slide 23: Common gateware blocks and strategies
Push toward sharing and reusability of gateware modules:
  Collection of pointers to repositories in SoC applications inventory
  Shared IP repository: starting from CEM-EPC shared repo, following Electronics Forum initiative
  AXI4 bus and Wishbone bus as light alternative
  Reference project + Board Support Packages for DI/OT v3 based reference schematics
Common interest in-house HDL modules under investigation:
  High bandwidth data transfer module to DDR Memory controller, controlled by PL
  CMS TCP/IP Fast data link over 10Gb Ethernet, available only inside CERN
Development tools:
  Cheby for memory map generation and EDGE tools integration
  Continuous Integration guidelines and infrastructure (following Electronics Forum initiative)
  Guidelines on sw-gw co-simulation based on QEMU and Questa and CROME framework

## Slide 24: CERN Control System Integration
Communication: CMW/RDA
  Standard for FEC communication and natively supported in FESA
  Integration with upper layers of CERN control system without introducing new protocols
Timing events distribution: through CMW/RDA
  Light SW timing event distribution implementation, cheaper alternative to timing receiver
Configuration storage: CCS (DB + API + UI Editor)
Monitoring server: COSMOS
Start-up services: LUMENS

## Slide 25: Outlook
Open-points and outlook of future activities

## Slide 26: Open points
FEC-OS:
  It is the fundamental basis, still open discussion on support model to define feasibility
  Proposal: single standard kernel and device tree supported by sysadmin, with project specific overlays under responsibility of the projects
    Device-tree and overlay mechanism to be tested
    Remote console tools to be identified
    Drafting list of HW requirements for standardized kernel
  WARNING: SoC with OS in TN comes with risk of forced update of the gateware development environment when forced to apply certain security patches
  Alternative (and only solution for not UltraScale+): kernel maintained by the SoC team
    Zynq 7000 legacy systems example: collaboration for single kernel and build tools adaptation, shared resource between ABT, HSE and sysadmin

## Slide 27: Open points
FESA on SoC:
  First tests are ongoing
    New timing class to be developed
    No Real-time patches in theory OK, to be tested
  Early-access to equipment groups for tests in Q4 2024
Reference design platform:
  IP Repository setting up, in the frame of Electronics Forum initiative
  DI/OT utils generalization and extension (depending on new SoC HW)
  Co-simulation GW-SW environment, possible collaboration with HSE
Challenging support model: cross-departments, need of a coordination and support body

## Slide 28: Summary
Two feasible ways of using SoCs in the sector:
  As FEC hardware accelerator: part of a crate, OS discouraged
  As integrated system with FEC-like capability: FEC-like software stack is recommended
FEC-like support for SoCs seems a feasible but tight target for LS3 systems
Formalization of the recommendation as document to be approved by the stakeholders
Fundamental for sustainability on the long term:
  Kernel and SoC knowledge retention/acquisition
    Hardware standardization
    Code sharing
    System diagnostics improvement
    Coordination

## Slide 29
Contact us: ats-soc-taskforce@cern.ch
Read about: ATS SoC Wiki