## Slide 1: Introduction to activation physics Christoph Schäfer (many thanks to the HSE RP team)
RSO committee – 1/3/2012

## Slide 2: Contents
Basics of activation physics
Hands-on example

## Slide 3
J
Basics of activation processes

## Slide 4: Basics of activation physics
What is activation?
Activation can be described as the imposed change of nuclear composition of given isotopes resulting in the production of radioactivity
At which particle accelerators can activation occur?
In principle at all high-energy accelerators. However, the radionuclide production rate is much higher at hadron or ion accelerators than those experienced at electron/positron accelerators.
Where does activation occur at accelerators?
At locations with (high) particle losses like:
  Target area
  Dump area
  Beam cleaning sections like collimators and scraper areas
  High-energy physics experiments

## Slide 5: Activation processes
Which production mechanisms of activation occur at high-energy accelerators?
At high-energy accelerators primary particles interact with matter. The primary particle itself or secondary particles interacting with nuclei can produce radioactive isotopes. Main production channels of activation at high-energy accelerators are:
  Spallation and other inelastic hadronic interactions ( (n,n’g), (n,2n), (n,p), (n,a) …)
  Particle capture (mainly neutrons)
  Photodisintegration especially (g,n)-reactions (important for electron accelerators)
proton
neutron

## Slide 6: Isotope production
Activation depends on:
chemical composition of target material
incident particle type
incident particle energy
irradiation & cooling time

## Slide 7: Creation of isotopes at an accelerator
Operation: direct production + decay
Cool-down: indirect production via decay
decay-chains with branching
110mAg
110Ag
110Cd
110Pd
110Cd
Operation
Cool-down
Operation
Cool-down

## Slide 8: Buildup & decay of isotopes
N … Number of isotopes
… Decay constant of isotope
N0 … Number of isotopes at t = 0
t1/2 … Half life
A … Activity (Bq)
N0 … Number of isotopes at t = 0
Decay of a mono-isotopic source described via an ordinary differential equation:

## Slide 9: Buildup & decay of isotopes (simple case)
the production rate P [nuclides/second] is constant
decay chains are neglected
consider only one irradiation & one cooling period
!!!
!!!
At an accelerator we also need to consider buildup  we need to solve a
differential equations, considering beside the decay also a production term P.
Solution for this simple case:

## Slide 10: Buildup & decay of isotopes considering decay chains and multiple irradiation+cooling cycles
…
…
…
…
Nn … Number of isotope n
Pn … Production rate of isotope n
ln … Decay constant of isotope n
bn … Branching ratio from isotope n-1 into n
k … index of irradiation/cooling cycle
At accelerators the production & decay described via Bateman equations:
build-up
decay
… Laplace transform + some algebra
cool-down  decay
operation  build-up & decay
branching
Use
or FLUKA
To solve these problems

## Slide 11: Example of residual activation @ CMS

## Slide 12: Example of residual activation @ CMS
180 days of irradiation,
109 pp/s, 1h of cooling
180 days of irradiation,
109 pp/s, 1d of cooling

## Slide 13: Example of residual activation @ CMS
180 days of irradiation,
109 pp/s, 1w of cooling
180 days of irradiation,
109 pp/s, 1m of cooling

## Slide 14: Air activation
High-energy particles and neutrons are crossing the air which is surrounding beam impact points
Production of radioactive air.
Problems to be considered:
People entering the area are exposed to and inhale the radioactive air
Release of airborne radioactivity to the environment
Beam pipe
Target
Beam traversing air

## Slide 15: Air activation example
Different main contributors to airborne radioactivity at different cooling times
Long lived isotopes (e.g. Be-7) become important for confined spaces for longer irradiation and cooling times
Example: Beam loss on an unshielded object in the SPS tunnel (short term irradiation of air)

## Slide 16: Exercise
Saturation level
After which irradiation time (expressed in multiples of half-lives) do we reach 90%
of the maximum saturation activity? (No cooling!)
Hints:
Operation

## Slide 17: Solution of the excercise
We talk about irradiation only, hence tcool is 0.
Full saturation occurrs after infinite time.
Hence the full saturation level is given with:
x 1.0
We are looking now for 90% of the saturation level
/ ln
with

## Slide 18: Reduction of radioactive waste
Optimization already crucial during the design phase
Beside other aspects also the radiological consequences of the implementation of a material have to be considered
Level of activation depends on the type of the material
Safety benefit
  Lower dose rates and committed doses
Operational benefit
  Reduced downtime due to faster access
  Less restrictions for manipulation & access
End of life-cycle benefit
  Smaller amount and less critical radioactive waste
  Smaller financial burden
S. Myers initiated the project concerning the radiological classification of materials