## Slide 1: Particle accelerators and their medical applications
Varchaswi K S Kashyap
School of Physical Sciences
National Institute of Science Education and Research (NISER) Bhubaneswar

## Slide 2: What are accelerators?
Accelerators are devices that increase the velocity/speed of objects at rest or in motion. Direction?
Accelerator | Driving Lessons Online UK (teachable.com)

## Slide 3
COUNTER-WEIGHT TREBUCHET
A screenshot in AOE2 from the internet
Source: Wikipedia
Picture of several counter-weight trebuchets
Source: Wikipedia
Are these
accelerators?

## Slide 4
ONAGER/MANGONEL
A picture of an onager as modelled in AOE2
Are these
accelerators?
Source: Wikipedia
A picture of an onager
Source: I Have You Now: The Onager, a double-edged sword (armadaihaveyounow.blogspot.com)
Source: Wikipedia
SLINGSHOT

## Slide 5: Particle accelerators in physics and their need
Development of particle accelerators was driven by the curiosity to probe more and more in to the constituents of matter
De Broglie’s principle is what guides the energy of particles needed to probe into matter
Where is the wavelength, is the Planck’s constant and is the momentum.
Larger the momentum (Energy), lower is the wavelength and hence smaller is the object that can be probed
Dimension to be probed | 1 Å (Atomic size) | 1 fm (Nuclear size)
Energy of electron required | ~150 eV | ~ 1 TeV

## Slide 6: Have you come across any particle accelerators in your daily life?

## Slide 7: What about these?
CRT television
CRT monitor
CR Oscilloscope
They have small accelerators that can accelerate electrons up to few keV

## Slide 8: Kinetic energy of a charged particle in an electric field
Speed of the particle is given by

## Slide 9: Ampere’s law
Source:
Jfmelero - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=3634402

## Slide 10: Ampere’s law
Source:
Jfmelero - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=3634402
Biot-Savart‘s law
Source:
Magnetic Field of a Current Loop. Authored by: OpenStax College. Located at: https://openstax.org/books/university-physics-volume-2/pages/12-4-magnetic-field-of-a-current-loop.

## Slide 11: Ampere’s law
Source:
Jfmelero - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=3634402
Biot-Savart‘s law
Source:
Magnetic Field of a Current Loop. Authored by: OpenStax College. Located at: https://openstax.org/books/university-physics-volume-2/pages/12-4-magnetic-field-of-a-current-loop.
Solenoid
Source: http://hyperphysics.phy-astr.gsu.edu/hbase/magnetic/solenoid.html

## Slide 12: Ampere’s law
Source:
Jfmelero - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=3634402
Biot-Savart‘s law
Source:
Magnetic Field of a Current Loop. Authored by: OpenStax College. Located at: https://openstax.org/books/university-physics-volume-2/pages/12-4-magnetic-field-of-a-current-loop.
Solenoid
Toroid
Source: http://hyperphysics.phy-astr.gsu.edu/hbase/magnetic/solenoid.html

## Slide 13: Types of accelerators
Electrostatic accelerators
Cockroft – Walton accelerator
Van de Graaff accelerator
Induction accelerators
Induction Linear accelerator
Betatron
Radio-Frequency (RF) accelerators
RF Linac
RF quadrupole
Pelletron
Cyclotron
Microtron
Synchrotron

## Slide 14: Cockroft – Walton accelerator
Source: Wikipedia
Converts AC voltage to very high DC voltage
Simple in principle and less bulky compared to transformers
Voltages can be tapped at different levels
K.E.

## Slide 15: Van de Graaff accelerator
A Van de Graaff particle accelerator in a pressurized tank at Pierre and Marie Curie University, Paris (Source: Wikipedia, Copyright © 2004 David Monniaux)
Voltages of the order of a few MV can be achieved.
A high voltage supply provides charges to be transported to the metal dome
Charges are collected in a metal dome over time
The potential difference between the dome and the ground can be used to accelerate particles
A Pelletron is very similar to the Van de Graaff having a metal belt with pellets instead of a rubber belt.
K.E.

## Slide 16: Linear accelerator
The Stanford University superconducting linear accelerator, housed on campus below the Hansen Labs until 2007.
(Image credit: Wikipedia)
RF LINAC (Image credit: Wikipedia)
RF LINAC | INDUCTION LINAC
Smaller length | Longer length
Higher acceleration gradient | Lower acceleration gradient
Requires lower power | Requires higher power
Low current and short pulse duration | High current and longer pulse duration
INDUCTION LINAC
(Image credit: INDUCTION, J De Mascureau, 1996)

## Slide 17: Linear accelerator (LINAC) contd.
RF LINAC configurations
Standing wave
Travelling wave
Image credit: By Patrick87 - https://commons.wikimedia.org/w/index.php?curid=29590284

## Slide 18: Medical LINAC
Image credit: www.iaea.org
Image credit: Medical Linear Accelerators in Radiation Therapy, Presentation by Haijun Song, Ph.D. Dept. of Radiation Oncology Duke University Medical Cente

## Slide 19: Medical LINAC configurations
RF power generator and waveguide are both in the gantry and the waveguide is directed straight towards the patient
RF power generator is in the gantry stand and waveguide is in the gantry directed towards the target above the patient
Both RF power generator and waveguide are in the gantry stand. The electrons have to be transported to the target.
Both X-rays and
electrons (upto MV)
Both X-rays and
electrons (upto MV)
Only X-rays
Image credit: Treatment machines for external beam radiotherapy, E.B. Podgorsak, Department of Medical Physics, McGill University Health Centre, Montreal, Quebec, Canada

## Slide 20: Medical LINAC configurations contd.
Image credit: Medical Linear Accelerators in Radiation Therapy, Presentation by Haijun Song, Ph.D. Dept. of Radiation Oncology Duke University Medical Centre

## Slide 21: Cyclotron
Image credit: Cyclotron (gsu.edu)
Image credit:
Hammer Throw - How to Play? (tutorialspoint.com)
Lawrence's 60-inch cyclotron, with magnet poles 60 inches (5 feet, 1.5 meters) in diameter, at the University of California Lawrence Radiation Laboratory, Berkeley, in August, 1939. Image credit: Wikipedia

## Slide 22: What to do if particle becomes relativistic?
Iso-cyclotron (Isochronous)
Keep frequency constant and vary the magnetic field
Synchro-cyclotron
Keep magnetic field constant and vary the frequency
Image source: Wikipedia
Image credit:
COMET Cyclotron | CPT | Paul Scherrer Institut (PSI)

## Slide 23: What to do if particle becomes relativistic?
Iso-cyclotron (Isochronous)
Keep frequency constant and vary the magnetic field
Alias: Azimuthal varying field cyclotron
Image credit: http://www.geology.wisc.edu/~johnf/g777/Misc/chap15.pdf

## Slide 24: What to do if particle becomes relativistic?
Synchro-cyclotron
Keep magnetic field constant and vary the frequency
Image credit: Wikipedia
Higher energy achievable
Lower average beam current
Compact dimension

## Slide 25: Layout of a cyclotron complex for proton therapy PSI
Image credit: Accelerators for proton therapy, Presentation by, Marco Schippers, PSI - JUAS

## Slide 26: What if both the frequency and magnetic field can be changed?

## Slide 27: Synchrotron
Image credit: Particle Accelerator Physics, Helmut Wiedemann, 4th edition, Springer
Image credit: http://www.geology.wisc.edu/~johnf/g777/Misc/chap15.pdf

## Slide 28: Particle accelerators and medical use
Particle | Accelerator | Energy | Use
Electron | LINAC | ~6-25 MeV | Cancer treatment
X-rays | LINAC | ~6 MeV | Cancer treatment
 | Synchrotron | ~100s of keV | Imaging - coronary angiography, bronchography, mammography, computed tomography, x-ray microscopy
Proton | Cyclotron | ~20-100 MeV | Radioactive assay preparation for PET, SPECT scanning
 | Synchrocyclotron | ~250 MeV | Cancer treatment
Carbon | Synchrotron | ~400 MeV/u | Cancer treatment

## Slide 29: How do you get free electrons?

## Slide 30: Particle sources?
Photocathode based electron source.
Image credit: Electron sources for accelerators Carlos Hernandez-Garcia, Patrick G. O’Shea, and Marcy L. Stutzman, Physics Today, February 2008 (Volume 61, Issue 2).
Penning ion source
Image source: electron and ion sources for particle accelerators R. Scrivens

## Slide 31: Thank you. Hope you’ve all been accelerated!!

## Slide 32: Some questions to think about
Q1: Can you design a multistage accelerator using the gravitational force?
Q2: Is it possible to calculate the electric field at the centre of a Toroid?
Q3: Suppose you want to build a LINAC to accelerate protons to energies of 1 TeV. How long would it have to be?
Q4: What is fundamental? Force/field or the particle charge?
OR