## Slide 1: Progress on Automating Experiments at the Argonne Wakefield Accelerator Using Advanced Bayesian Optimization Algorithms
Ryan Roussel
rroussel@slac.stanford.edu

## Slide 2: Automation Challenges at AWA
The Argonne Wakefield Accelerator (AWA) facility is an accelerator physics test facility at Argonne National Laboratory.
The accelerator does not run continuously, and is restarted and retuned from scratch every day  a major obstacle for the small team of operators
Sad operator during his PhD
(circa. 2019)

## Slide 3: Goals of this work:
The goal of this work is sequential start-to-end, autonomous configuration of the drive beamline from the photoinjector to a wakefield experiment:
Requires solving multiple different online optimization subtasks with varying objectives, constraints  multiple algorithms / strategies
Where possible, should leverage prior physics information to accelerate optimization convergence

## Slide 4: Trust Region + Constrained BO
Beam steering through linac cavities
Log-Expected improvement w/ trust region Bayesian optimization (TuRBO)
Constraints on beam bounding box extent in screen
Polynomial kernel to leverage physics info
Reinforcement learning approach will also be investigated
Diagnostic screens

## Slide 5: Trust Region + Constrained BO
Constraint:
Reinforcement learning approach will also be investigated
Diagnostic screens
Beam steering through linac cavities
Log-Expected improvement w/ trust region Bayesian optimization (TuRBO)
Constraints on beam bounding box extent in screen
Polynomial kernel to leverage physics info

## Slide 6: “Safety” Trust Region + Constrained BO
Beam focusing / transport through structures
Log-Expected improvement to maximize extracted power w/ “safety” TuRBO
Constraints on transmission (small valid region of parameter space)
Quadrupoles
Transmission
Extracted power
Steering magnets

## Slide 7: Bayesian Algorithm Execution
Bayesian Algorithm Execution (BAX) is a generalization of acquisition functions that enables more complex (potentially virtual) objectives
Uses an information-theoretic approach to the selection of future measurements
In layman’s terms: we select observations that are predicted to maximally reduce the uncertainty of optimal parameter configurations (ie. uncertainty in )
Four (!) applications of BAX @ AWA

## Slide 8: RF Phasing Inside Photoinjectors (Schottky Scan)
Goal: Determine the RF phase where photoemitted electrons start to be accelerated – set photoinjector gun phase to +50 deg this value
BAX Algorithm:
Entropy based TuRBO

## Slide 9: Beam Alignment Through Quadrupoles
Goal: Steer beam through the center of N quads
BAX Algorithm:
BAX Algorithm (English): Find the steering current that minimizes the beam deflection as the quadrupole current is scanned
Note: also subject to beam position / size constraints
R. Roussel, et. Al., LINAC2024-THPB066

## Slide 10: Aligning the Laser in the Solenoid
Goal: Align laser spot / steer electron beams through the center of a solenoid magnet
BAX Algorithm:
Note: also subject to beam position / size constraints
Laser spot

## Slide 11: Towards 6D Phase Space Distribution Control
Usually most challenging step of online control
Necessary as a starting point for various experiments
Staged R&D Approach:
RMS Control (4D)
  Autonomous phase space measurements
  Uncertainty quantification
  BAX emittance optimization
Exact beam distribution control (4D)
  GPSR
6D phase space control (future)
Normal / skew quadrupoles
Dipole
Cavity
Current distribution
Target distribution

## Slide 12: Autonomous Emittance Measurements
Varying upstream parameters changes the valid region of quadrupole scan strengths needed for a successful measurement
Autonomously sample quadrupole strengths based on exploration-weighted UCB + constraints
Demonstrated and refined at SLAC  transfer to AWA
9D optimization of LCLS injector
D. Kennedy

## Slide 13: Uncertainty Quantification Based Control
Use measurements collected from beamline alignment / optimization to reconstruct the beam distribution w/ uncertainties using VI / HMC
+
Feed reconstructed distribution into cheetah to predict optimal control params  twiss matching etc.
Uncertainty-aware reconstructions
Online control

## Slide 14: BAX Application: RMS Emittance Optimization
The BAX algorithm chooses beam size measurements that reduce uncertainty in without measuring emittance directly  20x speed up
Goal: Determine the ideal tuning configuration which minimizes emittance
Miskovich, Sara Ayoub, et al. MLST 5.1 (2024): 015004.
BAX Algorithm:

## Slide 15: 4D Generative Phase Space Reconstruction
Use data collected from autonomous emittance measurements to reconstruct the 4d distribution during operations (< 1 min)
Example from LCLS
Roussel, Ryan, et al. PRL 130.14 (2023): 145001.
pip install gpsr https://github.com/roussel-ryan/gpsr

## Slide 16: 6D Generative Phase Space Control
Normal / skew quadrupoles
Dipole
Cavity
Scan cavity phase and dipole state to manipulate longitudinal phase space + quadrupole scan
6D phase space measurement
(See talk by S. Kim on Thursday)
Similar approach to 4D case
Combine measurements with cheetah simulation to estimate beam parameters
Solve for beamline params to tailor phase space distribution
Use multi-fidelity approach to optimization of upstream parameters
Roussel, Ryan, et al. PRAB 27.8 (2024): 084801.
Ferran Pousa, Angel, et al PRAB 26.8 (2023): 084601.

## Slide 17: Outlook
Autonomous configuration of the AWA drive beamline and experimental beamlines
  4-8 hour tuning time  < 2 hour tuning time (w/o expertise)
Integrate GPSR measurements into online operations, detailed analysis of complex beam distributions

## Slide 18: Xopt
AI/ML R&D @ AWA

## Slide 19: Questions?
Thanks to the team!

## Slide 20: Backup

## Slide 21: Bayesian Statistical Analysis for Beam Matrix Components
p(B): the prior
p(A|B): the likelihood (evidence)
P(B|A): the posterior

## Slide 22: Beam Matrix Uncertainty Quantification
Posterior distribution
Prior distribution
Data
Bayesian inference

## Slide 23: Emittance Posterior + Beamsize Fit
Calculate mean, median, variance, quantiles etc.

## Slide 24: Hysteresis Modeling
Modeling w/o Hysteresis
Modeling w/ Hysteresis
Roussel R. et al., Accepted by PRL