## Slide 1
2025-04-08
Serval Applications of Machine Learning at HEPS
Wei Bao, Xiaohan Lu, Yi Jiao
Notes: Good afternoon, everyone.
I’m Bao Wei from IHEP, China. I’ m honor to be here. My presentation topic is “Several Applications of Machine Learning at HEPS”.

## Slide 2: Outline
Introduction
Machine Learning Applications
  Data-driven Evaluation and Optimization of Touschek Lifetime
  Optimizes beam lifetime using Sextupole combinations
  Vacuum early warning of HEPS based on CNN
Conclusion
Notes: I will discuss this topic in three sections. Under the Machine Learning Applications section, I will cover three specific cases: Data-driven Evaluation and Optimization of Touschek Lifetime, Beam Lifetime Optimization using Sextupole Combinations, and Vacuum Early Warning at HEPS Based on Convolution Neural Network.
First section is Introduction,

## Slide 3
Introduction to HEPS
High Energy Photon Source
Linac
Booster
Storage Ring &Experiment Hall
User Service Building
 | APS-U | ESRF-EBS | MAX-IV | Sirius | HEPS
E(GeV) | 6 | 6 | 3 | 3 | 6
C(m) | 1104 | 844.4 | 528 | 518 | 1360.4
Lattice | 7BA | 7BA | 7BA | 5BA | 7BA
Cell | 40 | 32 | 20 | 20 | 48
Emittance (pm*rad) | 42 | 150 | 330 | 250 | 34
Brightness |  |  |  |  | 
Construction period | 2018-2024 | 2015-2020 | 2010-2016 | 2015-2018 | 2019~2025
 | APS-U | ESRF-EBS | MAX-IV | Sirius | HEPS
E(GeV) | 6 | 6 | 3 | 3 | 6
C(m) | 1104 | 844.4 | 528 | 518 | 1360.4
Lattice | 7BA | 7BA | 7BA | 5BA | 7BA
Cell | 40 | 32 | 20 | 20 | 48
Emittance (pm*rad) | 42 | 150 | 330 | 250 | 34
Brightness |  |  |  |  | 
Construction period | 2018-2024 | 2015-2020 | 2010-2016 | 2015-2018 | 2019~2025
One of the world's brightest fourth-generation synchrotron light sources
The facility has the capacity for more than 90 high-performance beamlines and can provide X-rays with energy up to 300 keV
The facility offers 10nm spatial resolution, 1MeV energy resolution, and picosecond time resolution for high-frequency dynamic detection
Notes: HEPS is a fourth-generation synchrotron radiation facility under construction in Beijing, China. It is one of the brightest light sources in the world, equipped with 90 high-performance beamlines.

## Slide 4
Booster Energy up to 6GeV
Storage Ring Beam Commissioning Start
Beam Current reach 12mA
Beam Current reach 40mA
Launch first Light
Verify Displacement Injection
2023.08
2024.08
2024.09
2024.10
2024.12
2024.08
Emittance Below 100pm·rad at 27mA
2025.01
Joint-Commissioning Phase Launched！
2025.03
current 12 mA
Lifetime~ 2 min
Milestones of HEPS Construction and Beam Commissioning
Notes: We recently entered the Joint-Commissioning Phase. Before this, we completed four rounds of storage ring commissioning. During the first round, we achieved beam storage and increased the beam current to 12mA. In the second round, we further improved the current to 40mA. In the third round, we generated the first synchrotron light and began beamline alignment experiments. In the fourth round, we validated displacement injection and achieved an emittance below 100 pm·rad at a current of 27mA.

## Slide 5
Data-driven Evaluation and Optimization of Touschek Lifetime
Optimizes beam lifetime using Sextupole combination
Vacuum early warning of HEPS based on CNN
Several Machine Learning Applications
Notes: At HEPS, we have explored several machine learning applications. I will now introduce three of them.
The First Application is Data-driven Evaluation and Optimization of Touschek Lifetime

## Slide 6
Why do this?
Time cost is extremely high.
During the lattice design phase, thousands of candidate lattices must be evaluated, making the computation extremely time-consuming!
1000 turns Always requires 3 ~ 5 hours
300 turns example. ~1 hour
Notes: Calculating Touschek lifetime typically requires determining the Local Momentum Acceptance (LMA). For fourth-generation light sources, this is critical but time-consuming because we need to compute LMA at multiple longitudinal positions. Traditional methods involve long-term particle tracking. For example, tracking 300 turns takes about 1 hour, while tracking 1,000 turns requires 3 to 5 hours. During the lattice design phase, thousands of lattices must be evaluated, making the computation extremely time-consuming.

## Slide 7
Describe Initial particles:
At each (where i = 1, 2, ..., N, with N being the element index), we set and uniformly sample 𝛿 at each position.
Generate particles with these initial conditions and performing long-term tracking simulations
Evaluate the maximum positive and negative momentum deviations (and ) among all stably tracked particles at
Calculate the Touschek lifetime using the LMA
General Method to Calculate Toushek Lifetime
Notes: In the general method, we generate particles distributed across different s positions, set their coordinates (x, y, x’, y’, z) to zero, and uniformly sample delta (δ). Long-term tracking is then performed to determine the maximum surviving δ at each s position (LMA), which is used to calculate the Touschek lifetime. This serves as the ground truth.
To obtain the Local Momentum Acceptance (LMA) at each 𝑠_𝑖 (where i = 1, 2, ..., N, with N being the element index), we set 𝑥=𝑥^′=𝑦=𝑦^′=𝑧=0 and uniformly sample 𝛿 at each 𝑠_𝑖 position. By generating particles with these initial conditions and performing long-term tracking simulations, we evaluate the maximum positive and negative momentum deviations (𝛿_𝑚𝑎𝑥^+ and 𝛿_𝑚𝑎𝑥^−) among all stably tracked particles at 𝑠_𝑖. The LMA along the entire ring is thereby determined, enabling the calculation of the Touschek lifetime.

## Slide 8
Short-Term Tracking for All Initial Particle
  Track all particles for 1 or a few turns;
  select the 10% of surviving particles.
Long-term tracking (e.g., 300+ turns)
  Label these selected particles as survive (surviving 300+ turns) or loss (lost earlier) for supervised learning.
Classifier Training
  Train a classification model (e.g., Random Forest, AdaBoost) using features derived from the results of short-term tracking and long-term tracking.
Predict Particle status to obtain LMA
  Apply the trained model to predict stability for all initial particles.
  Identify the maximum momentum deviations of predicted stable particles to define the LMA.
Touschek Lifetime Calculation
  Compute the Touschek lifetime based on the predicted LMA.
Traditional Method
Using Random Forest here
Blue: Labeled as survive (+1)
Red: Labeled as lost (−1)
These dots form the training dataset for the classifier
ML-based Method Steps
Notes: To speed things up, we came up with a machine learning method. Let me walk you through how it works - you can follow along with the picture.
First, we do quick, short-term tracking runs for all the particles. Then we take about 10% of the particles that survive after short-term tracking and long-term tracking on them - these particle survive status become our training labels.
Then, we train a classifier using the data including the particles' short-term trajectories, s positions, and delta values. Once trained, the model can predict which particles will survive after long-term tracking, which lets us evaluate the LMA and calculate Touschek lifetime much faster.

## Slide 9
Black: Obtained via numerical simulation. (ground truth) Time cost: ~ 60 minutes. Touscke Lifetime : 0.4984h
Red: Predicted using machine learning method. Time cost : ~ 9 minutes. Touscke Lifetime: 0.5238 h
Green: Derived from direct tracking of 10% particles (without ML)
ML-Method reduces computation time by roughly an order of magnitude
Result of Numerical Experiment Based on the HEPS storage ring lattice
Notes: Let's look at the results. Here you can see our predicted LMA values (the red line) match up really well with the actual ground truth (black line). If we just used the 10% of particles we tracked long-term directly (that's the green line), the results would be much less accurate. Then, We're getting Touschek lifetime estimates within about 5% error, and we're doing it about 10 times faster than before.

## Slide 10
Different Sampling Rate / Model
Different Sampling Method
The prediction accuracy of the survival status of all initial particles.
Accuracy Comparison of Results with Different Hyperparameters
Notes: We didn't stop there - we tested all kinds of settings to make sure this works well. The left plot shows random forests give us stable results even when we only sample 10% of the particles. The right plot tells an interesting story - the more particles we sample, the better our accuracy gets. This means we can tune our sampling rate to get just the right balance between speed and accuracy.

## Slide 11
Test ML method in different Lattices：
Average Error: ~ 6%
Notes: Here's another thing - our method works with any lattice configuration because we generate fresh training data each time. To prove this, we created different lattice setups by tweaking the sextupole strengths. Even with these changes, our average error stayed around 6%, showing this method is robust no matter how you set up your lattice.

## Slide 12
Data-driven Evaluation and Optimization of Touschek Lifetime
Optimize beam lifetime using Sextupole combinations
Vacuum early warning of HEPS based on CNN
Several Machine Learning Applications
Notes: Next, is the Optimize beam lifetime using Sextupole combinations.

## Slide 13
Why do this?
HEPS has 12 sextupole groups leading to infinitely many possible combinations！
Searching for the optimal combination is a computationally intensive and time-consuming challenge.
So… we can use Machine Learning！
Notes: During the late Commissioning phase, the main target is optimization of beam lifetime. One of the keys is tuning our 12(twelve) pairs of sextupoles - but with so many possible combinations. The time cost is so expensive. So... We can use Machine Learning.

## Slide 14
Simulation Steps
The Simulation flow
Target： Adjusting the intensity of the Sextupole to optimize the injection efficiency and Touschek lifetime
Notes: Let me show our machine learning method:
First, we generate 10,000(ten thousands) different sextupole combinations. Now testing all of them would take forever, so here's what we do instead - we use a clustering algorithm to group them into 10 categories. From each group, we pick one representative combination, giving us 10 key combinations to test.
We then simulate these 10 combinations to get their beam lifetime results - these become our training data. With this data, we train a machine learning model that can predict the performance of all 10,000 combinations.

## Slide 15
Simulation Result
Simulation Results
Notes: The simulation results look really good! As you can see in the left plot, our predictions (the orange dots) match very closely with the actual simulation results (blue dots). The differences are quite small, which means our model is working well.

## Slide 16
How to do at HEPS?
The Experiment flow
Target： Adjusting the intensity of the Sextupole to optimize the injection efficiency and Touschek lifetime
Notes: Last year, we tried this method at HEPS Booster. The main differences were:
We used real machine data for both lifetime and injection efficiency. We added a verification step - after making predictions, we actually tested the top combinations in the machine. If the results didn't match predictions, we'd add this new data to our training set and repeat the process.

## Slide 17
Beam Experiments based on HEPS Booster
The Application for Sextupole Scanning
Method： Randomly generate sextupole seeds, measure the beam parameters of the actual machine, train a ML model, and obtain the optimal combination from the model
Experiment： Set the sextupole seed and measure the injection efficiency and beam Tousheck lifetime of the booster
Data from HEPS
Notes: For these experiments, we developed a special program to scan sextupole combinations. But because the Booster need to take time to ramp up, we could only collect about 120 data during our test period - you can see these in the right plot.

## Slide 18
Result and Future Work
For the Booster, data acquisition is time-consuming due to the required energy ramping.
Significant fluctuations in experimental data lead to large model errors.
To improve accuracy, a more stable machine state and increased measurement data are needed.
This method is more suitable for use in the mid-to-late stages of beam commissioning.
Actual Data Result
underfitting
Notes: Honestly, the results weren't great. The data was too noisy to build a reliable prediction model. After analyzing, we realized the machine was still too unstable during early commissioning - the variations were just too big. That's why we plan to repeat these experiments later when we're working with the storage ring. And the conditions should be more stable.

## Slide 19
Data-driven Evaluation and Optimization of Touschek Lifetime
Optimizes beam lifetime using Sextupole combinations
Early warning for vacuum at HEPS based on CNN
Several Machine Learning Applications
Notes: The final application is Early Warning for vacuum at HEPS based on CNN.

## Slide 20
For some vacuum error, the vacuum pressure may continue to rise before the vacuum valve interlock is triggered.
With early warning information available, operators can take timely action to prevent potential interlock failures！
Focus on the state of the local spatial region, and since multiple devices are correlated, using CNN is a good solution.
Early Warning is Important!
Notes: As we all know that vacuum faults can trigger machine interlocks, impacting operational stability. Slow pressure drifts are particularly challenging to detect. And for machine learning, we can focus on the local spatial region, so we can use convolution Neural Network!

## Slide 21
Following the CSNS Early Warning System [1]
The China Spallation Neutron Source (CSNS) has successfully implemented an early warning system based on 55 vacuum gauge readings.
[1] He Yongcheng, Zhang Yuliang, Wang Lin, et al. Prototype of an early warning system based on deep learning for the CSNS accelerator[J]. High Power Laser and Particle Beams, 2021, 33: 044008. doi: 10.11884/HPLPB202133.200340
Model Structure:
Result:
Deployed and Apply Successfully
Best Test Accuracy: 98.4%
CSNS has Developed and Apply Successfully!
Notes: We got this idea from our colleagues at China Spallation Neutron Source(CSNS). They built a CNN model that uses readings from 55 vacuum gauges to predict potential issues, and it works really well - about 98% accurate. Actually, they've already successfully deployed this system in operation. You can see in the graph on the right - this is a real example where their system successfully caught and warned about a vacuum fault before it became a problem.
Following their success, we decided to adapt this method for HEPS.

## Slide 22
HEPS Storage Rings are equipped with approximately 207 vacuum gauges.
Get warning timestamps from the alarm
Get data from Archiver
Data validation
Forward filling
Generate dataset
Verify dataset through raw data
Normalization
Train CNN model
Sort vacuum gauge readings by time
Data Process Flow：
Application to HEPS Storage Rings
Notes: For our implementation at HEPS, we had to make several adjustments. First, we scaled up the system to handle data from all 207 vacuum gauges. The model now takes 1-minute readings from each gauge and outputs a 10-level risk prediction. We pulled historical fault data from our Archiver Appliance and tweaked the model architecture to fit our needs.

## Slide 23
Model Structure and Result
Result:
Model Structure:
Input Matrix: 207 device read value
60 seconds
Output: 10 grades
0: normal
9: error
Conv Kernel: 7*7
Conv Kernel: 4*4
Flatten
Notes: As you can see from these results, the model shows good convergence on our training data - which is really encouraging.

## Slide 24
Problems and Future Work
Problems
Limited HEPS fault data restricts model training
The model converges well on existing data but lacks generalization
Future Work
Collect more fault data to improve robustness.
Introduce more relevant features (e.g., Beam Loss Monitor data) for better fault characterization.
Continuously update the model for improved generalization.
Train:
Model Structure:
Notes: However, we did run into some challenges. When we tested the model‘s generalization ability, the performance wasn’t as strong as we‘d hoped. After analyzing the results, we believe this is mainly because we simply don’t have enough fault cases in our dataset yet. Going forward, we plan to keep collecting more operational data and also explore adding other features - like beam loss monitor readings - to improve the model's performance.

## Slide 25
One more thing
Notes: One important lesson we've learned is just how important data quality is.

## Slide 26
Focus on Data at HEPS
The primary data source for accelerator: Archiver
HEPS Status:
Approx. 150k PVs are archived in Archiver, less than 50% of the total PVs.
Waveform, images, high repetition rate data, and some temperature and vibration data have not been stored in the archiver
In the archiver, PVs are collected and stored independently, lacking time synchronization
Extracting diverse data from the historical database is quite challenging
AI-Ready?
High-quality data: diversity and richness
Data preprocessing: label and clean
Structuring: unified format and definition
Easy access and retrieval: metadata
Build a multimodal database
Archiver batch data retrieval interface
Parameter scanner
Batch data processing module
Establish a metadata database
Generate structured datasets
Platform for AI-Ready Dataset
Notes: At HEPS, we deal with diverse data types - waveforms, images, and more. To really accelerate our machine learning research, we're building a platform that can automatically prepare AI-ready datasets from all these different sources.

## Slide 27: A FAIR-Compliant Platform for AI-Ready Dataset in Particle Accelerator
Scan/Fetch Data
High sampling rate data
Multi-Model Database
Data Processing
Dataset Publication
Dataset Application
To supply the historical database, the multimodal database stores waveform, image and high-repetition-frequency data.
For specific problems, a large amount of historical data of the accelerator is duplicate, which always is invalid training data.
Batch processing and targeted extraction of data from the historical database are necessary processes for obtaining high-quality data.
Large-scale parameter scanning + multi-modal data acquisition can effectively solve the problem of data diversity
To ensure the validity of the data, the beam state is monitored in real time while scanning.
progress：
Implemented by separating the front-end and back-end, developed the control interface based on the Web
Used MongoDB to build a multi-modal database
Completed the basic functions of the parameter scanning program
Preliminary completion of the construction and testing of the multi-modal database
Notes: Over the past few months, Here's what we've accomplished so far: - We've created a flexible system with separate frontend and backend components - Use MongoDB to build a multi-model database - Developed automated tools for parameter scanning and fetching historical data.
And then, we'll be testing it live with actual machine data and continuously improving the system.

## Slide 28
Conclusion
We proposed a data-driven approach for Touschek lifetime evaluation and optimization, achieving high accuracy while reducing computation time by an order of magnitude.
We explored sextupole combinations to optimize beam lifetime and conducted preliminary experiments on the HEPS booster.
We adapted a CNN model for vacuum early warning and will continue improving it in the future.
The FARAD platform is under development to generate AI-Ready dataset for particle accelerator.
Notes: In summary, We proposed a data-driven approach for Touschek lifetime evaluation and optimization, achieving high accuracy while reducing computation time by an order of magnitude. We explored sextupole combinations to optimize beam lifetime and conducted preliminary experiments on the HEPS booster. We adapted a CNN model for vacuum early warning and will continue improving it in the future. Finally, the FARAD platform is under development to generate AI-Ready dataset for particle accelerator.

## Slide 29
Thanks for your attention!
Wei Bao, Xiaohan Lu, Yi Jiao
2025-04-08
Notes: That is all. Thank you for your attention.

## Slide 30
backup

## Slide 31
Milestones of HEPS Construction and Beam Commissioning
2021.06, installation of the first equipment
2023.03, obtained radiation protection of the Linac and started beam commissioning
2023.06, completed process acceptance of the Linac
2023.07, beam commissioning of the booster started
2023.08, the energy of booster ramp to 6GeV
2024.07，beam commissioning of the storage ring started
2024.08, beam current has reached 12mA
2024.09, increase beam current, up to 40mA
2024.10, launch the first light and conduct beamline -related experiments
2024.12, verify the displacement injection based on high energy accumulation of booster
2025.01 beam emittance is below 100pm·rad at 27mA
2025.03 joint-commissioning phase launched
current 12 mA
Lifetime~ 2 min

## Slide 32: Round 1: Storage Beam Commissioning (7.23-8.27)
Start
First turn through
Beam circulation 10 turns
Beam circulation 1000 turns
Beam first storage
Beam Lifetime 1min
07.23
07.29
08.04
08.06
08.06
Turn 2 Beam Single
第11圈束流信号
>1000 turns
~1.3s
07.23
First storage multi-bunch
08.08
current~ 60uA
lifetime~ 1 min
Beam Current reach 7mA
08.15
current 7 mA
Lifetime ~ 2 min
08.18
Turn 12 Beam Single
Beam Current reach 12mA
current~ 0.4 mA
lifetime~ 1 min
current 12 mA
Lifetime~ 2 min

## Slide 33: Round 2: Increase current, up to ~40 mA (9.12-9.26)
Replace the vacuum box in R20 area to solve the vacuum limitation bottleneck
Replace the injection pulse impactor to solve the bottleneck of flow intensity limitation
Beam cleaning
9-23 Beamline commissioning

## Slide 34: Round 3: Launch the first light and conduct beamline-related experiments (10.5-11.1)
Start
Beam Commissioning
Large Current Experiment
Beamline commissioning
First light

## Slide 35: Round 4: Completed preliminary optimization of beam dynamics (11.30-1.26)
Successful verification of displacement injection based on high energy accumulation of Booster
Enabling higher charge injection
The beam emittance is below 100 pm·rad (acceptance index) at 27mA.

## Slide 36
For LMA, we describe the initial particle position using
: the six-dimensional phase-space coordinates of the particle.
: the longitudinal exit position of the beamline element.
Data-driven Evaluation and Optimization of Touschek Lifetime
Time cost is extremely high.
For HEPS, tracking over 1,000 turns requires 3~5 hours per evaluation.
During the lattice design phase, thousands of candidate lattices must be evaluated, making the computation extremely time-consuming!
Notes: To obtain the Local Momentum Acceptance (LMA) at each (where i = 1, 2, ..., N, with N being the element index), we set and uniformly sample 𝛿 at each position. By generating particles with these initial conditions and performing long-term tracking simulations, we evaluate the maximum positive and negative momentum deviations (and ) among all stably tracked particles at . The LMA along the entire ring is thereby determined, enabling the calculation of the Touschek lifetime.
To obtain the Local Momentum Acceptance (LMA) at each 𝑠_𝑖 (where i = 1, 2, ..., N, with N being the element index), we set 𝑥=𝑥^′=𝑦=𝑦^′=𝑧=0 and uniformly sample 𝛿 at each 𝑠_𝑖 position. By generating particles with these initial conditions and performing long-term tracking simulations, we evaluate the maximum positive and negative momentum deviations (𝛿_𝑚𝑎𝑥^+ and 𝛿_𝑚𝑎𝑥^−) among all stably tracked particles at 𝑠_𝑖. The LMA along the entire ring is thereby determined, enabling the calculation of the Touschek lifetime.