## Slide 1: Phase Space Reconstruction of CSR-affected Beams
MaLAPA Workshop
CERN, Switzerland
April 10th, 2025
Juan Pablo Gonzalez-Aguilera
Department of Physics and Enrico Fermi Institute
University of Chicago
jpga@uchicago.edu

## Slide 2: Team
This work was supported by:
NSF award PHY-1549132, the Center for Bright Beams
DoE contract No. DE-AC02-05CH11231, NERSC award BES-ERCAP0023724
Young-Kee Kim
J.P. Gonzalez-Aguilera
Ryan Roussel
Auralee Edelen
Eric Wisniewski
Wanming Liu
Alexander Ody
John Power
Philippe Piot
Seong-Yeol Kim
(now at PAL, Korea)
PhD Advisors
This work was supported by:
NSF award PHY-1549132, the Center for Bright Beams
DoE contract No. DE-AC02-05CH11231, NERSC award BES-ERCAP0023724

## Slide 3: Synchrotron Radiation
Radiation produced by relativistic charged particles moving along curved trajectory
Coherent / incoherent
K.-J. Kim et al.,2017

## Slide 4: Coherent synchrotron radiation in compressed beams
CSR is produced when bending beam trajectory
Radiation emitted by tail of beam kick particles ahead
FEL applications need highly compressed beams longitudinally
Dispersive lattices are used to compress the beams (e.g., chicanes)
H. Bartosik, 2022. arXiv:2201.01532
S. Di Mitri, USPAS 2015

## Slide 5: CSR Degrades Beam Quality
CSR wakefield induces nonlinear kick in vs
Dipoles also introduce correlations with
Result: rotation and centroid shift of longitudinal slices, increasing the projected
initial
final
initial
final

## Slide 6: Measurement of CSR Effects
Studies of CSR effects are limited to macro-scale description of beam distribution:
  Projected growth
Y. Jing et al., Phys. Rev.
ST Accel. Beams. 2013
Does not resolve detailed beam structure!
Full picture.
We want this!
Projection
misses detail!

## Slide 7: Measuring high-dimensional beam distributions
7
Cathey, Brandon, et al. PRL 121.6 (2018): 064804.
Multiple scanning slits with dipole and bunch shape monitor @ SNS (ORNL)
5D tomography with polarizable X-band TDC @ ARES (DESY)
960 measurements ~ 28 hrs
Tomographic reconstruction ~ 24 hrs
5 million (!) measurements ~ 32 hrs
Jaster-Merz, S., et al Proc. IPAC’22 (2022): 279-283.

## Slide 8: Generative Phase Space Reconstruction (GPSR)
    R. Roussel et al. PRAB 2024

## Slide 9: GPSR Scan
dipole
transverse deflecting cavity
quad
YAG 1
YAG 2
lower energy
higher energy
OFF/ON
OFF/ON
5 quad strengths
Total training images: 20

## Slide 10: GPSR Scan
5 quad strengths
OFF/ON
OFF/ON
    R. Roussel et al. PRAB 2024

## Slide 11: Experimental 6D GPSR at AWA
    R. Roussel et al. PRAB 2024
Temporal structure
likely from laser
homogenization optics
Magnetization due
to solenoid focusing
6D reconstruction from
  20 measurements
  15 minutes analysis time
  No pre-training needed

## Slide 12: CSR at the Argonne Wakefield Accelerator
Generate a beam influenced by CSR in double dogleg
Measure phase space after 4th dipole with beam diagnostics
generate CSR effects
Beam
1 nC, 43 MeV
diagnose CSR effects
Adapted from N. Majernik et al., PRAB, 2023.

## Slide 13: Simulated CSR Effects: and
`
CSR off
CSR on

## Slide 14: Simulated GPSR Training Data
Diagnostics lattice
Screen sizes: 30mm

## Slide 15: Simulated GPSR Results
Gonzalez-Aguilera et. al., Proc. IPAC’24
ground truth
reconstruction
      50th percentile reconstructed
      50th percentile ground truth
      95th percentile reconstructed
      95th percentile ground truth

## Slide 16: Dispersion dominates for larger energy spread
CSR
off
CSR
on
initial
Dispersive:
Emittance growth dominated
by dispersion
Non-dispersive
Emittance growth dominated
by CSR
Flip x

## Slide 17: Experiment data
Full beam (1nC)
Expect: significant CSR effects
Masked beam (0.05 nC)
Masked along x before first dipole
Expect: less CSR effects

## Slide 18
Experiment full beam (1 nC)

## Slide 19
Experiment masked beam (0.05 nC)

## Slide 20: Conclusions
Experiments at AWA look promising
  Reconstructed beam show indication of CSR effects at 1nC
  Must compare with more accurate simulations
GPSR can reconstruct structure of CSR-affected beams
  Fast
  Accurate
  Detailed
GPSR is a very powerful tool
  6D phase space information gives the full physical picture

## Slide 21: Thanks! Questions?
This work was supported by:
NSF award PHY-1549132, the Center for Bright Beams
DoE contract No. DE-AC02-05CH11231, NERSC award BES-ERCAP0023724
Young-Kee Kim
J.P. Gonzalez-Aguilera
Ryan Roussel
Auralee Edelen
Eric Wisniewski
Wanming Liu
Alexander Ody
John Power
Philippe Piot
Seong-Yeol Kim
(now at PAL, Korea)
PhD Advisors
This work was supported by:
NSF award PHY-1549132, the Center for Bright Beams
DoE contract No. DE-AC02-05CH11231, NERSC award BES-ERCAP0023724

## Slide 22: Bckp, reversing quads

## Slide 23: Bckp, CSR-induced emittance growth

## Slide 24: Bckp, NN Generator
6D phase space distribution parametrization that is
  flexible
  learnable
Fully connected NN with ~ O(1k) parameters