## Slide 1: Recirculating Linacs (RLAs) and beam parameters at RLA-RCS transfer
Avni Aksoy

## Slide 2: Collider Concept
Short, intense proton bunch
Ionisation cooling of muon in matter
Acceleration to collision energy
Collision
Fully driven by muon lifetime
Protons produce pions which decay into muons, muons are captured
Acceleration
from 0.25 GeV to 63 GeV

## Slide 3: High efficient low cost acceleration for low energy Muons
Well known acceleration scheme in literature is ‘dogbone’ RLA proposed for a future Neutrino Factory (Alex Bogacz)
Single linac is used to accelerate consecutive µ- and µ+ bunches in one RF pulse with many passes
Independent arcs due to large energy variation between passes..

## Slide 4: Low Energy Acceleration Layout

## Slide 5: Beam Parameters along the acceleration chain
Very long bunch after final coolling (375 mm)
  One can use induction linacs in injection. However bunch needs to be compressed at least by factor 10.
10 % emittance growth in the transverse and longitudinal planes, both for 3 and 10 TeV.
  Very tight tolerance with given longitudinal emittance!
Very large energy spread
  Chromatic aberrations by quadrupoles at low energy
Both longitudinal and transverse emittance has to be preserved
  Quasi-Isochronous arcs are necessary (with flexible momentum compaction)
Two bunches with opposite charge
  Good matching for both bunches (i.e. round beam at injection/extraction to arcs)
Rapid acceleration
...

## Slide 6: Choice of RF frequency
If we have RMS ~ 30 mm Gaussian bunch  200 mm full length
Typically the total bunch length should be < 10% of λRF
To preserve longitudinal emittance lower frequency is preferable
Reasonable frequency would be SC 350 MHz cavity (LEP cavity)
200MHz
350MHz
650MHz

## Slide 7: Previous study

## Slide 8: RLA2
Energy gain : 11.6GeV / pass
Total acceleration time ~25 μs
  No RF parameters are possible to change within one RF pulse
Minimum number of pulsed magnets
  Preferred not to use any
5-pass RLA 5-63 GeV
μ+
μ-
μ+
μ-
16.6 GeV
39.8 GeV
28.2 GeV
51.4 GeV
The goal is accelerating two bunches (μ+,μ-) spaced by λRF (n-1/2) from 5 to 63 GeV

## Slide 9: Beam Dynamics in Linac
Large initial energy spread causes emittance growth due to chromatic effects by quadrupoles
We need to use weak quadrupoles to preserve emittance
  Drawback: Sensitive to transverse wakefield effects
W/O linearizer
With linearizer

## Slide 10: Droplet Arcs
Arcs consists of two symmetric sections (-50º and 140º) and total turn is 380º, net turn is 180º
The curvature changes with energy
Large energy acceptance
  we still have large energy spread at the exit of first pass
    σΔp ~ 500 MeV → σΔp/p 3% (16.6 GeV ± 1.2 GeV)
Longitudinal emittance ≤≥ bunch length needs to be preserved/controlled
  Small Momentum compaction factor (R56 ≈ L αc)
We also need small dispersion in bending magnets to preserve transverse emittance
Small betatron oscillation to minimize chromaticity

## Slide 11: Basic arc cell
Different lattice configuration has been studied
  FODO, Triplet. TME : The sign of R56 is fixed. Control of bunch length can be done only with RF.
DB(A) lattice allows to control R56 with quadrupole strength as well as the chromaticity
To optimize individual arcs a tool (based on second order optics and tracking) has been developed
Basic cell of arcs
Bending angle/cell =10o
Bmax =7T
Aperture =50mm

## Slide 12: Arc Lattices
40o bending section of first arc
Dispersion is suppressed with half bending angle
Sextupoles are optimized with second order optics.
Dispersion suppression and matching
Basic cell

## Slide 13: Beam dynamics in arcs
Start to end simulation in first arc (tracking)
Extraction
40o bending
Straight section
140o bending
By-pass section
µ-
µ+

## Slide 14: Start to end RLA2
1st pass
1st arc
5th pass
4th arc
….
2nd pass

## Slide 15: Start to end simulation for RLA2

## Slide 16: By-pass section
The phase of beam respect to RF is defined by the arc length.
  1 degree RF phase (@350 MHz) is 2.4 mm (0.85 mm for 1 GHz)
If the beam is injected off-energy to the arc it is impossible to adjust path length within ± several mm
  Which is unlikely possible due to beam loading
A chicane is necessary to adjust path length precisely
  It can also be used to exchange of position of preceding/following bunch
µ-
µ+
Electrostatic deflector
Bending magnet

## Slide 17: New DBA Lattice for Arcs
Strong high order effects due to large energy spread
Nonlinear optimization based on tracking to minimize higher terms (dispersion + chromaticity + ..)
  Thanks to Andrea
Emittance evaluation for 360o turn

## Slide 18: Questions
Beam loading;
  ∆G= keV/structure  22.5 MeV energy difference between bunches at the end of linac for single pass.
  What about the second pass?
It seems we need to use inductive linac after cooling..
  Any proposal for the design?
  What is the average gradient for such structure?
Simulation results:
  σz= 20 mm, δp= 0.9%
  What is the requirement for RCS1? (In the tentative parameters it was OK)
Is there any proposal for injection to RCS?

## Slide 19: Thanks for your attention