## Slide 1: EMWSD / Wakis
Meeting #19
Elena de la Fuente, Carlo Zannini, Lorenzo Giacomel, Giovanni Iadarola
Electromagnetic and Wake Solver Development

## Slide 2: Outline
Where are we?
Main improvements in the code
Beam injection & Absorbing boundary conditions (ABC)
1st Benchmark with CST: PEC pillbox
Conclusions & Next steps

## Slide 3: Outline
Where are we?
Main improvements in the code
Beam injection & Absorbing boundary conditions (ABC)
1st Benchmark with CST: PEC pillbox
Conclusions & Next steps

## Slide 4: Wake solver milestones:
Jul ‘24
Jul ‘25
Jul ‘26
Jul ‘27
1st year
2nd year
3rd year
PhD %
1. FIT Maxwell Equations in 3D
2. PEC, Periodic, PMC boundaries
3. Embedded Boundaries: geometry import from .stl files
4. Beam injection
5. Materials:
6. Open boundaries: PML
7. Frequency-dependent materials
meetings #17, #18
In progress
To Do
xx. Automatic testing
8. …
0. Wake potential and impedance

## Slide 5: Outline
Where are we?
Main improvements in the code
Beam injection & Absorbing boundary conditions (ABC)
1st Benchmark with CST: PEC pillbox
Conclusions & Next steps

## Slide 6: PyFIT GitHub overview
FDTD EM solver
by Lorenzo
FIT EM Solver
Wake Solver
Benchmarks vs CST, WarpX …
Wakis code is refactored into class WakeSolver
Examples & university tests:
Plane wave propagation
Gaussian wavepacket propagation
Cubic Resonator
Field class to manage matrix formulation
are instances of this class
GridFIT3D class in charge of STL importer and grid definition
SolverFIT3D class that solves Maxwell equations
Pre-defined materials library (vacuum, dielectric, PEC)
Should we turn this into a package already?

## Slide 7: Merging wakis with PyFIT
WakeSolver instance is passed as a parameter to SolverFIT3D to perform Wakefield simulations
It’s kept optional since it is not needed to perform just EM time domain simulations
Moved all the relevant functions from wakis to the WakeSolver class
Should PyFIT become the wakis package instead?

## Slide 8: SolverFIT3D development (I): memory optimization
Deletes from memory the matrices that will not be used for the timestepping routine:
Improves memory allocation by 60%
Increases speed performance by 5%

## Slide 9: SolverFIT3D development (II): 1D, 2D, 3D plotting
Plot3D example:
examples/script_planewave_fit.py
A planewave interacting with a dielectric sphere (University test)
Using PyVista (vtk based) functions.
Plots can also be interactive:
clip_volume or clip_normal flags when off_screen =True

## Slide 10: SolverFIT3D development (II): 1D, 2D, 3D plotting
Plot2D and 1D example:
examples/script_planewave_fit.py
A planewave propagating through vacuum being repflected at the PEC boundary
Matplotlib based coutourf (2D) and line plot (1D)

## Slide 11: SolverFIT3D development (IV): EM solve
Runs Electromagnetic time domain simulation given an initial condition or source
EM solve example:
examples/script_wavepacket_fit.py
A gaussian wavepacket propagating through vacuum domain (University test)

## Slide 12: SolverFIT3D development (V): Wake solve
Runs Wakefield time domain simulation given a wakelength.
Beam source injected is defined by WakeSolver object.
Computes wake potential and impedance by saving Ez field every timestep and using the routines in WakeSolver class (needs h5py)
Wake solve example:
examples/script_cubcavity_fit.py
A gaussian beam traversing a PEC cubic pillbox cavity

## Slide 13: Outline
Where are we?
Main improvements in the code
Beam injection & Absorbing boundary conditions (ABC)
1st Benchmark with CST: PEC pillbox
Conclusions & Next steps

## Slide 14: Beam injection
The particle beam is injected as a linear current with a gaussian profile defined by the beam size and charge
Every timestep, the field is updated at , for all the cells in
The beam injection produces a big field perturbation at z- and z+, due to violation of the continuity equation (Gauss law)
FIT
Not included in update equations… Should we correct it / enforce it?

## Slide 15: Absorbing boundaries
A first attempt to reduce the perturbation of the field when the beam current enters/exits it to use absorbing boundary conditions (ABC)
Since PML formulation is complex, the simplest ABC, the FOEXTRAP, was tested first. This is a first order extrapolation that mimics a continuous field at the boundary cells
It has to be updated every timestep
Same for all 6 boundaries (low and high, x, y, z)

## Slide 16: Absorbing boundaries (II)
The effect of this simple ABC is clearly visible at the edges of the domain:
ABC gives a smaller perturbation amplitude but it oscillates from negative to positive
ABC
PEC

## Slide 17: Absorbing boundaries (III)
Order of magnitude reduction of the amplitude of the perturbation, specially at z+.
Line charge current per timestep

## Slide 18: Outline
Where are we?
Main improvements in the code
Beam injection & Absorbing boundary conditions (ABC)
1st Benchmark with CST: PEC pillbox
Conclusions & Next steps

## Slide 19: Pillbox Cavity (bellow cutoff): FIT vs WarpX vs CST
Geometry:
= 30 mm
= 50 mm
= 50 mm
= 100 mm
= 15 mm
= 15 mm
FIT: ABC
CST/WarpX: PML
Beam:
= 18.5 mm (5 GHz)
q = 1e-9 C
Mesh:
nx, ny, nz = 50, 50, 150
total: 375000 cells
Cutoff frequency: GHz
Remarks:
Some error comes from the CST field export, since it does not respect the sampling when it’s too close to the simulation timestep.
WarpX reflections are higher on z-, lower on z+, but are present longer in the domain -> FIT performs slightly better.
Simulation time: for 1m Wakelength (8760 timesteps)
CST: 42s, 16 threads, in `abpimp60g01`
FIT: 3m40s , single core in `abpimp60g01`, 5m20s in lxplus
WarpX: 42m to 1h 23m, single core in lxplus
  (high variability due to load of lxplus node…)
Jz and Ez along z axis

## Slide 20: Pillbox Cavity (bellow cutoff): FIT vs WarpX vs CST
Geometry:
= 30 mm
= 50 mm
= 50 mm
= 100 mm
= 15 mm
= 15 mm
FIT: ABC
CST/WarpX: PML
Beam:
= 18.5 mm (5 GHz)
q = 1e-9 C
Mesh:
nx, ny, nz = 50, 50, 150
total: 375000 cells
Cutoff frequency: GHz
*Calculation performed removing 10 cells at z+ and z- of the FIT domain to reduce the beam injection perturbation
Remarks: WarpX agreement worsens when not using the extended pipe model (pipe+50mm) see CEI-030823
Related to beam injection as seen with the goniometer in WarpX

## Slide 21: Pillbox Cavity (above cutoff): FIT vs CST
Geometry:
= 20 cm
= 30 cm
= 30 cm
= 70 cm
= 12 cm
= 12 cm
Beam:
= 5 cm (2 GHz)
q = 1e-9 C
Mesh:
nx, ny, nz = 51, 51, 104
total: 270,504 cells
20 cells/wavelength
Cutoff frequency: GHz
FIT: ABC
CST/WarpX: PML
Simulation time: for 10m Wakelength (10340 timesteps)
CST: 52s, 16 threads, in `abpimp60g01`
FIT: 4m50s , single core in `abpimp60g01`
Remarks:
Main pattern is there, contaminated by the high relfections from the boundaries for the modes above cutoff
Jz and Ez along z axis

## Slide 22: Pillbox Cavity (above cutoff): FIT vs CST
Geometry:
= 20 cm
= 30 cm
= 30 cm
= 70 cm
= 12 cm
= 12 cm
Beam:
= 5 cm (2 GHz)
q = 1e-9 C
Mesh:
nx, ny, nz = 51, 51, 104
total: 270,504 cells
20 cells/wavelength
Cutoff frequency: GHz
FIT: ABC
CST/WarpX: PML
*Calculation performed removing 10 cells at z+ and z- of the FIT domain to reduce the beam injection perturbation
Remarks: the agreement worsens the closer to cutoff frequency. The modes above cuttof present an artificial amplitude (not propagating) –> Need for PML

## Slide 23: Outline
Where are we?
Main improvements in the code
Beam injection & Absorbing boundary conditions (ABC)
1st Benchmark with CST: PEC pillbox
Conclusions & Next steps

## Slide 24: Conclusions
Progress on the code:
  Built-in plotting 1D, 2D, (matlab based) and 3D (pyvista/vtk based): Fast, flexible (**kwargs), proven not memory consuming, possibility of offscreen plotting to create animations.
  Attribute cleanup: reduces memory consumption 60% and slightly improves performance
  Solving routines:
    emsolve() for pure Electromagnetic time domain, source can be any user function: func(solver, t).
    wakesolve() for Wakefield time domain, source is a particle beam, computes wake potential and impedance .
Beam injection and Absorbing boundaries:
  Beam injection as in CST using line current: barely affects performance >0.1%. Produces perturbation at the boundaries due to breaking continuity equation + reflections
  Absorbing boundaries ABC FOEXTRAP implemented. Small impact on computation time <1%. Helps reducing perturbations, specially at boundary z+. Not comparable to PML.
1st Benchmark vs CST and WarpX:
  Simulated 2 cubic pillbox cavities: below and above cutoff.
    Agreement satisfactory below cutoff, while above cutoff the need of PML becomes relevant to get the right amplitude and frequency of the modes.
  Performance vs WarpX: FIT is 88% faster*, and ABC gives smaller reflections** than WarpX’s PML.
Safe to say we are in a better position with FITWakis Feb 2024 compared to July 2023 WarpX+Wakis ? 
Example 3D built-in plot of planewave in vacuum
*comparison on lxplus (same node). Workload variability may impact WarpX’s time
**probably due to beam injection with 10^6 macroparticles perturbations not being absorbed by PML

## Slide 25: Next steps / Questions
GitHub strategy: moving to a package? what to do with wakis? (I would like to keep the name )
Beam injection perturbation correction: enforce continuity equation?
Working on implementing conductivity :
  It can be fairly easy: Just add update equation for the current ->
  Or it can be quite convoluted: Weiland formulation & Berenguer formulation (backup)
  To be benchmarked with a lossy pillbox ?
Completing tests for university: probably trip around end of April
  Using the planewave and gaussian wave packet tests, we can perform tests in symmetry of the solver, dispersion, speed of light conservation, refraction angle when interacting with dielectric, energy conservation.. Etc. The idea is to use pytest
Try to make the code faster with cython?
CERN School of Computing?

## Slide 26
Thank you  !!!
Elena de la Fuente García (BE–ABP–CEI)
Electromagnetic and Wake Solver Development
meeting #19

## Slide 27: Berenguer PML vs Weiland update equations

## Slide 28: FIT theory: Grid Maxwell Equations
, ,
, ,
Grid Maxwell Equations
FIT
Operators
Spatial matrixes
Material properties
What we care about:
Update equations
We need to build all these matrices and then apply these equations every timestep !