## Slide 1
9th Meeting of Task 6.1 MuCol Design Study
10/6/2024
F. Batsch, L. Thiele, S. Albright, D. Amorim, R. Calaga, H. Damerau, A. Grudiev, I. Karpov,…
Updates on counter-rotating muon beams in the high-energy acceleration chain

## Slide 2
General aspects of counterrotating bunches
Simulations with FM wakefields from CR
Cavity voltage modulations (more in L. Thiele’s presentation)
Changes of the momentum compaction factor
Summary
Outline

## Slide 3
In the RLAs, the co-propagating bunches are separated by odd multiples of p
In the RCSs, the bunches are counterrotating (CR)
In the standing wave cavities, the bunches must pass with a relative offset of multiples of 2p
The positioning of the bunch crossing points with respect to the RF stations is an important assumption as it defines the intensity effects affecting the other bunch, the HOM power scales with I²
 Bunch crossing points in the middle of the arcs optimal
General situation
1
2
3
6
5
4
8
7
crossing point
crossing point
Example with 8 RF stations

## Slide 4
Use of ‘standard’ cavity and RCS parameters
Re-use the intensity effect calculations for multi-turn effects for one bunch in BLonD
Calculate in addition wakefields at the time of the passage of the CR bunch in the future
Apply it to the other beam at the moment of passage
Wakefields of the CR bunch
1
2
3
6
5
4
8
7
crossing point
crossing point
Example with 8 RF stations
Induced voltages in RF station 1:
Induced voltages in RF station 5:

## Slide 5
Exemplary longitudinal phase spaces for µ- and µ+ bunch for 32 RF stations:
Simulation example
µ-
µ+
RCS1

## Slide 6
For the fundamental mode (FM), and a relative phase offset of , the fundamental mode wakefields from the CR bunch are therefore also in phase and build up:
Simulation results
RCS1
Induced voltage per cavity

## Slide 7
Induced voltages of ~1MV per cavity and turn build up. Example of RCS2:
(value from Lisa Soubirou)
Only fundamental mode, multi-turn and CR intensity effects, no HOMs
 No sufficient beam loading compensation, bunch lost
Simulation results (1)
Induced voltage per cavity
Longitudinal phase space

## Slide 8
Providing more voltage by decreasing the synchronous phase:
(30% more total RF voltage)
Other parameters unchanged
 Bunch is transported, the fast synchrotron motion mitigates the beam loading
Simulation results (2)
Induced voltage per cavity
Longitudinal phase space
Time step
Ind. Voltage [V]
RF voltage
Ind. Voltage FM
Sum

## Slide 9
The linac acceleration scheme together with beam loading leads to a non-constant cavity voltage
 Study effect in BLonD with cavity voltage calculated by L. Thiele, see his presentation
Beam loading compensation
L. Thiele
Cavity amplitude in RCS2

## Slide 10
The transition gamma was proposed to be changed:
RCS1: from 20 to 79  15 times smaller momentum compaction factor
RCS4: 8 times larger transition gamma, 62.5 times smaller
Large effects on RF, RF bucket, beam dynamics, bunch length, etc.
Probably strong mismatch in RCS1, extreme changes of the RF bucket in RCS4
This also affects the transverse studies
Changes of the transition gamma
RCS1, mismatched bunch
RCS4, matched but excessive RF bucket

## Slide 11
The induced voltages of the counterrotating beams build up due to their relative phase offset of 0 (2np)
 Careful placement/alignment of cavities required, as done for LEP (see paper, section 4.1)
Providing larger RF voltages seems to allow for beam loading compensation
Modulation of the cavity voltage from the CR bunch under study
Changes in the momentum compaction factor might have large consequences on the longitudinal and transverse design and will be topic of a dedicated meeting end of June
Summary

## Slide 12
CERN summer student from July to August (01/07-30/08): Longitudinal beam dynamics simulations for a hybrid RCS demonstrator facility
Design for 0.1-3 GeV, assuming a fixed ramp rate of 3 kT/s
From 8th WP6.1 Meeting:
Moderately-sized hybrid (e-) RCS demonstrator to be constructed and commissioned from 2030 to 2033
Several purposes:
Test of hybrid RCSs and its beam dynamics
Evaluate fast ramping of magnets
Serve as an injector for an electron storage ring
Option to ramp only one half of the magnets and keep the others at a fixed field to simulate a hybrid scheme
Outlook