## Slide 1: Tuning studies with MADX
Tessa Charles
charlest@ansto.gov.au

## Slide 2: Australian Synchrotron & AS2.0
Parameter | Value | units
Emittance​ | 50​ | pm​
alphaC​ | 0.56​ | xE-4​
dE/turn​ | 785​ | keV​
Circumference​ | 454.8​ | m
Touschek​ | 5.173​ | h​
Qx​ | 70.25​ | ​
Qy​ | 20.81​ | ​
ChX​ | -151​ | ​
ChY​ | -76​ | ​
Straights​ | 5​ | m​
Bore radius​ | 12.5​ | mm​
Max Dipole​ | 1.048​ | T​
Max Quad​ | 110​ | T/m​
Max Sext​ | 10 000​ | T/m2​
βx
βy
A greenfield, 4th gen light source proposal
CDR in early stages of being developed
Foyer and Admin Buildings
Facility Layout
Building Cross Section

## Slide 3: Adding extra elements
Which elements, where?
Correctors (L = 0.2 m) before all quads. (Except, currently, QC1*, QC2*, QC0*, QRF*)
BPMs (L=0) before all quads
Trim quads and skew quads at every sextupole (inc. SY* sextupoles)
Naming conventions currently used (Can be changed if anyone has feedback)
BPMs: BPM.QD1.1
Correctors: MCB.QD1.1
Skew quads: MQS.SD20.1
Trim quads: MQT.SD20.1
Other naming issue:
RF quads at different RF stations have identical name. This could be problematic if using these quads for tune correction. I can rename them, but I don’t want to introduce inconsistent naming.
First 3 consistent with what’s at:
/eos/project/a/acc-models/public/fcc/fccee/V22/t
Notes: Long dipoles

## Slide 4: Emittance tuning results, ttbar Note: BPM errors not included

## Slide 5
Emittance tuning results, ttbar Note: BPM errors not included
Note: Despite linear optics appearing good, DA is still very limited. Further work needed, and tighter tolerances most likely needed.
Oide ttbar lattice
Notes: $\epsilon_{x, \textrm{median}} = 1.510$ \textrm{ nm rad }

## Slide 6
Emittance tuning results, ttbar Note: BPM errors not included
Note: Despite linear optics appearing good, DA is still very limited. Further work needed, and tighter tolerances most likely needed.
Notes: $\epsilon_{x, \textrm{median}} = 1.510$ \textrm{ nm rad }

## Slide 7: Emittance tuning results, ttbar Note: BPM errors not included
Note: Despite linear optics appearing good, DA is still very limited. Further work needed, and tighter tolerances most likely needed.

## Slide 8: Impact of COD
In this example, most properties of the machine are well-corrected, except for chromaticity.
After Chromaticity correction:
Before chromaticity correction:
And a large proportion of seeds start to fail
Chromaticity correction

## Slide 9: Impact of COD
In this example, most properties of the machine are well-corrected, except for chromaticity.
After Chromaticity correction:
Before chromaticity correction:
And a large proportion of seeds start to fail
Chromaticity correction
Highest 8 emittances removed, to better view lower end of distribution.
Chromaticity correction corrects chromaticity well, but increases coupling.
Of course, an iterative procedure is necessary, but nevertheless this massive increase in hor. emittance was despite a fairly small COD (see nest slide)

## Slide 10: Impact of COD
Below is the orbit for the example of chromaticity correction.
Improved orbit correction would help, but it’s already good (~48 um RMS in x and y).
Also BPM error were not yet included, so COD likely to be worse
RMS horizontal orbit and max orbit distortion, after corrections (BPM errors not included):
Notes: Why does this happen? Chromaticity corr changes sextupole strengths.
Improved orbit correction would help, but it’s already good.

## Slide 11: Next steps
Applying corrections to Z lattice (in collab with Simone Liuzzo and Elaf Musa)
DA calculations (for ttbar and Z lattice)
Explore synergies with the Australian Synchrotron and AS2.0

## Slide 12: Thank you

## Slide 13: Misalignments and field errors

## Slide 14: Assigning girder misalignments
  - 2 independent DX and DY misalignments for each end of the girder, and which can be used to calculate DTHETA and DPHI.
(not to scale)
dipole
girder
sextupoles/ quadrupoles
dipole
girder