## Slide 1: MPGD technologies 1
Micro Pattern Gaseous Detectors
Esther Ferrer Ribas
CEA/IRFU

## Slide 2: MPGD technologies 1
Outline
Birth of Micro Pattern Gaseous Detectors (MPGD)
Gas Electron Multipliers
Micromegas
Micro Resistive Well
Applications

## Slide 3
Birth of Micro Pattern Gaseous Detectors
In the 90’s advances in microelectronics and photolithographic technology on flexible and standard PCB substrates favored the invention
Pitch size of a few hundred microns, an order of magnitude improvement in granularity over wire chambers
First Micro Pattern Gaseous Detector (MPGD): Micro-strip Gas Counter (MSGC) Oed, 1988

## Slide 4
MSGC
Performance
Intrinsic high-rate capability (>106 Hz/mm2),
excellent spatial resolution (down to 30 μm),
multiparticle resolution (∼500 μm),
single photo-electron time resolution in the ns-range,
large sensitive area and dynamic range.
Limitations:
Destructive sparks,
time-dependent gain shifts (substrate polarization and charging up),
deterioration during sustained irradiation (“aging”).
Credit: Sauli « Gaseous Radiation Detectors »

## Slide 5
TPC
Time Projection Chamber
D. R. Nygren et al., 1974
MSGC
Micro-Strip Gas Chamber
A. Oed, 1988
GEM
Gas Electron Multiplier
F. Sauli, 1997
MWPC
Multi-Wire Proportional Chamber
G. Charpak et al., 1968
ANODE
CATHODE
CATHODE
200 µm
MICROMEGAS
MICRO-MEsh GAseous Structure
I. Giomataris et al., 1996
MPGD
Birth of MPGD

## Slide 6
Gas Electron Multiplier (GEM)

## Slide 7
GEM
A thin, metal-clad polymer foil chemically perforated by a high density of holes, typically 100/mm2
Large ΔV between the two sides of the foil creates a high field
Electrons released in the upper region, drift towards the holes acquiring enough energy to provoke ionisations
Large fraction of electrons are transferred into the lower section

## Slide 8
GEM
Full decoupling of amplification stage (GEM) and readout stage (PCB, anode)
Amplification and readout structures can be optimized independently
“Study of long-term sustained operation of gaseous detectors for the high rate environment in CMS”, J. Merlin,
CERN PHD theses, https://cds.cern.ch/record/2155685/files/CERN-THESIS-2016-041.pdf

## Slide 9
Manufacturing of GEM: single mask
From F. Sauli RD51 school 2023
Large size detectors
« MPGD manufacturing » by Rui de Oliveira on 3/12

## Slide 10
STANDARD
Double-Conical
Hourglass
CYLINDRICAL
CONICAL
Manufacturing of GEM: double mask
From F. Sauli RD51 school 2023
« MPGD manufacturing » by Rui de Oliveira on 3/12

## Slide 11
STANDARD
Double-Conical
Hourglass
CYLINDRICAL
CONICAL
Manufacturing of GEM: double mask
From F. Sauli RD51 school 2023
Shape of the holes influence performance
Trade off: high gains/charging up effects
Standard: patch for discharge longer/reaching higher gains but more insulator so more charging up

## Slide 12
Performance in single GEM

## Slide 13
Multi-GEM
S. Bachmann et al, Nucl. Instr. and Meth. A479 (2002)294
Cascade of GEM electrodes
Allows attaining higher gain with each GEM at lower voltage
Discharges disfavoured
Notes: Use of three GEM electrodes and an anode separated by 2mm gaps.
A scheme to distributed the apropriated voltage to all electrodes
The detector gain is characterised with an Fe source.
The maximum safe operating voltage is found and then with an alpha source Radon
Amount of moisture in the gas should be kept below 50 ppm

## Slide 14
GEM Rate capability
J. Benlloch et al, IEEE NS-45(1998)234
5.9 keV X-rays:
> 2.106 mm-2

## Slide 15
GEM spatial resolution
F. Sauli, NIM A 805 (2016) 2-24
Notes: Staggered: pads in every second row are shifted by half pitch

## Slide 16
GEM family
THICKGEM/LEM
GLASSGEM
Cylindrical GEM
GEMPix: a triple GEM structure read by 50 micron pixels
F. Murtas, JINST (2014) 9 C01058
Y. Mitsuya et al., NIM A 795 (2015) 156-159
S. Bressler et al. , Progress Particle and Nuclear Physics 130 (2023) 104029
Notes: Depending on the insulator substrate kapton, pcb, or glass. You can hace standard gem, thick gem also called Large electron multiplier.
You can curve them an obtained a cylindrical GEM or if you coupled GEM electodes to a Medipix chip o Timepix you will have a GEMPIX which is an extremely pixelated structure

## Slide 17
Micromegas

## Slide 18
Micromegas

## Slide 19
Multiplication takes place in high E field (~ 40 kV/cm) between the anode and the mesh
  High gain (up to 105 or more)
  Single stage of amplification
    Fast signals (< 1 ns)
    Fast & natural ion collection
    Low ion backflow to the drift region
    Short recovery time (~150 ns)
     High-rate capability (>MHz)
Signal is induced by both electron & ion movement towards the anode / micromesh
  Thin amplification gap (50-150 µm) 
    Small imperfections  no gain variations
Micromegas

## Slide 20
+
-
Cathode
Mesh
Anode
Pillars
~ mm
~ 100 µm
Readout pads
Incident particle
Micromegas
A. Cools PhD animation

## Slide 21
+
-
Incident particle
E
E ≈ 70 V/cm
Micromegas
A. Cools PhD animation

## Slide 22
e-
Electronics
E ≈ 50 kV/cm
Micromegas
A. Cools PhD animation

## Slide 23
Manufacturing of Micromegas
I. Giomataris et al., NIM. A 560 (2006) 405-40

## Slide 24
Micromegas Gain
David Attié, “Gaseous tracking detectors for academic and societal applications”, Habilitation à diriger des recherches, October 2022

## Slide 25
Micromegas spatial resolution
David Attié, “Gaseous tracking detectors for academic and societal applications”, Habilitation à diriger des recherches, Octobre 2022

## Slide 26
Micromegas rate capability
Current increases with the flux
All curves parallel
Gain independent of the rate
No saturation is observed
10 MeV protons
Particle fluxes from 4×102 up to 2×107particles mm−2s−1
Ar + 5% isobutane
G. Charpak et al. NIMA 1998 412 47-60

## Slide 27
Microbulk
Pitch 100 µm,
Holes 30 µm
Micromesh
5 µm copper
Kapton 50 µm
Readout pads
S. Andriamonje et al. JINST 2010 5 P02001

## Slide 28
Resistive Micromegas
Resistive coating:
  Charge dispersion
  Spark protection
David Attié, HDR, October 2022
A. Bellerive et al., eConf C050318 (2005) 0829

## Slide 29
Resistive strips Micromegas
T. Alexopoulos et al., NIM 1 640 (2011) 110-118

## Slide 30
Resistive Micromegas
From R. De Oliveira
RD51 MPGD School 2023
M. Alviggi et al., e-print:2411.1702

## Slide 31
Thermal Bonded Micromegas
J. Feng et al 2021 NIM A 989 (2021) 16958
Stretching of the mesh
Pre-setting the spacers on the anode
Setting the borders for the mesh fixation
Stacking the mesh
Thermal bonding using a hot roller
Complete view after full assembly

## Slide 32
Thermal Bonded Micromegas
G. Liang et al 2011 Chinese Phys. C 35 163
Z. Zhang et al 2014 JINST 9 C10028
J. Feng et al 2021 NIM A 989 (2021) 16958

## Slide 33
TWO mechanical entities
Mesh
Readout plane
INTEGRATED:
ONE single entity
Type of mesh
30 µm
Stainless steel
1 µm
Aluminium
5 µm
Copper
Any
type
Advantages
Demontability
Large Surface
Robust
Industrial manufacturing process (PCB)
Intrinsically Flexible
Low mass
Radiopure
Excellent energy resolution
Single electron efficiency
Micromegas family
Standard
1996
Bulk
2003
Ingrid
2005
Microbulk
2006
Thermal Bonded
2011
XY Microbulk (2012)
Piggyback (20213)
30 µm
Stainless steel
Easy mass production without the need for etching
High gains

## Slide 34
µ-Rwell
The µRWELL is composed of a µ-RWELL PCB + Cathode
µRWELL PCB : amplification stage coupled to the readout PCB through a resistive layer
Resistive layer: Diamond-Like-Carbon with a resistivity 20-100 MOhm/square

## Slide 35
µ-Rwell Low rate: Single resistive layer
Single resistive layer (2014-1017)
Based on GEM fabrication techniques. Micromegas like amplification and signal formation
2D current evacuation based on a single resistive layer
Grounding around the active area
For large area: problem the path of the current depends on position=> detector inhomogeneity
Limited rate capability < 100 kHz/cm2
G. Bencivenni et al, 2019 JINST 14 P05014

## Slide 36
µ-Rwell high rate
Double resistive layer
M. Poli Lener, MPGD 2022
Silver grid
PEP (Patterning-Etching-Plating)
Very good performance
Complex manufacturing due to the double matrix of vias
Single DLC layer
DLC grounding from top by kapton etching and plating
No alignment problems
Scalable to large sizes
Good performance
2D evacuation scheme by a conductive grid (screen printed or etched)
Alignment of the conductive grid pattern with the amplification pattern difficult

## Slide 37
µ-Rwell high rate
PEP Groove
PEP Dot
G. Bencivenni et al, NIM A 1069 (2024) 169725

## Slide 38
µ-Rwell high rate
G. Bencivenni et al,
NIM A 1069 (2024) 169725

## Slide 39
MPGD Applications

## Slide 40
MPGD @ CERN experiments
M. Titov
Gaseous detector lecture
at the ICFA school 2023
(Not up-to-date)

## Slide 41
MPGD @ nuclear physics
RD51 MPGD School 2023 M. Cortesi

## Slide 42
MPGD neutrino physics
M. Titov
Gaseous detector lecture
at the ICFA school 2023
(Not up-to-date)

## Slide 43
MPGD @ rare event detection
M. Titov
Gaseous detector lecture
at the ICFA school 2023
(Not up-to-date)

## Slide 44
Two chosen applications

## Slide 45
45
Charge readout
Optical readout
Frontend and backend electronics
Charge and optical readout
Optical readout of MicroPattern Gaseous detectors (MPGDs) relies on recording scintillation light emitted during electron avalanche multiplication
Scintillation spectrum of gas mixtures with CF4 is well suited for readout with CCD or CMOS imaging sensors
High spatial resolution can be obtained

## Slide 46
46
Charge readout
Optical readout
Frontend and backend electronics
Charge and optical readout
Use of camera (large number of pixels, use of lens for large field of view)
Easy handling of the data (light intensity matrix)
Online imaging thanks to very low data processing and light integration approach

## Slide 47
X-ray fluorescence with optically read-out GEM
F.M. Brunbauer et al 2018 JINST 13 T02006
Materials are excited by X-rays
Characteristic X-ray emisson is produced
X-ray fluorescence identification of different materials in an image
Recorded light proportional to the energy of the incident particle

## Slide 48
X-ray fluorecence with optically read-out GEM
F.M. Brunbauer et al. 2018 JINST 13 T02006

## Slide 49
Beta imaging with Glass Micromegas
Context: oncological research
Drugs labelled with tritium 3H
Drug efficiencymeasurement of 3H activity

## Slide 50
50
Camera
Micromegas
Sample holder
e-
Light
β
6 mm
20 cm
Cathode
3H concentration ↔ Sample activity (Bq)
Assess the activity measurement sensitivity and dynamic range → Activities: 0.1 Bq, 1 Bq and 10 Bq
Mesh
Glass
ITO
3H glucose
Camera
Beta imaging with Glass Micromegas
A. Cools PhD 2024 Université Paris-Saclay

## Slide 51
Beta imaging with Micromegas
Light intensity profile over time
5 s exposure time frames for 1h acquisition
Gain ~ 104
A. Cools et al NIMA (2023)1048 167910

## Slide 52
Summary
MPGDs, GEM and Micromegas, are mature technologies
Thin amplification region (~100 μm), well separated from conversion / drift region
Fast collection of positive ions (~100 ns)
Fast signals (~ ns)
High gain (~105)
High spatial resolution (~30 μm)
High rate capability (~MHz/mm2)
Low ion backflow (~ 1%)
More robust than wires
Better ageing / radiation hardness
Large area scalability
Fabrication simplicity / lower cost
Versatility (tracking, TPC, imaging)

## Slide 53
Summary
MPGDs today: GEM, Micromegas and µRWell
Versatile, adaptable  wide range of applications
  High Energy Physics
  Nuclear Physics
  Rare event detection
  Neutrino physics
  Polarimetry
  Applications beyond fundamental research: Muon tommography, Medical Physics, Neutron detection
Talks by P. Iengo, M. Cortesi, J. Bortfeld

## Slide 54
Perspectives
Challenging R&D
  Optical readout
  High rates/Ageing
  Large areas
R&D for future colliders: Future Cicular collider (FCC),Cicular electron positron collider (CEPC), Electron Ion Collider (EIC)…
  Trackers
  Muon detectors
RD51 MPGD School 2023 E. Oliveri
Talk D. Gonzalez

## Slide 55
Acknowledgements
D. Attié, F. Jeanneau, Y. Giomataris, E. Oliveri,
T .Papaevangelou, F. Sauli, M. Titov, M. Vandenbroucke
Thanks!

## Slide 56
F. Sauli and A. Sharma, «Micro-patern Gaseous Detectors», Ann.Rev.Nucl.Part.Sci. 49 (1999) 341-388
Y. Giomataris, “Development and prospects of the new gaseous detector Micromegas”, NIM A 419 (1998) 239-250
F. Sauli, “The gas electron multiplier (GEM): Operating principles and applications”, NIM A 805 (2016) 2-24
S. Bressler, «The Thick Gas Electron Multiplier and its derivatives: Physics, technologies and applications, Progress Particle and Nuclear Physics 130 (2023) 104029
D. Attié et al., « Current Status and Future Developments of Micromegas Detectors for Physics and Applications”, Appl.Sciences 11 (2021) 12, 5362
Gaseous Radiation Detectors, Fundamental and Applications, Fabio Sauli, Cambridge Monographs on Particle Physics, Nuclear Physics and Cosmology, Cambridge University Press
Micro-Pattern Gaseous Detectors: Principles of Operation and Applications, Fabio Sauli, World Scientific
Further reading

## Slide 57
Spare

## Slide 58
GEM Properties
High Rate Capability  MHz/mm2 (MIP - Minimum Ionizing Particles, 2MeV cm2 /g)
High Gain Up to 105 -106
High Space Resolution <100 mm
Good Time Resolution In general few ns , sub-ns in specific configuration
Good Energy Resolution10-20% FWHM @ soft X-Ray (6 KeV)
Excellent Radiation Hardness
Good Ageing Properties
Ion Backflow Reduction  ~% level, below % in particular configurations
Large size
Low material budget
Low cost

## Slide 59
Micromegas properties
High gain ( >104)
Good energy (11% @ 6 keV) and time resolution (< 1 ns)
Good spatial resolution (~100 µm)
Reduced ion feedback < 1%
Radiation hardness (106 p/cm2)
Fast ion collection operation at high flux
Good Ageing Properties
Large size
Low material budget
Low cost
Cope with sparks: resistive coating

## Slide 60
Ingrid
Mesh is directly built on the silicon pixel readout chip
High gain and small pixel size allow single electron detection
High resitive silicon oxide layer protection against discharges
M. Chefdeville et al., Nucl. Instr. Meth. Phys. Res. A 556, 490 (2006)
H. van der Graaf, Nucl. Instr. Meth. Phys. Res. A 580, 1023 (2007)

## Slide 61
Hybrid Implementation: GEM + Micromegas

## Slide 62
GEM Implementations
COMPASS
TOTEM
KLOE-2
BONUS RADIAL TPC
ALICE TPC UPGRADE
HBD for PHENIX
LHCB
Notes: COMPASS 30 x 30 cm2 with 2D readout
TOTEM TWO-ARMS FORWARD TRACKER IN CMS
Cylindrical Inner tracker for the Kloe 2 experiment
BONUS radial TPC at the CLAS experiment at JLAB

## Slide 63
Micromegas Implementations
COMPASS
CAST
NTOF
T2K
CLAS12
ATLAS-NSW
ND280 upgrade High-Angle TPCs
ACTAR-TPC
MINOS
ATLAS-NSW