## Slide 1
Gas properties and mixtures
Marcello Abbrescia
University and INFN Bari, Italy
DRD1 gaseous detector school
CERN, November 27 – December 6, 2024

## Slide 2: Basics
The gas (or gas mixture) is the «core» of any gaseous detector
It is where (almost) everything happens
Its properties contribute to determine the shape, amplitude and duration of the signals generated  The performance of the detector
Aging processes in gaseous detectors strongly depend on the nature of the gas mixture used
How do we choose the «best» gas mixture?

## Slide 3: Working principle of gaseous detectors
Detection of an impinging particle takes place because this ionizes the gas, generating ion-electron pairs.
Drift and amplification
due to electric field

## Slide 4: Ionization
I0
Not the whole energy lost by the impinging particle goes in ionization processes; a part (roughly half) goes in excitation of the gas molecules.
 The average energy Wi needed to create an ion-electron pair is ≈ 2-3 I0
Interest in maximizing ionization processes

## Slide 5: Statistics of ion-electron pair production
Primary ionization events are independent and therefore follow Poisson statistics.
- Each time an impinging particle crosses a layer of gas, it has a certain probability to produce a certain number of primary electrons
- If nP is the average number of primary electrons (ions), the probability P(k) to have k electrons (ions) is:
Therefore there is always a finite probability to produce no electron-ion pairs:
In the other cases the impinging particle is not revealed
Intrinsic inefficiency of the detector
Note: of course nP is proportional to the gas layer thickness and the energy loss
 Limit on the thickness of the gas volumes that can be used.

## Slide 6: High E fields: excitation and ionization
- When an applied electric field exceeds few kV/cm,
more and more electrons can reach enough energy
to produce excitation and ionization.
- The plot shows the energy distribution in Ar for three different values of the electric field, compared to the energy needed for excitation and ionization
Multiplication processes

## Slide 7: Multiplication processes
In gaseous detectors typically few tens of ion/electron pairs are produced by a MIP in few mm of gas;
To be compared to ≈24.000 hole/electron pairs produced in 300 μm of Si.
Multiplication processes (a la Townsend) are fundamental in gaseous detectors
Because there’s no hope to distinguish the signal generated by few tens of electrons from all sources of noise
All these considerations leads to the necessity of optimizing (namely enhancing as much as possible) primary and secondary ionization in gaseous detectors.

## Slide 9: Choice of the gas filling
Noble gases are preferentially used due to the absence of vibrational and rotational states ionization dominates.
(Polyatomic gas have non-ionizing de-excitation modes available)
Possible electron multiplication at low electric field
Choose cheap noble gases with low ionization potential
Expensive and rare

## Slide 10: Choice of the gas filling
Noble gases are characterized by the largest I0/Wi ratio
In principle noble gases with large Z should be preferred, because of their large dimensions, leading to larger nt/cm
 Kr and Xe would be ideal choices, but their drawback is their cost
 Rn is radio active
Hence Ar was (and still is) a very popular choice
In principle one could release the requirement on I0/Wi in the case of large molecules, characterized by large nt/cm
Large hydrocarbons would be suitable
 But they are flammable

## Slide 11: First Townsend coefficient for Ar/CH4 mixtures
The first Townsend coefficient represents the average number of pairs produced per unit length by an electron drifting in the gas

## Slide 12: Not only ionization…
From: F. Sauli, Gaseous radiation detectors: Fundamentals and Applications, Cambridge University Press, 2014

## Slide 13: Penning effect
When using gas mixtures, Penning effect can take place, if the excitation potential on one species is larger than ionization potential of the other.
A* + B  A + B+ + e
Ar excitation and ionization energy levels

## Slide 14: Penning effect
Ionization coefficient of Ne/Ar mixtures larger than ionization coefficients both of Ar and Ne
Additional ion-electron pairs are produced, increasing the «effective» ionization coefficient, especially during multiplication processes.
From the original paper by Penning et al., 1940

## Slide 15: Penning effect: complications
Gain in an gaseous ionization counter, filled with Ar/isopentane mixture.
Two effects:
Increase of the gain due to Penning effect for low concentration of iso-pentane
Decrease of the gain for larger concentrations due to electron cooling by iso-pentane

## Slide 16: Choice of the gas filling
If only a noble gas is used to fill the counter, it can operate at
relatively low gains (M ≈ 103 - 104) before entering the permanent discharge regime
When the avalanche forms, excited Ar atoms are created, which can return to the ground state only emitting UV photons
- The energy of these photons can be sometimes larger than the energy needed to extract electrons from the cathode walls (7.7 eV for copper)
- Photoelectrons can be extracted from the walls, which cause farther ionization of the gas
Possible spurious delayed pulses due to ions neutralizing on the cathode
- Ar+ ions reaching the cathode are neutralized
The neutral Ar atom is sometimes produced in an excited state, decays emitting UV photons  An additional electron can also be extracted from the wall
Both processes induce spurious delayed pulses

## Slide 17: Emission spectra from various gases
Emission spectra of the noble gases typically fall in the UV region

## Slide 18: Radiation trapping
Photons emitted by radiative decay to ground of excited noble gas atoms have a high probability of being re-absorbed and subsequently re-emitted by the noble gas: radiation trapping.
Eventually, after many absorption/emission cycles, the photons are absorbed by the walls of the gaseous detector (or a quencher gas molecule).
Excited states may effectively have a long lifetime

## Slide 19: Geiger-Muller counters
Entire gas volume is involved
Loss of information on space
Loss of information on energy
Simple, easy to use, cheap, suitable for measuring radiation counts
Sometimes optimization of gas mixtures is easy… 
Filling gases: He, Ne or Ar
High electric fields
Gains of the o(1010)

## Slide 20: Use of quencher gases
The problem of UV photons is solved by adding to noble gas percentages of other polyatomic gases, usually called "quenchers"
Gas quencher molecules have non-radiative (rotational and vibrational) mode and can absorb UV photons in a wide energy range.
- CH4 absorbs photons between 7.9 and 14.5 eV
- Other polyatomic gases used are freons, CO2, BF3, C4H10, etc.
Polyatomic gases dissipate energy by elastic collisions
- Some of these gases can dissociate, and/or form solid or liquid polymers which can deposit on the electrodes, altering their properties
Malter effect, where the E field close to the electrode is distorted, causing undesired discharges
Aging effects (one of the main issues in all particle detectors)
Even small quantities of quencher allow to operate these detectors up to gain of 106 without discharges.

## Slide 21: Quenching by UV absorption
Photo-absorption cross sections for various gases and for the principal hydro-carbons
 They extend down to 7-8 eV

## Slide 22: Electronegative gases
- Some gases, like O2, Cl2, H2O vapour, etc., are characterized by a high probability to capture drifting electrons and form negative ions;
- The net effect is reducing the total number of drifting electrons  electronegative gases
- The probability of capture per collision (or per unit length)
is called "attachment coefficient"
The attachment coefficient strongly depends on electron energy .
Attachment coefficient of electrons in Oxigen, vs. electron kinetic energy

## Slide 23: Effects of electronegative gases
Fraction of electrons surviving after a drift of 20 cm in two gas mixtures, as a function of the contamination of O2, under the action of E = 200 V/cm

## Slide 24: Use of quencher gases
Also electronegative gases are used as quenchers, like many freons (CF3Br), ethyl-bromide (C2H5Br), etc. which help operate detectors at high gain without discharges.
- They are characterized by an electron capture mean free path that is less than typical anode-cathode distance (≈ 1 cm) and larger than avalanche size (few μm)
These gases capture electrons possibly extracted at the cathode forming negative ions, preventing the formation of spurios delayed avalanches
Sometimes quenchers, in particular various kinds of freon, can dissociate resulting in simpler molecules, sometimes harmful to the detector, like HF  aging

## Slide 25: «Classical» gas mixtures
Popular gas mixtures in use for a wide variety of gaseous detectors were ternary:
Noble gases (typically Ar) to enhance primary, secondary ionization and Towsend avalanches in the gas
 enhance the signal produced
 Reduce the intrisic inefficiency
 They do not dissociate in pollutants
Small fractions of hydrocarbons (CH4 or i-C4H10), or CO2, and/or fractions of some kind of Freon
When no simulation were available the «best» gas mixture for a certain detector was chosen by making, literally, hundreds of tests
Simulations have made life easier to particle detector physicists

## Slide 27: Exploiting ligth emission
Charged particles leave trails of excited molecules
Certain gases release part of this excitation energy producing visible or UV photons
This can be exploited if the gases are transparent to these photons

## Slide 28: Gaseous detectors with optical readout
Energy carried away by scintillation light is small: < 1% of dE/dx
Up to 104 photons per MeV of dE/dx
 use the scintillation ligtht produced during the avalanche multiplication processes
Typically Micro Pattern Gaseous Detectors (MPGDs) are used coupled with CCD or CMOS cameras.

## Slide 29: Exploiting ligth emission
Spectrum of the noble gases is typically in the UV region.
Maximum sensitivity of photosensors is typically for visible light.
 Need to use wavelength shifters
 Add suitable gases to noble gases
Sharp peaks from noble gases
Broad spectrum from CF4

## Slide 30: Images from optical readout GDs
Muon tracks
Muon + δ ray
Hadronic shower
Scintillation light decay time:
≈ 10 μs for noble gases  suitable for typical CCD integration time
10-1000 ns in inorganic scintillatos
2 ns for fast organic scintillator
First particle detectors were «imaging» detectors
 Intuitive and direct visualization of what happens

## Slide 31: Electron Drift velocity
Ionization probabilty (and gain) are not the only parameters to be optimized in gaseous detectors.
Drift velocity is typically related to time resolution in GDs.
- In RPC, where the whole volume is active for multiplication processes:
In wire chambers and most MPGDs time resolution is related to fluctuations in the drift time toward the amplification region.
- CF4 is added to Ar to improve time resolution
In general:
Iind = qe vd Ew  the signal amplitude is proportional to drift velocity

## Slide 32: Drift velocity in Ar/CO2
Adding even small percentages of a gas to another can change the drift velocity dramatically
CO2 added to Ar makes the drift velocity of the mixture max larger
In general, mixtures characterized by large drift velocities are preferred: «fast» gas mixtures
Drift velocities computed by Magboltz at Ar/CO2 at 3 bar

## Slide 33: «Slow» gas mixtures: the cluster counting technique
Principle: In He based gas mixtures the signals from each ionization act can be spread in time to few ns.
By counting the number of ionization acts per unit length (dN/dx), it is possible to identify the particles (P.Id.) with a better resolution w.r.t the dE/dx method.
dE/dx: truncated mean cut (70-80%), with a 2m track at 1 atm give σ ≈ 4.3%
dNcl/dx: for He/iC4H10=90/10 and a 2m track gives σdNcl/dx /(dNcl/dx) < 2.0%
Landau distribution of dE/dx, originated by the mixing of primary and secondary ionizations, has large fluctuations and limits separation power of PID  primary ionization is a Poisson process, has small fluctuations

## Slide 34: Diffusion coefficients for Ar/CO2
Calculated by Magbolts for Ar/CO2 at 3 bar
Transversal and longitudinal diffusion should be optimized together with other parameters (gain, drift velocity).
Transversal diffusion related, typically, to spatial resolution
Longitudinal diffusione related, sometimes, to time resolution
 In drift tube (or TPC) it can affect spatial resolution as well

## Slide 35: Diffusion of electrons and ions in gases
While diffusing, electrons and ions do not have an easy life.
Possible interaction of positive ions:
- Neutralization with a negative charge carrier (either an electron or a negative ion)
- Neutralization after the extraction of an electron from the walls of the detector
- Charge transfer
- to a molecule of its own gas (A+ + A --> A + A+)
- to a molecule of another gas with lower ionization potential (A+ + B --> A + B+)
Possible interactions of electrons:
- Neutralization with a positive ion (e + A+ --> A)
- Attachment to a molecule with negative electron affinity (e + A --> A-)
- This attachment probability is negligible for noble gases and hydrogen
- Oxigen is a gas with strong electronegative affinity
- The attachment coefficient depends strong on the electric field (if any)
- Absorption in the walls of the detector

## Slide 36: Changing of paradygm
Until 1980s most succesfully gaseous detectors were cylindrical
 yes, MWPCs are «cylindrical»
Drift and multiplication region separated from each other
 quite good spatial resolution
 relatively poor devices for time resolution
Using a parallel plate geometry was considered difficult
Detectors unstable and with limited lifetime
Once that a discharge started the whole energy stored in the electrodes was dissipated
Detectors had to be externally triggered
Δt

## Slide 37: Changing of paradygm
Time resolution ≈ 1 ns
Keuffel PPCs (1949)
Madansky and PIDD PPCs

## Slide 38: Including resistive elements in gaseous detectors
Resistive electrodes allow auto-quenching mechanisms due to the switching off of the LOCAL electric field
Limitation of rate capability
Including resistive elements in gaseous detectors was (and is) a major breakthrough in GD R&D
RPCs succesfully operated with Ar/iC4H10/CF3Br mixtures

## Slide 39: Trasferring amplification to front-end electronics
Sometime large gains (charge) are not acceptable:
RPCs operated in streamer mode were NOT suitable for LHC experiments because of their too low rate capability
The solution was to increase the fraction of quencher gases and transfer part of the needed amplification to the front-end electronics
0% CF3Br
4% CF3Br
8% CF3Br
R. Cardarelli et al., Performance of a Resistive Plate Chamber operating with pure CF3Br, NIMA 333(1993), 399-403

## Slide 40: Passage from streamer to avalanche mode in RPCs
The use of CF3Br enriched mixtures allowed an increase of the rate capability of more than one order of magnitude
Allowed the use of RPCs in muon systems of the LHC experiments
How a gas mixture can change your life…
Later on, it was found that CF3Br was harmful for the ozone layer, and was banned from production and use.
It was replaced by C2H2F4, a gas largely used in refrigerating systems
RPCs gas mixtures are nowdays almost completely made out of C2H2F4.

## Slide 41
Twenty years later (not by Alexandre Dumas)  …

## Slide 42: The problem of GreenHouse Gases
- Not only CO2 contributes to the greehouse effect. There are other gases (and families of gases) that contribute: H20, CH4, CFC, HCFC, NOx, SOx
To compare various gases, the Global Warming Potential was introduced:
it is a measure of how much energy the emission of 1 ton of a gas will absorb over a given period of time, relative to the emission of 1 ton of carbon dioxide (CO2).
The larger the GWP, the more that a given gas warms the Earth compared to CO2 over that time period.
The time period usually used for GWPs is 100 years(*).
(*) Some gases, once arrived in the high atmosphere, dissociate, producing by-products that may or may NOT be greenhouse gases: therefore the lifetime a a gas species MUST be considered when computing its GWP

## Slide 43: GWP for various gases
The Relative instantaneous radiative forcing, is independent of the lifetime of the gas in the atmoshpere.
The GWP take also into account the lifetime of the gas in the atmoshpere.

## Slide 44: Temperature and CO2 concentration: last 800.000 years
CO2 concentration < 300 ppm
Temperature
CO2 concentration
Lüthi, D., et al. High-resolution carbon dioxide concentration record 650,000–800,000 years before present. Nature 453, 379–382 (2008). https://doi.org/10.1038/nature06949

## Slide 45
GHGs are used in several gaseous particle detectors due to their characteristics suitable for optimal detector performance AND long term operation
30 years ago we had to get rid of Ozone Depletion gases
There was not the feeling about GHGs  many detectors were designed from the beginning to be used with GHGs
Use of Greenhous gases in HEP

## Slide 46: The use of GHGs at the LHC experiments
- 40% GHG emissions from Run 1 to Run 2 excluding from the calculations ATLAS and CMS RPC systems
- ATLAS and CMS RPC systems: +35% increase of GHG emissions due to development of new leaks

## Slide 47: Replacement of GHGs with eco-friendly gases
We need to replace:
  C2H2F4 = R134a = TFE mainly used in RPCs
  SF6 mainly used in RPCs
  CF4 used in CSCs, GEMs, RICH, etc.
with more ecological gases, namely with a much lower Global Warming Potential.
Difficult problem: gases are the core of gas-filled detectors.
We also need:
  to get the same performance
  not to change the electronics and HV (for existing systems)
Of course we can also re-circulate
the gases used, after purifying them,
and reduce leaks
HEP experiments, present and future, last several (dozens) of year
 A good performance must be mantained for an adequate period of time
 Aging tests are needed as well.
It’s not a problem concerning just the RPC community

## Slide 48: The importance of collaborative effort
All high energy experiments (ALICE, ATLAS, CMS, LHCb, etc.) and the CERN gas group (CERN EP-DT) started, already several years ago, an intense R&D program to find suitable gas mixtures.
Practically all research trendlines concentrate around the idea of replacing:
C2H2F4 (GWP=1430) C3H2F4ze (GWP=4)
+ CO2 (GWP=1) or He
EEE
C3H2F4 (here indicated as HFO for short) is the molecule most similar to TFE but with low GWP
CO2 (or He) are essentially added to reduce the operating voltage.
The RPC EcoGas@GIF++ is a Collaboration transversal to ALICE, ATLAS, CERN EP-DT, CMS, and LHCb willing to put together expertise and resources in order to test potential candidates of eco-friendly gas mixtures with different detectors and electronics.

## Slide 49: The RPC ECOGas@GIF++ timeline
The RPC EcoGas@GIF++ is a collaboration transversal to ALICE, ATLAS, CERN EP-DT, CMS, and LHCb willing to put togethere expertise and resources in order to test different detectors and electronics, in the same conditions and 2-3 potential candidates of eco-friendly gas mixtures.
Assessment of the possibility of using HFO in place of TFE
 ECO1, ECO2 and ECO3

## Slide 50: Experimental set-up @GIF++
Three gas mixtures identified, with various concentrations of HFO and CO2.
Attention focussed on ECO2 and ECO3 because of the good stability and performance demonstrated in home-labs tests.
Aging tests performed at GIF++
12.5 TBq 137Cs source
to generate background (high rate)
to accelerate aging processes
100 GeV muon beam
to measure detector performance

## Slide 51: Detectors @ GIF++
Various detectors, mounted on two trolleys, equipped with various electronics.
 Help in disentagling common observed effect from effects specific of ONE detector
Trolley 3
Trolley 1
The results presented here refer particularly to the detectors equipped with TDC

## Slide 52: Determination of baseline perfomance
Fit of efficiency curves with a sigmoid:
Efficiency at plateau basically similar for STD, ECO2 and ECO3 > 95%
Efficiency curves shifted at higher voltages depending on fraction of HFO
 WP(ECO2) > WP(ECO3) > WP(STD)
Source OFF, 2021 data

## Slide 53: Efficiency and counting rate with irradiation
Source ON, 2021 data
STD
ECO2
EC03
Efficiency > 90% at the highest rate for all detectors
LHCb/SHiP (SG 1.6 mm)
With ECO2 and ECO3 the presence of larger charge events (not streamers) observed
ATLAS 2021 (digitizer)

## Slide 54: Aging and causes for aging in RPCs
54
2023 t.b.
2024 t.b.
Start of the irradiation
Generally, the charge integrated along a certain elapsed time is considered the most important factor for aging in RPCs;
The targets of integrated charge are different for various experiment: for instance, for ALICE is ≈ 100 mC/cm2, for CMS is ≈ 1 C/cm2 CMS, including a safety factor of 3.

## Slide 55: Further considerations about aging
55
Caveat: The importance of the integrated charge derives from the fact that production of HF was measured to be proportional to the integrated charge
Direct damage of the detector
However, HFO typically dissociates producing TriFluoroAcetic acid
How TFA causes aging in RPCs and affects their performance on the long term is still to be investigated.
Aging is also caused by irradiation itself
 Chemical modifications in the HPL electrodes
Aging is also caused by time itself
 e.g. changed in HPL resistivity because of drying up.

## Slide 56: Efficiency before and after irradiation campaign
56
ALICE, comparison 2022 – 2023
SOURCE OFF
STD
ECO2
CMS (double gap), comparison 2021 – 2023
SOURCE OFF
SOURCE ON
≈ 0.7-1 kHz/cm2

## Slide 57: Plateau efficiency before and after irradiation
57
Comparison 2022-2023 data
ALICE
LHCb/SHiP RPC
The usual decrease of plateau efficiency with rate (or dose) is observed.
Nevertheless, there seems NOT to be any efficiency degradation in the time lapse 2022-23

## Slide 58: The other piece of the puzzle
The replacement of TFE is just part of the problem; in ECO2 and ECO3 the residual GWP is almost ALL due to the presence of SF6.
Mixture | GWP (100 y) | CO2e (g/l)
Standard | 1485 | 6824
ECO2 | 475 | 1522
ECO3 | 527 | 1529
Gas mixture replacement is generally done at constant number of gas volumes
 CO2e is the parameter to consider when evaluating the reduction of the impact on greenhouse effects
With ECO2 and ECO3 achieved a reduction of 4 times the CO2e wrt. STD
The residual CO2e is ALL due to SF6
 Need to find replacement for SF6, with low GWP and CO2e, which could reduce the fraction of large charge events when in combination with HFO.

## Slide 59: Looking for replacements for SF6
One proposed solution is
Chloro-trifluoropopene C3H2ClF3 (HFO1233zd)
Avalanche/streamer separation (“useful” plateau) larger than 400V
G.Proto et al, 2022 JINST 17 P05005
NOVEC 5110
GWP < 1
Atm. lifetime = 15 days
Application in industry
B. Mandelli, Possible alternatives to SF6 for Resistive Plate Chambers RPC2022

## Slide 60: What about CF4?
60
Used in CSCs and GEMs
For instance, gas mixture used in CSCs of CMS:
Used in GEMs basically to increase drift velocity  better time resolution. Anyhow without CF4 time resolutions still within requirements,
Main ideas:
Reduce (or eliminate) CF4
HFO to replace CF4, but this implies an increased HV  more studies needed

## Slide 61: Reduction of CF4 in CSC
61
No significant degradation seen, in terms of performance, in all longevity tests
However cathode modifications were seen in all cases.
Anode surface depositions are seen with 0 and 2% CF4 even with naked eye.

## Slide 62: Replacement of CF4 with HFO1234ze
Just 1000V increase in the operating voltage, good efficiency, reasonable plateau length
No gain reduction up to 1 C/cm, but significant increase in the dark current in first irradiation tests

## Slide 63: Conclusions
There are no conclusions!
  Activities are in full steam, there is a LOT to do!
  Join in, be part of the party!
Interpretation of the effects observed not trivial
Collaborative effors of paramount importance at this stage.
The gaseous detector community is on the eve of its ecological transition