## Slide 1: Gaseous Detector Applied to Fundamental Research Beyond HEP
Marco Cortesi Detector System, Group Leader cortesi@frib.msu.edu
2 December 2024

## Slide 2: Preamble: Constraints, Limitations, and Assumptions
During preparation
After slides has been completed
Goal
Reality
Warning: the task has a massive scope!
 Constrain: Time Boundary!
 Limitation: Personal (limited) experience is the basis for the materials here presented!
 Assumption: I most probably miss something important!

## Slide 3: “Speculative & Ambitious” Program Outline
General intro: requirements of gaseous detectors applied to other field than HEP
  Example HEP vs LENP etc.
Examples of application to LENP/HENP
  RIBs physics, gaseous detector for PID in fixed-target spectrograph
  Inverse kinematic nuclear reactions study: TPCs and Active target mode of operation
    -) physics, technology, challenges, ... (low pressure operation, pure elemental gas, etc.)
    -) Examples of Active-Target TPCs
  TPC for Fission Fragment Studies
  R&D project with MPGDs for EIC
Rare Event Search Applications & Neutrino Physics
  Exotic decays with MPGD-TPC (Dark Decay, X17 boson, etc..)
  Directional TPC (Negative-ion OTPC)
  Cryogenic detector: mostly exotic ideas

## Slide 4: Nuclear physics and gaseous detectors
Rutherford & Geiger alpha particle counter (1908)
Used in early fundamental research on alpha particles.
First gaseous detect ever build:
“Single-wire” Cathode image Readout for Drift Chamber (CRDC) still used today
X = pulse height analysis
Y = drift time
e.g., S800 CRDC @ FRIB/NSCL
BELLE central drift chamber
SHARAQ CRD @ RiKEN
Tracking MAGNEX Spectrometer ………
High-E Particle Physics
-) High gain (MIPs, Photons, etc.)
-) High Multiplicity
-) Specificity
-) High rate
-) Large & complex
-) IBF  mostly from the gas avalanche readout
-) …
Low-E Nuclear Physics
-) Modest gain (heavy charged particles)
-) Low Multiplicity
-) Versatility (one setup many experiments)
 large dynamic range (different pressure)
 active target mode (pure elemental gas)
-) Low/moderate rate
-) Small setup, simple
-) IBF  mostly from the beam particles
-) …
pAT-TPC (NSCL)  few tracks per event!

## Slide 5: Low-Energy Nuclear Physics with Rare Isotope Beams (RIBs)
The paradigm shift has led to significant change in detectors requirements
Significant advances in rare isotope beam production technology (accelerators and fragment separators) have been achieved in the last decades, crucial for the exploration of the nuclear chart.
PID
PID
Stable Target
RIBs
Experiment with very different energy regime are possible (Fast beams, slow “reaccelerated” beams, and stopped beams)!
Direct Kinematic
Inverse Kinematic

## Slide 6: World view & reach of Modern Rare Isotope Facilities
Next generation facilities will produce more than 4500 isotope available for study
about 80% of the isotopes predicted to exist in the universe
Main Gaseous Detector Applications:
-) Active Target TPC with fast & slow beams
-) Study (PID) of exotic decay with stopped beams
-) Fission Fragment tracking (fission reaction studies)
-) Focal-plane tracking for fast beam in spectrometers
-) Beam diagnostics/tuning

## Slide 7: Gaseous detectors for PID in RIBs spectrometers (FRIB S800)
Focal Plane detector system for heavy-ion PID
PID: Bρ-dE-ToF
Cathode Readout Drift Chamber (CRDC):
Position and angles
2 x CRDCs (30x60), 1m apart, filled with 40 Torr CF4(20%)+C4H10
Slow detector, Rate < 5kHz
Position resolution > 1mm
Aging problems
Ionization chamber: ΔE/E
32 fragile thin foils
Energy resolution
ΔE/E ≈ 1.2% (A≈100)
Plastic Scintillator:
Time resolution ~450ps
Hodoscope:
Hydroscopic CsI crystals
TKE resolution 0.85%
Gaseous detector used for Tracking and dE/E measurements:
-) Good tracking & PID capability for heavy ions  low energy/angular straggling needed low material budget (low pressure operation)
-) Large area coverage  low cost with good performance

## Slide 8: Cathode Image Drift Chamber (CRDC)
Single-wire readout
1 meter
Energy versus scattering angle from the reaction 12C(7Li,3H)16O
Position resolution  0.5 mm
Tracking resolution  < 2 mrad
Raw data
Rigidity-corrected data

## Slide 9: PID with the SAMURAI spectrometer (RIKEN)
Z
A/Q

## Slide 10: RIKEN Forwards Drift Chamber (FDC)
Tracking system
Before the target
Before the Dipole
After the Dipole
Low-pressure MWPC-based readout
Gaseous Detectors
xx
vv
uu

## Slide 11: Inverse Kinematic with gaseous detector targets
Goal: Study of inverse-kinematic nuclear reactions with resolutions equal to the one achieved in direct kinematics with high-resolution spectrometers + higher efficiency & thicker targets
Direct Kinematic
-) Thin Targets (low luminosity, low straggling, good ΔE/E)
-) Thick Targets (high luminosity, high straggling, poor ΔE/E)
-) Small acceptance angle
-) Low energy event trapped in the target
Projectile
Solid “heavy” target
  -) 4π acceptance of reaction products
  -) Energy loss like thin target = excellent ΔE/E
  -) Very high effective thickness  high luminosity
  -) Detection efficiency ~100% (+ low energy events < 200 keV)
  -) Event-by-event reconstruction in 3 dimensions
  -) Different target pressure  Large dynamic range
Inverse Kinematic (AT-TPC)  gas is simultaneously the target and the tracking medium
Heavy, short-lived projectile
Gaseous “light” target
Particle identification
Gaseous avalanche readout

## Slide 12: TPC operated in active target mode  MPGDs
Science program with AT-TPCs
Suzuki et al., NIM A, 691 39 (2012)
Micromegas +
M-THGEM
Cylindrical geometry
Readout > 10k pads
and many more ….
Same goal, different paths:
-) geometry:
 Cylindrical vs cubicle
-) Gas avalanche readout:
 Micromegas
 Hole-Types (GEM, …)
 μ-PIC
 Hybrid …..
-) Coupled to Ancillary detector
 Isomer tagging
 Triggering
 Particle identification
 Neutron detection
-) With/Without magnetic field

## Slide 13: Inverse Kinematic: what is needed
What we measure:
Beam
 (3D) track
 Energy (Ebeam) at the reaction point known from vertex determination
 excitation function reconstruction
Reaction Products
 Angle θlab
 Energy, Eprod (Bragg curve, range, curvature in a magnetic field)
Cross Sections: dσ/dΩ(E,θ)
What we need:
Detector with excellent Position (< 1 mm) & Energy resolution (a few %)
6He beam
6He
4He
pAT-TPC
He/CO2 (1 atm)

## Slide 14: ACtive TARget and Time Projection Chamber (ACTAR TPC)
Two operational modes:
ACTAR mechanical design
TPC designed to include additional detectors (e.g. Si-PIN):
• tracking of particles escaping the drift region
 reaction studies and active target mode
• additional position and energy information
used also for commissioning
Bulk micromegas
220 um avalanche gap
(also possibility to use GEM)
B. Mauss et al., NIM A 940 (2019), 498-504.
(iC4H10) gas at 100 mbar

## Slide 15: Mu(μ)-PIC based Active target for Inverse Kinematics (MAIKo)
T. Furuno et al., NIM A 908 (2018), 215-224.
Ancillary Si-CsI(Tl) detectors used to generate trigger
And measure Energy of particle escaping the volume

## Slide 16: Active-Target TPC @ Facility for Rare Isotope Beams (FRIB)
pAT-TPC
Active volume 25 liters
(L = 50 cm, Ø = 25 cm)
Cylindrical pad plane (1,000 pads)
Full scale AT-TPC
‣ Active volume 200 liters
(L = 100 cm, Ø = 50 cm)
‣ 10,240 triangular pads
‣ Placed inside 4 Tesla solenoid
Cortesi et. al. EPJ Web of Conferences 174, 01007 (2018)
Ayyad et al. Eur. Phys. J. A (2018) 54: 181
M-THGEM
Position-sensitive MM
AT-TPC Readout pad  GET electronics
Cylindrical configuration:
Use with solenoid
 Magnetic field for PID
Problem:
Need to suppressed beam!
 Smart-ZAP
Gain Provided mainly by M-THGEM
Position-sensitive MM for track encoding
Position-sensitive
micromegas pad
Field Cage

## Slide 17: AT-TPC project @ FRIB
E20009  pure D2 (760 Torr)
10Be(d,p)11Be
The cinnamon roll: 8 MeV p (5 m range)
SOLARIS (up to 4 Tesla)
E20020  pure He (700 Torr)
4  decay of 16O
The big Kraken: 5 -particle tracks
Spokesperson: Clementine Santamaria
Spokesperson: Daniel Bazin
More Tracks
D. Bazin Courtesy

## Slide 18: TPC for Neutron Induced Fission Fragment Tracking Experiments
n
Motivation: Study and improve cross section ratio systematics
NIFFTE: two-chamber MICROMEGAS TPC  precision cross section measurements of neutron-induced fission
range
Energy (ADC)
N Beam
Position-sensitive MM board with 2976 pad (2 mm wide)
Fixed target
Gas: 95% argon, 5% isobutane
α-particle
252Cf fission

## Slide 19: MM-THGEM for Fission Fragment experiments
Goal: Understand Fusion-Fission and quasi-Fission reaction mechanisms  production of super-heavy elements
CFFD (NSCL)
Heavy-ion Imaging system:
Velocity vector
 Mass/Angle distribution
Esum
Time (ns)
PPAC-based tracking system
Requirements:
-) Large area, low pressure
-) Resolution < 1 mm (FWHM)
-) Modest rates (up to a few kHz)
MM-THGEM imaging detector prototype (10x10 cm2)
Performance:
-) Spatial Resolution < 0.5 mm (σ)
-) Time resolution ~ 1 ns (σ)
10x10 cm2
Fission events
Isobutane (7 Torr)
252Cf (sf)

## Slide 20
Motivation: Free neutron lifetime measured in beam and in bottle are ~4σ away!
Different observables measuring different decay modes?
TPC for exotic decays studies: Neutron lifetime puzzle & Dark decay
Bottle
Beam
Possible explanation (Fornal and Grinstein):
-) the neutron decay to a dark matter particle
 3 different decay mechanisms could be possible
-) A branching ratio of ~1% would explain the n lifetime puzzle
Fornal and Grisntein
PRL 120, 191801(2018)
Pfutzner, PRC 97, 042501 (2018)
Suggestion: Dark decay also possible in halo nuclei (weakly bound n)  Sn<1.572 MeV
Possible candidates: 6He, 11Li, 11Be, 15C, and 17C
 branching ratio upper limit of 10-4 depending on the dark particle mass.
11Be  10Be (β-delay proton emission + dark decay)
 measured using AMS with a branching ratio of 8.3(9) ·10-6

## Slide 21: Dark decay Scenarios
Scenario 3
Scenario 2
Scenario 1
Tang et al., Phys Rev Lett 121 (2018), 022505
Sun et al., Phys. Rev. C
97 (2018), 052501
(?)
X
X
Fornal and Grisntein, PRL 120, 191801(2018)

## Slide 22: First observation of a β- delay proton emission!
11Be
β- track
α-particle track
Example of tracks from a
beta(minus)-delay alpha emission
7Li track
Calorimetry is not enough for PID!
pAT-TPC  tracking of particles with two order of magnitude difference in specific ionization density
MPGD-based TPC readout for dark decay search
α and 7Li
α
α* and 7Li
7Li*
β background
and proton
region
Y. Ayyad (NSCL) et al., Phys. Rev. Lett. 123, 082501
Micromegas + M-THGEM
He:CO2
390 keV/u
PID based on analysis of dE
Proton
7Li
(11Be  10Be + p) branching ratio results (10-5- 10-6) compatible with AMS 11Be  10Be value (8.3·10-6).
Beta-delayed proton decay of 11Be explained by an exotic near-threshold resonance that favors proton decay
 No room for dark decay!
E. Lopez-Saavedra et al., PRL 129 (2022), 012502

## Slide 23
Applications to exotic decays: The X17 Boson
-) Photo-production in 8Be* via p+7Li
-) Fraction of the photons converted into e+e- by IPC
-) Measure angular distribution of the e+e- pair
P. Schlüter et al, Physics Reports 75 (1981), pp 327-392.

## Slide 24: Decay and Internal Pair Creation (IPC): ATOMKI’s Anomaly
A.J. Krasznahorkay et al., Phys. Rev. Lett. 116 (2016) 042501
A.J. Krasznahorkay et al, J. Phys.: Conf. Ser. 1643 (2020) 012001

## Slide 25: Example of X17 search with MPGD tracking
Proposed Detector concept  Three detectors:
1) Timepix3  angle measurement
2) MWPC  angle and scattering measurement
3) MPGD-TPC  energy measurement and PID
X17 spectrometer at CTU
TPC readout based on 3 GEM foils
Track recognition with machine learning techniques
1) Unusual E×B configuration:
 Physics reconstruction under development from simulated tracks
A.F.V. Cortez et al., NIMA 1047, February 2023, 167858

## Slide 26: TPC with solid target for X17 boson search
p
e-
e+
e-
e+
Courtesy Y. Ayyad (AT-TPC collaboration)
M-THGEM+Micromegas
Target:
-) 400 μg/cm Lithium Hydroxide (LiOH)
-) 10 μg/cm Lithium Fluoride (LiF)
TwinSol – Notre Dame University (Indiana)
Single Beta
Gas filling: P10 @ 1 atm
Beam 1 μA
protons 1 MeV

## Slide 27: Studying smaller and smaller things…
Optical microscope  λphotons ~ 380-740 nm
Resolution > 200 nm
Electron microscope  λelectron = 2.5 pm (200 keV)
Resolution > 0.1 nm (limited by objective lens system)
21 century nuclear science  probe the nuclear matter in all its forms and explore their potential for applications
Build powerful microscope using particle accelerators
Example: In the 1960s Experiments at SLAC established the quark model and our modern view of particle physics “the Standard Model”
Fixed Target Particle
Accelerator experiment  λelectron ≈ 0.062 fm (20 GeV)
Resolution ≈ 0.1 fm

## Slide 28: Electron Ion Collider (EIC)
NNPSS at U. of Tennessee, Lecture on Electron Ion Collider, Abhay Deshpand
EIC science program:
-) Precision 3D imaging of protons and nuclei
-) Solving the proton spin puzzle
-) Search for saturation
-) Quark and gluon confinement
-) Quarks and gluons in nuclei
At least one large-acceptance detector that can capture most of the particles scattering from the collisions in all directions and at wide range of energies.
Polarized electron-proton/light ion & electron-Nucleus collider
Many baseline EIC detector designs involved various gaseous detectors technologies for tracking in the central as well as end cap region

## Slide 29: EIC detector and tracking requirements
p/A
e
Central Detector Layout
MPGD readout
MPGD R&D
Tracking detectors provide:
➢ Space point coordinates and trajectory of charged particles  Vertex
➢ Momentum measurements in magnetic (B) field
➢ Angle measurements
➢ Measurements of primary and secondary vertices
➢ Multitrack separation
➢ Particle identification (if possible)
➢ Low material budget to minimize scattering and secondary interactions.
Selected tracking detector technologies:
Hybrid tracking detector design: Monolithic Active Pixel Sensor (MAPS, ITS3) based silicon vertex/tracking subsystem, the MPGD tracking subsystem and the AC-LGAD outer tracker, which also serves as the ToF detector.
Electron – photon separation: charged particles leave a track while the photon interact at most once

## Slide 30: MPGD for tracking/Vertex
Barrel Main Tracker
Hermetic coverage, close to 4π acceptance
  pseudorapidity range up to +/-1
  Large area detectors
Low material budget on the level of 3-5% of X/X0 for the central tracker region
  Gaseous detectors
Spatial resolution below 100 μm
Minimization of ion back flow with quad-GEM (ALICE TPC)
Example of proposed concept: GEM for gas amplification
Readout based on μRWELL and capacitive coupling

## Slide 31: EIC Focused R&D projects
Sourav Tarafdar, MPGD as tracker for EIC. CPAD workshop Stanford 2023

## Slide 32: Directional Detection
Directional Recoil Detectors
  enable 3D track reconstruction for vector directionality
  reconstruction of incident particle directionality
Many science applications (at different energy scale)
S. Vahsen et al Annu. Rev. Nucl. Part. Sci. 2021. 71 189-224
Example of Detector performance requirements:
(if targeting solar neutrinos & mDM= ~10 GeV)
Event-level recoil directionality
  angular resolution ≤ 30 degrees
  excellent head/tail sensitivity
• Rejection of internal electron backgrounds
  by factor >= 10 for 1000 m3 detector
• All of above down to Erecoil ~ 5 keV
• Energy resolution ~ 10% at 5.9 keV
• Timing resolution ~ 0.5 h
Gas TPC  time-resolved recoil imaging, enabling broad physics program beyond DM cost-effective: non-cryogenic and easily scalable to large volumes

## Slide 33: Directional DM search using NI-OTPC
 Optical TPC readout and negative ion drift for directional nuclear recoil detection: Low-pressure, direction-sensitive TPC
Example: Dark Matter Search
Detection of T/H direction
Measure spatial ionization
distribution resulting from
nuclear recoils
Experimental approach:
Target (He, CF4) + Highly electronegative gas (CS2, SF6, …)
Conventional OTPC
5.9 MeV α-particles
NI-OTPC
D. Loomba (UNM)

## Slide 34: Directional DM search via Migdal Effect
 Use Migdal Effect in DM search to extend the sensitivity to low mass region (mDM < 1 GeV).
How it works: OTPC to record the two simultaneously tracks, from the Migdal electron & the nuclear recoil, both originating from the same vertex
DM
DM
DM
DM
DM
DM
Simulation of DM events
From P. Majewski (STFC)
Glass-THGEM as gas avalanche light multiplier
DM
-) Low-pressure gas: 50 Torr of CF4
 extended particle track
-) TPC Signal amplification
 NI low diffusion for high resolution
-) Optical Readout
 High SNR
-) Electron and nuclear recoil tracks
 Directionality (common vertex)
Trigger
(z-axis)
Localization
(x,y axes)

## Slide 35: The Cryogenic Frontier for Rare Event Search
Read-out elements of cryogenic noble liquid detectors  Rear event detectors (n, DM) & Medical Physics (PET)
  Detecting the scintillation light produced in the noble liquids
  Options of scintillator light and ionization charge detection by a same detector!
S.Duval et al., JINST 6 (2011) P04007
Bondar et al., NIMA 556 (2006) 273
& Rubbia group ETHz - LArTPC
with windows
Windowless (2-phases)
Operated in Cryogenic Liquid

## Slide 36: Noble liquid radiation medium as detector
A. Breskin, FRIB seminar 2023

## Slide 37: Dual-phase liquid noble-gas TPC
A. Breskin, FRIB seminar 2023
A. Breskin, FRIB seminar 2023

## Slide 38: LArTPC for Dune
DUNE originally considered two LArTPC technologies: Single-Phase and Dual-Phase

## Slide 39: Proto-DUNE TPC
Single vs Dual

## Slide 40: MPGD: cryogenic R&D (Concept Gallery)
A.Buzulutskov et al, IEEE TNS 50 (2003) 2491;
A.Bondar et al, NIMA 524 (2004) 130
A.Bondar et al, NIMA 556 (2006) 273
A.Rubbia, J. Phys. Conf. Ser. 39 (2006) 129
A.Buzulutskov, A.Bondar, JINST 1 (2006) P08006
Y.L.Ju et al, Cryogenics 47 (2007) 81
A. Bondar et al, JINST 5 (2010) P08002
A.Buzulutskov et al, EPL 94 (2011) 52001
Periale et al, IEEE TNS 52 (2005) 927
M.Gai et al, Eprint arxiv:0706.1106 (2007)
D.Akimov et al, JINST 4 (2009) P06010
A.Bondar et al, JINST 3 (2008) P07001
Lightfoot et al, JINST 4 (2009) P04002
D.Akimov, NIMA 628 (2011) 50
S. Duval et al, JINST 6 (2011) P04007
S. Duval et al, JINST 4 (2009) P12008

## Slide 41: Bubble-assisted Liquid Hole Multiplier LHM
A. Breskin, FRIB seminar 2023

## Slide 42: Summary
General intro Gaseous Detector applied fields beyond HEP
  Example of requirements HEP vs LENP
Application to HENP/LENP
  R&D project with MPGD for EIC
  Active Target TPC, inverse kinematic nuclear reactions study
    -) physics, technology, challenges, ...(Operation pure elemental gas)
    -) Examples of Active Target TPC project
  Fission Fragment imaging system
Rare Event Search Applications & Neutrino Physics
  Exotic decays with MPGD-TPC (Dark Decay, X17 boson, etc..)
  Directional TPC (Negative-ion OTPC)
  Cryogenic detector: mostly exotic ideas