## Slide 1: Recuperation systems for fluorinated gas at the CERN LHC Experiments
Maria Cristina Arena EP-DT-FS gas team and University of Pavia
EP-DT seminar, 28/02/2024

## Slide 2
Outline
Introduction
  LHC gaseous detectors
  Focus on GHGs at CERN
  CERN strategies for reducing fluorinated gas emissions
  Separation techniques
Recovery systems:
  CMS CSC CF4
  LHCb RICH2 CF4
  LHCb RICH1 C4F10
  CMS RPC R134a
Conclusions

## Slide 3: INTRODUCTION

## Slide 4: LHC gaseous detectors
Gaseous detectors are installed in all of the four main LHC Experiments and in many not-LHC facilities
Among gaseous detectors, there are: Muon systems (located in the outermost region, covering large surface areas) Trackers (located closer to the interaction point, usually operated in high-rate environments) Particle identification systems (used to identify charged particle momenta)
They are used for: Triggering (e.g., Resistive Plate Chambers, Cathode Strip Chambers, Drift Tubes) Tracking (e.g., CSC, DT) Particle identification (e.g., RICH)
CMS CSC
CMS RPC
RICH1
RICH2
LHCb

## Slide 5: LHC gas mixtures
Depending on the purpose and the geometry of the detectors, different gas mixtures are required
Some detectors work with a single pure gas:
  C4F10
  RICH1
Other detectors need mixtures with 2 up to 4 components CO2/Ar-CO2/Ar/ CF4 – CO2/ CF4
  CSC
  MWPC
  RICH2
  GEM
  DT
  C2H2F4/iC4H10/SF6
  RPC
  MID
  TOF
Some of these gases are GREENHOUSE GASES (GHG)
Notes: Fare schema invece di lista  gas freccia e detector (esempio)

## Slide 6: Global Warming Potential (GWP) and GHG emissions at LHC
Greenhouse Gases (also known as GHGs) are gases in the earth’s atmosphere that trap heat.
Global warming potential (GWP) is an index to measure of how much infrared thermal radiation a GHG would absorb over a given time. It is expressed as a multiple of the radiation that would be absorbed by the same mass of added carbon dioxide, which is taken as a reference gas.
Gas | Atmospheric lifetime | GWP100 years
CO2 | 50-200 years | 1
R-134a | 14 years | 1430
CF4 | 50,000 years | 7390
C4F10 | 2600 years | 9200
SF6 | 3200 years | 22800

## Slide 7: GHGs consumption and cost at CERN
https://doi.org/10.25325/CERN-Environment-2023-003
The use of gas mixtures containing fluorinated compounds account for about 78% of the Organization’s direct emissions
CERN’s objective is to reduce its GHGs emissions by 28% by the end of Run 3 (baseline 2018)
Thanks to the strategies adopted for reducing the emissions, the intense campaign performed during LS2 to repair leaks, especially in CMS and ATLAS, R&D activity (Gas recirculation, Gas recuperation and new more eco friendly mixtures), for the first months of Run 3 the emissions due to particle detectors decreased respect to Run 2
Since 2014 new EU legislation 
Since 2021 the GHG consumption allowed is 45% respect to the average 2009-2012 consumption
F- gases banned if more eco friendly alternatives are available
New strategies for controlling and preventing emissions
% GHG consumption reduction respect to 2009-2019 consumption (EU ETS)
Average R134a price variation in EU (from 2014)
CERN scope 1 emissions for 2017-2022

## Slide 8: CERN strategies for reducing emissions of GHGs
In collaboration with Experiments and the CERN Environmental Protection Steering board

## Slide 9: CERN strategies for reducing emissions of GHGs

## Slide 10: Gas Recirculation
PROS
  Reduction of gas consumption
CONS
  Lot of parameters need to be controlled, as flow, pressure, etc.
  Accumulation of impurities such as fluorides (if fluorinated compounds are present in the gas mixture), oxygen and nitrogen
  Additional modules to the gas system in order to purify the gas mixture

## Slide 11: CERN strategies for reducing emissions of GHGs

## Slide 12: Gas Recuperation
Some detectors cannot work with a 100% recirculated flow, usually for air accumulation in the gas mixture
Most of the systems work with a recirculation fraction of 90% (detector requirements)  10% sent to the atmosphere
In some cases, this gas is sent to recovery plants where the GHG is separated from the other components, stored and then re-injected in the mixer through a dedicated line
PROS
  Further reduction of gas consumption
CONS
  Higher complexity
  R&D activities to design custom made systems, maintain and improve the efficiency
  Gas analysis to monitor the quality of recuperated gas
Notes: Togliere testo

## Slide 13: Gas separation techniques
DISTILLATION
CMS RPC R134a
CMS RPC SF6
Old LHCb RICH1 C4F10
New LHCb RICH1 C4F10
MEMBRANE SEPARATION
CMS CSC CF4
LHCb RICH2 CF4
ABSORPTION
DESORPTION
PRESSURE & THERMAL SWING ADSORPTION (PSA & TSA)
CMS CSC CF4
LHCb RICH2 CF4
Old LHCb RICH1 C4F10
Notes: Aggiungere absorber

## Slide 14: Gas separation techniques Membrane separation
selectivity
Permeability A
Permeability B
Ability of a membrane to separate two molecules
Separation process is driven by 
  Partial pressure gradient
  Nature of membrane (chemical structure)
  Permeability (P)  capability of a membrane to permeate gas molecules
  Solubility (S) thermodynamic parameter given the amount of penetrant absorbed by membrane
  Diffusivity (D)  dependent on geometry of penetrant: if molecular size increases the coefficient decreases
Transport of gas is described by the solution-diffusion mechanism  difference in thermodynamic activities existing across the membrane and interacting forces working between membrane material and permeating molecules
Notes: Aggiungere absorber

## Slide 15: Gas separation techniques Distillation
Purification method to separate 2 or more compounds based on differences in boiling points or volatility
Schematic view of a distillation column
The composition of vapor phase depend on the initial one of the liquid phase  lighter (lower-boiling) component tend to concentrate in vapor phase heavier (higher-boiling) component tend toward the liquid phase
Simple distillation  Can be used when the components have widely different boiling points (>100˚C)
Fractional distillation  Subsequent vaporization-condensation event (called a "theoretical plate"), and each event enriches the distillate in the lower boiling component. Specific packed columns are used for this purpose
Typical liquid-vapor plot
Notes: Aggiungere absorber

## Slide 16: Gas separation techniques Thermal Swing Adsorption & Pressure Swing Adsorption
ABSORPTION
DESORPTION
THERMAL SWING ADSORPTION (TSA)  After the contaminants have been absorbed, the sieve bed is heated, usually using a clean hot stream of pure gas, to regenerate the MS for reuse. Then it is cooled down to restart the process. Temperature regeneration is the most effective one.
PRESSURE SWING ADSORPTION (PSA)  gas feed stream fed to the sieve beds at high pressure and then the sieve bed pressure is reduced to regenerate the MS and remove adsorbent contaminants. Vacuum regeneration has the advantage of not overheating the material, avoiding break down processes.
Schematic view of an absorber module of gas system
MS 3A
MS 4A
MS 5A
MS 13X
Structure model of 4Å molecular sieve
Crystalline metal aluminosilicates having a three-dimensional interconnecting network of silica and alumina tetrahedra
Notes: Aggiungere absorber

## Slide 17: Monitoring of gas quality
Gas recirculation and gas recuperation systems imply the need to monitor both the quality of the recuperated gas and the gas circulating in the loop
uGC analysis
IR analysis
Detector based analysis
Notes: Aggiungere absorber

## Slide 18: CMS CSC CF4 Recovery system

## Slide 19: CF4 recovery plant Overview
First plant for CF4 warm adsorption, non-standard gas system
Gas mixture to separate Ar/CO2/CF4 : 40/55/5 or 40/50/10
Full software control on plant parameters
Modules:
  Input to plant
  Membrane separation module
  CO2 adsorption module
  CF4 adsorption module
  CF4 compression module
  CF4 injection module
  Infrared analysis module
  SWPC monitoring module
Plant operational since 2012, a lot of tuning and upgrades realized

## Slide 20: CF4 recovery plant Recuperation process
Phase 0  CSC gas mixture is injected in the first module of the recovery system from the Exhaust module
Phase 1  the gas passes through the membrane module optimized for the CO2 separation; CF4 is recovered at the retentate side with 15% of Ar, 0.4% of CO2 and 2% of N2
Phase 2  All the remained CO2 is absorbed in the MS 4Å
Phase 3  CF4 is absorbed in the MS 13X, N2 and Ar are vented and the CF4 is then recovered through pressure swing adsorption
Phase 4 (3b)  CF4 is extracted and stored in the battery, ready to be reinjected in the mixer
Ar ~ 10% CF4 ~ 89.6%
N2 ~ 0.4%
Main contaminants: O2 and N2

## Slide 21: CF4 recovery plant R&D Membrane module
 | Model | Working flow | Specifications
Membrane 1 | CO-C10 | Up to 300 l/h | High thickness and density gradient
Membrane 2 | CO-C10A | Up to 300 l/h | High thickness and density gradient
Membrane 3 | CO-C10A | Up to 300 l/h | High thickness and density gradient
Membrane 4 | CO-410A | More than 600 l/h | High thickness and density gradient
Memb. Highly sensitive | CO-C07FS | Up to 300 l/h | Reduced thickness and density gradient
=
Feed
Permeate (negative pressure)
Retentate (positive pressure)

## Slide 22: CF4 recovery plant R&D Membrane module - Results
Increasing the feed flow, the recuperation efficiency increases for all the membranes tested
Ar fraction in retentate stream is a contamination of our recuperate gas  C07FS not good for our purpose
The general efficiency of membrane module increase with the feed flow  smoothing and stabilization of CSC exhaust flow
Notes: Sistemare asse y

## Slide 23: CF4 recovery plant R&D CF4 13X Absorber Module
Last separation module of CF4 recovery system
Molecular sieve 13X
Working principle: Pressure swing adsorption
4 steps at 4 different pressure values:
  Column filling (from -0.9 barg to -0.050 barg)
  Separation phase
  Venting of components not absorbed by MS (from-0,050 barg to -0.450barg)
  Emptying of column (from -0.45barg to -0.9 barg)

## Slide 24: CF4 recovery plant R&D CF4 13X absorber module - Results
Chart: Ar low limit pressure vs Recuperation efficiency
| 44229.02847222222 | 44229.284722222219 | 44229.451388888891 | 44229.618055555555 | 44229.8125 | 44230.041666666664 | 44230.208333333336 | 44230.333333333336 | 44230.5
-0.7 bar | 0.493 | 0.505 | 0.512 | 0.499 | 0.499 | 0.499 | 0.493 | 0.432 | 0.487
-0.6 bar | 0.635 | 0.647 | 0.647 | 0.623 | 0.661
-0.55 bar | 0.709 | 0.708 | 0.697 | 0.709 | 0.722 | 0.709 | 0.641 | 0.69 | 0.696 | 0.708 | 0.69 | 0.629 | 0.665 | 0.679 | 0.684 | 0.678 | 0.678 | 0.679 | 0.69 | 0.678 | 0.659 | 0.69
-0.5 bar | 0.746 | 0.733 | 0.703 | 0.733 | 0.647
Efficiency | 0.245 | 0.304 | 0.588 | 0.37 | 0.684 | 0.335 | 0.596 | 0.49 | 0.524 | 0.552 | 0.516 | 0.591 | 0.513 | 0.771 | 0.785 | 0.747 | 0.653 | 0.731 | 0.911 | 0.585 | 0.853 | 0.668 | 0.766 | 0.757 | 0.735 | 0.745 | 0.754 | 0.645 | 0.644 | 0.682 | 0.738 | 0.632 | 0.642 | 0.747 | 0.828 | 0.843 | 0.73 | 0.48 | 0.758 | 0.63 | 0.472 | 0.745 | 0.495
Many tests performed to find out the best pressure value to start the CF4 recovery
Tradeoff between quality of recuperated CF4 and total recuperation efficiency
ANALYSIS CF4 ABSORBER
Before optimization
Ar 17.14% CF4 80.95% O2 460 ppm N2 37625 ppm
After optimization
Ar 1.78% CF4 97.16% O2 173 ppm N2 2646 ppm
CF4 RECUPERATION EFFICIENCY
Before optimization
45%
After optimization
66%

## Slide 25: CF4 recovery plant Recuperation batteries
Problem with pump module
2023-2024 average composition of the battery
Ar 11% CF4 88% N2 1.9%
O2 0.2%
Problem with pump module
The N2 concentration is reduced by a factor 10 in the recuperation system
Considering that CF4 (10% in the CSC mixture) is injected 50/50 fresh/recuperated, the N2 reinjected in the mixer is of the initial concentration

## Slide 26: CF4 recovery plant Software
Dedicated mixer line for CF4 recuperated

## Slide 27: CF4 recovery plant Recuperation summary
Efficiency mean value: 70% in the period January-November 2023, (higher than 2021 and 2022, 65% and 51% respectively)
In 2023, out of 358 m3 of CF4 injected into the mixer, 242 m3 were recovered CF4 (70%)
2023  300m3 and 60kCHF saved
2012  42m3
The CF4 recuperation system is also important to overcome possible CF4 shortage  in 2023 no fresh CF4, without CSC no CMS data taking!

## Slide 28: LHCb rich2 cf4 recovery system

## Slide 29: LHCb CF4 recovery plant Overview
Recovery system used when the detector is filled or emptied
LS2  detector filled with 100% CO2
Run 3  92/8 CF4/CO2
4 volumes of gas needed to have the correct gas mixture in the RICH2, lot of GHG exhausted
Full software control on plant parameters
Modules:
  Input to plant
  Membranes
  Compressor module
  Storage battery
The recovery system is not projected to work in continous since a control of paramaters is needed
Membrane 2
Membrane 1
Pump 1
Pump 2
Plant Input
To Purifier/Storage
Exh
GC
ExhGC

## Slide 30: LHCb CF4 recovery plant Software

## Slide 31: LHCb CF4 recovery plant Recuperation setup
Membrane 2
Membrane 1
Pump 1
Pump 2
Plant Input
To Purifier/Storage
Exh
GC
ExhGC
Membrane 2
Membrane 1
Pump 1
Pump 2
Plant Input
To Purifier/Storage
Exh
GC
ExhGC
Membrane 2
Membrane 1
Pump 1
Pump 2
Plant Input
To Purifier/Storage
Exh
GC
ExhGC
Single membrane
Double membrane
Double membrane with reinjection
Membrane Performance

## Slide 32: LHCb CF4 recovery plant Recuperation process – Emptying
Recuperation started with a composition of 60/40 CF4/CO2
#Hours of Recovery Plant Operation
0
100
200
300
400
500
]
3
Volume [m
4
CF
0
5
10
15
20
25
30
Membrane Output
Storage Battery
Recuperated CF4 volume
28.5m3 of recuperated CF4 at the end of operation
Recuperation efficiency of 65% (lot of CF4 when gas system turned off before the LS2 due to changing in atmospheric pressure)
CF4 Membrane Efficiency
Significant drop in the recuperation efficiency due to CF4 concentration at the input lower than 20%

## Slide 33: LHCb CF4 recovery plant Recuperation process – Filling
PHASE 1
RECUPERATION MODE
Injection on the bottom part of the detector
Exhaust from the top part  almost only CO2 exhausted
PHASE 2
PROCESS STARTED IN OPEN MODE
Phase 2 started with 37% of CF4 in the loop
Single membrane configuration until 70% of CF4 present in the loop, then double membrane configuration to recover the huge volume of CF4 in the permeate stream
CF4 from retentate side sent back to the loop
Permeate stream exhausted
Increase of CF4 concentration at the input of the membrane module  Increase of recuperation efficiency

## Slide 34: LHCb rich1 c4f10 recovery system

## Slide 35: C4F10 recovery plant Overview
Recovery system used for detector filling, emptying or cleaning
Old recuperation system used for DELPHI  New recuperation system installation by end of 2024
LS2/EYETS  detector filled with 100% CO2
Run  100% C4F10
2 volumes of gas needed to have the correct gas in the RICH1, lot of GHG exhausted
Some parameters can be controlled by software but lot of manual control needed  operator must be there during operation
Modules:
  Input to plant
  Cold box
  Bottle for recovery and injection
Recuperation is critical due to C4F10 shortage

## Slide 36: C4F10 recovery plant Software

## Slide 37: C4F10 recovery plant Recuperation setup
Recuperation started with 30% of C4F10 at the Exhaust
Gas mixture sent to liquifier (-15°C)  C4F10 liquified, air and CO2 exhausted to air
Pressure in liquifier set by pressure in the bottle  it must be higher to let the liquid go inside
Due to high pressure (3-5 barg) some CO2 is solubilized in C4F10 and then recoverd in the bottle  contamination
Different composition of gas and liquid phase in the bottle

## Slide 38: LHCb C4F10 recovery plant Recuperation summary
Since Run 3, recuperation procedure done 5 times  80% of efficiency
Some C4F10 lost to the exhaust of liquifier due to a lack of software control on the recovery system
The nagative value is due to the fact that the pump is located in the surface gas room while the detector is 100m underground. The pressure changes based on the ratio between the two gases

## Slide 39: C4F10 recovery plant New recovery systems
Double Stage Equilibrium
(conservative approach since ~equal to present system)
Distillation Columns
(better performance expected, but more difficult to tune)

## Slide 40: CMS rPC R134a recovery system

## Slide 41: RPC R134a RECUPERATION Plant Overview
ELECTRICAL RACK
SEPARATION MODULES
CHILLER
COMPRESSOR
New system installed in April 2023 and commissioning in May 2023
Goal: to recover the R134a from the mixture R134a/SF6/iC4H10 95.2/0.3/4.5
Problem: R134a forms an azeotrope with iC4H10
2 racks for the separation columns, 4 columns
The system was designed to work both in series and in parallel
The plant was designed following the tests done with prototype between 2020 and 2022

## Slide 42: RPC R134a RECUPERATION Software
Dedicated mixer line for R134a recuperated

## Slide 43: RPC R134a RECUPERATION Separation process
Chart: T-xy @ 1 bar
| 0 | 0.16459299999999999 | 0.28070699999999998 | 0.36488599999999999 | 0.427423 | 0.474881 | 0.51154599999999995 | 0.54029000000000005 | 0.56313299999999999 | 0.58135700000000001 | 0.59607699999999997 | 0.60799400000000003 | 0.61766500000000002 | 0.62549900000000003 | 0.63186900000000001 | 0.63699099999999997 | 0.64108799999999999 | 0.64431899999999998 | 0.64684600000000003 | 0.64873499999999995 | 0.65017400000000003 | 0.65116399999999997 | 0.65180700000000003 | 0.65193100000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65193500000000004 | 0.65203699999999998 | 0.652721 | 0.65381800000000001 | 0.65543399999999996 | 0.65769699999999998 | 0.66075899999999999 | 0.66480799999999995 | 0.67007099999999997 | 0.67683400000000005 | 0.68545299999999998 | 0.696384 | 0.71021199999999995 | 0.72770199999999996 | 0.74986600000000003 | 0.77805400000000002 | 0.81410400000000005 | 0.86054299999999995 | 0.920879 | 1
Bubble curve | -12.26 | -16.2697 | -19.5586 | -22.1584 | -24.226 | -25.8791 | -27.2066 | -28.2756 | -29.1394 | -29.8341 | -30.3934 | -30.8433 | -31.203 | -31.4868 | -31.7139 | -31.8893 | -32.0246 | -32.1269 | -32.2015 | -32.2548 | -32.293 | -32.3173 | -32.3319 | -32.3345 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3348 | -32.3349 | -32.333 | -32.3271 | -32.3147 | -32.2925 | -32.2565 | -32.2011 | -32.1199 | -32.0045 | -31.8443 | -31.6262 | -31.3335 | -30.9452 | -30.4349 | -29.7691 | -28.9055 | -27.7913 | -26.3612
Dew curve | -12.26 | -16.2697 | -19.5586 | -22.1584 | -24.226 | -25.8791 | -27.2066 | -28.2756 | -29.1394 | -29.8341 | -30.3934 | -30.8433 | -31.203 | -31.4868 | -31.7139 | -31.8893 | -32.0246 | -32.1269 | -32.2015 | -32.2548 | -32.293 | -32.3173 | -32.3319 | -32.3345 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3347 | -32.3348 | -32.3349 | -32.333 | -32.3271 | -32.3147 | -32.2925 | -32.2565 | -32.2011 | -32.1199 | -32.0045 | -31.8443 | -31.6262 | -31.3335 | -30.9452 | -30.4349 | -29.7691 | -28.9055 | -27.7913 | -26.3612
Azeotrope  mixture that exhibits the same concentration in the vapor phase and the liquid phase. This contrasts with ideal solutions with one component typically more volatile than the other
Slow heating of liquified azeotrope (blue curve) allows to enrich the liquid of R134a and the vapor phase of iC4H10
Thermodynamic simulation done by M. Bruno (PoliTO)

## Slide 44: RPC R134a RECUPERATION Plant Overview
Heat exchangers
Top Buffers
Bottom Buffers
Optimal conditions:
  Filling rate  200 l/h up to 600 l/h Chiller Temp.  -36.2°C Top buffer P  10 mbar (C1&C2), 35 mbar (C3)
  Bottom buffer T  20°C Emptying rate  600 l/h (air)
80% of Recuperation Efficiency
Compressor module
FLAMMABLE EXHAUST

## Slide 45: RPC R134a RECUPERATION Tests results
Lot of parameters tested for both single columns and entire system
Increasing the feed, more gas is lost at the exhaust due to lower heat exchange For the same reason, it increases decreasing chiller T
Increasing chiller T, more azeotrope is exhausted and the quality of R134a increases

## Slide 46: RPC R134a RECUPERATION Tests results
When the pressure in the top buffer increases, also the recuperation efficiency increases because less gas is sent to the exhaust line and more is recuperated
The effect is having more iC4H10 in the recuperated R134a  lower quality
Tradeoff between the two parameters

## Slide 47: RPC R134a RECUPERATION Recuperated R134a Quality
More than 70 tests were performed to find the best parameters for the plant
If we inject 50/50 R134a fresh/recuperated, with a flow of 700 l/h, we will inject: 500 ppm iC4H10

## Slide 48: RPC R134a RECUPERATION New SF6 recuperation plant
SF6: 0,126 iC4H10 : 0,22
R134a: 0,62
N2: 0,04
SF6: 0,00189
R134a: 0,85
iC4H10: 0,148
N2: 8,32-09
SF6: 0,013
iC4H10 : 0,7934
R134A : 0,19
N2 : 0,0036
SF6 : 0,591
iC4H10 : 1,27 E-10
R134A : 0,00022
N2: 0,408
SF6: 0,075
iC4H10 : 0,240
R134a: 0,684
N2: 1,23 E-13
Two distillation columns for reasonable reflux ratio (from 140 to 20/20)
output mixture composition:
59% SF6 , 40% N2, 1% freon + residue of isobutane
 Easier to separate in the second stage with a membrane or a MS that are more selective for SF6  test ongoing
Studies on SF6 solubility in R134a ongoing

## Slide 49: Conclusions
Common effort for reduction emissions  Gas system Team, Experiments and the CERN Environmental Protection Steering board
Fluorinated gases are responsible for more than 80% of CERN GHG emissions  strategies for reducing them is fundamental
In 2023, 560m3 of GHG were recuperated  10000 tCO2  -8% CERN emissions
4 operational recovery systems (2 CMS and 2 LHCb) and a new recovery systems by the end of 2024
New qualified operators for R&D and M&O of recovery systems engineers, chemists
Use of recuperation system implies more control on gas quality  daily gas chromatograph analyses and online monitoring systems (e.g., SWPC and IR)
Intense R&D activity to design new custom made recovery systems, improve the recuperation efficiency and the quality of recuperated gases
Recovery systems allowed to overcome critical situations when the new/fresh gas was not available

## Slide 50: Thanks for your kind attention