## Slide 1: Metallic beams and charge breeding
Collaborative R&D
EURISOL-net meeting, CERN, 26th- 27th of June
ISOL ion source & beam manipulation R&D
P. Delahaye, H. Franberg – Delahaye, T. Stora and F. Wenander for the « Hoplites » and « EMILIE » projects

## Slide 2: Why metallic beams and charge breeding are ‘hot topics’*
Metallic (+ halogen + non metallic) elements
  effusion times from ISOL targets are usually a penalty compared to rare gases
  High ionization efficiencies require dedicated developments (FEBIAD or RILIS), whereas for rare gases almost any ECRIS can do the job
N+ beams for post-acceleration
  SPIRAL concept: 0 to n+ ionization efficiencies are very high for rare gases
  BUT application to metallic beams not straightforward as ECRIS are cold wall sources
  1+ n+ (=charge breeding) works fairly well with EBIS but pulsed beams (not suited to GANIL experiments)
  1+ n+ with ECRIS works well in CW even with high intensities but several weaknesses:
    Comparably lower charge states
    Beam purity not guaranted
    Low efficiencies with light metallic beams: <5% up to K
* Seen from GANIL

## Slide 3: Collaborative R&D
SPIRAL Upgrade at GANIL: « hoplites » project
  Metallic beams from a FEBIAD
    VADIS from ISOLDE
  1+ n+ for SPIRAL with an ECRIS
    Phoenix ECRIS from Daresbury, tested at CERN, on a design from LPSC, recently given to GANIL
    upgrade with the help of LPSC and ANL
  Target development
    Nb, Y2O3 … targets with the help of ISOLDE
Charge breeding for future ISOL facilities: « EMILIE » project:
  Test of a CW EBIS charge breeder concept
    A Paul trap as debuncher
    REXEBIS –like charge breeder
    Partnership between GANIL, CERN ISOLDE, JYFL, LPC Caen and CSNSM Orsay
  Optimization of the SPIRAL 2 Phoenix ECRCB from LPSC
    INFN as task leader (A. Galata), optimization initiated for the SPES project
    LPSC, GANIL, JYFL and Warsaw as partners
Submitted to the french national research agency: ANR
Submitted to Nupnet
« EURISOL R&D »

## Slide 4: Latest news: SPIRAL upgrade
First beams from VADIS coupled to the SPIRAL targets
  Promising results with radioactive Cu, Fe, Mn
  Consolidation to be done
    Transfer tube broke after 5 days of heating

## Slide 5: Results: 1+ beams from VADIS
ISOTOPE | Half-life (s) | Power (W) | Measured 1+ intensity | 1+ intensity (1.5kW) | Efficiency/EPAX (%)
38K | 456 | 4 | 3.8E+04 | 1.5E+07 | 2.08E+01
38mK | 0.923 | 4 | - | - | 
53Fe | 510.6 | 34 | 6.6E+04 | 2.9E+06 | 1.07E+00
53mFe | 154.8 | 34 | 1.4E+04 | 6.1E+05 | 2.24E-01
58Mn | 3 | 37 | 5.7E+04 | 2.3E+06 | 
58Cu | 3.204 | 37 | 4.3E+03 | 1.8E+05 | 
59Cu | 81.5 | 38 | 7.3E+04 | 2.9E+06 | 
60Cu | 1422 | 35 | 2.5E+03 | 1.0E+05 | 
>105 pps!
From Gamma line intensities at saturation
Despite reliability and a rather low target temperature, the target ion source exhibits performances as good as one could wish!
PRELIMINARY
Contains:
Release efficiency (diffusion + effusion delays)
Ionisation efficiency

## Slide 6: Latest news: SPIRAL upgrade
First beams from VADIS coupled to the SPIRAL targets
  Promising results with radioactive Cu, Fe, Mn
  Consolidation to be done
    Transfer tube broke after 5 days of heating
Design of the new charge breeder ongoing
  Should be ready by December this year
  Booster upgrade – 2012 - Installation 2013
  First beams in SPIRAL at the end of 2013

## Slide 7: Latest news: « EMILIE » project
Evaluation of the « EMILIE » project is ongoing
  Results of the Nupnet call by the end of July

## Slide 8: Summary
The SPIRAL upgrade and « Hoplites » project
And the « EMILIE » project
Can bring interesting results concerning the charge breeding of metallic beams for EURISOL…

## Slide 9
… as it was (almost) considered in the EURISOL DS
P. Delahaye, O. Kester, C. Barton, T. Lamy, M. Marie-Jeanne, F. Wenander Eur. Phys. J. A 46(2010)421
EBIS + ECRIS in parallel
EBIS: High charge states
ECRIS: High intensities

## Slide 10: Latest news: SPIRAL upgrade
First beams from VADIS coupled to the SPIRAL targets
  Promising results with radioactive Cu, Fe, Mn
  Consolidation to be done
    Transfer tube broke after 5 days of heating
Design of the new charge breeder ongoing
  Should be ready by December this year
  Booster upgrade – 2012 - Installation 2013
  First beams in SPIRAL at the end of 2013
Unofficial news: ANR will not support « Hoplites » this year
  Application for funds to submit again next year
  Possible delays compared to the original planning if no support from ANR