## Slide 1: rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Mohammad Mehdi Rahimifar, Hamza Ezzaoui Rahali,
Audrey Corbeil Therrien
FastML 2024
Notes: Good afternoon, I’m Hamza, a phd student from the University of Sherbrooke, Canada. And in this talk, I’m going to be introducing rule4ml, which is an open-source tool we’re developing, where one of the main goals is to predict resource usage and latency of ML algorithms on FPGA.

## Slide 2
Larger models take hours
Keras, Pytorch or ONNX Architecture
Model Synthesis
Resources and Latency Reports
Vivado Implement.
hls4ml Configuration
If synthesis fails or exceeds available resources, latency constraints
Fast approximation using ML
Inputs
Outputs
Generate a Dataset of Synthesized NNs
Trained Predictor(s)
Feature Engineering and Training
Takes model architectures and synthesis configs as input
Predictions for all input combinations as Pandas Dataframe
Data Generation
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Motivation
1
14
/
Notes: Some of the previous talks showed how edgeML is becoming a popular solution for processing huge data rates close to the sources, especially in physics experiments with low-latency requirements. And I think a lot of us here are familiar with existing NN-to-FPGA pipelines such as hls4ml. Those who used such conversion pipelines in the past might also be familiar with the time-consuming cycle: You try to synthesize your model, but it either fails or exceeds the available resources of your board, or goes past your latency constraints. You then have to go back, modify your architecture or the config, possibly retrain your NN, and re-synthesize. This is where rule4ml comes in and offers an ML-based solution to estimate the resource and latency reports, using only input model architectures and conversion parameters. To do this, we first need to collect a large dataset composed of NN architectures and configs as inputs and resource and latency reports as outputs. Then we can train predictors for the regression task. At the end, the user can pick the most optimal architecture and parameters and do the synthesis while hopefully avoiding the time-consuming design cycle. This sounds great, but there are a few difficulties we face in practice, and the main one is the need for a large, high-quality dataset.

## Slide 3
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Large variety of NN architectures
C/RTL Synthesis
Logic Synthesis
Implementation
Report Accuracy
Ease of Production
Most
Least
Most
Least
Wide range of hls4ml parameters
When to collect resource and latency reports?
Precision
Reuse Factor
Board
Strategy
FCNN
RNN
CNN
Transformer
Motivation
Inputs & Targets
Data Generation
2
14
/
Notes: Some of the previous talks showed how edgeML is becoming a popular solution for processing huge data rates close to the sources, especially in physics experiments with low-latency requirements. And I think a lot of us here are familiar with existing NN-to-FPGA pipelines such as hls4ml. Those who used such conversion pipelines in the past might also be familiar with the time-consuming cycle: You try to synthesize your model, but it either fails or exceeds the available resources of your board, or goes past your latency constraints. You then have to go back, modify your architecture or the config, possibly retrain your NN, and re-synthesize. This is where rule4ml comes in and offers an ML-based solution to estimate the resource and latency reports, using only input model architectures and conversion parameters. To do this, we first need to collect a large dataset composed of NN architectures and configs as inputs and resource and latency reports as outputs. Then we can train predictors for the regression task. At the end, the user can pick the most optimal architecture and parameters and do the synthesis while hopefully avoiding the time-consuming design cycle. This sounds great, but there are a few difficulties we face in practice, and the main one is the need for a large, high-quality dataset.

## Slide 4
Motivation
Inputs & Targets
Parameter | Value Range | Range Type
Input Size | [16, 1024] | Powers of 2
Layer Count | [2, 20] | Increments of 1
 | [2, 4096] | Powers of 2
Output Size | [1, 200] | Increments of 1
 | ReLU, Tanh, Sigmoid, Softmax | -
Precision | 2, 8, 16 | -
 | [1, 64] | Powers of 2
Board | Pynq-z2, ZCU102, Alveo-u200 | -
Strategy | Latency, Resource | -
Focus on generating FCNNs using parameters randomly sampled from pre-defined ranges
Neurons Count
Activations
Reuse Factor
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Collect RTL synthesis resource and latency reports
Make data generation an accessible part of rule4ml
Content set to evolve, either through user contribution, or group collaboration
First Dataset Iteration
Data Generation
3
14
/

## Slide 5
Motivation
Inputs & Targets
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Generated and synthesized ~15000 FCNNs (~29k CPU-core hours @ 2.2 GHz)
Training set: 95% of synthetic data.
Test set: 500+ models split from synthetic data.
Benchmark models: MNIST + 7 models from scientific applications + 3 custom models using several hls4ml configs; 900+ samples in total.
https://borealisdata.ca/dataverse/rule4ml
Saved as a large JSON file
TF 2.15.1 + Keras 2.15.0
hls4ml 0.8.1
Vivado 2019.1 (small changes with neighboring versions)
Meta data
Model + hls4ml configs
Resource information
Latency information
Data Generation
4
14
/

## Slide 6
Data Generation
Baseline Predictor
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Prediction Targets
DSP
BRAM
FF
LUT
Sequential Features
Global Features
Layer Counts (per type)
# Parameters (total and per layer type)
Averages (I/O, reuse, params)
Board
Precision
Strategy
Layer Type
Input Size
Output Size
Number of Parameters
Activation Function
Reuse Factor
Layer Type
I/O Size
# Parameters
Reuse Factor
Layer Type
I/O Size
Act Function
Reuse Factor
Input Layer
Dense Layer
Activation Layer
Layer Type
I/O Size
Reuse Factor
…
Layer Implementation
Add Op
Mult Op
Logical Op
Lookup Op
Cycles (Absolute Terms)
Inputs & Targets
Frequency
Values
5
14
/

## Slide 7
Inputs & Targets
Test Results
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Predictor | R2 Score |  |  |  | 
 | BRAM | DSP | FF | LUT | CYCLES
LSTM | 0.81 | 0.03 | 0.48 | 0.74 | 0.80
Transformer | 0.78 | 0.93 | 0.85 | 0.74 | 0.88
Random Forest | 0.89 | 0.88 | 0.79 | 0.83 | 0.86
GB Trees | 0.84 | 0.86 | 0.77 | 0.86 | 0.88
MLP | 0.92 | 0.85 | 0.72 | 0.85 | 0.87
Categorical Inputs
Numerical Inputs
Embeddings
Dense Block
Concatenate
Dense Block
Baseline Predictor
6
14
/

## Slide 8
Test Results
Baseline Predictor
Benchmark Results
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Does it work?
WE
70%
7
14
/

## Slide 9
Test Results
Baseline Predictor
Benchmark Results
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Test set: 500+ models split from synthetic data.
80% BRAM
89% DSP
88% FF
66% LUT
Error
85% Cycles Predictions
Cycles
(10 ns clock period => 1 μs)
MAE (%)
Resources values
are capped <= 200%
MAE (Cycles)
8
14
/

## Slide 10
Benchmark Results
Test Results
Package Structure
1: Ground Truth
2: Prediction
3: Failed Synthesis
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Pynq-z2, ap_fixed<8,3>, Reuse Factor 32
9
14
/
1
2
3

## Slide 11
Benchmark Results
Test Results
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Reuse Factor
%
Package Structure
ZCU102, Latency, 16-bit width
Pynq-z2, Resource, 2-bit width
1
2
4
8
16
32
64
4
8
16
32
64
2
1
10
14
/

## Slide 12
Benchmark Results
Test Results
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Package Structure
Reuse Factor
Cycles
1
2
4
8
16
32
64
11
14
/

## Slide 13
Package Structure
Bench. Results
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Quick Demo
rule4ml
data_gen
notebooks
parsers
models
12
14
/

## Slide 14
Quick Demo
Package Structure
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
13
14
/
Outlook
~30 lines of code
Preprocess + Inference 1.7s
21 Synthesis Prediction

## Slide 15
Outlook
Quick Demo
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Continue efforts to build a community around rule4ml.
What we
explored
Expand the dataset, include more architectures and configurations.
Formalize a benchmark for contributors.
(Ben Hawks lightning talk)
Experiment beyond resource and latency estimation.
14
14
/
~15000 FCNNs

## Slide 16
Thank You!

## Slide 17
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
ZCU102, ap_fixed<8,3>, Reuse Factor 32

## Slide 18
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA

## Slide 19
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
DSP
BRAM
FF
LUT
Cycles

## Slide 20
rule4ml: Resource Utilization and Latency Estimation for ML on FPGA
Transformer Architecture
Each layer is treated as a “token” in the sequence